Source	MARKET NEWS
Date	06/17/2014
Time	05:39:46 AM

Company	 Savant Explorations Ltd.
Title	Ip 
Defines High priority Drill Targets On The Bu





    CDNX Symbol: SVT











Press Release	





SAVANT EXPLORATIONS LTD ("SVT-V")
- Ip Defines High-priority Drill Targets On The Buckhorn Copper
- Property, Arizona

Savant Explorations Ltd. ("Savant") is pleased to announce that a
recently completed Induced Polarization ("IP") survey on the Buckhorn
copper porphyry property in Arizona returned two strong chargeability
anomalies that warrant drill testing. One of the anomalies, referred to
below as Anomaly 1, coincides directly with an exploration target that
was established by the presence of key surface indicators of porphyry
copper mineralization which suggests that the IP anomaly may be related
to a buried copper porphyry body.

IP Survey Results - Buckhorn Property

The IP survey was conducted along two lines; a main east
north-east line of 4.2 kilometres in length and a northwest cross line
of 2 kilometres in length. The array used should detect chargeable
material to a depth of about 450 metres. The main survey line was
designed to test for porphyry copper mineralization beneath younger
post mineralization volcanic rocks east of basement rocks that host
distal porphyry copper-type alteration and where a basal conglomerate
at the contact of the younger volcanic and basement rocks contains both
fragments of leached porphyry rocks and exotic copper oxide.

A graphic presentation of the IP survey results is presented on a
plan map and a fence diagram of the IP chargeability section with
superimposed geology. The maps can be found on Savant's website at
www.savantexplorations.com and should be referred to when reading this
release.

The two anomalies, referred to as Anomaly 1 and 2, are defined by
chargeability levels that are at least three times background, which,
in this favourable geological setting, may suggest a metallic sulphide
source.

The Buckhorn property is one of three properties recently acquired
under option from Eurasian Minerals Inc. (TSX VENTURE:EMX)(NYSE
MKT:EMXX) through its wholly owned subsidiary Bronco Exploration Inc.
(see the Company's news release dated October 30, 2013).

Anomaly 1

Anomaly 1 is a 600 metre long feature that begins east of the
contact of the covering volcanic rocks. The eastern end of this anomaly
may mark the end of chargeable minerals or could be caused by the
easterly thickening wedge of volcanic rocks exceeding the depth limit
of the IP survey array. The north-westerly cross line indicates that
the anomaly is at least 600 metres wide. To the southeast on this cross
line, the anomaly may be offset by a fault that down-drops the zone
beneath the detection depth of the survey.

John McClintock, President & CEO of Savant commented, "The
location of Anomaly 1 east of the basement alteration is exactly where
we would expect to find a porphyry copper deposit buried at a shallow
depth beneath the younger volcanic rocks. The target is large,
potentially open at depth and to the southeast and northeast, and
represents a priority target for drill testing."

Anomaly 2

Anomaly 2 is approximately 800 metres long and occurs in an area
of covering river gravels and on a slope where the bed rock is covered
by talus from younger volcanic rocks. The feature is interpreted to be
flat lying, extending from surface to a depth of 250 metres. There is
no obvious explanation for the anomaly, but its position and associated
geology make it a compelling target for a shallow drill test.

IP Survey Specifications

Savant contracted Zonge International of Tucson Arizona to carry
out 6.4 line kilometres of induced polarization surveying on the
Buckhorn Property in May, 2014. The survey was a frequency domain,
dipole - dipole complex resistivity IP survey using a dipole spacing of
200 metres and readings from N 1 to 8. Zonge used a 30 Kw generator and
a 6 channel Zonge GDP - 3224 instrument. Data was decoupled and a 2D
smooth-model inversion of the data produced using Zonge's TSDIP
program. Based on the 2% sensitivity level of the inversion model, the
survey is conservatively looking to depths between 400 and 450 metres.
IP chargeability effect can be caused by metallic sulphides as well as
other minerals such as graphite, clays and magnetite.

Drill testing

Planning and permitting for a program of reverse circulation
drilling to test both Anomaly 1 and Anomaly 2 has commenced.

About Savant

Savant is an exploration and discovery stage company focused on
generating and exploring high quality precious and base metal
properties in stable jurisdictions. Savant has recently initiated a new
exploration and discovery strategy in Southwest United States with the
acquisition of the Buckhorn, Jasper Canyon, and Frazier Creek
properties. Savant also owns three other high-quality properties,
Yuby-Gabriela, Blue Moon and Yava that management is seeking to
monetize for maximum value to Savant and its shareholders. These other
properties and assets are 100% owned with combined annual holding costs
of approximately $30,000.

John McClintock, P. Eng., CEO of Savant is the Qualified Person,
as defined by National Instrument 43-101, responsible for the technical
data in this news release.

More information on the Company's activities is available at the
Company's website at www.savantexplorations.com.

Neither TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release contains forward-looking statements. These
statements are based on assumptions and judgments of management
regarding future events or results that may prove to be inaccurate as a
result of failure to obtain necessary regulatory approvals, the failure
to reach agreement on final documentation, exploration results and
other risk factors that are beyond Savant's control. There can be no
assurance that such forward-looking statements will prove to be
accurate as actual results and future events could differ materially
from those anticipated in such statements. Accordingly, readers should
not place undue reliance on forward-looking statements contained in
this news release.

TSX Venture closing price for SVT-V
Date: 2014/06/16
Closing Price: 0.04

TEL: (604) 568-5817           John McClintock
info@SavantExplorations.com   President and CEO
www.SavantExplorations.com    Savant Explorations Ltd.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1416700007TS11416700699-05381520140617