Source	MARKET NEWS
Date	06/17/2014
Time	04:12:32 PM

Company	 Victory Resources Corporation
Title	Clarification of Reforma Property Exploration Re





    CDNX Symbol: VR











Press Release	





Clarification of Reforma Property Exploration Results --->@NEWS RELEASE
VICTORY RESOURCES CORP ("VR-V;VRCFF-0")
- Clarification of Reforma Property Exploration Results

Victory Resources Corp. (the "Company") has been the subject of a
Cease Trade Order (the "CTO") in British Columbia since March 23, 2014.

The Company owns the Reforma property ("Reforma"), located at the
common boundary of Sinaloa and Chihuahua States, in west central
Mexico. A technical report, dated September 14, 2010 (the "Original
Reforma Report"), was prepared for the Company's by its Qualified
Person ("QP") in accordance with the requirements of NI 43-101.
After the date of the Original Reforma Report, the Company
continued to explore Reforma; however, a cohesive update to the
Original Reforma Report was not prepared. The totality of subsequent
exploration programs conducted by the Company at Reforma is material to
the property, and NI 43-101 requires the subsequent work to be included
in a current technical report. In addition, a current technical report
is necessary to verify and correct the Company's reporting of
subsequent exploration work and the results obtained. As a result, an
updated Reforma report, dated June 16, 2014 (the "Updated Reforma
Report"), has now been prepared and filed on www.SEDAR.com.
The Company's MD&A for the period ended November 30, 2013 has also
been amended and refiled.
To the extent that the Updated Reforma Report is inconsistent with
past public disclosures, this press release seeks to highlight the
resulting corrections and retractions.
In a press release of July 12, 2011, the Company disclosed certain
drill core results, some of which are not confirmed in the Updated
Reforma Report. The table contained in that press release is retracted
and is replaced with the following:
//st
Hole ID     From (m)  To (m)  Interval  Au    Ag   %    %      %
ppm   ppm  Cu   Pb     Zn

RDH-001     0.65      1.10    0.45      0.056 565  0.14 17.85  0.04
1.10      4.14    3.04      0.371  42  1.70  0.71  0.07
4.14      5.70    1.56      0.082  18  1.90  0.04  0.04
RDH-002     3.85      6.30    2.45      0.287  40  2.22  0.04  0.03
RDH-003 No Significant Assays              -    -     -     -     -
RDH-004     1.37      1.70    0.33      0.035 133  0.71  4.69 14.55
2.50      3.23    0.73      0.009  11  0.03  1.50  3.32
RDH-005 Hole aborted due to bad ground     -    -     -     -     -
RDH-006   200.85    203.85    3.00      0.089 118  0.88  1.44 12.45
RDH-007 No Significant Assays              -    -     -     -     -
RDH-008    34.24     36.72    2.48      0.037  75  0.87  3.46  6.96
36.72     39.26    2.54      0.013  13  0.09  0.62  1.40
40.11     43.09    2.98      0.021  35  0.14  0.27  1.32
43.09     46.07    2.98      0.008  14  0.08  0.62  1.50
146.23    149.00    2.77      0.122  47  2.05  0.03  0.19
149.00    151.79    2.79      0.090  26  1.54  0.009 0.05
RDH-009   No Significant Assays             -   -     -     -     -
RDH-010   No Mineralization Intersected     -   -     -     -     -
RDH-011   198.34    201.16    2.82      0.104 144  1.93  1.34  5.68
RDH-012   Hole aborted due to bad ground    -   -     -     -     -
RDH-013   No Significant Assays
RDH-014   No Significant Assays
RDH-015    11.91     14.92    3.01      0.018 4.2  0.21  0.007 1.20
42.43     45.46    3.03      0.024 62.2 0.27  1.33  4.03
//et
In press releases of August 9, 2012, October 13, 2012, January 9,
2013 and February 13, 2013, the Company reported the results of
underground sampling at Reforma. The news releases disclosed a zone of
80 m length with weighted average grades of 231 g/t silver, 0.84%
copper, 6% lead and 14% zinc, without reporting the thickness of the
zone. The compilations and reporting of sampling results for this zone
of underground mineralization was incomplete and potentially
misleading. The Updated Reforma Report clarified that out of 29 samples
collected, 24 are contiguous over a stretch of 55m. The samples were
taken every 3m across true widths ranging from 0.85m to 3.9m. Assay
results of the 24 samples returned weighted averages of 152.17g/t
silver, 0.53% copper, 8.63% lead and 0.91% zinc over an average width
of 2.08m.
Initial bulk sampling of tailings (each sample weighing 10kg) from
the "Matanza" and "Altamira" tailings ponds extracted from 13 backhoe
trenches were tested by assay and have been reported in the Updated
Reforma Report. The values reported in the Company's press releases of
March 1, 2012 and October 31, 2012 (most notably a typographical error
whereby 2.33% zinc was incorrectly reported as 12.33%) are restated as
follows:
//st
Matanza       Au      Ag       Cu       Fe       Zn      Pb
Sample        ppm     ppm      ppm      %        %       %
638747        0.076   12.4     0.08     11.25    0.86   0.2
638748        0.059   17.6     0.09      8.56    0.73   0.36
638749        0.052   10.7     0.06      7.74    0.58   0.19
638750        0.152   26.6     0.35     12.55    2.43   0.44
638751        0.149   60.8     0.36     12.6     2.86   1.28
638752        0.057   17.9     0.14      8.08    1.33   0.34
638753        0.081   44.1     0.16     10.8     1.91   0.78

Altamira      Au      Ag       Cu       Fe       Zn      Pb
Sample        ppm     ppm      ppm      %        %       %
638754        0.108   19       0.17     11.85    2.33    0.32
638755        0.104   12.6     0.15      7.88    0.95    0.25
638756        0.067   12.5     0.15      8.48    1.43    0.33
638757        0.035   10.8     0.09      8.41    0.42    0.27
638758        0.031    4.2     0.03      7.49    0.3     0.14
638759        0.098   10.2     0.08     11.05    1.26    0.29
//et
Each trench measured 0.70 m wide by 5.0 m long and 3.5 m deep.
Seven trenches were dug at the Matanza and six at the Altamira. Bulk
samples of 70 kg each of the Matanza and Altamira tailings were
subsequently run through a processing plant in Chihuahua, Mexico for
preliminary testing. No relevant results were obtained.
A total of 218 auger samples were taken from both tailings ponds
using a 4-inch diameter sand auger. The samples were collected at 1.5
metre intervals from each hole. The Company did not assay the samples
from any auger drill testing conducted and the samples are presently
stored at ALS Chemex, awaiting further instructions from the Company.
Ruben Verzosa, P. Eng., a Qualified Person (QP) as defined by
National Instrument 43-101, is responsible for the technical
information contained in this Press Release.

On behalf of The Board of Directors of Victory Resources Corporation
WALLY BOGUSKI, CEO

This news release contains certain forward looking statements which involve
known and unknown risks, delays, and uncertainties not under the control of
Victory Resources Corp. which may cause actual results, performance or
achievements of Victory Resources Corporation to be materially different
from the results, performance or expectation implied by these forward
looking statements.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that
term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this press release, which
has been prepared by management.



Website: www.victoryresourcescorp.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1416700074TS11416702852-16104620140617