Source	MARKET NEWS
Date	06/25/2014
Time	05:45:19 AM

Company	 MAX Resource Corp.
Title	Max Drills 
222.6 M @ 0.27% Cu And 10.1 G/t Ag, I





    CDNX Symbol: MXR











Press Release	





MAX RESOURCE CORP ("MXR-V;MXROF-L")
- Max Drills 222.6 M @ 0.27% Cu And 10.1 G/t Ag, Inclusive Of 117.4 M
- @ 0.43% Cu And 12.0 G/t Ag, In Oxides At Majuba Hill, Nevada

MAX Resource Corp. has received assays from the first core hole
drilled at it's Majuba Hill silver/copper/gold project in Nevada in
June 2014. This first hole, MMX-24, was drilled to a depth of 365.8
metres ("m") and intercepted 222.6 m @ 0.27% Cu and 10.1 g/t Ag,
inclusive of 117.4 m @ 0.43% Cu and 12.0 g/t Ag.MMX-24 was drilled
roughly parallel to and 85 m northwest and 25 m below the collar of
MAX's hole MM-21, drilled in 2012, which intersected 332 m @ 0.13% Cu
and 12 g/t Ag.

Drill hole MMX-24 was drilled from the opposite side of Majuba
Ridge as hole MM-21 and successfully tested the down-dip extension of
copper/silver mineralization intercepted by MM-21, hole DDH-4 drilled
by Freeport in 1940's, and hole MF-1 drilled by Minefinders in 1974.
The alteration of the mineralization is mainly potassium feldspar and
quartz and the probable copper mineralization is chalcocite and the
silver mineral acanthite and or chloargyrite. Alteration is increasing
as the holes are extended to depth and appear to be continuous. MMX-24
and MM-21 both intersected mineralization exposed at surface as copper
oxides running as high as 7.72% Cu (see our news release of February 5,
2014).

MMX-24 was collared approximately 415 m east-northeast of the
middle portal of the past producing Majuba Hill mine, where MAX
drilling in 2011 intercepted high grade copper/silver supergene oxide
mineralization over long intervals that included:

//st

Hole MM-07: 50.3 m of 50.8 g/t Ag, 0.31 g/t gold and 0.31% Cu

Hole MM-06: 96.0 m of 39.2 g/t Ag and 0.57% Cu, including 44.2 m of 71.0
g/t Ag, 0.15 g/t Au and 1.14% Cu

Hole MM-03: 42.7 m of 37.5 g/t Ag and 0.38% Cu

//et

Significant intervals from MMX-24 are summarized in the following
table:

//st
Hole  Azimuth  Angle   Total   From     To  Thickness     Cu     Ag
Depth    (m)    (m)        (m)    (%)  (g/t)
MMX-24  235.6  -43.9 365.8 m  114.3  336.9    222.6 m  0.27%   10.1

includes                      219.5  336.9    117.4 m  0.43%   12.0
includes                      219.5  288.1     68.6 m  0.61%   11.6
//et

Maps indicating the location of this drill hole as well as
locations from previous programs at Majuba Hill are available on our
web site at www.maxresource.com.

Analysis was performed by Bureau Veritas (Inspectorate), an ISO
certified facility in Reno, Nevada, using multi-element method MA330
(ICP-ES) techniques producing assays for a 30 element suite of
minerals. Over-limit analyses were performed according to procedure
MA410. No analysis was conducted for gold. Standards, duplicates and
blanks were used for quality control of the samples. After the core is
logged for each drill hole, the location of each site is located using
a GPS in UTM coordinates using NAD 83 datum. The core is then
hydraulically split and put into a sample bag which is labeled for each
interval and taken from the core facility to the Bureau Veritas
laboratory.

Majuba Hill is the site of numerous past producing mines, with
historic production reported of 12% Cu (Mason Valley Copper, 1918) and
silver grades up to 40 oz/t Ag. Majuba Hill encompasses 2,568 acres of
surface and mineral rights that includes patented lode mining claims.
The property is easily accessed via 23 miles of well-maintained dirt
roads leading from U.S. Interstate 80, and lies 30 miles northwest of
Coeur Mining's Rochester silver mine, which contains a NI 43-101
compliant Measured and Indicated Resource of 263.9 million tons grading
0.46 oz/ton Ag and 0.004 oz/ton Au. (The Coeur Technical Report on the
Rochester Mine is available on SEDAR). For more detailed information on
the Majuba Hill copper/silver project, including maps showing the
results of soil sampling and the drilling completed to date, please
visit our web site at www.maxresource.com.

About MAX Resource Corp.

MAX Resource Corp. is a Canadian exploration company focused on
gold and silver exploration in Nevada. For more information, please
visit our web site at www.maxresource.com.

On behalf of the Board of Directors of MAX Resource Corp.

Stuart Rogers, President

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This News Release includes certain "forward looking statements".
Without limitation, statements regarding potential mineralization and
resources, exploration results, and future plans and objectives of the
Company are forward looking statements that involve various degrees of
risk. The following are important factors that could cause MAX's actual
results to differ materially from those expressed or implied by such
forward looking statements: changes in the world wide price of mineral
commodities, general market conditions, risks inherent in mineral
exploration, risks associated with development, construction and mining
operations, the uncertainty of future profitability and the uncertainty
of access to additional capital.


TEL:   604-637-2140   Leonard MacMillan
TSX Venture closing price for MXR-V
Date: 2014/06/24
Closing Price: 0.06

TEL: 1-866-331-5088   Corporate Communication
info@maxresource.com  MAX Resource Corp.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1417500007TS11417500672-05432920140625