Source	Marketwire
Date	06/25/2014
Time	05:00:31 AM

Company	 MAX RESOURCE CORP.
Title	MAX Drills 222.6 m @ 0.27% Cu and 10.1 g/t Ag, Inclusive of 117.4 m @ 
0.43% Cu and 12.0 g/t Ag, in Oxides at Majuba Hill, Nevada





    CDNX Symbol: MXR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: MAX Resource Corp

FRANKFURT SYMBOL: M1D
TSX VENTURE SYMBOL: MXR
OTCBB SYMBOL: MXROF

June 25, 2014

MAX Drills 222.6 m @ 0.27% Cu and 10.1 g/t Ag, Inclusive of 117.4 m @ 0.43% Cu 
and 12.0 g/t Ag, in Oxides at Majuba Hill, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - June 25, 2014) - MAX Resource Corp. 
(TSX VENTURE:MXR) (OTCBB:MXROF) (FRANKFURT:M1D) has received assays from the 
first core hole drilled at it's Majuba Hill silver/copper/gold project in 
Nevada in June 2014. This first hole, MMX-24, was drilled to a depth of 365.8 
metres ("m") and intercepted 222.6 m @ 0.27% Cu and 10.1 g/t Ag, inclusive of 
117.4 m @ 0.43% Cu and 12.0 g/t Ag. MMX-24 was drilled roughly parallel to and 
85 m northwest and 25 m below the collar of MAX's hole MM-21, drilled in 2012, 
which intersected 332 m @ 0.13% Cu and 12 g/t Ag.

Drill hole MMX-24 was drilled from the opposite side of Majuba Ridge as hole 
MM-21 and successfully tested the down-dip extension of copper/silver 
mineralization intercepted by MM-21, hole DDH-4 drilled by Freeport in 1940's, 
and hole MF-1 drilled by Minefinders in 1974. The alteration of the 
mineralization is mainly potassium feldspar and quartz and the probable copper 
mineralization is chalcocite and the silver mineral acanthite and or 
chloargyrite. Alteration is increasing as the holes are extended to depth and 
appear to be continuous. MMX-24 and MM-21 both intersected mineralization 
exposed at surface as copper oxides running as high as 7.72% Cu (see our news 
release of February 5, 2014).

MMX-24 was collared approximately 415 m east-northeast of the middle portal of 
the past producing Majuba Hill mine, where MAX drilling in 2011 intercepted 
high grade copper/silver supergene oxide mineralization over long intervals 
that included:

/T/

--  Hole MM-07: 50.3 m of 50.8 g/t Ag, 0.31 g/t gold and 0.31% Cu
--  Hole MM-06: 96.0 m of 39.2 g/t Ag and 0.57% Cu, including 44.2 m of 71.0
g/t Ag, 0.15 g/t Au and 1.14% Cu
--  Hole MM-03: 42.7 m of 37.5 g/t Ag and 0.38% Cu

/T/

Significant intervals from MMX-24 are summarized in the following table:

/T/

----------------------------------------------------------------------------
Hole   Azimuth Angle   Total     From    To     Thickness    Cu     Ag
Depth      (m)    (m)       (m)       (%)  (g/t)
----------------------------------------------------------------------------
MMX-24   235.6  -43.9  365.8 m    114.3  336.9    222.6 m    0.27%  10.1
----------------------------------------------------------------------------

----------------------------------------------------------------------------
includes                           219.5  336.9    117.4 m    0.43%  12.0
----------------------------------------------------------------------------
includes                           219.5  288.1     68.6 m    0.61%  11.6
----------------------------------------------------------------------------

/T/

Maps indicating the location of this drill hole as well as locations from 
previous programs at Majuba Hill are available on our web site at 
www.maxresource.com.

Analysis was performed by Bureau Veritas (Inspectorate), an ISO certified 
facility in Reno, Nevada, using multi-element method MA330 (ICP-ES) techniques 
producing assays for a 30 element suite of minerals. Over-limit analyses were 
performed according to procedure MA410. No analysis was conducted for gold. 
Standards, duplicates and blanks were used for quality control of the samples. 
After the core is logged for each drill hole, the location of each site is 
located using a GPS in UTM coordinates using NAD 83 datum. The core is then 
hydraulically split and put into a sample bag which is labeled for each 
interval and taken from the core facility to the Bureau Veritas laboratory.

Majuba Hill is the site of numerous past producing mines, with historic 
production reported of 12% Cu (Mason Valley Copper, 1918) and silver grades up 
to 40 oz/t Ag. Majuba Hill encompasses 2,568 acres of surface and mineral 
rights that includes patented lode mining claims. The property is easily 
accessed via 23 miles of well-maintained dirt roads leading from U.S. 
Interstate 80, and lies 30 miles northwest of Coeur Mining's Rochester silver 
mine, which contains a NI 43-101 compliant Measured and Indicated Resource of 
263.9 million tons grading 0.46 oz/ton Ag and 0.004 oz/ton Au. (The Coeur 
Technical Report on the Rochester Mine is available on SEDAR). For more 
detailed information on the Majuba Hill copper/silver project, including maps 
showing the results of soil sampling and the drilling completed to date, please 
visit our web site at www.maxresource.com.

About MAX Resource Corp.

MAX Resource Corp. is a Canadian exploration company focused on gold and silver 
exploration in Nevada. For more information, please visit our web site at 
www.maxresource.com.

On behalf of the Board of Directors of MAX Resource Corp.

Stuart Rogers, President

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This News Release includes certain "forward looking statements". Without 
limitation, statements regarding potential mineralization and resources, 
exploration results, and future plans and objectives of the Company are forward 
looking statements that involve various degrees of risk. The following are 
important factors that could cause MAX's actual results to differ materially 
from those expressed or implied by such forward looking statements: changes in 
the world wide price of mineral commodities, general market conditions, risks 
inherent in mineral exploration, risks associated with development, 
construction and mining operations, the uncertainty of future profitability and 
the uncertainty of access to additional capital.

- 30 -

CONTACT INFO:

MAX Resource Corp.
Leonard MacMillan
Corporate Communication
604-637-2140 or Toll Free: 1-866-331-5088
info@maxresource.com

or

Paradox Public Relations
514-341-0408 or Toll Free: 1-866-460-0408
info@paradox-pr.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=488090738