Source	MARKET NEWS
Date	06/30/2014
Time	06:34:50 AM

Company	 Columbus Gold Corporation
Title	Resource 
Estimate At Montagne D'Or; Obtains Perm





    CDNX Symbol: CGT











Press Release	





COLUMBUS GOLD CORP ("CGT-V;CBGDF-0")
- Resource Estimate At Montagne D'Or; Obtains Permit For And
- Commences Drilling On Principal Gold Zone

Columbus Gold Corporation ("Columbus Gold") announces the results
of a resource estimate, dated June 28, 2014, prepared by independent
consultant Coffey Mining Pty Ltd ("Coffey") on Columbus Gold's Montagne
d'Or gold deposit, Paul Isnard Project, French Guiana.

Utilizing a cut-off grade of 0.4 g/t gold, the estimate yields
140.1 million tonnes at an average grade of 1 g/t gold for a total of
4.31 million contained Inferred ounces of gold. See the table below for
0.3 and 0.5 g/t cut-offs. Based on the current drilling density, the
estimate does not fully take into account the potential of the high
grade zones occurring within the low grade envelopes. Coffey strongly
recommends infill drilling to define these high grade zones.

The best mineralised and most consistent zones on the Montagne
d'Or deposit, based on current interpretation, are located in the
principal Upper Felsic Zone ("UFZ"). The drilling permits required to
drill the UFZ were very recently obtained on June 16th, and the present
26,600 metre Phase II drilling program, designed to complete a tighter
drill pattern at 50 metre spacing, commenced on the UFZ on June 23rd,
and on a 24 hour basis. There are approximately 19,000 metres remaining
in the planned Phase II program, which on deployment of a second drill
rig, expected to arrive imminently in French Guiana, will take
approximately 4 months to complete.

Robert Giustra, CEO of Columbus Gold, commented: "The new estimate
by Coffey has been helpful in gaining a better understanding of the
inferred nature of the deposit, but with more than 70% of Phase II
drilling still to occur and with nearly all that drilling targeting the
UFZ (which is the principal mineralised zone) with denser spacing, it's
reasonable to anticipate that the next resource update planned for
completion by the end of this year, could better reflect the potential
of the high grade zones and convert a significant portion of the
Inferred resources to Indicated and Measured."

Montagne d'Or Updated Resource Estimate

The NI 43-101 compliant resource estimate was prepared by Coffey's
Perth, Australia office as a result of comments from SRK Consulting
(U.S.) Inc. on the appropriateness of certain methodologies previously
employed by Coffey International Ltd (Toronto) in their 2012 resource
estimate (see February 5th, 2013 and May 5th, 2014 press releases).

The updated Inferred Mineral Resources are tabulated following at
the reportable 0.3, 0.4 and 0.5 g/t Au cut-off grade. Columbus Gold is
aiming to file an updated NI 43-101-compliant technical report on SEDAR
in July.

//st

PAUL ISNARD PROJECT
Montagne d'Or Inferred Resource Report
----------------------------------------------------------------------------
Average Grade      Contained Gold
Cut-off Grade      Million Tonnes        (g/t Au)            (M oz)
----------------------------------------------------------------------------
0.3               169.2               0.9                4.6
0.4               140.1               1.0                4.3
0.5               116.0               1.1                4.0
//et

Technical Information on Resource Estimate and Qualified Person

The current modelling and updated mineral resource estimate were
prepared by independent consultants Coffey Mining Pty Ltd ("Coffey") in
Perth, Western Australia, in accordance with National Instrument 43-101
Standards of Disclosure for Mineral Projects ("NI 43-101"). The
estimation is based on 56 historical drill holes (10,916m) together
with the results of 100 diamond drill holes (22,905m) completed by
Columbus Gold from November, 2011, to June, 2014. Drilling core
diameter was HQ for the saprolite zone, changing to NQ for fresh rock.

The Montagne d'Or deposit consists of closely-spaced sub-parallel
east-west-striking and steeply south-dipping mineralised horizons. A
total of eight (8) elongated gold mineralised domains were defined
along the strike length of the deposit with the latest drill hole
information. The domains were wire-framed by snapping to drill holes at
a mineralisation cut-off of 0.25 g/t Au. Care was taken to minimize the
amount of internal dilution. The average dilution (values (0.25 g/t Au)
was estimated at 18.7%. An additional and separate domain was created
for the saprolite horizon defined by the boundary between fresh rock
and the topography surface.                 The mineral resource
estimation were prepared from a geostatistical block modelling method
based on the drill hole data. The resource was classified as an
Inferred resource due to available drill hole density and distance
between drill holes. The resource remains open in several directions.
Additional infill drilling to a nominal spacing of 50m between drill
holes along strike as well as down-dip drilling may convert some or all
of the existing Inferred Mineral Resource to an Indicated Mineral
Resource.                Parameters used for the evaluation mineral
resources are:

Drill hole samples were composited into 3m composite lengths
within the mineralised domains and coded with the domain number. All
samples were combined for the definition of a variogram model to define
the spatial distribution of the gold mineralisation; a reasonably
well-defined correlogram model was fitted. The spatial model follows
the trend of the mineralisation along strike with a rotation of 85
degrees east of north and a dip of 70 degrees towards the south. The
major directions of continuity occur along strike and down-dip. The
gold data shows a high nugget and the model was fitted with a nugget
effect of 50%. Cross validation of the variogram indicates that the
model is relevant.  Separate omni-directional models were defined for
waste and the saprolite horizon and used for modelling waste for areas
in between the main mineralised domains.

A density model was generated by a kriging interpolation of the
raw data that was coded with average density values based on the
results of the available density measurements.

A top-cut of 16 g/t Au has been applied to the 3m composite data
before use in block interpolation, which is based on standard linear
Ordinary Kriging. Only data within the mineralised domain was used to
inform blocks within the domain. All available grade values are used
within the domains but unwanted smearing of high grades was controlled
in the Ordinary Kriging process.

A number of different block model sensitivities with different
parent cell sizes, composite lengths and differing kriging
neighbourhoods were run, validated, and compared to ensure that
sensitivity to high grade populations, search strategy and parent cell
size is monitored. The maximum search radius was set at 150m along
strike and 150m down dip and interpolation of high grades above a value
of 10 g/t Au was limited to a distance of maximum 35m along strike and
down dip, and 10m across strike to avoid unwanted smearing of high
grades during block estimation. The final block model is generated at a
parent cell size of 25m along strike, 10m across strike and 10m down
depth.

The block model is not rotated but search and interpolation
directions follow the geological dip at 70 degrees towards the south.
The model is extended to a depth of approximately 350m below topography
and the estimation interpolation is allowed to run to its maximum depth
within the mineralised zones. The model is then truncated by defining a
wire-frame shell that encloses a relative distance of approximately
150m from available drill hole data. Only portions of the mineralised
domains that lie within this shell have been classified as an Inferred
Mineral Resource.

Louis Voortman, Principal Consultant - Resources, at Coffey Mining
Pty Ltd, Qualified Person for the resource estimation, has reviewed and
approved the contents of this news release as far as it relates to
their work.

Rock Lefrancois, P.Geo. (OGQ), Columbus Gold's COO and Qualified
Person has reviewed and approved the technical content of this news
release.

ON BEHALF OF THE BOARD,

Robert F. Giustra, Chairman & CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This release contains forward-looking information and statements,
as defined by law including without limitation Canadian securities laws
and the "safe harbor" provisions of the US Private Securities
Litigation Reform Act of 1995 ("forward-looking statements"),
respecting a new 43-101-compliant report being completed by Coffey;
that the new 43-101-compliant report will be completed and filed on
SEDAR in July 2014, that a second drill rig will arrive imminently,
that an additional 19,000 meters of Phase II drilling will be completed
and take approximately 4 months to complete and that such additional
drilling will improve average grade or convert a significant portion of
the inferred resources to indicated and measured, and that another
resource update will be completed by the end of the year.
Forward-looking statements involve risks, uncertainties and other
factors that may cause actual results to be materially different from
those expressed or implied by the forward-looking statements, including
without limitation: whether a new 43-101-compliant report will be
completed by Coffey; whether the new 43-101-compliant report will be
completed and filed on SEDAR in July 2014; whether a second drill rig
will arrive imminently; whether an additional 19,000 meters of Phase II
drilling will be completed and take approximately 4 months to complete;
whether such additional drilling will improve average grade or convert
a significant portion of the inferred resources to indicated and
measured; whether another resource update will be completed by the end
of the year ; cost increases; availability of qualified workers and
drill equipment; risks associated with exploration projects, mineral
reserve and resource estimates (including the risk of assumption and
methodology errors); dependence on third parties for services;
non-performance by contractual counterparties; title risks; and general
business and economic conditions. Forward-looking statements are based
on a number of assumptions that may prove to be incorrect, including
without limitation assumptions: that the conclusions provided by Coffey
and reported herein are accurate and that new 43-101-compliant reports
will be able to be provided within the target timeframe or at all;
general business and economic conditions; the timing and receipt of
required approvals; availability of financing; power prices; ability to
procure equipment and supplies including without limitation drill rigs;
that political risk will remain on current levels; and ongoing
relations with employees, partners and joint venturers.

Although Columbus Gold has attempted to identify important factors
that could cause actual actions, events or results to differ materially
from those described in forward-looking statements, there may be other
factors that cause actions, events or results not to be anticipated,
estimated or intended. There can be no assurance that forward-looking
statements will prove to be accurate, as actual results and future
events could differ materially from those anticipated in such
statements. Columbus Gold undertakes no obligation to update
forward-looking statements if circumstances or management's estimates
or opinions should change except as required by applicable law. The
reader is cautioned not to place undue reliance on forward-looking
statements.


TEL:  604-634-0970   Investor Relations
TSX Venture closing price for CGT-V
Date: 2014/06/27
Closing Price: 0.52

TEL:  1-888-818-1364
info@columbusgroup.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1418000017TS11418000905-06330120140630