Source	Marketwire
Date	06/03/2014
Time	05:57:45 AM

Company	 DESERT GOLD VENTURES INC.
Title	Desert Gold Ventures Reports the Mapping of a 24 km2 Anomalous Zone on Its 
Segala Ouest Permit in Western Mali





    CDNX Symbol: DAU











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Desert Gold Ventures Inc.

TSX VENTURE SYMBOL: DAU

June 3, 2014

Desert Gold Ventures Reports the Mapping of a 24 km2 Anomalous Zone on Its 
Segala Ouest Permit in Western Mali

High grade values in anomalous zone

TORONTO, ONTARIO--(Marketwired - June 3, 2014) - Desert Gold Ventures Inc. (TSX 
VENTURE:DAU) (the "Company" or "Desert Gold") is pleased to announce results 
from soil geochemical surveys on the Segala Ouest tenement, which has now been 
completely covered by soil geochemistry. The results delineate a very large 
anomalous zone covering an area approximately 24 km2 (Fig. 1) in extent, with 
high assay values noted.

The Segala Ouest prospect is situated in the middle of the gold mining district 
of Kenieba about 20 km NW of the town of Kenieba. Endeavour's Segala mine abuts 
the eastern boundary of the exploration permit and their Tabakoto mine is 
approximately 5 km away to the southeast. Some 15 km to the northwest are 
Randgold's Loulo-Gounkoto mine complex.

To view Figure 1 please click on the following link: 
http://media3.marketwire.com/docs/DAU0603.pdf

The recently conducted soil geochemical survey, in which 2342 soil samples were 
collected by GeoActiv Pty Ltd (a South African geological contracting and 
consulting company) and analysed by the ALS Chemex SA PTY Ltd laboratory in 
South Africa, completes a blanket geochemical analysis of the exploration 
permit . The results delineate an 8 km long and 3 km wide corridor traversing 
the tenement in a northwesterly direction. The soil sample database comprises 
6032 lognormally distributed Au Values with thresholds of 669 ppb, 204 ppb and 
20 ppb, for the respective 1, 5 and 50 percentiles.

There are significant artisanal mining activities focused in two areas: (1) on 
the NW strike extension of Endeavour's Segala mine, (the "Segala pit") and, (2) 
in the southeastern part of the tenement nearby the village of Baroya, (the 
"Baroya pit"). These mining sites target mineralised vein systems within the 
metasediment host rocks. Grab samples of the material being mined within the 
property were collected and assayed. Results are tabulated below (Table 1) and 
demonstrate high grades in the mineralised vein systems.

/T/

-----------------------------------------------------------------
Sample source             Sample ID      depth (m)         Au g/t
-----------------------------------------------------------------
BAROYA PIT                  B534205          35.00           0.58
-----------------------------------------------------------------
BAROYA PIT                  B534206          35.00          15.65
-----------------------------------------------------------------
BAROYA PIT                  B534207          40.00           3.82
-----------------------------------------------------------------
BAROYA PIT                  B534208          25.00           0.09
-----------------------------------------------------------------
BAROYA PIT                  B534209          25.00          76.30
-----------------------------------------------------------------
BAROYA PIT                  B534210          30.00           0.84
-----------------------------------------------------------------
BAROYA PIT                  B534211          30.00           1.60
-----------------------------------------------------------------
BAROYA PIT                  B534225          40.00          39.80
-----------------------------------------------------------------
BAROYA PIT                  B534226          40.00           2.38
-----------------------------------------------------------------
BAROYA PIT                  B534227          40.00           1.31
-----------------------------------------------------------------
SEGALA PIT                  B534215          20.00           8.82
-----------------------------------------------------------------
SEGALA PIT                  B534216          20.00           5.53
-----------------------------------------------------------------
SEGALA PIT                  B534217          50.00           1.05
-----------------------------------------------------------------
SEGALA PIT                  B534218          30.00           1.14
-----------------------------------------------------------------
SEGALA PIT                  B534221          25.00          26.60
-----------------------------------------------------------------
SEGALA PIT                  B534222           7.00           0.37
-----------------------------------------------------------------
SEGALA PIT                  B534223          10.00           0.58
-----------------------------------------------------------------
Table 1. Table of assay results of selected grab samples collected from the
artisanal mining operations. Approximate in situ depths from which the
samples were collected are given.

/T/

Given the mineralisation in the district is hosted by geological structures, 
the company recently completed an analysis of structure both from remote 
sensing data as well as from previous drill core data. The results point to a 
coherent set of fractures congruent with the mineralised systems noted both at 
Tabakoto mine and at the Segala mine. Both the Segala and Baroya artisanal 
mining sites follow these structural orientations.

The company will drill both sites shortly to confirm the continuity of the 
mineralisation and will selectively trench some of the other significant soil 
geochemical anomalies to determine the source of these anomalies.

Permit Strategy

It is the company's intention to define a sizable economic 43-101 compliant 
resource on the permit and engage nearby mining operations to discuss possible 
ore offtake agreements.

About Desert Gold

Desert Gold Ventures Inc. is an advanced exploration and development company 
which holds mining assets in Mali and Rwanda.

The geological results stated in this report have been reviewed by Mr Neil 
Andersen, registered as a Fellow of the Geological Society of South Africa 
(FGSSA) No 5520 and is registered with the South African Council for Natural 
Scientists (Pr. Sci. Nat., 401458/83). BSc. (Geology, Chemistry, UCT), BSc 
(Special Hons. Exploration Geology, UR), MSc (Structural Geology, UP). He has 
sufficient experience which is relevant to the style of mineralisation and 
metallurgical processes under consideration and to the activity which he is 
undertaking to qualify as a Qualified Person as defined in National Instrument 
43-101.

This news release has been prepared on behalf of the board of directors of 
Desert Gold, which accepts full responsibility for its contents.

For further information concerning Desert Gold Ventures Inc. and the 
TransAfrika material properties, please refer to Desert Gold's SEDAR profile at 
www.sedar.com or visit our website at www.desertgold.ca.

- 30 -

CONTACT INFO:

Desert Gold Ventures Inc.
Jared Scharf
CFO
1 (416) 662-3971
Fax: 1 (604) 408-9301
jared.scharf@desertgold.ca
www.desertgold.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=484850284