Source	Marketwire
Date	06/12/2014
Time	08:39:05 AM

Company	 DIOS EXPLORATION INC.
Title	Summer Program on DIOS AU33WEST Gold Project





    CDNX Symbol: DOS











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: DIOS Exploration Inc.

TSX VENTURE SYMBOL: DOS

June 12, 2014

Summer Program on DIOS AU33WEST Gold Project


MONTREAL, QUEBEC--(Marketwired - June 12, 2014) - Dios Exploration Inc. (TSX 
VENTURE:DOS) plans to undertake field work (including prospecting, mapping, 
trenching) on wholly-owned AU33WEST gold property, a few km from the Eastmain-1 
hydropower facilities, James Bay area, Quebec.

Main target focus will be the extent of the Heberto gold showing that assayed 
up to 5 g/t Au over some 5 meters in diamond saw track-sampling. This gold 
showing is coincidental with a weak induced polarization conductor 
(chargeability) north-south striking along the margin of a sub-circular 
magnetic anomaly, itself included within a larger low magnetic structure. 
Several gold soil anomalies are also coincidental with induced polarization 
conductors. A structurally-controled oxidized IRG (Intrusion Related Gold) 
model is proposed for the AU33WEST gold project.

A felsic (tonalite-granodiorite) intrusive complex hosts several gold 
porphyry-type showings (grading from 1.77 to 23 g/t Au in grab samples) within 
a 5,0 by 2,0 km area at the head (up-ice) of a significant gold glacial 
dispersal train. The gold mineralization appears as 1-5% pyrite as 
disseminations and fracture fillings that are associated with potassic 
alteration and/or silicification. It appears structurally controlled by zones 
of shearing and foliation along two main orientations (N160 and N080E).

Recent compilation of the AU33W data show good correlation between gold and 
presence of pyrite, (of chalcopyrite) and/or magnetite-hematite (oxidized 
system) located at the margins of intrusions. The intrusions are interpreted 
from total field & vertical gradient magnetics and geological mapping. These 
associated mineralizations are enclosed within large halos of potassic 
feldspar, silica, epidote, magnetite-biotite and hematite alterations. The 
juxtapposition of structural measurements and magnetic data suggests the 
presence of buried intrusive domes within the mineralized and altered area 
which is mainly developped along a north-south structural vector in the 
plutonic domain. The concentration of sulfidic mineralization along the margins 
of distinctive magnetic intrusions is also coincidental with higher potassium 
content (ground spectrometry).

This news release was prepared by M. J Girard, M.Sc. Geo, the Qualified Person 
(43-101).

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

www.diosexplo.com

http://blog.diosexplo.com/

- 30 -

CONTACT INFO:

Marie-Jose Girard, M.Sc. Geo
President & CEO
mjgirard@diosexplo.com
(514) 923-9123

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MAT - MATERIAL CHANGE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=486241999