Source	MARKET NEWS
Date	06/16/2014
Time	05:37:31 AM

Company	 GFK Resources Inc.
Title	Adventure 
Gold And Gfk Resources Outline 1.5 Kil





    CDNX Symbol: GFK











Press Release	





ADVENTURE GOLD INC ("AGE-V")
GFK RESOURCES ("GFK-V")
- Adventure Gold And Gfk Resources Outline 1.5 Kilometer Gold
- Bearing Corridor On The Florence Property

Adventure Gold Inc. and GFK Resources wish to announce the initial
results of the 2014 exploration diamond drilling program on the
Casa-Cameron project. The program totaling 9,000 metres of drilling, of
which the Phase 1, has been completed on the Florence property outlined
two gold zones over at least 1.5 kilometre along strike and up to 300
metres at depth. The gold zones are associated with a large alkaline
intrusive complex along the Casa-Berardi - Cameron Gold Trend (CBCGT).
The Florence property is located 23 kilometres north of the town of
Lebel-sur-Quevillon, about 70 kilometres east of the Sleeping Giant
mine and mill and about 60 kilometres southwest of the Bachelor mine
and mill.

The Phase 1 drilling program on the Florence property consisted of
eight (8) diamond drill holes totaling 2,951 metres (Figure 1). The
first five (5) drill holes were designed to test the Chieftain gold
deformation over a strike length of 1.5 km around a 200 to 300 metres
depth (Figure 2). Three (3) other holes tested Induced polarization
(IP) and Megatem (EM) anomalies in the area of new gold showing
discovered by Adventure Gold (7.0 g/t and 3.2 g/t Au in grab samples).
Drilling confirmed the presence of a large gold system associated with
two major gold deformation zones up to 45 metres in thickness. The best
intersect returned 0.6 g/t Au over 20 metres including 1.0 g/t Au over
9 metres in hole F-14-01 at a 160 metre depth. Other results are
presented in Table 1.

The two gold deformations zones are characterized by a large
alteration envelop of carbonate, chlorite and hematization and intruded
by deformed metric alkaline dykes. Gold is associated with
hematite-silica-albite alteration (Pictures 1 and 2) generally located
in the central part of the deformation zone. The gold system remains
open laterally and at depth. The south-east extension remains untested
by drilling for over five (5) kilometres where several promising
untested IP anomalies have been outlined (Figures 1 and 2). Additional
fieldwork is scheduled this summer to evaluate IP anomalies and to
formalize new drilling target. Additional drilling is required to
adequately evaluate this large gold system.

"Initial drilling program on the Florence property confirmed the
presence of a large alkaline gold system typical of many gold mining
camps in the Abitibi Greenstone Belt. All the key geological features
are there and further exploration work is definitively warranted,"
stated Marco Gagnon, President and CEO of Adventure Gold.

"The confirmation of a 1.5 kilometre gold trend on Florence is
proof that this is a significant system with all the indicators of a
major gold deposit. We are pleased to be involved in this project, and
we look forward to the commencement of the upcoming phases of
fieldwork," stated Patrick Fernet, CEO of GFK Resources.

Figure 1: Location of drillhole - Surface map of Florence Property

Figure 2: Long section - Chieftain Gold Deformation Zone

Table 1: Result on the Phase 1 drilling program on Florence
property

Picture 1: Alteration zone (F-14-03 - Zone 1)

Picture 2: Alteration, mineralization and Alkaline Dyke (F14-03 -
Zone 2)

Other Casa-Cameron properties exploration work

Additional geophysics (IP and Mag) and prospecting work is
scheduled for this summer. A total of 33 line-kilometres of IP will be
completed on Casagosic, Bell-Vezza and Sinclair-Bruneau properties, 90
km of ground magnetics on Vezza North, Vezza Extension, and
Sinclair-Bruneau properties and 40 days of prospecting work on Florence
and Bachelor Extension properties. The next 3,000 metres drilling
program is slated to begin in August on the Vezza North property to
test kilometre-scale gold deformation zones with historical gold values
of 11 g/t Au over 4 metres and 4.5 g/t Au over 3.4 metres within a zone
grading 2.1 g/t Au over 8.5 metres between 100 to 200 metres of the
surface and open in all direction.

The Casa-Cameron Project

The Casa Cameron Project includes nine (9) gold Properties (436
mining claims): (1) Casagosic, (2) KLM, (3) Vezza North, (4) Vezza
Extension, (5) Bell-Vezza, (6) Sinclair-Bruneau, (7) Florence, (8)
Cere-113 and (9) Bachelor Extension (see Press Release dated March 3,
2014 and the web site). The Properties are located north of La Sarre,
Amos and Lebel-sur-Quevillon, in the northwest region of the province
of Quebec and they are accessible all year long by paved and gravel
roads. GFK and AGE have an agreement pursuant to which GFK has acquired
the option to earn between 51% or 100% interest in AGE's Casa-Cameron
project covering an area of 231 km (see Press Release dated December
12th, 2013).

The Properties straddle segments of the major Casa-Berardi/Cameron
gold break between the Casa-Berardi Gold Mine (proven reserves of 1.0
Mt at 5.7 g/t Au for 185,200 ounces and probable reserves of 7.2 Mt at
5.2 g/t Au for 1.2M ounces for a total of proven and probable reserves
of 8.2 Mt at 5.3 g/t Au for 1.4M ounces; measured resources of 1.8 Mt
at 5.9 g/t Au for 340,600 ounces and indicated resources of 9.0 Mt at
3.7 g/t Au for 1.1M ounces for a total of measured and indicated
resources of 10.8 Mt at 4.1 g/t Au for 1.4M ounces and inferred
resources of 3.4 Mt at 5.5 g/t Au for 601,300 ounces - Hecla Mining
(formerly Aurizon Mines), NI 43-101, March 31, 2014) and the Bachelor
Gold Mine (also currently in operation by Metanor Resources with proven
reserves of 193,100 Mt at 8.3 g/t Au for 51,750 ounces and probable
reserves of 650,700 t at 7.1 g/t Au for 148,400 ounces for a total of
proven and probable reserves of 843,800 t at 7.4 g/t Au for 200,200
ounces and inferred resources of 426,100 t at 6.5 g/t Au for 89,400
ounces - Metanor Resources, NI 43-101, April 26, 2011). All the
Properties contain known gold-bearing zones and most of them are also
strategically located adjacent and on strike to significant gold mines
or deposits. However, at their exploration stages, the Properties have
had insufficient exploration to define mineral resources and despite
their strategic locations it is uncertain if further exploration will
result in delineating mineral resources.

Very few exploration programs using up to date technology have been
completed on the Properties from the 1990's to 2008, prior to their
acquisition by Adventure Gold. Gold exploration work conducted by
Adventure Gold since then returned very encouraging results and many
valuable drill targets were outlined (see the Company's press release
dated June 11, 2013 and the technical report (the "Report") filed by
GFK on SEDAR in connection with the transaction and prepared in
accordance with National Instrument 43-101 - Standards of Disclosure
for Mineral Projects ("NI 43-101")). As described in the Report, the
geological setting of the Casa-Cameron properties appears to be very
favorable for the identification of new high-grade gold-bearing
structures or bulk-style ore deposit. Past exploration work did not
entirely test the numerous gold occurrences and many positive
historical drilling intersections warrant follow-up drilling. In
addition, recent geophysical surveys outlined also quality drilling
targets. The authors of the Report recommend significant exploration
work including a 21,000-meter drilling program (see the Report
available on AGE's website).

Quality control

Mr. Jules Riopel, Vice-President Exploration and Acquisitions of
Adventure Gold and Denis Chenard, P.Eng. of GFK Resources act as the
qualified persons (as defined by NI 43-101) and have reviewed and
approved the scientific and technical information in this press
release. Adventure Gold is acting as the field operator for the
exploration work on the Casa-Cameron project during the first option as
per the agreement between AGE and GFK.

During the ongoing drilling program, assay samples were taken from
the NQ core and sawed in half, with one-half sent to Agat Laboratory, a
commercial laboratory and the other half retained for future reference.
A strict QA/QC program was applied to all samples; which includes
insertion of mineralized standards and blank samples for each batch of
20 samples. The gold analyses were completed by fire-assayed with an
atomic absorption finish on 50 grams of materials. Repeats were carried
out by fire-assay followed by gravimetric testing on each sample
containing 3.0 g/t gold or more.

Profile

Adventure Gold Inc. is a mineral exploration company focused on
discovering and developing high-quality gold deposits in the Abitibi
region located in eastern Canada - one of the richest gold mining areas
in the world. Adventure Gold has become, in a few years, an important
player in the mineral exploration industry with one of the best
portfolios of exploration properties along the main gold-bearing
structures of the Abitibi Greenstone Belt. The Company is exploring
mainly close to gold mines where mining production infrastructure is
already in place, which distinguishes it from several other exploration
companies. Adventure Gold's exploration team consists of mining
professionals having worked previously for well-established producing
companies, who understand industry challenges. The Company owns 100% of
the rights on its two main projects namely: Val-d'Or East and Detour
Quebec.The Val-d'Or East flagship project encompasses the
Pascalis-Colombiere property where Cambior Inc. (now IAMGOLD) produced
gold between 1989 and 1993 at the Beliveau Mine. Close to the former
mine, Adventure Gold recently discovered a significant new gold system
containing 770,000 gold ounces at 2.63 g/t in the inferred resource
category (SGS Canada Inc., NI 43-101 Technical Report Mineral Resource
Val-d'Or East Property filed on Jan. 4th, 2013) and is actively working
on its development. With a total of 74.0M shares issued and close to
10% owned by the management, Adventure Gold is well-positioned to
benefit its shareholders.

Twitter: http://twitter.com/Adventure_AGE

LinkedIn: http://www.linkedin.com/company/2253943

The foregoing information may contain forward-looking statements
and events relating to the future performance of the Company.
Forward-looking statements, specifically those concerning future
performance, are subject to certain risks and uncertainties, and actual
results may differ materially. These risks and uncertainties are
detailed from time to time in the Company's filings with the
appropriate regulatory authorities. We seek safe harbour.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Image Available:
http://www.marketwire.com/library/MwGo/2014/6/15/11G017042/Images/Fig1_Flor
ence_Surfacemap_june2014-34232349084.jpg (br/) Image Available:
http://www.marketwire.com/library/MwGo/2014/6/15/11G017042/Images/Fig2_Flor
ence_Longsection_june2014-726072261249.jpg (br/) Image Available:
http://www.marketwire.com/library/MwGo/2014/6/15/11G017042/Images/Table1_Fl
orence_Result2014-388658931124.jpg (br/) Image Available:
http://www.marketwire.com/library/MwGo/2014/6/15/11G017042/Images/PR_Floren
ce_Picture1_2_june2014-803150513402.jpg

ENQUIRIES:
Marco Gagnon
President & CEO
marco@adventure-gold.com
450.743.5527
www.adventure-gold.com

Jules Riopel
Vice-President Exploration and Acquisitions
jules@adventure-gold.com
819.797.9770
TSX Venture closing price for GFK-V
Date: 2014/06/11
Closing Price: 0.24

TEL:  450.743.5527       Adventure Gold Inc.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1416600006TS11416600738-05361620140616