Source	MARKET NEWS
Date	06/01/2015
Time	09:38:39 AM

Company	 Endurance Gold Corporation
Title	007 Zone 
Drilling Update Pardo JV, Ontario





    CDNX Symbol: EDG











Press Release	





ENDURANCE GOLD CORP ("EDG-V;ENDGF-0")
- 007 Zone Drilling Update - Pardo JV, Ontario

Endurance Gold Corporation announces drilling results from
the 007 Zone Target on the Pardo Joint Venture Property ("Pardo JV
Property"). The Pardo JV Property is comprised of 16 claims located
approximately 65 kilometres ("km") northeast of Sudbury, Ontario.

Assays for the five (5) drill holes in the 007 Zone Target Area
have now been received. Mineralization considered significant, and
which approximates true width, is summarized in the following table:



//st

Hole               From       To    Thickness    Gold (g/t)
PD-15-21            0.7     1.65         0.95           0.3
PD-15-22                      No Significant Mineralization
PD-15-23              0      1.5          1.5           0.2
4.9      6.5          1.6           0.4
8.5      9.7          1.2           0.5
26.05    26.77         0.72           0.4
32.6     33.3          0.7           0.8
PD-15-24            6.6     8.45         1.85           0.8
Including           7.1      7.9          0.8           1.5
PD-15-25            2.2      3.1          0.9           0.3
4.75      6.2         1.45           0.2

//et




Holes 15-21 through 15-25 were drilled at approximately 50 to 70
metre step-outs from the 007 Zone high-grade channel samples reported
in August 2013 to test both the extent and thickness of the host
conglomerate for the high-grade surface mineralization exposed at the
007 Zone. The drilling has confirmed that the basal boulder
conglomerate "MiBC" is continuous surrounding the 007 Zone and remains
open for expansion towards the north, east and west (see 007 Section).
Due to the easterly dip of a north-south fault the MiBC was not
encountered in hole 15-25 and only partially encountered in 15-23 due
to faulting. The MiBC is also interpreted to continue to the southeast
but this area between the 007 and Godzilla zone is complicated and
semi-continuous as a result of the effects of a post mineral diabase
dike in the area. The location map and section for the 007 drilling can
be viewed in the news release on the Company's website at
www.endurancegold.com.

The elevated gold values obtained from this drilling correspond
with the detrital pyrite-rich conglomerate facies observed in the 2015
drill core. The facies observed can also be correlated with the facies
in holes 14-01 and 14-03 drilled on the 007 Zone which returned gold
values of 3.6 g/t over 1.03 metres and 4 g/t over 1.21 metres
respectively. This correlation implies the channel that deposited the
high-grade surface mineralization at the 007 Zone extends under cover
towards the north, east and west.

The majority of mineralization on surface and drill core in the
MiBC at the 007 Zone consists of detrital pyrite and free gold
"clustered" in fluvial traps that are interstitial to the boulders in
the conglomerate. With the diameter of the drill core used, the grade
of the vertical drill intersections through the MiBC in the 007 Zone
drill holes may not be indicative of the representative grade of the
MiBC Reef in this area. The higher grade mineralized conglomerate at
the 007 Zone and the Godzilla zone, both in surface channels and drill
holes, have now been confirmed as the same MiBC conglomerate facies.

The assay results for eight (8) selected better grade samples from
these drill holes were assayed at a second independent assay lab and
results from the second lab showed consistently higher gold values by
an average of 29 percent. The values included in the table above are an
average of the grade reported by both labs.

Inventus Mining Corp., formerly Ginguro Exploration Inc.
("Inventus") is the operator of the Pardo JV Property and holds a 64.5%
ownership interest and Endurance owns a 35.5% ownership interest.

About Endurance

Endurance Gold Corporation is a company focused on the
acquisition, exploration and development of highly prospective North
American mineral properties with the potential to develop world-class
deposits. The Company's exploration focus, for projects operated by
Endurance, is intrusive-related mineral systems with potential for
discovery of major new precious or rare metals deposits, and its
business plan offers shareholders exposure to several majority-owned
exploration projects with significant discovery potential such as the
Elephant Gold Property in Alaska, the Rattlesnake Hills Gold Property
in Wyoming, and the Bandito Rare Earth-Niobium Property in the Yukon.
Please visit www.endurancegold.com.

ENDURANCE GOLD CORPORATION

Robert T. Boyd

Per:

President & CEO

FOR FURTHER INFORMATION, PLEASE CONTACT

Endurance Gold Corporation

(604) 682-2707, info@endurancegold.com

www.endurancegold.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release. This news release may contain forward looking statements
based on assumptions and judgments of management regarding future
events or results that may prove to be inaccurate as a result of
factors beyond its control, and actual results may differ materially
from the expected results.

In the preparation of this news release, Endurance has relied on
information prepared by the operator of exploration programs, and
summarized to the Company for this release. Robert T. Boyd, P.Geo. is a
qualified person as defined in National Instrument 43-101 and
supervised the information provided by the operator and forming the
basis for this release. There has been insufficient exploration to
define a mineral resource on the Pardo JV Property to date, and it is
uncertain if further exploration will result in a delineated mineral
resource.

The operator of the JV reports that the samples of this release
were transported in security sealed bags for preparation and assay at
Act Labs located in Sudbury, Ontario. Act Laboratories Ltd. is an ISO
17025 registered laboratory. The additional sample checks mentioned
above were made at Agat Laboratories Ltd. The samples reported were
crushed in their entirety, with a 1kg split then pulverized. Two 50 g
aliquots of the pulp were cut out and fire assayed. Results were
reported as a weighted average of gold in the fractions. In instances
where the averages exceed 3 g/t, the sample is re-run with a
gravimetric finish and the gravimetric result is reported. The operator
of the JV inserts a certified reference standard or an analytical blank
in every batch of 20 samples. Validation parameters are established in
the database to ensure quality control.



__________________________________________________
_______________________________________________
TSX Venture closing price for EDG-V
Date: 2015/05/29
Closing Price: 0.05
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1515100030TS11515101691-09363520150601