Source	MARKET NEWS
Date	06/29/2015
Time	05:40:19 AM

Company	 Source Exploration Corp.
Title	Preliminary Metallurgical Test Work Yields Excel





    CDNX Symbol: SOP











Press Release	





Preliminary Metallurgical Test Work Yields Excellent Recoveries ForLas Minas 
Project --->@NEWS RELEASE
SOURCE EXPLORATION CORP ("SOP-V;SRXLF-0")
- Preliminary Metallurgical Test Work Yields Excellent Recoveries
- For Las Minas Project

Source Exploration Corp. (the "Company" or "Source") is pleased to
report results for preliminary metallurgical test work, indicating
recoveries of 95% copper, 89% gold and 84% silver for its Las Minas
gold -silver - copper project (the "Las Minas project") located in,
Veracruz State, Mexico. The metallurgical test work, included flotation
testing and was undertaken by ALS Metallurgy of Kamloops, British
Columbia, Canada.

Preliminary work included assessment of chemical and mineralogical
characteristics, comminution tests including Bond ball mill work index
and Bond abrasion, a preliminary flotation program, Davis tube magnetic
separation, and a Trace Mineral Search using QEMSCAN.

Approximately 59 kilograms of sample was collected from drill core
and constructed as a composite sample for test work. The average grade
of the composite sample measured 2.2% copper, 1.3 g/tonne gold, and 7.0
g/tonne silver. The iron content measured 31.5%.

Metallurgical Test Results

In addition to characterization test work, a series of rougher and
cleaner test were carried out to optimize a preliminary flotation flow
sheet, followed by a locked cycle flotation test to test metallurgical
performance under closed circuit conditions. Highlights from the test
work were:

Locked cycle test work recorded recoveries of 95% copper, 89% gold
and 84% silver.

The bulk concentrate from the locked cycle test graded 22% copper,
13 g/tonne gold and 57 g/tonne silver.

Bond ball work index was 13.3 kW-hr/ tonne, indicating a
moderately soft mineralized sample in terms of ball milling.

Bond abrasion index was 0.14, indicating only mildly abrasive
mineralized sample

Davis Tube Magnetic Separation Results

A Davis tube magnetic separation conducted on the rougher tail
produced a magnetic concentrate grading 67% iron, with 65% of the iron
in the tail recovered. This would be considered a high grade magnetic
concentrate, which may require little further treatment to meet
saleable grade requirements.

Brian Robertson, President and CEO, stated, "We are very pleased
with the results from the preliminary characterization test work on
mineralization from the Las Minas project. Recoveries for gold, silver
and copper were excellent, and the Bond ball mill index and Bond
abrasion indexes indicated that the sample tested was relative soft and
only mildly abrasive. Both of these results reduce operating costs for
milling operations. The high recoveries for all metals suggest the
potential for the recovery of gold, silver and copper from the
mineralization into a clean concentrate. Most importantly, high
recoveries for all metals may be attainable without using cyanide for
the extraction of precious metals. The preliminary magnetic separation
suggests that a high grade magnetic concentrate can be produced, which
could provide a by-product credit."

Additional test work would focus on a more comprehensive program
to optimize recoveries, reagent mix and circuit design, including
detailed magnetic testing on the rougher tailings to test the viability
of producing iron concentrate.

About Las Minas

The Las Minas Project hosts near-surface gold - silver and copper
skarn mineralization and high-grade gold - silver epithermal vein
deposits. The project is comprised of six mineral concessions covering
approximately 1,616 hectares (3,995 acres), with several small scale,
past-producing mines and a number of untested targets.

The district is host to one of the largest under explored gold -
silver copper skarn systems known in Mexico, and has a production
history that extends back to the Aztec era. The Las Minas granodiorite
intrusive measures approximately 10 kilometres in diameter and
underlies the Las Minas concessions. The mineralization controls and
association with magnetite appear to be similar to the Guerrero Gold
belt, which is the site of the Los Filos and Morelos gold deposits.

Quality Assurance/Quality Control

The technical information in this news release has been reviewed
and approved by Sonny Bernales, P. Geo., a registered Professional
Geoscientist in the Province of British Columbia and a qualified person
as defined by NI 43-101. Mr. Bernales is responsible for logistics and
supervision of all exploration activity conducted by Source on the
property.

The Company has implemented and adheres to a strict Quality
Assurance/Quality Control program which includes inserting mineralized
standards and blanks into the sample stream, about 1 for every 10
samples. The standards and blanks were obtained from CDN Resource
Laboratories Ltd. of Langley, BC, Canada. Each sample bag is properly
sealed and kept in a secured, restricted storage place prior to
shipping to the lab. Samples are shipped directly by Source or
picked-up by the lab vehicle with chain of custody/sample submittal
signed and dated. The Company sends it samples to SGS Mineral Services
(ISO/IEC 17025) at Durango, Mexico, an accredited and independent
laboratory. Check samples are also sent to ALS-Chemex Laboratories in
North Vancouver, Canada.

About Source Exploration

Source Exploration is a Canadian based mineral exploration company
committed to building long-term value through ongoing discoveries and
strategic acquisitions of prospective precious metals deposits in
Mexico. Source is exploring the Las Minas Project, which is located in
the core of the Las Minas district in the Veracruz State, Mexico. The
district is host to one of the largest under explored skarn systems
known in Mexico and has a strong production history that dates back to
the Aztec era.

CAUTIONARY STATEMENT REGARDING FORWARD-LOOKING INFORMATION: This
news release includes certain information that may constitute
"forward-looking information" under applicable Canadian securities
legislation. Forward-looking information includes, but is not limited
to, statements about the magnitude or quality of mineral deposits,
anticipated advancement of mineral properties or programs, future
operations, results of exploration, prospects, commodity and precious
metals prices, future work programs, anticipated financial and
operational results, capital expenditures and objectives and the
completion and timing of mineral resource estimates. Forward-looking
information is necessarily based upon a number of estimates and
assumptions that, while considered reasonable, are subject to known and
unknown risks, uncertainties, and other factors, which may cause the
actual results and future events to differ materially from those
expressed or implied by such forward-looking information, including the
risks identified in the Company's disclosure documents available at
www.sedar.com. There can be no assurance that such information will
prove to be accurate, as actual results and future events could differ
materially from those anticipated in such information. Accordingly,
readers should not place undue reliance on forward-looking information.
All forward-looking information contained in this press release is
given as of the date hereof and is based on the opinions and estimates
of management and information available to management as at the date
hereof. The Company disclaims any intention or obligation to update or
revise any forward-looking information, whether as a result of new
information, future events or otherwise, except as required by law.

Neither the TSX Venture Exchange nor its regulation services
provider (as that term is defined in the policies of the TSX Venture
Exchange) has reviewed or accepts responsibility for the accuracy or
adequacy of this release


TEL:  807-474-4270  Brian Robertson, President & CEO
TSX Venture closing price for SOP-V
Date: 2015/06/26
Closing Price: 0.05

TEL:  807-251-1816
FAX:  807-474-4272
EMAIL:  info@sourceexploration.com
INTERNET:  www.sourceexploration.com
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1517900007TS11517900559-05382220150629