Source	MARKET NEWS
Date	06/11/2015
Time	07:01:20 AM

Company	 Merrex Gold Inc.
Title	2015 RC and DD 
Drill Results from Siribaya's Dia





    CDNX Symbol: MXI











Press Release	




[200/News Release]MXIVMERREX GOLD INCJUN 11 2015  06:59 AM2015 RC and DD 
Drill Results from Siribaya's Diakha Discovery ZoneIncluding Assays of 40 m of 
2.52 g/t and 38 m @ 2.52 g/t Gold --->@NEWS RELEASE
MERREX GOLD INC ("MXI-V;MXGIF-0")
- 2015 RC and DD Drill Results from Siribaya's  Diakha Discovery
- Zone Including Assays of 40 m of 2.52 g/t and 38 m @ 2.52 g/t
- Gold

Greg Isenor, President and CEO of Merrex Gold Inc., ("Merrex"
or the "Company") announces initial 2015 Reverse Circulation ("RC") and
core ("DD") drill results from Siribaya gold project's Diakha discovery
zone in West Mali.

Highlights

-100 RC and 13 DD holes completed January 1 to May 29, 2015

-22 out of the 41 RC and DD holes fully analyzed as of May 30th
had significant gold mineralization

-Continuity of gold mineralization over a wide area continues to
be evidenced

-Numerous significant assays including:

SRD15-156: 40 m @ 2.52 g/t gold including 9 m @ 8.83 g/t gold

SRC15-539: 38 m @ 2.52 g/t gold including 10 m of 5.70 g/t gold

Commentary

"During my site visit in late May I had the opportunity to observe
the drilling operations at Diakha first-hand" said Merrex President
Greg Isenor "and I was impressed by the competence of the drill crew,
the commitment of the field staff and the professionalism of the
supervisory geological team. It is a very well-run program. There were
two drills operating, a RC and a DD drill, and the progress executing
the planned 2015 program is impressive. Together with the supervisory
field geologist I reviewed the assay results released today and
discussed preliminary cross sections and interpretations of the
exploration results to date. I also examined the drill core, including
SRD15-156 which assayed at 40 m of 2.52 g/t gold including 9 m of 8.83
g/t gold, and noted the similarities between it and the core from both
IAMGOLD's Boto and B2Gold's Fekola deposits. My conclusion is that the
2015 DD and RC infill drill program at Diakha continues to deliver
positive drill results and the assay results reported today will be
incorporated into the resource estimate planned for year-end. These
results reinforce our enthusiasm for the gold discovery made last year
at Diakha. I again extend my congratulations to the IAMGOLD exploration
team."

2015 Diakha Exploration Program

The 2015 US$3.8M exploration program is a RC and DD (core) infill
and expansion delineation drilling program with the objective of
enabling the completion of a maiden NI43-101 compliant resource
estimate by year end as results may merit.

Drill Results

From January 1 to May 29, 2015 100 RC holes totalling 11,010
metres and 13 DD holes totalling 2,422 metres were completed. Many of
these holes were tails added to 2014 holes (which were originally
drilled to approximately 100 to 120 metres) extending those holes to
new depths reaching up to 350m.

Assay results for 39 RC holes totalling 4628 metres and the 2 DD
holes totalling 528 metres have now been validated and compiled and are
reported herein. See Tables of Significant Assays below.

These assay results, as reported below, confirm the presence of
multiple zones of gold mineralization over a wide area with several
lenses related to alteration zones, with little quartz veining and low
associated sulphides. The deposit area is open in all directions and at
depth.

Table of Significant RC Assay Results

//st
--------------------------------------------------------------
|RC Hole# |Hole |From   |To       |Interval and Average Grade|
|         |Depth|(Metre)|(Metre)  |                          |
|------------------------------------------------------------|
|SRC15-508|150  |68     |86       |18 m @ 1.23 g/t           |
|------------------------------------------------------------|
|SRC15-509|150  |2      |12       |10 m @ 0.55 g/t           |
|------------------------------------------------------------|
|         |     |34     |42       |8 m @ 2.56 g/t            |
|------------------------------------------------------------|
|         |     |112    |118      |6 m @ 0.60 g/t            |
|------------------------------------------------------------|
|SRC15-510|100  |0      |6        |6 m @ 0.95 g/t            |
|------------------------------------------------------------|
|SRC15-515|127  |42     |46       |4 m @ 1.55g/t             |
|------------------------------------------------------------|
|SRC15-517|102  |42     |48       |6 m @ 0.77 g/t            |
|------------------------------------------------------------|
|SRC15-519|150  |90     |100      |10 m @ 2.58g/t            |
|         |     |90     |92       |including2 m @ 8.18 g/t   |
|------------------------------------------------------------|
|         |     |108    |124      |16 m @ 0.93g/t            |
|------------------------------------------------------------|
|SRC15-520|120  |54     |58       |4 m @0.87g/t              |
|------------------------------------------------------------|
|         |     |66     |82       |16 m @ 0.91g/t            |
|------------------------------------------------------------|
|SRC15-521|100  |22     |26       |4 m @ 0.65g/t             |
|------------------------------------------------------------|
|         |     |38     |46       |8 m @ 1.87g/t             |
|------------------------------------------------------------|
|SRC15-523|91   |82     |86       |4 m @ 2.01g/t             |
|------------------------------------------------------------|
|SRC15-525|150  |20     |24       |4 m @ 2.08g/t             |
|------------------------------------------------------------|
|         |     |42     |46       |4 m @2.08g/t              |
|------------------------------------------------------------|
|         |     |62     |72       |10 m @ 1.38g/t            |
|------------------------------------------------------------|
|         |     |76     |80       |4 m @ 0.66g/t             |
|------------------------------------------------------------|
|SRC15-527|120  |18     |22       |4 m @0.53g/t              |
|------------------------------------------------------------|
|SRC15-528|114  |84     |92       |8 m @ 1.25g/t             |
|------------------------------------------------------------|
|         |     |108    |112      |4 m @ 0.58g/t             |
|------------------------------------------------------------|
|SRC15-529|113  |88     |94       |6 m @ 2.37g/t             |
|------------------------------------------------------------|
|SRC15-532|100  |82     |88       |6 m @ 1.61g/t             |
|------------------------------------------------------------|
|SRC15-533|126  |40     |56       |16 m @ 1.12g/t            |
|------------------------------------------------------------|
|SRC15-537|150  |82     |94       |12 m @ 1.85g/t            |
|------------------------------------------------------------|
|         |     |106    |112      |6 m @ 1.25g/t             |
|------------------------------------------------------------|
|SRC15-538|140  |48     |52       |4 m @ 0.69g/t             |
|         |     |106    |110      |4 m @ 1.22 g/t            |
|         |     |116    |122      |6 m @ 4.10 g/t            |
|------------------------------------------------------------|
|         |     |118    |120      |including2 m @ 9.36g/t    |
|------------------------------------------------------------|
|SRC15-539|150  |10     |16       |6 m @ 0.60g/t             |
|------------------------------------------------------------|
|         |     |44     |48       |4 m @ 1.38g/t             |
|         |     |54     |60       |6 m @ 6.31 g/t            |
|         |     |58     |60       |including2 m @ 10.80 g/t  |
|------------------------------------------------------------|
|         |     |84     |122      |38 m @ 2.52g/t            |
|         |     |106    |116      |including10 m @ 5.70 g/t  |
|         |     |106    |108      |including2 m @ 11.60 g/t  |
|------------------------------------------------------------|
|SRC15-540|150  |10     |20       |10 m @ 0.92g/t            |
|------------------------------------------------------------|
|         |     |56     |62       |6 m @ 2.57g/t             |
|------------------------------------------------------------|
|         |     |76     |82       |6 m @ 8.20g/t             |
|         |     |80     |82       |including2 m @ 23.60 g/t  |
|------------------------------------------------------------|
|         |     |94     |102      |8 m @ 1.28g/t             |
|------------------------------------------------------------|
|SRC15-541|130  |6      |36       |30 m @ 0.74g/t            |
|------------------------------------------------------------|
|         |     |88     |92       |4 m @ 1.05g/t             |
|------------------------------------------------------------|
|SRC15-542|100  |38     |44       |6 m @ 0.67g/t             |
|------------------------------------------------------------|
|         |     |92     |100 (EOH)|8 m @ 2.90g/t             |
|------------------------------------------------------------|
|SRC15-543|150  |38     |50       |12 m @ 0.97g/t            |
|------------------------------------------------------------|
|SRC15-546|102  |80     |88       |8 m @ 4.30g/t             |
|         |     |80     |82       |including2 m @ 10.50 g/t  |
--------------------------------------------------------------
Table of Significant DD Assay Results
-----------------------------------------------------
|DD Hole# |Hole |From|To |Interval and Average Grade|
|         |Depth|(M) |(M)|                          |
|---------------------------------------------------|
|SRD15-155|260.1|49  |52 |3 m @ 1.82g/t             |
|---------------------------------------------------|
|         |     |94  |103|9 m @ 0.84g/t             |
|---------------------------------------------------|
|         |     |99  |101|including2 m @ 2.43g/t    |
|---------------------------------------------------|
|         |     |234 |239|5 m @1.15g/t              |
|---------------------------------------------------|
|SRD15-156|358  |84  |124|40 m @ 2.52g/t            |
|---------------------------------------------------|
|         |     |84  |93 |including9 m @ 8.83g/t    |
|         |     |84  |87 |including3 m @ 14.83      |
|         |     |    |   |g/t                       |
-----------------------------------------------------
//et

Note 1:  All RC samples sent to the laboratory are 2 meter
composite samples while DD samples are 1 metre in length

Note 2:  QA/QC and additional technical information are described
below

Note 3:  RC Drill hole intercepts are calculated using a minimum
down-hole length of 2 meters. , DD Drill hole intercepts are calculated
using a minimum down-hole length of 1 meter. All intercepts use a
cut-off grade

of 0.5 g/t gold, are uncapped, and may include up to 5 metres of
internal dilution

Note 4:  The widths of intersections are downhole lengths; true
widths are unknown at this time

Note 5:  All holes were drilled azimuth 115 and dipping -60o

Note 6:  "EOH" means 'end of hole'

Note 7:  Seventeen RC holes returned no significant assays.

A drill plan plan (Map 1) showing drill collar locations is
provided below. The map contains a selected sample of assay results.
For a comprehensive list of assays and intervals see the Table of
Significant Assays above, and for assay results from previous drill
programs at Diakha refer to the news release archive on Merrex's
website at www.merrexgold.com.

Map 1

The Diakha discovery zone drill plan collar location map

(img src='https://www.thenewswire.com/client_files/tnw6wmJE0_.png'
/) @ https://www.thenewswire.com/client_files/tnw6wmJE0.png
Click Image To View Full Size

About the Diakha Discovery

The Diakha gold discovery area is located in the western-most of
the 910 km2 Siribaya exploration concessions, occurs approximately 10
kilometres south along strike of IAMGOLD's Boto gold discoveries
(IAMGOLD is currently undertaking resource estimation, economic and
mine design studies for Boto) and approximately 20 kilometres south
along strike from B2Gold's (formerly Papillon's) Fekola deposit (Fekola
is permitted for production). See Map 2 below.

Map 2

The Diakha discovery zone is at the southern end of the
Fekola-Boto-Diakha trend

in alignment with major deposits at Malikoundi and Boto 6
(IAMGOLD) and Fekola (B2Gold/Papillon).

(img src='https://www.thenewswire.com/client_files/tnw1uiDlG_.png'
/) @ https://www.thenewswire.com/client_files/tnw1uiDlG.png
Click Image To View Full Size

Note 1:  Fekola (B2Gold/Papillon) resource estimate is at
September 3, 2013

//st

-----------------------------------------
|Resource Category|Grade Au|Total Ounces|
|---------------------------------------|
|Measured         |2.43 g/t|3,160,000   |
|---------------------------------------|
|Indicated        |2.35 g/t|1,480,000   |
|---------------------------------------|
|Inferred         |1.90 g/t| 500,000  |
|---------------------------------------|
|Total Resources  |2.35 g/t|5,150,000   |
-----------------------------------------

//et

Note 2:  Boto (IAMGOLD) resource estimate is at December 31, 2014

//st

-----------------------------------------
|Resource Category|Grade Au|Total Ounces|
|---------------------------------------|
|Indicated        |1.68 g/t|1,232,000   |
|---------------------------------------|
|Inferred         |1.80 g/t| 635,000   |
-----------------------------------------

//et

Note 3: Fekola has as current measured and indicated mineral
resource estimate of 63.7 Mt for 3.91 Million ounces grading 1.91g/t
based on January 2013 B2GOLD PEA Mineral Resource Estimate at a 0.6 g/t
cut-off 1

The Diakha area was highlighted for exploration by the presence of
a gold geochemical anomaly delineated from a regional termite mound
sampling survey and coincident with artisanal (orpailleur) mining
activity.

Technical Information and Quality Control Notes

The Siribaya Gold drilling results contained in this news release
were prepared in accordance with National Instrument 43-101 Standards
of Disclosure for Mineral Projects. The sampling of, and assay data
from, rock chips and drill core is monitored through the implementation
of a quality assurance - quality control program by IAMGOLD designed to
follow industry best practice.

Rock chips from the Reverse Circulation drilling are collected at
the rig site, at one metre intervals, under the direct supervision of
IAMGOLD geologists. Samples are riffle split to obtain two 3 kg
samples. One sample is retained for reference purposes and the other isused to 
prepare 2-meters composite samples for assay. The 2 meter
composite samples are prepared at the project site, by trained
technicians supervised by IAMGOLD geologists.

Drill core (HQ and NQ size) samples were selected by the IAMGOLD
geologists and sawn in half with a diamond blade at the project site.
Half of the core is retained at the site for reference purposes. Sample
intervals are generally one metre in length.

Samples are analyzed at both ALS Chemex Analytical Laboratory and
SGS-Minerals located in Bamako, Mali, using a standard fire assay with
a 50 gram charge and an Atomic Absorption finish.

About Merrex's Siribaya Gold Project

The Siribaya Gold Project is a 50/50 joint Merrex-IAMGOLD
advanced-stage gold exploration project in West Mali comprised of
approximately 910 square kilometres of gold-prolific exploration
permits and permit applications pending. Exploration of the Siribaya
Gold Project is conducted under a joint management committee with
IAMGOLD as the project operator. Expenditures to date on the Siribaya
Project total approximately $42 million.

The Siribaya Gold Project presently hosts a gold resource
estimated at 303,900 ounces grading 2.34 g/t Indicated, and 301,400
ounces grading 2.17 g/t Inferred. The gold resource estimate was
prepared in accordance with CIM definitions as required by NI 43-101
and is at July 31, 2012 by ACA Howe International Limited. The deposit
areas are open to the north, south and at depth. Numerous other
gold-anomalous target areas have been identified by geochemistry and
require drilling.

About the Karita Gold Project, Guinea

The Karita Gold Project is an approximately 100 km2 Authorization
for Exploration concession located at the tri-point boundary of Guinea,
Mali and Senegal. It is also on strike 1.5 kilometres north of
Merrex-IAMGOLD's Diakha gold discovery, which is located in the
western-most portion of the 760 km2 Siribaya joint venture exploration
concessions, and approximately 7 kilometres south along strike from
IAMGOLD's Boto gold deposit (scoping study in progress). This is also
that same structure as B2Gold's (formerly Papillon's) Fekola deposit
(permitted for production) approximately 15 kilometres to the north.
The Karita permit area is 100% owned by Merrex, not within the area of
influence of the Merrex - Iamgold Siribaya joint venture and,
importantly, the Karita Gold Project hosts approximately two kilometres
of the Fekola-Boto-Diakha gold trend which is in the southern portion
of the prolific Mali - Senegal shear.

Merrex first recognized the significance of the Karita permit area
over two years ago, and after protracted efforts including numerous
trips to Guinea by our strategic partner to settle issues with the
Department of Mines, Guinea Merrex was successful in securing the
Karita Authorization for Exploration from the Guinean government.

Together, Merrex's Siribaya Gold Project, Mali and Karita Gold
Project, Guinea total 860 km2.

Gregory P. Isenor, P. Geo., is the Qualified Person as defined
under NI 43-101 who has reviewed and is responsible for the technical
information presented in this news release.



Merrex is primarily a West African focused gold exploration
company with experienced management, a solid exploration team, a
prominent gold-producer as a JV partner and an expanding gold resource.


For further details about the Company's exploration activities or
to view the most recent corporate presentation visit Merrex's website
at www.merrexgold.com. To be added to Merrex's email contact list
please email your request to info@merrexgold.com.

On Behalf of the Board



Gregory Isenor, P.Geo.
President & CEO



MERREXGOLD
Suite 802,

1550 Bedford Highway,

Bedford, NS B4A 1E6  T

el.: (902) 832-5555

Fax: (902) 832-2223



This press release includes certain statements that may be deemed
"forward-looking statements". All statements in this release, other
than statements of historical facts, that address future exploration
drilling, exploration activities and events or developments that the
Company expects, are forward-looking statements. Although the Company
believes the expectations expressed in such forward-looking statements
are based on reasonable assumptions, such statements are not guarantees
of future performance and actual results or developments may differ
materially from those in forward-looking statements. Factors that could
cause actual results to differ materially from those in forward-looking
statements include market prices, exploitation and exploration
successes, continued availability of capital and financing, and general
economic, market or business conditions.



Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.



__________________________________________________
_______________________________________________
TSX Venture closing price for MXI-V
Date: 2015/06/10
Closing Price: 0.18
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1516100008TS11516100778-06590420150611