Source	Marketwire
Date	06/16/2015
Time	07:03:05 AM

Company	 AMEX EXPLORATION INC.
Title	New Mineralization Discovered by Drilling in the Normetal Mine Horizon at 
Amex's Perron Property, Abitibi





    CDNX Symbol: AMX











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Amex Exploration Inc.

TSX VENTURE SYMBOL: AMX

June 16, 2015

New Mineralization Discovered by Drilling in the Normetal Mine Horizon at 
Amex's Perron Property, Abitibi


MONTREAL, QUEBEC--(Marketwired - June 16, 2015) - Amex Exploration Inc. (TSX 
VENTURE:AMX) ("Amex" or the "Corporation") is very pleased to announce that 
Agnico Eagle Mines Ltd (TSX:AEM)(NYSE:AEM) has presented the results of its 
2015 winter drilling work program on Amex's Perron property. This program is 
under the terms and conditions of the second year of the Perron option 
agreement that was signed in 2013 (see PR of June 21, 2013 for details on the 
option agreement terms and conditions).

The three different objectives of this phase of drilling returned positive 
results (see below and Table 1), but the highlight of this work is the 
discovery of a new unknown polymetallic mineralization that returned 2.23 % Cu, 
0.11% Zn, 8.30 g/t Ag and 0.20 g/t Au over 1.0 meter within the Normetal Mine 
Horizon (NMH). This mineralization is hosted within a highly chloritized 
stratabound unit of tuffeceous material located between a unit of rhyolite and 
a unit of andesite of the NMH at the same stratigraphic position of the former 
producer Normetal Mine (historical lifetime production of 10.1 MT @ 2.15% Cu, 
5.12% Zn, 0.55 g/t Au and 45.25 g/t Ag) situated at less than 3 km to the East 
of the property.

Winter 2015 drill program and results

As a whole, this latest phase of work consisted of 13 drill holes totalling 
4,846 meters of drilling that has been executed with two diamond drill rigs 
between January and April 2015. Three distinct types of targets were identified 
with this work based on the previous phases of drilling and last year's 
airborne geophysical survey that covered the entire Perron property (see PR 
2015-01-19).

The three target areas are:

First, in the vicinity of Amex initial discovery hole PE-2013-03 drilled by 
Amex in 2013, and a follow up of new polymetallic gold-bearing structure in 
hole #163-14-004 that has been identified in 2014 drilling (see PR of January 
8th, 2015).

Second, to test the lateral potential contact between the Rhyolite unit and the 
Andesite unit of the Beaupre bloc, host of the known Perron polymetallic 
mineralization, on a large spacing grid.

Third, on new airborne geophysical anomalies identified last year that have 
never been drilled before and that are located within the Normetal Mine 
Horizon. This specific geological unit, located at some 0.5 km to 1.0 km to the 
North of the Rhyolite-Andesite contact of the Beaupre Bloc, can be followed 
over a strike length of 8 km within the Perron Property. This unit, which has 
never been drilled previously by Amex, is the host of several polymetallic VMS 
deposit including the former Normetal Mine.

Overall, three drill holes were drilled in the vicinity of the initial Perron 
Polymetallic Mineralization (Target 1; namely holes 163-15-008, 012 and 020), 
five following the favourable Rhyolite-Andesite contact of the Beaupre bloc 
(Target 2 ; from West to East; holes 163-15-017, 018, 021, 013and 011) and 
finally five holes on the Normetal Mine Horizon (Target 3; from East to West; 
holes 163-15-009, 010, 015, 019 and 014).(see figure 1 for location and Table 1 
for results).

Table 1 : Perron Winter 2015 Best Drilling Results

/T/

----------------------------------------------------------------------------
Length       Au       Ag       Cu       Zn
Hole              From       to      (m)    (ppm)    (ppm)    (ppm)    (ppm)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-15-008       332,5    337,5      5,0     0,06     0,18       75     1536
----------------------------------------------------------------------------
394,5    401,2      6,7     0,20     1,30       51     1545
----------------------------------------------------------------------------
429,0    432,0      3,0     0,42     0,65       11      283
----------------------------------------------------------------------------
523,0      530      7,0     0,29     1,14        5       85
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-15-011       352,0    353,0      1,0     0,13     0,10      122     7440
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-15-012       276,0    279,9      3,9     2,70    18,95      736    13788
----------------------------------------------------------------------------
incl.    277,1    277,6      0,5    13,25    99,60     1205    42200
----------------------------------------------------------------------------
351,5    367,0     15,5     0,51     1,05       56      354
----------------------------------------------------------------------------
367,0    375,5      8,5     0,13     1,39      109     2404
----------------------------------------------------------------------------
395,4    396,0      0,6    10,35    10,90       50     1165
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-15-013       165,6    166,6      1,0     7,33     2,80       43      115
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-15-015       128,4    129,4      1,0     0,20     8,30    22300     1065
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-15-017       318,0    327,4      9,4     0,64     0,14       10      210
----------------------------------------------------------------------------
incl.    319,5    321,0      1,5     1,17     0,30        4       30
----------------------------------------------------------------------------
and incl.    326,4    326,9      0,5     2,91     0,30       61      204
----------------------------------------------------------------------------
500,5    501,0      0,5    11,80     1,50        1       85
----------------------------------------------------------------------------
514,5    535,5     21,0     0,22     0,58       16       97
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-15-018       356,5    370,5     14,0     0,36     0,11        6       61
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-15-019       171,0    171,5      0,5     0,74     0,20      402      651
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-15-020       162,5    163,0      0,5     0,27     0,20       30    16150
----------------------------------------------------------------------------
271,3    273,0      1,7     0,89     2,05      171     6792
----------------------------------------------------------------------------
331,0    331,5      0,5     0,16     1,10       73     6960
----------------------------------------------------------------------------
346,4    347,2      0,8     0,86     1,10       40     2760
----------------------------------------------------------------------------
370,0    382,0     12,0     1,79     7,84      983     1700
----------------------------------------------------------------------------
incl.    378,0    378,5      0,5     1,61     5,70      354    14900
----------------------------------------------------------------------------
and incl.    380,2    381,0      0,8    15,80    17,30      480     1585
----------------------------------------------------------------------------
and incl.    381,0    381,5      0,5     2,04   121,00    20100     3780
----------------------------------------------------------------------------
389,0    392,2      3,2     0,44     2,28      195     8996
----------------------------------------------------------------------------
incl.    391,0    392,2      1,2     0,37     4,34      325    22925
----------------------------------------------------------------------------
411,4    412,4      1,0     2,79    28,60     3850      366
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-15-021       215,4    220,9      5,5     1,70     0,58       87      557
----------------------------------------------------------------------------
incl.    217,5    219,0      1,5     5,67     1,48      149      621
----------------------------------------------------------------------------
incl.    218,2    219,0      0,8     9,45     2,60      300     1100
----------------------------------------------------------------------------
Table 1: Geochemical analysis was executed by ALS Chemex Laboratories in Val
D'Or under Agnico Eagle Mines QA/QC program and supervision.

/T/

Target 1: Vicinity of initial Perron Polymetallic discovery

Two out of three holes (i.e. 163-15-012 and 020) were drilled perpendicular to 
the discovery hole PE-2013-03 in order to better understand the geometry and 
the continuity of the now interpreted as a typical polymetallic VMS stockwerk 
zone made of veins and veinlets of almost semi-massive sulfides (mostly 
sphalerite, chalcopyrite and pyrite/pyrrhotite) associated with highly altered 
rhyolite with a significant content of Manganese-bearing porphyroblasts of 
garnets.

The two holes intersected the overall stockwork structure at different 
locations and depths, but with expected narrower intervals with values of up to 
2.70 g/t Au, 18.95 g/t Ag, 1.38% Zn and 0.07% Cu over 3.9 meters including 0.5 
meter at 13.25 g/t Au, 99.60 g/t Ag, 4.22% Zn and 0.12% Cu in hole 163-15-012 
and 1.79 g/t Au, 7.84 g/t Ag, 0.17% Zn and 0.10% Cu over 12.0 meters including 
0.8 meter at 15.80 g/t Au, 17.30 g/t Ag 0.16% Zn and 0.05% Cu and including 0.5 
meter at 2.04 g/t Au, 121.00 g/t Ag, 0.38% Zn and 2.01% Cu in hole 163-15-020. 
These results indicate that this mineralized structure can be followed over an 
area of a minimum lateral extent of 50 meters by a vertical extent of at least 
100 meters and still open in all directions.

The third hole in this area (ie hole 163-15-008) was drilled to test a second 
mineralized structure similar to the first one outlined in the former drill 
program done last year but located at some 300 meters to the east (ie hole 
163-14-004), but closer to the surface. Only wide spread gold and zinc 
anomalies were intersected (see Table 1).

Target 2: Favourable Rhyolite-Andesite contact in the Beaupre Bloc

In total, 5 holes have been drilled to test the Rhyolite-Andesite favourable 
contact within the Beaupre bloc (host of the Perron Polymetallic 
Mineralization) at the eastern portion of this horizon over a distance of about 
4,0 km. These 5 DDH were drilled at a spacing of about 250 meters along a 
strike length of about 1.5 km starting with hole 163-15-017 located at a 
distance of about 75 meters to the west of hole PE-2013-04 and ending with hole 
163-15-011 located at 2.5 km of the same hole. Except for hole 163-15-021, all 
of these holes returned some anomalous polymetallic gold zones associated with 
the same alteration type that for the Perron Polymetallic structure, 
characterized by the presence of pinkish porphyroblasts of garnet, with values 
of up to 11.8 g/t Au and 1.50 g/t Ag over 0.5 meters in hole 163-15-017 where 
some visible gold was also noted.

In the case of hole 163-15-021, a highly pyritized stratabound mineralization 
associated with high silica and sericite alteration that is totally different 
of the Perron polymetallic mineralization has been intersected close to the 
Rhyolite-Andesite contact of the Beaupre Bloc. This intersect has returned 1.70 
g/t Au over 5.5 meters including 0.8 meter at 9.45 g/t Au. It is important to 
note that this intersect seems to be associated with a VTEM airborne geophysics 
that is parallel to the mineralization and can be followed over a strike length 
of at least 400 meters.

Target 3: 2014 VTEM airborne anomalies located within the Normetal Mine Horizon

Following the 2014 VTEM airborne survey and a geological compilation work of 
the property, five holes were drilled in order to test the Normetal Mine 
Horizon. From this work, one drill hole (ie 163-15-015) has intersected a 
significant semi-massive sulfide horizon associated with heavy dark chlorite 
alteration that returned 2.23 % Cu, 0.11% Zn, 8.30 g/t Ag and 0.20 g/t Au over 
1.0 meter. This mineralization is hosted within a stratabound unit of 
tuffeceous material located between a unit of rhyolite and a unit of andesite 
of the NMH at the same stratigraphic position of the former producer Normetal 
Mine (historical lifetime production of 10.1 MT @ 2.15% Cu, 5.12% Zn, 0.55 g/t 
Au and 45.25 g/t Ag). Moreover, this intersect is associated with a VTEM 
anomaly identified last year by airborne survey over more than 300 meters in 
strike length. Down hole geophysics survey (Pulse EM) in this hole has detected 
an EM conductor associated directly to this intercept that confirmed the 
airborne anomaly and open up new promising ground for additional work.

Comments on the Results

The management of Amex is very enthusiastic about the results of this latest 
phase of drilling done by Agnico Eagle Mines on Amex's 100% owned Perron 
property. Jacques Trottier, Ph.D, president and CEO of Amex says: 'This less 
than 5,000 meters phase of drilling has, in our opinion, successfully returned 
positive results on each of three different types of target. Namely, not only 
on follow-up drilling in the Amex 2013 discovery area, but also on two very 
different types of target. This shows how much this underexplored property 
potential has. I want to personally congratulate the Agnico Eagle Mines 
exploration team for this new discovery on the Normetal Mine Horizon done by 
their skilled experienced exploration geologists. We are looking forward to see 
the follow-up program on each of the favourable targets that they have 
outlined, hopefully in a very near future'.
Amex Exploration Inc. is a junior mining exploration company listed on the TSX 
Venture Exchange whose primary objective is to develop and bring into 
production viable gold and base metal deposits. Jacques Marchand, P.Eng. Geo., 
Qualified Person as defined by Canadian N43-101 has approved the technical 
information reported in this news release.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

FIGURE 1 is available at this address: 
http://media3.marketwire.com/docs/1012772_Amex_Figure1.jpg

- 30 -

CONTACT INFO:

Jacques Trottier
514-866-8209

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=532933004