Source	MARKET NEWS
Date	06/22/2015
Time	08:58:13 AM

Company	 Visible Gold Mines Inc.
Title	Provides 
Drilling and Exploration Update





    CDNX Symbol: VGD











Press Release	





VISIBLE GOLD MINES INC ("VGD-V;VGMIF-0")
- Provides Drilling and Exploration Update

Visible Gold Mines Inc. is pleased to provide an update of its
current summer exploration activities on its 167 Property and its
recent diamond drilling program.

Summer Exploration Update

Induced Polarization Ground Survey

On June 2, Remy Belanger Geophysics and his crew initiated a 40
kilometres phase-domain induced polarization ground survey along the
new 167 provincial road. The purpose of this survey will map the
lithologies, geological units and structural features underlying the
167 Property, to investigate potentially favourable zones of alteration
and to map with a better accuracy the distribution of disseminated and
stringer sulfides in the bedrock. The geophysical survey is carried out
along the new road and was chained and picketed every 50 metres. The
Phase I.P. survey is using a dipole-dipole electrode configuration. The
dipole dimension is 50 metres and successive separations at multiples
of n=1,2,3,4,5 and 6 times the dipole dimensions is used, in order to
investigate at depth. This configuration should provide a depth
penetration of about 125 to 180 metres, depending on target size.

The data processing and interpretation will be performed by Mr.
Joel Dube, P. Eng. from Dynamic Discovery Geoscience of Ottawa, an
engineering firm specialized in geophysics. Inversion models of the
resistivity and chargeability distribution within the ground will be
generated to better understand the geometry and possible nature of
anomaly sources. These products will be available by the end of June
2015. They will be integrated to other available data in the area and
will ultimately provide guidance for the next exploration phase planned
for the upcoming summer, which will include exploratory drilling.

Till Sampling

Visible Gold Mines has retained the services of Inlandsis
consultants, who have been specializing in boulder tracing since 1996
and who have been involved in many technical successes with a wide
range of exploration companies. Inlandsis has already completed a first
appraisal of glacial landforms and ice-flow sequences for Visible Gold
Mines' 100% owned 167 Property. An exploration campaign based on full
use of the glacial indicator tracing technique is to be initiated in
the near future, in order to locate the bedrock source of the
gold-rich-boulders discovered on the 167 Property. This campaign will
use both rock fragments and free gold grains in till as tracers to be
followed-up to their source.

Prospection

On June 3, 2015, a prospecting program was initiated on both the
south and north sectors of the 167 Property. It is expected that a crew
of at least six geologists and technicians will be working on the 167
Property for a period of six weeks during the months of June and July,
prospecting mainly for mineralized outcrops in unexplored areas of the
property. The objective of the prospecting program is to identify the
sources of the various boulders found during our previous prospection
and exploration programs. As Visible Gold Mines cannot guarantee the
origin of some of the boulders collected on the 167 Property and in
order to avoid any potential contamination of samples collected to date
caused by the significant work done during the construction of the new
167 provincial road or caused by any other source the prospecting team
will focus on prospection and exploration of outcrops and boulders
located further away from areas which may have been contaminated.
Visible Gold Mines believes that the outcrops samplings method will
provide more accuracy on the origin of the samples, which is not the
case with boulders that can come from different sources, even sources
external to the property.

Since the beginning of that prospecting program, several
mineralized outcrops with pyrrhotite, pyrite and chalcopyrite were
identified in the southern sector of the 167 Property. A first series
of samples has been sent for analysis, the results of which will be
released as they become available.

Drilling update

A 20-hole diamond drilling program totalling approximately 4,184
metres was performed from January to March 2015. The main objective of
this drilling program was to better understand the geology and the
nature of some electromagnetic (EM) conductors identified during the
airborne survey completed in December 2014. The main objective of that
program has been achieved. Though several drill holes have intersected
mineralization over several metres, none of the 20 holes has produced
results which may generate economic returns. The information obtained
from this drill program is very useful for the exploration programs
underway and for those to come.

However, the hole 167-15-06 is interesting. This drill hole was
initially supposed to test a target in an area with an isolated intense
electromagnetic (EM) anomaly located in the northern sector of the 167
Property (km144), but due to the impossibility of reaching that area,
the hole was done approximately 500 metres West from the main target,
but between two moderate electromagnetic (EM) anomalies. Anomalous
values of 0.2% nickel were obtained on 13.5 metres.

Visible Gold Mines encountered significant delays in publishing
its drilling results. The delays were mainly caused by a backlog at the
laboratory used to conduct analysis of our samples and in some cases,
the re-analysis of certain samples. Visible Gold Mines has taken the
necessary measures to avoid these delays in the future.

Qualified Persons

Mr. Martin Dallaire, P.Eng., President and Chief Executive Officer
of Visible Gold Mines, is the qualified person on the 167 Project
exploration information presented in this press release under National
Instrument 43-101 Standards of Disclosure for Mineral Projects, is also
responsible for the technical contents of this press release and has
approved the disclosure of the technical and exploration information
contained herein. The data verification was conducted by Jeannot
Theberge, P.Geo. under the supervision of Martin Dallaire, P.Eng.

About the 167 Project

In 2011, the Quebec Government launched its ambitious Plan Nord
project to develop Quebec's northern region, which included the
construction of a 243 kilometre-long all-season road linking
Stornoway's Renard Diamond project to the provincial highway network.
At that time, Visible Gold Mines' management decided to acquire the
available mining rights along each side of the new road in order to
have access to new outcrops and strippings generated by the road
construction. Visible Gold Mines acquired claims by acquisition and
staking, and so the 167 Project was born. Out of the 140 kilometres of
new road available for mining exploration (the first 102 kilometres are
a planned provincial park), Visible Gold Mines owns more than 110
kilometres. The road was completed on October 1, 2014 at a construction
cost of approximately $350 million. The 167 Project is 100% owned by
Visible Gold Mines and with recent acquisitions covers up to 61,178
hectares, or 611 km2.

About Visible Gold Mines

Visible Gold Mines Inc. is a dynamic corporation aggressively
searching for the next important gold deposit in the province of
Quebec, an area consistently ranked as one of the world's best
jurisdictions for mining and exploration.

Forward-Looking Statements

This news release contains statements that may constitute
"forward-looking information" within the meaning of applicable Canadian
securities legislation. Forward-looking information may include, among
others, statements regarding the future plans, costs, objectives or
performance of Visible Gold Mines, or the assumptions underlying any of
the foregoing. In this news release, words such as "may", "would",
"could", "will", "likely", "believe", "expect", "anticipate", "intend",
"plan", "estimate" and similar words and the negative form thereof are
used to identify forward-looking statements. Forward-looking statements
should not be read as guarantees of future performance or results, and
will not necessarily be accurate indications of whether, or the times
at or by which, such future performance will be achieved. No assurance
can be given that any events anticipated by the forward-looking
information will transpire or occur, including the development of the
167 Project, or if any of them do so, what benefits Visible Gold Mines
will derive. Forward-looking information are based on information
available at the time and/or management's good-faith belief with
respect to future events and are subject to known or unknown risks,
uncertainties, assumptions and other unpredictable factors, many of
which are beyond Visible Gold Mines' control. These risks,
uncertainties and assumptions include, but are not limited to, those
described under "Financial Risk Management Objectives and Policies, and
Financial Risks" in Visible Gold Mines' Annual Report for the fiscal
year ended on July 31, 2014, a copy of which is available on SEDAR at
www.sedar.com, and could cause actual events or results to differ
materially from those projected in any forward-looking statements.
Visible Gold Mines does not intend, nor does Visible Gold Mines
undertake any obligation, to update or revise any forward-looking
information contained in this news release to reflect subsequent
information, events or circumstances or otherwise, except if required
by applicable laws.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of the
release.

TSX Venture closing price for VGD-V
Date: 2015/06/19
Closing Price: 0.07

TEL:     819-762-0107 Martin Dallaire, President and CEO
E-mail:  mdallaire@visiblegoldmines.com
Website: www.visiblegoldmines.com
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1517200022TS11517201303-08563920150622