Source	MARKET NEWS
Date	06/29/2015
Time	04:09:43 PM

Company	 Para Resources Inc.
Title	Results on 
the Drilling Program at its Tucuma Pr





    CDNX Symbol: PBR











Press Release	




[200/News Release]PBRVPARA RESOURCES INCJUN 29 2015  16:08 PMResults on 
the Drilling Program at its Tucuma Property In ParaState, Brazil --->@NEWS 
RELEASE
PARA RESOURCES INC. ("PBR-V")
- Results on the Drilling Program at its Tucuma Property
- In Para State, Brazil

Para Resources Inc. ("Para Resources" or the "Company"), a mineral
exploration company listed on the TSX Venture Exchange (the
"Exchange"), is pleased to announce the results on the drilling program
at Angelim and Serrinha targets in its Tucuma Gold-Copper Project (the
"Project"), located in Carajs Province, Brazil. The Project is 100%
owned by Para Resources.
A shallow drilling program was conducted at Zone 1 of Angelim
Target with the aim of exploring and detailing the mineralized area,
defined by the previous trenching program, until the bottom of
saprolite/saprock level.
The fourteen drill holes performed at Zone 1 were located under an
approximated 25x25m grid and most of them had a 90o azimuth direction,
45o inclined, as shown in the map below:
Note that some of them had a different azimuth, as to infill
information at 12.5m and test plunge control possibilities.
The 717.67m of drilling carried out on 14 holes from 38.30 to
59.70m of depth at Zone 1 had the double function of confirming
mineralization underneath the trenches, improving the confident level
of information, and fulfilling the obligation of presenting a Final
Exploration Report to the Brazilian government related to Angelim and
Serrinha targets.
Only a further drill hole of 60.65m of depth was performed at
Serrinha Target to confirm an historical gold-copper intersection
obtained by Anglo American in the beginning of the 90's.
Core sampling was taken in respect to a 1.00 to 2.00m support,
respectively in mineralized and non-mineralized intervals, although
always prioritizing the geological features and breaks, such as
lithological, regolith and alteration contacts.
Most of the core-drilling sampling results confirmed gold
mineralization obtained in the channel sampling of the trenching
program, until 40 vertical meters from surface. Saprolite/saprock
bottom varies between 25 to 35m of depth, averaging 30m of weathered
material.
Drilling has intercepted gold mineralization, mainly in saprolite
and saprock, sometimes in fresh rock materials, represented by a
brecciated quartz-sulphidized (partially oxidized) vein with veinlets
in the neighborhood hydrothermally altered envelopment over metandesite
rock.
Highlights of the drilling assays, obtained in Zone 1 at Angelim
Target, include down-hole composite results over such core linear
sampling, as follows:
North (from the fault) Block:
8.30 meters @ 8.62 gpt Au, including 2.60 meters @ 25.72 gpt Au
South (from the fault) Block:
11.05 meters @ 10.95 gpt Au, including 3.40 meters @ 19.28 gpt Au
and
8.95 meters @ 4.94 gpt Au, including 2.75 meters @ 9.33 gpt Au.

Considering the drilling was programmed in order to cut the
mineralized structure as perpendicular as possible, to get
approximately true width, down-hole width should be multiplied by the
cosin of the drill hole inclination angle.
Mineralization at Zone 1 seems to be filling a stretching (.3)
discontinuity structure represented by a spaced foliation varying from
N-S to N35oW direction steeply to subvertical dipping west. In
addition, stretching could be also forming a lineation which plunges
NW, and could be controlling gold high grade concentrations. This could
explain the restrict mineralization expression at surface, making the
potential be very expressive along the plunge at depth.
Highlights of the Roque Pit Zone at Serrinha Target drilling assay
results include down-hole composite gold-copper mineralization, as
follows:
7.00 meters @ 1.67 gpt Au and 0.14% Cu, including 3.00 meters @
2.97 gpt Au and 0.17% Cu.
4.00 meters @ 6.03 gpt Au and 0.50% Cu, including 2.00 meters @
4.87 gpt Au and 0.98% Cu.
Serrinha primary gold-copper mineralization, previous identified
by the old informal open pit mining activity at Roque Pit Zone and
proved by Anglo American historical drilling, comprises a set of
quartz-tourmalinearsenopyrite-chalcopyrite-pyrite veins, which follows
a NE-SW opening structure and is probably related to a felsic
intermediate subvolcanic rock, intruding the greenstone belt sequence.
The whole drilling program yielded 694 samples for assay, where the
grade of gold was between (0.005 - 48.95 gpt. The ranges were as
follows:
//st
Ranges of assay Results       Number of Samples     %
(grams per ton of Au)
10.00 - 48.95                     12                1,73%
5.00 - 9.99                       10                1,44%
0.30 - 10.00                      93                13,40%
Assays above 0.30 gpt cut-off    115                16,57%
0.005 - 0.29                     454                65,42%
(0.005                           125                18,01%
Total of samples                 694               100,00%
//et

A complete table of drilling gold intersections at Zone 1 of
Angelim Target is presented below:
//st
DDH     Hole    Hole   From  To   Down    True    Au
In-     Azi-   (m)   (m)  Hole    Width   (g/t)
clina-  muth              Width   (m)
tion    (o)               (m)
(o)

ANGD-001 -45    90     0.00  2.35 2.35    1.66     0.90
ANGD-001 -45    90     7.00 10.00 3.00    2.12     1.05
18.00 24.00 6.00    4.24     2.13
including             18.00 21.00 3.00    2.12     3.66
ANGD-003 -60    90    24.80 31.25 6.45    3.23     0.78
including             30.25 31.25 1.00    0.71     3.05
ANGD-004 -45    90    40.00 42.00 2.00    1.41     0.54
ANGD-005 -45    90    33.60 35.60 2.00    1.41     0.31
ANGD-006 -45    90     5.95 17.00 11.05   7.81    10.95
including              8.25 12.60 4.35    3.08    12.13
including             13.60 17.00 3.40    2.40    19.28
ANGD-007 -45    135    6.50 17.90 11.40      -     2.44
including              7.65 13.95 6.30       -     4.00
including             10.20 13.05 2.85       -     7.04
ANGD-008 -45    135   13.95 20.40 6.45       -     3.39
including             18.20 20.40 2.20       -     5.74
ANGD-008              39.05 44.10 5.05       -     2.43
including             39.05 41.10 2.05       -     3.10
ANGD-009 -45    90    24.50 26.50 2.00     1.41    4.21
ANGD-010 -45    90    31.25 40.20 8.95     6.33    4.94
including             31.25 34.00 2.75     1.94    9.33
ANGD-011 -45    90    25.00 30.35 5.35     3.78    3.48
including             29.00 30.35 1.35     0.95   12.13
ANGD-012 -45    90    12.40 14.70 2.30     1.63    0.76
ANGD-013 -45    270   21.35 23.75 2.40     1.70    0.49
ANGD-014               9.00 17.30 8.30     -       8.62
including -45   60    11.80 14.40 2.60     1.84   25.72
//et
The only one drill hole performed at Serrinha Target beneath the
Roque Pit Zone to date has its results shown as follows:
//st
DDH     Hole    Hole   From  To   Down    True    Au     Cu
In-     Azi-   (m)   (m)  Hole    Width   (g/t)  (%)
clina-  muth              Width   (m)
tion    (o)               (m)
(o)

ANGD-015 -60    340    28.80 35.80 7,00    3.50    1.67   0.14
including              32.80 35.80 3,00    1.50    2.97   .017
ANGD-015               52.35 56.35 4,00    2.00    6.03   0.50
including              54.35 56.35 2,00    1.00    4.87   0.98
//et

QUALITY ASSURANCE / QUALITY CONTROL (QA/QC)
All drilling core was transported by Para Resources' personnel
from drill site to the core shed at Tucuma town and then the respective
samples taken, straight to an Intertek Laboratory unit located in
Parauapebas City, about 260km far North from Tucuma.
All core samples from Angelim Target were analyzed for gold. In
addition to gold analysis, the core samples from Serrinha Target were
also assayed for copper.
Usually one quarter of the core was sent for analysis, while the
other three quarters were retained in the core boxes for future
reference, petrographic studies, eventual checking re-sampling, etc.
However, when a duplicate sample was required for QA/QC, two quarters
of the core was sent to lab and a half of the core was let in the
boxes.
After preparation under PT-01 method which includes a sample
grinding at 150 mesh, gold analysis for all samples were done via
FA50Au method, comprising Au by Fire assay and Atomic Absorption
finishing of 50g nominal sample weight. The detection range for this
method is 5 ppb to 200,000 ppb.
The 46 core-samples from Serrinha Target were also analyzed for
copper by GA-20 Cu method, which includes an aqua regia
(nitrohydrochloric acid) attach and Atomic Absorption finishing of
2.50g nominal sample weight. The detection range for this method is 5
ppm to 250,000 ppm.
Samples of the gold standard reference materials used for the
QA/QC program were obtained and prepared by CDN Resource Laboratories
Limited and their gold values were certified and supervised
respectively by Mr. Duncan Sanderson, Licensed Assayer of British
Columbia, and Dr. Barry Smee, PhD, P.Geo. and Independent Geochemist.
Coincident to each batch of 40 samples, a standard sample was
inserted alternating high, medium and low grade samples, preferentially
in places where gold mineralization is visually evident. Other control
samples such as duplicate and blank (collected in the field) were
inserted as well for each 40 samples taken, intercalated to the
standards.
Eleven blank samples had their gold values three times over the
lower detection limit of 5 ppb. This indicates that Para Resources
should buy or get a more accurate blank from the field. Although these
samples were accepted due to be out of mineralized intervals.
In other hand, the results tested to date are fully satisfactory
as the results for duplicate samples and for the standard sample assays
were in the acceptable error range to meet the standards. Standard
graphics did not show any bias.
Density or Specific Gravity (SG) tests were carried out at Tucuma
Project - Angelim Target in order to have a good accurate measure of
this parameter.
The methodologies of Hydrostatic Scale (Archimedes Principle) and
Water Volume Displacement were used respectively for hard and massive
materials, such as vein and breccia units, and for unconsolidated and
weathered materials such as veining saprolite and saprock.
Specific Gravity (SG), Density or Apparent Specific Mass is
defined by the division between the total mass of the sampled trial
body (expressed in tonnage or kilos) and its volume (expressed in m3 or
cm3).
Samples for density determination were taken from the core as
always as possible, coincidentally to the sampling intervals.
Average results for all the 303 density samples taken were:
- Wet weathered Rock (saprolite+saprock): 2.02 g/cm3.
- Dry weathered Rock (saprolite+saprock): 1.67 g/cm3.
- Fresh Rock: 2.77 g/cm3.

Individual density values will be part of block modeling and will
allow the estimative of density for each block to be used in resources
calculations.
GEOLOGICAL MODELING
Ten transversal sections to the drill holes and trenches
directions in Zone 1 of Angelim Target, were interpreted in 2D, as well
as a detailed geological map was yielded based on the trenches wall
mapping.
Modeling considered both trenches and drill holes and was
discriminated by a conjunction of gold grade classes and geological
alteration features defining a probable mineralized envelopment.
This work allowed a 3D solid creation of the mineralized
envelopment at Zone 1, yielded in specific software, as represented by
the following figure:

This solid will be the geological basis for a block model creation
and resources and reserves calculation under CIM's standards and the
preparation of a NI-43-101 independent report, which are going to be
the next steps for Zone 1.
The Company remains very optimistic with Zone 1 drilling results
as they suggest that a small operation could be implemented in the
short term.
In addition, the consistent continuity of the high grade gold
mineralization at depth suggests a potential for underground mining to
be explored.
Para Resources has recently presented a Final Exploration Report
for the property which comprises both Angelim and Serrinha targets to
the Brazilian Government and has also filed an application for trial
mining and environmental licenses usual for small mineral deposits in
Brazil.
Mr. Paulo J. Andrade, Senior Geologist, VP and Country Manager for
Para Resources stated: "The expressive width of the high grade
mineralization maintained at depth is making us to think that Zone 1 is
probably not only a near surface saprolitic level gold concentration,
but it should be continuous at bigger depths than the already known and
that it should not be a standalone high grade mineralization neither.
Beside this enhancing of potential expectation at Zone 1, we should
keep in mind the Tucuma Project potential as a whole, using the
geological and structural comprehension gotten at Angelim Target as a
model for new discoveries in the property."
Mr. Paulo J. Andrade, a Member of the Australian Institute of
Geoscientists (MAIG #6136), Senior Geologist, VP and Country Manager
for Para Resources, Inc., and a competent and qualified person under
NI-43-101, has reviewed and approved the scientific and technical
information in this press release.
About Para Resources:
Para Resources, Inc., is a publicly-listed company on the Exchange
with a focus on small scale, South American mining properties. Para
owns 100% of a gold and copper bearing property near the town of Tucuma
in Para State in Brazil. Tucuma is located within a prospective area
for gold and copper deposits, and the Company is looking to add
additional prospective or advanced stage properties in LatAm to
leverage the experienced and qualified geological team already on the
ground.
Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

ON BEHALF OF THE BOARD OF DIRECTORS
"C. Geoffrey Hampson"
C. Geoffrey Hampson, Chief Executive Officer, President and Director

For further information, please contact Andrea Laird
Telephone: 604- 806-0916, Fax: 604- 806-0956

Cautionary Statement Regarding Forward-Looking Information
Except for statements of historical fact, this news release contains
certain "forward-looking information" within the meaning of applicable
securities law, including statements regarding the proposed private
placement. Forward-looking information is frequently characterized by words
such as "plan", "expect", "project", "intend", "believe", 
"anticipate","estimate" and other similar words, or statements that certain 
events or
conditions "may" or "will" occur. Forward-looking statements are based on
the opinions and estimates of management at the date the statements are
made, and are subject to a variety of risks and uncertainties and other
factors that could cause actual events or results to differ materially from
those anticipated in the forward-looking statements. Although Para
Resources believes the expectations expressed in such forward-looking
statements are based on reasonable assumptions, such statements are not
guarantees of future performance and actual results may differ materially
from those in forward-looking statements. Factors that could cause the
actual results to differ materially from those in forward-looking
statements include exploitation and exploration success, continued
availability of capital and financing, inability to obtain required
regulatory or governmental approvals and general economic, market or
business conditions. The Company undertakes no obligation to update
forward-looking information if circumstances or management's estimates or
opinions should change except as required by law. The reader is cautioned
not to place undue reliance on forward-looking statements. More detailed
information about potential factors that could affect financial results is
included in the documents filed from time to time with the Canadian
securities regulatory authorities by the Company.
This news release does not constitute an offer to sell or the
solicitation of an offer to buy any securities of Para Resources. Nor
is it an offer to sell securities or a solicitation of an offer to buy
securities in any state or jurisdiction where prohibited by law. No
securities referred to herein have been or will be registered under the
United States Securities Act of 1933, as amended, and may not be
offered or sold in the United States absent registration or an
applicable exemption from the registration requirements.
______________________________________
_______________________________________________
TSX Venture closing price for PBR-V
Date: 2015/06/08
Closing Price: 0.06
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1517900048TS11517902125-16082420150629