Source	Filing Services Canada
Date	06/01/2016
Time	05:00:16 AM

Company	 GREAT THUNDER GOLD CORP.
Title	Great Thunder Provides Technical Overview of its Optioned Chubb and 
Bouvier Lithium Prospects





    CDNX Symbol: GTG











Press Release




SOURCE: Filing Services Canada
Date: 06/01/2016
Time: 08:00:00

Company: GREAT THUNDER GOLD CORP.
Title:Great Thunder Provides Technical Overview of its Optioned Chubb and 
Bouvier Lithium Prospects (GTG - TSXV) 
TSXV SYMBOL: GTG


NEWS TRANSMITTED BY FILING SERVICES CANADA
FOR: Great Thunder Gold Corp.
TSXV SYMBOL: GTG
Wednesday, June 01, 2016 - 8:00 AM

Original Source Location: 
http://www.fscwire.com/newsrelease/great-thunder-provides-technical-overview-its
-optioned-chubb-and-bouvier-lithium

Great Thunder Provides Technical Overview of its Optioned Chubb and Bouvier 
Lithium Prospects


VICTORIA, BC (FSCwire) - Great Thunder Gold Corp. (TSXV: GTG) is pleased to 
provide a technical overview of its recently optioned Chubb and Bouvier lithium 
properties located in the Preissac-Lacorne plutonic complex of the Abitibi 
Greenstone Belt near Val dOr, Quebec.



The Chubb Property



The Chubb lithium property is situated within the Preissac-Lacorne plutonic 
complex of the Abitibi Greenstone Belt  the complex forming one of the best 
prospective areas for lithium mineralization. The plutonic complex generated 
the Quebec Lithium mine for which Canada Lithium reported measured and 
indicated resources of 29.3 Mt grading 1.19% Li2O and 20.9 Mt of inferred 
resources grading 1.15% Li2O, respectively, according to a technical report by 
Canada Lithium filed on SEDAR June 8, 2011.



The Chubb property lies 32 kilometres north of Val dOr and consists of 35 
contiguous recorded mineral claims with a total area of 1,509 hectares. The 
propertys geology is dominated by quartz monzodiorite and metasomatized quartz 
diorite (tonalite). A swarm of spodumene-rich granitic pegmatite dykes intrude 
fractures and small faults within the plutonic rocks. The pegmatite dykes are 1 
to 6 m thick, oriented 345[[50]]  350[[50]] and vary in length from 25 to 250 
m. They are crudely zoned, some having quartz cores and border zones of aplite. 
The granitic pegmatites are composed of quartz, albite and/or cleavelandite, 
K-feldspar, muscovite, with 5 to 25% spodumene. There are three important 
granitic pegmatite dykes containing spodumene mineralization (Dyke #1, #2 and 
Main Dyke).



Exploration of the Chubb property persists since the early 1950s and has 
consisted mainly of mapping, trenching, geophysical surveys and diamond 
drilling. The best drilling intersections were obtained in 1994 by Abitibi 
Lithium Corp., producing intervals of 3.72 m @1.78 wt. % Li2O, 2.75 m @1.00 wt. 
% Li2O and 2.38 m @1.25 wt. % Li2O. In 2010, Mineral Hill Industries Ltd. 
carried out magnetic and IP geophysical surveys, mapping, channel sampling and 
grab sampling in the area surrounding the three principal spodumene-bearing 
dykes. The main dyke  which is 300 m long  was shown to have Li2O concentration 
of 1.00 wt. % (n=41).



The Bouvier Property



The Bouvier property is located within the Preissac-Lacorne plutonic complex of 
the Abitibi Greenstone Belt, in the Saint-Mathieu Municipality of Figuery 
Township. The geological setting and structure of the volcano-sedimentary 
assemblages form an ideal host for lithium-rich pegmatites being located 
between the Northern Manneville Deformation Zone and the northern edge of the 
fertile Lacorne monzogranite pluton.



The Bouvier property consists of 16 contiguous recorded mineral claims for a 
total area of 692 hectares. The southern Bouvier property contains several 
exposures of biotite[[51]]muscovite monzogranitic plutonic rocks intruding 
metasediments and injected by granitic pegmatite and aplite dykes that 
constitute nearly 20% of the rock. Many granitic pegmatites contain beryl and 
tantalite, but very few have spodumene.



To the north, the metasediments are in structural contact with the metavolcanic 
rocks of the Malartic and Harricana groups, with the Manneville Deformation 
Zone marking the contact between the metasedimentary and metavolcanic 
formations. Spodumene-bearing granitic pegmatite dykes occur only south of the 
Manneville Fault and were emplaced principally in metasediments. The dykes are 
oriented parallel to the Manneville Fault and can reach 100 m in length and 10 
m in apparent thickness. Most granitic pegmatites are zoned, some having quartz 
cores and border zones of aplite. They are composed of quartz, albite and/or 
cleavelandite, K-feldspar, muscovite, with 5 to 25% spodumene. Accessory 
minerals are beryl, tantalite, garnet, bismuthine and molybdenite.



The Bouvier property was submitted to sporadic mining exploration from the 
early 1950s to 1979 that included geological mapping, rock sampling, trenching 
and diamond drilling. A bulk sample taken by Teck Corporation and reported in 
their 1979 Annual Report, returned an average grade of 1.39% Li2O and an 
estimated possible historical resource of 907,000 tons.[1] In 2010, Mineral 
Hill Industries Ltd. carried out an exploration program involving line cutting, 
a magnetic and IP survey, trenching, and panel and grab rock sampling. The work 
unearthed east-west oriented spodumene-bearing granitic pegmatites parallel to 
the Manneville Deformation Zone. The main dyke displayed an average lithium 
concentration of 1.51 Li2O wt. % (n=20).



[1]  The estimates presented are treated as historic information and have not 
been verified or relied upon for economic evaluation by the Company. These 
historical mineral resources do not refer to any category of sections 1.2 and 
1.3 of National Instrument 43-101, such as mineral resources or mineral 
reserves as stated in the 2010 CIM Definition Standards on Mineral Resources 
and Mineral Reserves. The Company is unable to verify the data acquired by the 
various historical drilling campaigns, and must undertake additional sampling 
and drilling to verify historical estimates. A Qualified Person has not done 
sufficient work to classify the historical estimates as current mineral 
resources or mineral reserves. The Company is not treating the historical 
estimates as current mineral resources or mineral reserve 



Technical Reports



The Chubb and Bouvier properties were the subject of a National Instrument 
43-101 report written in 2010 by Dr. Michel Boily for Mineral Hill Industries 
Ltd. entitled, Technical Report and Recommendations for Three Li-Mo Properties 
Associated With the Preissac-Lacorne Batholith in the Abitibi Subprovince, 
Quebec, Canada: The Chubb, International and Athona Properties. Great Thunder 
Gold Corp. has commissioned an updated NI 43-101 report on both properties from 
Dr. Boily and expects the report to be filed on SEDAR in the coming months.



The technical contents of this release were approved by Michel Boily, PhD, geo, 
an independent Qualified Person as defined by National Instrument 43-101.



ON BEHALF OF THE BOARD



Signed Kevin C. Whelan  

Kevin C. Whelan, President

Direct line: (250) 474-6640



Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.




To view this press release as a PDF file, click onto the following link:
http://fscwire.com/sites/default/files/news_release_pdf/GreatThunder06012016.pdf
Source: Great Thunder Gold Corp. (TSX Venture:GTG) 
http://www.greatthundergold.com/



Maximum News Dissemination by FSCwire. http://www.fscwire.com



Copyright(C)2016 Filing Services Canada Inc.