Source	Marketwire
Date	06/06/2016
Time	04:01:17 AM

Company	 TERRAX MINERALS INC.
Title	TerraX Drills 8.00 m @ 60.60 g/t Au Including 2.25 m @ 212.48 g/t Au at 
the Mispickel Zone, Yellowknife City Gold Project





    CDNX Symbol: TXR











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: TerraX Minerals Inc.

TSX VENTURE SYMBOL: TXR
FRANKFURT SYMBOL: TX0
OTC PINK SYMBOL: TRXXF

June 6, 2016

TerraX Drills 8.00 m @ 60.60 g/t Au Including 2.25 m @ 212.48 g/t Au at the 
Mispickel Zone, Yellowknife City Gold Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - June 6, 2016) - TerraX Minerals 
Inc. (TSX VENTURE:TXR)(FRANKFURT:TX0)(OTC PINK:TRXXF) has received the final 
assay results from 22 holes totalling 3,485 meters drilled at multiple zone on 
the Yellowknife City Gold Project ("YCG"), immediately north of Yellowknife in 
the Northwest Territories. Drilling reported here includes our primary target, 
Mispickel, as well as the Barney, AES, Pinto and VSB zones.

Drilling at Mispickel again intersected visible gold zones in quartz veins with 
highlights that included:

/T/

--  8.00 m @ 60.60 g/t Au including 2.25 m @ 212.48 g/t Au in hole TWL16-016
--  10.68 m @ 2.34 g/t Au including 2.57 m @ 6.84 g/t Au in hole TWL16-015
--  12.95 m @ 1.53 g/t Au including 4.81 m @ 3.38 g/t Au in hole TWL16-017

/T/

Drilling at Mispickel comprised five holes totalling 980 meters that followed 
up on four holes (384 m) drilled at Mispickel in February, 2016 that returned 
8.60 m @ 12.87 g/t Au in TWL16-001 and 7.30 m @ 23.60 g/t Au in TWL16-002 (news 
release of February 23, 2016). The high grade intersection in TWL16-016 (8.00 m 
@ 60.60 g/t Au) is located 40 meters down dip from TWL16-002 (7.30 m @ 23.60 
g/t Au).

All five holes at Mispickel reported today intersected significant zones of 
mineralization. Each hole contained wide zones of low grade mineralization, 
including 145.90 meters @ 0.34 g/t Au in TWL16-017. This hole was collared in 
mineralization and ended in mineralization, with the bottom of the hole 
assaying 4.60 m @ 1.31 g/t Au. Within these pervasive zones of low grade gold 
mineralization are areas of higher grade gold, usually accompanied by visible 
gold, as indicated in the highlights listed above.

Joe Campbell, President of TerraX, states "The areal extent of the gold 
mineralization at Mispickel indicates a large mineralizing system within which 
exist significant high grade gold zones, as evidenced by the drill results 
reported today. Our summer drill program will follow-up on this success by 
further testing along the strike and dip extensions of the Mispickel structure, 
which was only discovered this winter and has had limited drill testing."

The drilling reported here, coupled with a recently completed surface magnetic 
survey, resulted in a re-interpretation of the Mispickel mineralized zones. The 
pervasive low grade mineralizing trend is contained within a 75-200 meter wide, 
north to north-northwest trending, sub-vertical shear zone. Within this wider 
zone of mineralization the higher grade zones migrate in a northwest to 
north-northwest direction with minor splays along the dominant northerly trend 
of the shear.

Drill holes TWL16-017 and 018 were drilled along strike to the north of the 
discovery drill holes but were collared too far to the east and did not cross 
the entire zone of mineralization (see plan map on web site under "2016 Field 
Exploration"). In the case of TWL16-017 the hole was collared in the 
mineralized shear, and drilling was terminated just as it began to intersect 
the Main Zone (8.60 m @ 0.80 g/t Au, including the final 4.60 m @ 1.31 g/t Au). 
Drill hole TWL16-018 was also collared in the shear, but was drilled too 
steeply and was terminated well short of the Main Zone (approximately 150 
meters below the end of hole).

A map overlain on the magnetic survey and a cross section showing the location 
of drill holes on the Mispickel target area are available on our web site under 
"Mispickel 2016 Field Exploration" under the "Walsh Lake" section.

Current interpretations for dip and strike at Mispickel indicate that the true 
widths of the drill holes reported here are approximately 65-75% of drill 
intersection width.

/T/

----------------------------------------------------------------------------
Mispickel
----------------------------------------------------------------------------
Interval
Drill Hole  Dip Azimuth   UTM Location         From (m) To (m)     (m)Au g/t
-----------------
Easting Northing
----------------------------------------------------------------------------
TWL16-014   -55     271  640324  6945810          47.50 131.00   83.50  0.27
------------------------------------
incl.   70.00  73.29    3.29  1.27
------------------------------------
and  116.00 118.00    2.00  1.26
incl.
------------------------------------
and  149.50 158.00    8.50  1.08
------------------------------------
incl.  149.50 151.50    2.00  2.60
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TWL16-015   -45     276  640298  6945830          16.00  94.00   78.00  0.57
------------------------------------
incl.   24.00  31.00    7.00  1.59
------------------------------------
and   71.32  82.00   10.68  2.34
incl.
------------------------------------
and   79.43  82.00    2.57  6.84
incl.
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TWL16-016   -46     275  640310  6945850          34.00  57.43   23.43  0.47
------------------------------------
incl.   53.89  57.43    3.54  1.47
------------------------------------
and   88.00  96.00    8.00 60.60
------------------------------------
incl.   92.30  94.55    2.25212.48
------------------------------------
and  106.00 115.63    9.63  0.68
------------------------------------
incl.  112.63 114.63    2.00  1.66
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TWL16-017   -67     270  640291  6945869           6.00  53.45   47.45  0.59
------------------------------------
incl.   26.75  39.70   12.95  1.53
------------------------------------
and   26.75  31.56    4.81  3.38
incl.
------------------------------------
and  120.10 135.38   15.28  0.64
------------------------------------
incl.  120.10 128.10    8.00  1.02
------------------------------------
and  143.30 151.90    8.60  0.80
------------------------------------
incl.  147.30 151.90    4.60  1.31
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TWL16-018   -73     269  640282  6945913           7.50  81.50   74.00  0.31
------------------------------------
incl.   17.57  25.70    8.13  0.97
------------------------------------
and   18.65  20.70    2.05  2.57
incl.
------------------------------------
and   32.35  35.45    3.10  1.13
incl.
------------------------------------
and   44.00  46.80    2.80  2.14
incl.
----------------------------------------------------------------------------

/T/

BARNEY

Drilling on the Barney target was comprised of 3 deep holes totaling 1,593 
meters.

Two holes (TBY16-012 and 013) were testing the interpreted location of the 
Barney Zone where it intersects a mafic volcanic / felsic intrusive contact. 
Hole TBY16-013 successfully intersected the mafic / felsic contact and crossed 
the Barney Zone approximately 35 meters into the felsic intrusive, intersecting 
18.10 meters @ 1.10 g/t Au, including 5.34 m @ 3.09 g/t Au. Hole TBY16-013 also 
intersected broad areas of molybdenite mineralization within the felsic 
intrusive (51.50 m @ 0.02% Mo, including 7.50 m @ 0.05% Mo).

Hole TBY16-012 failed to intersect the mafic / felsic contact, but successfully 
crossed the Barney mineralized structure within the mafic volcanics, confirming 
its continuity at a depth of 500 meters vertical. It only intersected minor 
gold (13.79 m @ 0.13 g/t Au) in this location. This hole also intersected 
ultramafic volcanic flows with spectacular spinifex textures near the collar of 
the hole. This ultramafic zone contained a narrow quartz vein with visible gold 
that assayed 0.50 m @ 4.56 g/t Au.

Hole TBY16-014 was testing approximately 70 m down dip of previously drilled 
mineralization at Barney (22.42 m @ 6.35 g/T Au in hole NB95-16W1 reported 
August 25, 2014) and intersected the Barney Zone at approximately 290 meters 
vertical depth, returning 28 m @ 0.41 g/t Au, including 9.00 m @ 0.83 g/t Au, 
confirming the continuity of the Barney structure.

The drilling at Barney greatly improved our knowledge of the controls on the 
high grade lodes within the Barney structure, and this will allow TerraX to 
plan drilling to follow these lodes in the next drill program.

AES

Four short holes totaling 278 meters were drill to intersect the AES structure 
close to surface. The AES structure had historical gold production near the 
southern boundary of the YCG property. The AES structure extends for 5 
kilometers on TerraX ground and has had modest but consistent gold 
mineralization sampled along its strike. The four holes were drilled along 210 
meters of strike length in an area of previous surface sampling. All holes 
intersected narrow (0.60-1.00 m) quartz vein style mineralization with gold 
values up to 2.98 g/t Au. This small drill program did not indicate a 
significant gold zone proximal to the drilling area, but has established that 
potential exists along the 5 kilometer trend.

PINTO and VSB

The Pinto program consisted of four holes totalling 432 meters in an area of 
prior surface sampling. None of the drill holes intersected significant gold 
(best assay 1.20 m @ 0.38 g/t Au). The VSB program consisted of two holes 
totalling 203 meters and was located in an area of narrow quartz veining with 
visible gold located to the west of the Crestaurum Zone. Neither drill hole 
intersected significant gold (best assay 0.60 m @ 0.42 g/t Au).

TerraX collected 2096 samples for assay from the drilling reported here. 
Results ranged from below detection to 379 g/t Au. Drill hole collar locations 
were surveyed to sub-meter accuracy. Down hole surveying (Easy Shot) was 
completed on all holes. TerraX inserts certified standards and blanks into the 
sample stream as a check on laboratory QC. Drill core samples are cut by 
diamond saw at TerraX's core facilities in Yellowknife. A halved core sample is 
left in the core box. The other half core is sampled and transported by TerraX 
personnel in securely sealed bags to ALS Chemex's (ALS) preparation laboratory 
in Yellowknife. After sample preparation, samples are shipped to ALS's 
Vancouver facility for gold and ICP analysis. Gold assays of greater than 3 g/t 
are re-assayed on a 30 gm split by fire assay with a gravimetric finish. ALS is 
a certified and accredited laboratory service. ALS routinely inserts certified 
gold standards, blanks and pulp duplicates, and results of all QC samples are 
reported.

The technical information contained in this news release has been approved by 
Joseph Campbell, the President of TerraX, who is a Qualified Person as defined 
in "National Instrument 43-101, Standards of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold ("YCG") encompasses 118 sq km of contiguous land 
immediately north and south of the City of Yellowknife in the Northwest 
Territories. Through a series of acquisitions, TerraX now controls one of the 
six major high-grade gold camps in Canada. Being within 15 km of the City of 
Yellowknife, the YCG is close to vital infrastructure, including 
transportation, service providers, hydro-electric power and skilled 
tradespeople.

The YCG lies on the prolific Yellowknife greenstone belt, covering 23 km of 
strike length on the southern and northern extensions of the shear system that 
hosted the high-grade Con and Giant gold mines. The project area contains 
multiple shears that are the recognized hosts for gold deposits in the 
Yellowknife gold district, with innumerable gold showings and recent high grade 
drill results that serve to indicate the project's potential as a world-class 
gold district.

For more information on the YCG project, please visit our web site at 
www.terraxminerals.com.

On behalf of the Board of Directors

"JOSEPH CAMPBELL"

Joe Campbell
President and CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release contains forward-looking information, which involves known 
and unknown risks, uncertainties and other factors that may cause actual events 
to differ materially from current expectation. Important factors - including 
the availability of funds, the results of financing efforts, the completion of 
due diligence and the results of exploration activities - that could cause 
actual results to differ materially from the Company's expectations are 
disclosed in the Company's documents filed from time to time on SEDAR (see 
www.sedar.com). Readers are cautioned not to place undue reliance on these 
forward-looking statements, which speak only as of the date of this press 
release. The company disclaims any intention or obligation, except to the 
extent required by law, to update or revise any forward-looking statements, 
whether as a result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

Paradox Public Relations
info@paradox-pr.ca
514-341-0408
Toll Free: 1-866-460-0408

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=568551316