Source	Marketwire
Date	06/08/2016
Time	01:00:30 AM

Company	 UNITY ENERGY CORP.
Title	Unity Energy Corp.: Surface Sampling at Miller's Crossing Identifies 
Anomalous Lithium Concentrations





    CDNX Symbol: UTY











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Unity Energy Corp.

TSX VENTURE SYMBOL: UTY
FRANKFURT SYMBOL: UJN2

June 8, 2016

Unity Energy Corp.: Surface Sampling at Miller's Crossing Identifies Anomalous 
Lithium Concentrations


VANCOUVER, BRITISH COLUMBIA--(Marketwired - June 8, 2016) - Unity Energy Corp. 
(TSX VENTURE:UTY)(FRANKFURT:UJN2) "Unity" or the "Company is pleased to 
announce that it has received chemical assays from its Phase 1 surface sampling 
program on its 100% owned Miller's Crossing Lithium Project in Southern Nevada. 
The sampling was carried out in April 2016 to investigate lithium 
concentrations in the uppermost 1.5m of the playa and a total of 15 samples 
were analyzed.

The results not only confirmed presence of lithium in alluvial gravels and 
clays but also indicated anomalous values of boron and potassium.

Highlights from the sampling program are:

/T/

--  Maximum values for lithium in sediments is 81 ppm, boron 400 ppm, and
potassium 7,100 ppm,
--  Average lithium concentration in all sediment samples is 46 ppm, boron
184 ppm, potassium 5,153 ppm

/T/

These results are significant in that even though the samples were taken with 
pick, shovel and hand auger and contained large amounts of waste material, the 
average lithium values encountered were more than twice that of the 20 ppm 
cut-off used by Pure Energy Minerals Ltd. to calculate their mineral resource 
in the neighboring Clayton Valley.(i) All of the fifteen samples taken on 
surface exceeded the 20 ppm cut off limit. The results also correlate well with 
results obtained by Ultra Lithium at their Big Smoky Valley project, which, 
like the Miller's Crossing Project, lies in the South Big Smokey 
hydrogeological system. ((i) Technical Report dated July 2015 by Raymond P. 
Spanjers, MS, PG.)

The samples were shipped to WETLAB Western Environment Testing Laboratory 
("WETLAB") in Sparks, Nevada, an EPA accredited independent laboratory. Samples 
were analyzed for lithium, potassium, boron, and magnesium using Standard 
Methods for the Examination of Water and Wastewater, Online Edition, Methods 
for Determination of Organic Compounds in Drinking Water, EPA-600/4-79-020, and 
Test Methods for Evaluation of Solid Waste, Physical/Chemical Methods (SW846), 
Third Edition. WETLAB used its own quality control and quality control and 
quality assurance protocols for sample analysis.

Unity will be looking significantly deeper into the playa in the coming weeks 
with its fully permitted Phase 2 short hole drilling program, which is designed 
to investigate to depths of up to 50m.

Regarding these results, CEO Ian Graham commented: "The results of the surface 
sampling are very encouraging and confirm the potential of the Miller's 
Project. There remains a need for substantial ongoing work and the Company is 
in the process of mobilizing its field crew for deeper sampling."

The technical contents of this news release have been prepared under the 
supervision of Dr. Peter Born, P. Geo. Dr. Born is a Qualified Person, as that 
term is defined in National Instrument 43-101, and has approved this news 
release.

For more information, visit www.unityenergycorp.com.

On Behalf of the Company,

Anita Algie, President

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Unity Energy Corp.
Anita Algie
President
604-681-0004
www.unityenergycorp.com

INDUSTRY: Energy and Utilities - Oil and Gas
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=568865775