Source	Marketwire
Date	06/09/2016
Time	12:43:44 PM

Company	 GOLDEN VALLEY MINES LTD.
Title	Golden Valley Mines Ltd.: High-Grade Gold Intersected at Cheechoo





    CDNX Symbol: GZZ











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Golden Valley Mines Ltd.

TSX VENTURE SYMBOL: GZZ

June 9, 2016

Golden Valley Mines Ltd.: High-Grade Gold Intersected at Cheechoo


VAL-D'OR, QUEBEC--(Marketwired - June 9, 2016) - Golden Valley Mines Ltd. 
("Golden Valley" or the "Company") (TSX VENTURE:GZZ) provides the following 
information on the recently concluded diamond drilling campaign at the Cheechoo 
gold project ("Cheechoo") in James Bay, Quebec. The information that follows 
has been prepared by program operator Sirios Resources Inc. (TSX VENTURE:SOI) 
and has not been independently verified by Golden Valley:

"Besides partial results already published, new results of the twenty-six holes 
undertaken include grades of 37.2 g/t Au over 4.1 metres including 102 g/t Au 
over 1.4 metres in drill hole #35; 31.8 g/t Au over 6 metres, including 124.0 
g/t Au over 1.5 metres in drill hole #41; 6.0 g/t Au over 7.4 metres in drill 
hole #54; and 13.0 g/t Au over 2.7 metres, 29,1 g/t Au over 1,2 metres and 29.3 
g/t Au over 1 metre in drill hole #53. Gold grades were also confirmed in drill 
holes where visible gold was observed (press release March 7, 2016) in the new 
sector located at more than 1.5 km from the main drilled sector, yielding up to 
5.5 g/t Au over 1 metre and 5.3 g/t Au over 1.1 metres in drill hole #47 and up 
to 10.7 g/t Au over 1 metre in #48.

Gold grades, reaching respectively 16.1 g/t Au over 1 metre and 2.3 g/t Au over 
6 metres, were obtained in meta-sedimentary rocks in drill hole #52 in addition 
to the section already announced at the end of March, of 12.1 g/t Au over 20.3 
metres located at the contact between these units and the tonalite. Other gold 
grades were also obtained in meta-sedimentary rocks such as 1.2 g/t Au over 
16.3 metres in drill hole #54.

Fourteen drill holes out of seventeen completed in the main drill sector 
yielded significant results, only drill holes #34, 39 and 56 yielded at most, 
anomalous gold grades. Three drill holes, #31, 47 and 48, out of thirteen 
undertaken outside of this sector yielded significant results. The Winter 2016 
diamond drilling program consisted of twenty-six drill holes (#31 to 56) in 
addition to the extension of #22 for a total of 4,432 metres. Maps showing 
locations of drill holes as well as long sections are available at the 
following links:

http://sirios.com/images/Carte-Zoomin-2016-06-06.jpg

http://sirios.com/images/Carte-Zoomout-2016-06-06.jpg

http://sirios.com/images/Longitudinale%20L.jpg

http://sirios.com/images/Longitudinale_I.jpg

http://sirios.com/images/Longitudinale_Jordi.jpg

http://sirios.com/images/Longitudinale_K.jpg

The table below lists all significant results:

MAIN ASSAY RESULTS FROM 2016 WINTER DRILLING CAMPAIGN

/T/

----------------------------------------------------------------------------
Drill
hole                           From        To       Interval             Au
CH-16-           Note            (m)       (m)         (m)(i)          (g/t)
----------------------------------------------------------------------------
35             Zone K           52.5      55.5              3            1.2
----------------------------------------------------------------------------
Zone Jordi           75.4      79.5        (ii)4.1           37.2
----------------------------------------------------------------------------
75.4      79.5        (ii)4.1      (iii)19.4
----------------------------------------------------------------------------
Incl, 77.0      78.4        (ii)1.4       ms 102.0
----------------------------------------------------------------------------
Zone I2           88.5      91.5        (ii)3.0              2
----------------------------------------------------------------------------
Zone I          110.8     113.5            2.7            4.6
----------------------------------------------------------------------------
Incl, 112.5     113.5              1          12.32
----------------------------------------------------------------------------
122       125              3            1.7
----------------------------------------------------------------------------

----------------------------------------------------------------------------

----------------------------------------------------------------------------
41             Zone L           16.4      19.2            2.8            1.4
----------------------------------------------------------------------------
Zone K            137       143        (ii)6.0           31.8
----------------------------------------------------------------------------
137       143        (ii)6.0      (iii)13.3
----------------------------------------------------------------------------
Incl, 141.5       143        (ii)1.5       ms 124.0
----------------------------------------------------------------------------
Zone Jordi            206       209              3            1.4
----------------------------------------------------------------------------
Zone I          227.5      2305              3              1
----------------------------------------------------------------------------
267.5       270            2.5              3
----------------------------------------------------------------------------
325       328              3            1.4
----------------------------------------------------------------------------
358.5       363            4.5            2.9
----------------------------------------------------------------------------

----------------------------------------------------------------------------
54     meta-sediments           40.9      57.2           16.3            1.2
----------------------------------------------------------------------------
contact
sediments-
tonalite           82.7        94           11.3            4.1
----------------------------------------------------------------------------
Incl, 83.8      86.9            3.1          13.36
----------------------------------------------------------------------------
Zone K          121.5       126            4.5              1
----------------------------------------------------------------------------

----------------------------------------------------------------------------
53                              27.5      30.2            2.7             13
----------------------------------------------------------------------------
Incl, 29.0      30.2            1.2           29.1
----------------------------------------------------------------------------
Zone L in re-
assay           79.5      80.6        (ii)1.0 ms in re-assay
----------------------------------------------------------------------------
154.6     155.6        (ii)1.0        ms 29.3
----------------------------------------------------------------------------
Zone I          285.4       288        (ii)2.6            7.8
----------------------------------------------------------------------------
Incl, 287.0       288        (ii)1.0        ms 20.0
----------------------------------------------------------------------------

----------------------------------------------------------------------------
52     Meta-sediments           38.0      39.0            1.0           16.1
----------------------------------------------------------------------------
Meta-sediments           77.0      99.6           22.6            1.3
----------------------------------------------------------------------------
Meta-sediments     incl. 88.8      99.6           10.8              2
----------------------------------------------------------------------------
Zone L contact
sediments-
tonalite a.p            120     140.3       (ii)20.3        ms 12.1
----------------------------------------------------------------------------
a.p          120.0     140.3       (ii)20.3       (iii)8.2
----------------------------------------------------------------------------
51                              10.9        16        (ii)5.1           10.4
----------------------------------------------------------------------------
Incl, 10.9      12.2        (ii)1.3        ms 39.6
----------------------------------------------------------------------------
30      31.7            1.7            8.8
----------------------------------------------------------------------------
Zone Jordi            104       105        (ii)1.0         ms 1.1
----------------------------------------------------------------------------
Zone I          173.6     176.2            2.6           10.3
----------------------------------------------------------------------------
Incl, 173.6     174.8            1.2           18.6
----------------------------------------------------------------------------

----------------------------------------------------------------------------
40             Zone L             64      65.5            1.5           10.5
----------------------------------------------------------------------------
91       100              9            0.9
----------------------------------------------------------------------------
Zone K          187.5     193.5              6            0.9
----------------------------------------------------------------------------
Zone Jordi          252.5     258.5              6            1.1
----------------------------------------------------------------------------
Zone I2            272       275        (ii)3.0            3.1
----------------------------------------------------------------------------
272     273.5        (ii)1.5         ms 5.8
----------------------------------------------------------------------------
Biotite
schistea.p          295.0       334       (ii)39.0            1.3
----------------------------------------------------------------------------
a.p    Incl, 320.6       327        (ii)6.4            3.1
----------------------------------------------------------------------------
a.p      and 346.9     350.1            3.2            2.9
----------------------------------------------------------------------------

----------------------------------------------------------------------------
55             Zone K           25.9      28.6            2.7            1.3
----------------------------------------------------------------------------
Zone Jordi           58.5      64.0            5.5            1.1
----------------------------------------------------------------------------
Zone I2          112.5     117.2            4.7            2.3
----------------------------------------------------------------------------
136.5     144.0            7.5            1.1
----------------------------------------------------------------------------
Zone I          150.5     153.5            3.0            3.1
----------------------------------------------------------------------------

----------------------------------------------------------------------------
31                               6.6      12.1            5.5            0.9
----------------------------------------------------------------------------
58.5      70.5           12.0            1.6
----------------------------------------------------------------------------
79.9      98.0           18.1            1.1
----------------------------------------------------------------------------
incl. 96.0      98.0            2.0            3.4
----------------------------------------------------------------------------

----------------------------------------------------------------------------
22Ext             a.p          209.0     210.0            1.0           16.3
----------------------------------------------------------------------------
a.p          240.5     245.4        (ii)4.9            1.7
----------------------------------------------------------------------------

----------------------------------------------------------------------------
32                a.p           15.5      17.0            1.5            4.4
----------------------------------------------------------------------------
a.p          122.8     123.8        (ii)1.0         ms 9.1
----------------------------------------------------------------------------

----------------------------------------------------------------------------
33                a.p            9.3      16.8            7.5            0.7
----------------------------------------------------------------------------
a.p           41.9      42.9            1.0            2.7
----------------------------------------------------------------------------

/T/

New north-west sector

/T/

----------------------------------------------------------------------------
Drill
hole                           From        To       Interval             
AuCH-16-           Note            (m)       (m)         (m)(i)          (g/t)
----------------------------------------------------------------------------
47           tonalite           36.5      37.5        (ii)1.0         ms 1.2
----------------------------------------------------------------------------
Contact
tonalite-meta-
sediments           57.9      58.9        (ii)1.0         ms 5.5
----------------------------------------------------------------------------
meta-sediments           88.1      89.2            1.1            5.3
----------------------------------------------------------------------------

----------------------------------------------------------------------------
48                                27      33.5            6.5            0.9
----------------------------------------------------------------------------
71      79.3        (ii)8.3            1.6
----------------------------------------------------------------------------
incl, 73.80      74.8        (ii)1.0           10.7
----------------------------------------------------------------------------
(i) Interval along the hole, true thickness non-indicated
(ii) Visible gold observed
(iii) Maximum gold grade cut at 50 g/t
ms: Gold grade obtained by fire assay with metallic sieve
a.p : announced previously

/T/

Information and coordinates of drill holes

/T/

----------------------------------------------------------------------------
Drill hole     Direction       Plunge       Length        UTM E        UTM N
----------------------------------------------------------------------------
#              degrees    degrees            m       NAD 83       NAD 83
----------------------------------------------------------------------------
CH919-16-
22-Ext.             254          -41           54       438500      5830171
----------------------------------------------------------------------------
CH919-16-31          300          -50          156       438054      5830500
----------------------------------------------------------------------------
CH919-16-32          300          -50          201       438514      5830175
----------------------------------------------------------------------------
CH919-16-33          300          -50           81       438430      5830333
----------------------------------------------------------------------------
CH919-16-34          300          -50           81       438480      5830431
----------------------------------------------------------------------------
CH919-16-35          300          -50          141       438552      5830433
----------------------------------------------------------------------------
CH919-16-36          300          -50           72       438035      5830168
----------------------------------------------------------------------------
CH919-16-37          300          -50           75       437872      5830263
----------------------------------------------------------------------------
CH919-16-38          300          -50          102       437688      5830040
----------------------------------------------------------------------------
CH919-16-39          300          -50          141       438604      5830527
----------------------------------------------------------------------------
CH919-16-40          295          -55        355.4       438666      5830147
----------------------------------------------------------------------------
CH919-16-41          300          -50          367       438598      5830176
----------------------------------------------------------------------------
CH919-16-42          300          -50          150       437325      5830924
----------------------------------------------------------------------------
CH919-16-43          300          -50          150       437224      5830744
----------------------------------------------------------------------------
CH919-16-44          300          -60          150       436725      5830982
----------------------------------------------------------------------------
CH919-16-45          295          -55          231       436968      5831476
----------------------------------------------------------------------------
CH919-16-46          300          -50          165       437067      5831651
----------------------------------------------------------------------------
CH919-16-47           55          -45           96       436970      5831476
----------------------------------------------------------------------------
CH919-16-48          240          -45          150       437161      5831211
----------------------------------------------------------------------------
CH919-16-49           55          -45           78       437651      5831028
----------------------------------------------------------------------------
CH919-16-50          235          -55        148.5       437650      5831027
----------------------------------------------------------------------------
CH919-16-51          300          -50          201       438577      5830321
----------------------------------------------------------------------------
CH919-16-52          300          -50          192       438830      5830228
----------------------------------------------------------------------------
CH919-16-53          300          -55          330       438717      5830236
----------------------------------------------------------------------------
CH919-16-54          300          -53        252.4       438694      5830365
----------------------------------------------------------------------------
CH919-16-55          300          -50          170       438428      5830128
----------------------------------------------------------------------------
CH919-16-56          300          -50          141       438579      5830486
----------------------------------------------------------------------------

/T/

Assay quality control

NQ-caliber drill cores of current campaign were sawed in half, with one half 
sent to a commercial laboratory for analysis and other half retained for future 
reference. A strict QA/QC program was followed by integrating blanks and 
certified reference materials to the drill core samples, all of which were 
prepared by IOS Services Geoscientifiques inc. of Chicoutimi, and assayed for 
gold by fire assay and atomic absorption finish (AA24) by the ALS Minerals 
laboratories in Val d'Or, Quebec. Samples grading more than 3 g/t were 
re-assayed by fire assay with gravimetric finish. (GRA22). Samples with visible 
gold were assayed by pyro-analysis with metallic sieve (SCR24) from a sample of 
about 1 kg."

Mr. Dominique Doucet, P. Eng., President of Sirios Resources Inc., is the 
Qualified Person pursuant to National Instrument 43-101, who prepared and is 
responsible for the technical information reported herein and has approved this 
written disclosure, including verification of the data disclosed, the sampling, 
and the analytical and QA-QC data underlying the technical information.

In 2012, Sirios concluded an agreement with Golden Valley regarding the 
ownership of Cheechoo that allowed it to, upon completion of certain 
obligations and counterparts, increase its current interest to 100%. Sirios has 
recently completed all these obligations and counterparts and will file shortly 
a request for transfer of mining claims to the competent authorities.

Golden Valley now owns 4,148,374 shares of Sirios, representing approximately 
4.1% of the company. Golden Valley also holds a 4% net smelter royalty from all 
mineral products mined or removed from Cheechoo. Notwithstanding the foregoing, 
the royalty relevant to gold mineral products mined or removed from Cheechoo 
(the "Gold Portion") may be reduced as follows depending on the market price of 
Gold at the time of the payment of the Gold Portion:

/T/

1.  If the price of Gold is less than $3,000 per ounce and higher than
$2,400 per ounce, a 3.5% royalty on the Gold Portion shall be payable to
Golden Valley;
2.  If the price of Gold is less than $2,400 per ounce and higher than
$1,200 per ounce, a 3% royalty on the Gold Portion shall be payable to
Golden Valley; and
3.  If the price of Gold is less than $1,200 per ounce, a 2.5% royalty on
the Gold Portion shall be payable to Golden Valley.

/T/

About Golden Valley Mines Ltd.: The Company typically tests initial grassroots 
targets while owning a 100% interest therein and then seeks partners to 
continue exploration funding. This allows the Company to carry on its 
generative programs and systematic exploration efforts at other majority-owned 
grassroots projects. The Company (together with its various subsidiaries) holds 
property interests in projects in Canada (Saskatchewan, Ontario and Quebec).

Forward Looking Statements:

This news release contains certain statements that may be deemed 
"forward-looking statements. Forward looking statements are statements that are 
not historical facts and are generally, but not always, identified by the words 
"expects", "plans", "anticipates", "believes", "intends", "estimates", 
"projects", "potential" and similar expressions, or that events or conditions 
"will", "would", "may", "could" or "should" occur. Although the Company 
believes the expectations expressed in such forward-looking statements are 
based on reasonable assumptions, such statements are not guarantees of future 
performance and actual results or realities may differ materially from those in 
forward looking statements. Forward looking statements are based on the 
beliefs, estimates and opinions of the Company's management on the date the 
statements are made. Except as required by law, the Company undertakes no 
obligation to update these forward-looking statements in the event that 
management's beliefs, estimates or opinions, or other factors, should change.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

- 30 -

CONTACT INFO:

Glenn J. Mullan
Chairman, President, and CEO
Golden Valley Mines Ltd.
819.824.2808 ext. 204
glenn.mullan@goldenvalleymines.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=569126952


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Golden Valley Mines Ltd.

TSX VENTURE SYMBOL: GZZ

June 9, 2016

Golden Valley Mines Ltd.: High-Grade Gold Intersected at Cheechoo


VAL-D'OR, QUEBEC--(Marketwired - June 9, 2016) - Golden Valley Mines Ltd. 
("Golden Valley" or the "Company") (TSX VENTURE:GZZ) provides the following 
information on the recently concluded diamond drilling campaign at the Cheechoo 
gold project ("Cheechoo") in James Bay, Quebec. The information that follows 
has been prepared by program operator Sirios Resources Inc. (TSX VENTURE:SOI) 
and has not been independently verified by Golden Valley:

"Besides partial results already published, new results of the twenty-six holes 
undertaken include grades of 37.2 g/t Au over 4.1 metres including 102 g/t Au 
over 1.4 metres in drill hole #35; 31.8 g/t Au over 6 metres, including 124.0 
g/t Au over 1.5 metres in drill hole #41; 6.0 g/t Au over 7.4 metres in drill 
hole #54; and 13.0 g/t Au over 2.7 metres, 29,1 g/t Au over 1,2 metres and 29.3 
g/t Au over 1 metre in drill hole #53. Gold grades were also confirmed in drill 
holes where visible gold was observed (press release March 7, 2016) in the new 
sector located at more than 1.5 km from the main drilled sector, yielding up to 
5.5 g/t Au over 1 metre and 5.3 g/t Au over 1.1 metres in drill hole #47 and up 
to 10.7 g/t Au over 1 metre in #48.

Gold grades, reaching respectively 16.1 g/t Au over 1 metre and 2.3 g/t Au over 
6 metres, were obtained in meta-sedimentary rocks in drill hole #52 in addition 
to the section already announced at the end of March, of 12.1 g/t Au over 20.3 
metres located at the contact between these units and the tonalite. Other gold 
grades were also obtained in meta-sedimentary rocks such as 1.2 g/t Au over 
16.3 metres in drill hole #54.

Fourteen drill holes out of seventeen completed in the main drill sector 
yielded significant results, only drill holes #34, 39 and 56 yielded at most, 
anomalous gold grades. Three drill holes, #31, 47 and 48, out of thirteen 
undertaken outside of this sector yielded significant results. The Winter 2016 
diamond drilling program consisted of twenty-six drill holes (#31 to 56) in 
addition to the extension of #22 for a total of 4,432 metres. Maps showing 
locations of drill holes as well as long sections are available at the 
following links:

http://sirios.com/images/Carte-Zoomin-2016-06-06.jpg

http://sirios.com/images/Carte-Zoomout-2016-06-06.jpg

http://sirios.com/images/Longitudinale%20L.jpg

http://sirios.com/images/Longitudinale_I.jpg

http://sirios.com/images/Longitudinale_Jordi.jpg

http://sirios.com/images/Longitudinale_K.jpg

The table below lists all significant results:

MAIN ASSAY RESULTS FROM 2016 WINTER DRILLING CAMPAIGN

/T/

----------------------------------------------------------------------------
Drill
hole                           From        To       Interval             Au
CH-16-           Note            (m)       (m)         (m)(i)          (g/t)
----------------------------------------------------------------------------
35             Zone K           52.5      55.5              3            1.2
----------------------------------------------------------------------------
Zone Jordi           75.4      79.5        (ii)4.1           37.2
----------------------------------------------------------------------------
75.4      79.5        (ii)4.1      (iii)19.4
----------------------------------------------------------------------------
Incl, 77.0      78.4        (ii)1.4       ms 102.0
----------------------------------------------------------------------------
Zone I2           88.5      91.5        (ii)3.0              2
----------------------------------------------------------------------------
Zone I          110.8     113.5            2.7            4.6
----------------------------------------------------------------------------
Incl, 112.5     113.5              1          12.32
----------------------------------------------------------------------------
122       125              3            1.7
----------------------------------------------------------------------------

----------------------------------------------------------------------------

----------------------------------------------------------------------------
41             Zone L           16.4      19.2            2.8            1.4
----------------------------------------------------------------------------
Zone K            137       143        (ii)6.0           31.8
----------------------------------------------------------------------------
137       143        (ii)6.0      (iii)13.3
----------------------------------------------------------------------------
Incl, 141.5       143        (ii)1.5       ms 124.0
----------------------------------------------------------------------------
Zone Jordi            206       209              3            1.4
----------------------------------------------------------------------------
Zone I          227.5      2305              3              1
----------------------------------------------------------------------------
267.5       270            2.5              3
----------------------------------------------------------------------------
325       328              3            1.4
----------------------------------------------------------------------------
358.5       363            4.5            2.9
----------------------------------------------------------------------------

----------------------------------------------------------------------------
54     meta-sediments           40.9      57.2           16.3            1.2
----------------------------------------------------------------------------
contact
sediments-
tonalite           82.7        94           11.3            4.1
----------------------------------------------------------------------------
Incl, 83.8      86.9            3.1          13.36
----------------------------------------------------------------------------
Zone K          121.5       126            4.5              1
----------------------------------------------------------------------------

----------------------------------------------------------------------------
53                              27.5      30.2            2.7             13
----------------------------------------------------------------------------
Incl, 29.0      30.2            1.2           29.1
----------------------------------------------------------------------------
Zone L in re-
assay           79.5      80.6        (ii)1.0 ms in re-assay
----------------------------------------------------------------------------
154.6     155.6        (ii)1.0        ms 29.3
----------------------------------------------------------------------------
Zone I          285.4       288        (ii)2.6            7.8
----------------------------------------------------------------------------
Incl, 287.0       288        (ii)1.0        ms 20.0
----------------------------------------------------------------------------

----------------------------------------------------------------------------
52     Meta-sediments           38.0      39.0            1.0           16.1
----------------------------------------------------------------------------
Meta-sediments           77.0      99.6           22.6            1.3
----------------------------------------------------------------------------
Meta-sediments     incl. 88.8      99.6           10.8              2
----------------------------------------------------------------------------
Zone L contact
sediments-
tonalite a.p            120     140.3       (ii)20.3        ms 12.1
----------------------------------------------------------------------------
a.p          120.0     140.3       (ii)20.3       (iii)8.2
----------------------------------------------------------------------------
51                              10.9        16        (ii)5.1           10.4
----------------------------------------------------------------------------
Incl, 10.9      12.2        (ii)1.3        ms 39.6
----------------------------------------------------------------------------
30      31.7            1.7            8.8
----------------------------------------------------------------------------
Zone Jordi            104       105        (ii)1.0         ms 1.1
----------------------------------------------------------------------------
Zone I          173.6     176.2            2.6           10.3
----------------------------------------------------------------------------
Incl, 173.6     174.8            1.2           18.6
----------------------------------------------------------------------------

----------------------------------------------------------------------------
40             Zone L             64      65.5            1.5           10.5
----------------------------------------------------------------------------
91       100              9            0.9
----------------------------------------------------------------------------
Zone K          187.5     193.5              6            0.9
----------------------------------------------------------------------------
Zone Jordi          252.5     258.5              6            1.1
----------------------------------------------------------------------------
Zone I2            272       275        (ii)3.0            3.1
----------------------------------------------------------------------------
272     273.5        (ii)1.5         ms 5.8
----------------------------------------------------------------------------
Biotite
schistea.p          295.0       334       (ii)39.0            1.3
----------------------------------------------------------------------------
a.p    Incl, 320.6       327        (ii)6.4            3.1
----------------------------------------------------------------------------
a.p      and 346.9     350.1            3.2            2.9
----------------------------------------------------------------------------

----------------------------------------------------------------------------
55             Zone K           25.9      28.6            2.7            1.3
----------------------------------------------------------------------------
Zone Jordi           58.5      64.0            5.5            1.1
----------------------------------------------------------------------------
Zone I2          112.5     117.2            4.7            2.3
----------------------------------------------------------------------------
136.5     144.0            7.5            1.1
----------------------------------------------------------------------------
Zone I          150.5     153.5            3.0            3.1
----------------------------------------------------------------------------

----------------------------------------------------------------------------
31                               6.6      12.1            5.5            0.9
----------------------------------------------------------------------------
58.5      70.5           12.0            1.6
----------------------------------------------------------------------------
79.9      98.0           18.1            1.1
----------------------------------------------------------------------------
incl. 96.0      98.0            2.0            3.4
----------------------------------------------------------------------------

----------------------------------------------------------------------------
22Ext             a.p          209.0     210.0            1.0           16.3
----------------------------------------------------------------------------
a.p          240.5     245.4        (ii)4.9            1.7
----------------------------------------------------------------------------

----------------------------------------------------------------------------
32                a.p           15.5      17.0            1.5            4.4
----------------------------------------------------------------------------
a.p          122.8     123.8        (ii)1.0         ms 9.1
----------------------------------------------------------------------------

----------------------------------------------------------------------------
33                a.p            9.3      16.8            7.5            0.7
----------------------------------------------------------------------------
a.p           41.9      42.9            1.0            2.7
----------------------------------------------------------------------------

/T/

New north-west sector

/T/

----------------------------------------------------------------------------
Drill
hole                           From        To       Interval             
AuCH-16-           Note            (m)       (m)         (m)(i)          (g/t)
----------------------------------------------------------------------------
47           tonalite           36.5      37.5        (ii)1.0         ms 1.2
----------------------------------------------------------------------------
Contact
tonalite-meta-
sediments           57.9      58.9        (ii)1.0         ms 5.5
----------------------------------------------------------------------------
meta-sediments           88.1      89.2            1.1            5.3
----------------------------------------------------------------------------

----------------------------------------------------------------------------
48                                27      33.5            6.5            0.9
----------------------------------------------------------------------------
71      79.3        (ii)8.3            1.6
----------------------------------------------------------------------------
incl, 73.80      74.8        (ii)1.0           10.7
----------------------------------------------------------------------------
(i) Interval along the hole, true thickness non-indicated
(ii) Visible gold observed
(iii) Maximum gold grade cut at 50 g/t
ms: Gold grade obtained by fire assay with metallic sieve
a.p : announced previously

/T/

Information and coordinates of drill holes

/T/

----------------------------------------------------------------------------
Drill hole     Direction       Plunge       Length        UTM E        UTM N
----------------------------------------------------------------------------
#              degrees    degrees            m       NAD 83       NAD 83
----------------------------------------------------------------------------
CH919-16-
22-Ext.             254          -41           54       438500      5830171
----------------------------------------------------------------------------
CH919-16-31          300          -50          156       438054      5830500
----------------------------------------------------------------------------
CH919-16-32          300          -50          201       438514      5830175
----------------------------------------------------------------------------
CH919-16-33          300          -50           81       438430      5830333
----------------------------------------------------------------------------
CH919-16-34          300          -50           81       438480      5830431
----------------------------------------------------------------------------
CH919-16-35          300          -50          141       438552      5830433
----------------------------------------------------------------------------
CH919-16-36          300          -50           72       438035      5830168
----------------------------------------------------------------------------
CH919-16-37          300          -50           75       437872      5830263
----------------------------------------------------------------------------
CH919-16-38          300          -50          102       437688      5830040
----------------------------------------------------------------------------
CH919-16-39          300          -50          141       438604      5830527
----------------------------------------------------------------------------
CH919-16-40          295          -55        355.4       438666      5830147
----------------------------------------------------------------------------
CH919-16-41          300          -50          367       438598      5830176
----------------------------------------------------------------------------
CH919-16-42          300          -50          150       437325      5830924
----------------------------------------------------------------------------
CH919-16-43          300          -50          150       437224      5830744
----------------------------------------------------------------------------
CH919-16-44          300          -60          150       436725      5830982
----------------------------------------------------------------------------
CH919-16-45          295          -55          231       436968      5831476
----------------------------------------------------------------------------
CH919-16-46          300          -50          165       437067      5831651
----------------------------------------------------------------------------
CH919-16-47           55          -45           96       436970      5831476
----------------------------------------------------------------------------
CH919-16-48          240          -45          150       437161      5831211
----------------------------------------------------------------------------
CH919-16-49           55          -45           78       437651      5831028
----------------------------------------------------------------------------
CH919-16-50          235          -55        148.5       437650      5831027
----------------------------------------------------------------------------
CH919-16-51          300          -50          201       438577      5830321
----------------------------------------------------------------------------
CH919-16-52          300          -50          192       438830      5830228
----------------------------------------------------------------------------
CH919-16-53          300          -55          330       438717      5830236
----------------------------------------------------------------------------
CH919-16-54          300          -53        252.4       438694      5830365
----------------------------------------------------------------------------
CH919-16-55          300          -50          170       438428      5830128
----------------------------------------------------------------------------
CH919-16-56          300          -50          141       438579      5830486
----------------------------------------------------------------------------

/T/

Assay quality control

NQ-caliber drill cores of current campaign were sawed in half, with one half 
sent to a commercial laboratory for analysis and other half retained for future 
reference. A strict QA/QC program was followed by integrating blanks and 
certified reference materials to the drill core samples, all of which were 
prepared by IOS Services Geoscientifiques inc. of Chicoutimi, and assayed for 
gold by fire assay and atomic absorption finish (AA24) by the ALS Minerals 
laboratories in Val d'Or, Quebec. Samples grading more than 3 g/t were 
re-assayed by fire assay with gravimetric finish. (GRA22). Samples with visible 
gold were assayed by pyro-analysis with metallic sieve (SCR24) from a sample of 
about 1 kg."

Mr. Dominique Doucet, P. Eng., President of Sirios Resources Inc., is the 
Qualified Person pursuant to National Instrument 43-101, who prepared and is 
responsible for the technical information reported herein and has approved this 
written disclosure, including verification of the data disclosed, the sampling, 
and the analytical and QA-QC data underlying the technical information.

In 2012, Sirios concluded an agreement with Golden Valley regarding the 
ownership of Cheechoo that allowed it to, upon completion of certain 
obligations and counterparts, increase its current interest to 100%. Sirios has 
recently completed all these obligations and counterparts and will file shortly 
a request for transfer of mining claims to the competent authorities.

Golden Valley now owns 4,148,374 shares of Sirios, representing approximately 
4.1% of the company. Golden Valley also holds a 4% net smelter royalty from all 
mineral products mined or removed from Cheechoo. Notwithstanding the foregoing, 
the royalty relevant to gold mineral products mined or removed from Cheechoo 
(the "Gold Portion") may be reduced as follows depending on the market price of 
Gold at the time of the payment of the Gold Portion:

/T/

1.  If the price of Gold is less than $3,000 per ounce and higher than
$2,400 per ounce, a 3.5% royalty on the Gold Portion shall be payable to
Golden Valley;
2.  If the price of Gold is less than $2,400 per ounce and higher than
$1,200 per ounce, a 3% royalty on the Gold Portion shall be payable to
Golden Valley; and
3.  If the price of Gold is less than $1,200 per ounce, a 2.5% royalty on
the Gold Portion shall be payable to Golden Valley.

/T/

About Golden Valley Mines Ltd.: The Company typically tests initial grassroots 
targets while owning a 100% interest therein and then seeks partners to 
continue exploration funding. This allows the Company to carry on its 
generative programs and systematic exploration efforts at other majority-owned 
grassroots projects. The Company (together with its various subsidiaries) holds 
property interests in projects in Canada (Saskatchewan, Ontario and Quebec).

Forward Looking Statements:

This news release contains certain statements that may be deemed 
"forward-looking statements. Forward looking statements are statements that are 
not historical facts and are generally, but not always, identified by the words 
"expects", "plans", "anticipates", "believes", "intends", "estimates", 
"projects", "potential" and similar expressions, or that events or conditions 
"will", "would", "may", "could" or "should" occur. Although the Company 
believes the expectations expressed in such forward-looking statements are 
based on reasonable assumptions, such statements are not guarantees of future 
performance and actual results or realities may differ materially from those in 
forward looking statements. Forward looking statements are based on the 
beliefs, estimates and opinions of the Company's management on the date the 
statements are made. Except as required by law, the Company undertakes no 
obligation to update these forward-looking statements in the event that 
management's beliefs, estimates or opinions, or other factors, should change.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release.

- 30 -

CONTACT INFO:

Glenn J. Mullan
Chairman, President, and CEO
Golden Valley Mines Ltd.
819.824.2808 ext. 204
glenn.mullan@goldenvalleymines.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=569126952