Source	Marketwire
Date	06/27/2016
Time	06:02:35 AM

Company	 AMERICAS PETROGAS INC.
Title	Americas Petrogas Announces Updated  Phosphate Mineral Resource Estimate 
for Bayovar, Peru  and Initial Resource Report for Bayovar 5





    CDNX Symbol: BOE











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Americas Petrogas Inc.

TSX VENTURE SYMBOL: BOE
AND GrowMax Agri Corp.



June 27, 2016

Americas Petrogas Announces Updated  Phosphate Mineral Resource Estimate for 
Bayovar, Peru  and Initial Resource Report for Bayovar 5


CALGARY, ALBERTA--(Marketwired - June 27, 2016) - Americas Petrogas Inc. (TSX 
VENTURE:BOE) ("Americas Petrogas" or the "Company") is pleased to announce that 
it has received an updated National Instrument 43-101 compliant Mineral 
Resource estimate, including an initial Mineral Resource estimate for one of 
the concessions, for its Bayovar phosphate project on its property located in 
the Sechura Desert in Peru.

The independent estimate was prepared by Golder Associates ("Golder") and is an 
update of the previous Mineral Resource estimates prepared by Golder dated May 
11, 2015 and April 28, 2016 titled "Mineral Resource Technical Report on the 
GrowMax Bayovar Phosphate Project, Piura Region, Peru."

This Mineral Resource estimate update is based on all drill holes drilled by 
the Company to date including recent 2016 drilling on the Bayovar 5, 6, 7 and 8 
concessions.

Based on an evaluation of the drill hole spacing and geological continuity of 
the phosphorite beds (both thickness and grade parameters were evaluated) 
Golder has applied a Mineral Resource classification schema of zero-metre to 
400-metre spacing for Measured Mineral Resources, 400-metre to 800-metre 
spacing for Indicated Mineral Resources and 800-metre to 1,600-metre for 
Inferred Mineral Resources.

On Bayovar 5 concession -- an independent initial estimate was also prepared by 
Golder based on three wide spaced reconnaissance drill holes completed in 2015 
and an additional eight drill holes in Q1-2016 based on 1600-metre spacing. 
Inferred Mineral Resources were estimated to be 26.5 million tons and the mean 
grades of the individual beds vary from 8.93% P2O5 (PH13) to 14.22% P2O5 
(PH04). The thickness of beds varied from 0.10 metres (m) up to 0.70 m with the 
upper most phosphate bed encountered at a shallow depth of 8.85 m in the 
central portion of the property. Additional drill holes are planned for later 
this year to further evaluate the area.

On Bayovar 7 concession -- the most significant result of the 2016 drilling 
campaign is the confirmation of 29.7 million tonnes of Measured Mineral 
Resources, 137.4 million tonnes of Indicated Mineral Resources, and 63.7 
million tonnes of Inferred Mineral Resources with mean grades varying from 
6.95% P2O5 (PH14) to 15.97% P2O5 (PH02) in the individual beds in the Measured 
category, from 7.5% P2O5 (PH14) to 15.72% P2O5 (PH02) in the Indicated 
category, and from 7.33% P2O5 (PH14) to 15.37% P2O5 (PH02) in the Inferred 
category. In comparison with the previous (April 2016) Mineral Resource 
estimate, the current estimate represents the first instance of Measured 
Mineral Resources for the project along with an increase of 127.9 million 
tonnes of Indicated Mineral Resource, and a decrease of 5.2 million tonnes of 
Inferred Mineral Resource. The decrease in Inferred Mineral Resource is due to 
upgrading resources from the Inferred Resources category to the Indicated and 
Measured Mineral Resource categories. The thickness of the upper four beds 
varied from 0.45 m up to 0.69 m with the upper most phosphate bed encountered 
at a shallow depth of 3.00 m in the central portion of the property.

The Company's executive chairman, Abby Badwi, commented "With the positive 
results obtained on Bayovar 7, reporting total Measured and Indicated resources 
exceeding 167 million tonnes and an additional 63 million tonnes of Inferred 
resources, the Company is focusing its Preliminary Economic Assessment to 
develop a mine in this area. Bayovar 7 contains significant resources of good 
concentration of phosphate in the various beds with minimal thickness of the 
overburden beds and close to existing production by other producers from the 
same formation."

Table 1: Summary of Measured(i) Mineral Resources, All Areas, All Beds

/T/

----------------------------------------------------------------------------
Vertical       Dry       Wet                     Dry      Wet
Thickness    Tonnes    Tonnes   P2O5  SiO2    Density  Density
Area                (m)  (MT)(ii)  (MT)(ii)  (wt%)  (wt%)   (g/cm3)  (g/cm3)
----------------------------------------------------------------------------
Bayovar 7          0.61      29.7      38.9  12.00  30.90      1.21     1.58
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total
Measured          0.61      29.7      38.9  12.00  30.90      1.21     1.58
----------------------------------------------------------------------------

/T/

(i) In Situ Measured Mineral Resources, no minimum thickness applied.

(ii) MT: million tonnes

Table 2: Summary of Indicated(i) Mineral Resources, All Areas, All Beds

/T/

----------------------------------------------------------------------------
Vertical       Dry       Wet                     Dry      Wet
Thickness    Tonnes    Tonnes   P2O5  SiO2    Density  Density
Area                (m)  (MT)(ii)  (MT)(ii)  (wt%)  (wt%)   (g/cm3)  (g/cm3)
----------------------------------------------------------------------------
Bayovar 7          0.60     137.4     181.0  12.33  31.38      1.20     1.58
----------------------------------------------------------------------------
Bayovar
6S/8N(iii)        0.47      11.9      15.8  14.20  29.48      1.18     1.56
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total
Indicated         0.59     149.3     196.8  12.48  31.23      1.20     1.58
----------------------------------------------------------------------------

/T/

(i) In Situ Indicated Mineral Resources, no minimum thickness applied.

(ii) MT: million tonnes

(iii) Previously reported values have not changed.

Table 3: Summary of Inferred(i) Mineral Resources, All Areas, All Beds

/T/

----------------------------------------------------------------------------
Vertical       Dry       Wet                     Dry      Wet
Phosphorite   Thickness    Tonnes    Tonnes   P2O5  SiO2    Density  Density
Bed                (m)  (MT)(ii)  (MT)(ii)  (wt%)  (wt%)   (g/cm3)  (g/cm3)
----------------------------------------------------------------------------
Bayovar 5          0.48      26.5      34.6  12.17  35.37      1.21     1.58
----------------------------------------------------------------------------
Bayovar 7          0.58      63.7      83.8  11.94  31.34      1.21     1.58
----------------------------------------------------------------------------
Bayovar
6S/8N(iii)        0.42     114.5     151.6  13.86  29.94      1.17     1.54
----------------------------------------------------------------------------
Bayovar
8S(iii)           0.46     225.4     298.8  14.10  28.97      1.17     1.54
----------------------------------------------------------------------------
----------------------------------------------------------------------------
Total
Inferred          0.47     430.1     568.8  13.60  29.97      1.18     1.55
----------------------------------------------------------------------------

/T/

(i) In Situ Inferred Mineral Resources, no minimum thickness applied.

(ii) MT: million tonnes

(iii) Previously reported values have not changed.

The scientific and technical information within this news release was prepared 
under the supervision of John A. Nicholson, P.Geo, of Geominex, who is a member 
of the Association of Professional Engineers and Geoscientists of British 
Columbia and is an independent qualified person under NI 43-101.

The Resource Estimation was prepared by Golder, under the supervision of Jerry 
DeWolfe, MSc. P.Geo, an Independent Qualified Person as defined under NI 43-101.

As per NI 43-101 guidelines, Golder is reporting only in situ phosphate Mineral 
Resources as a mine plan, processing/metallurgy study, environmental study, 
economic analysis, marketing analysis, and other modifying factor studies have 
not been completed as of the effective date of the resource estimate. A 
Preliminary Economic Assessment (PEA) study incorporating the above information 
is currently underway and the Company anticipates completion and release of its 
results in September, 2016.

The full NI 43-101 report will be posted on SEDAR within 45 days of this news 
release.

An updated Corporate Presentation will be posted on the Company's website later 
today following the close of the North American markets.

About Americas Petrogas Inc.

Americas Petrogas Inc. is a Canadian company whose shares trade on the TSX 
Venture Exchange under the symbol BOE. Americas Petrogas has conventional and 
unconventional shale oil and gas and tight sands oil and gas interests in 
numerous blocks in the Neuquen Basin of Argentina. Americas Petrogas owns 89% 
and Indian Farmers Fertiliser Co-operative Limited (IFFCO) owns 11% of GrowMax 
Agri Corp, a private company involved in the exploration for near-surface 
phosphates, potash and other minerals, and potential development of a 
fertilizer project in Peru.

Forward-Looking Statements

Certain statements contained in this press release constitute "forward-looking 
statements" as such term is used in applicable Canadian and US securities laws. 
Any statements that express or involve discussions with respect to predictions, 
expectations, beliefs, plans, projections, objectives, assumptions or future 
events or are not statements of historical fact and should be viewed as 
"forward-looking statements". These statements relate to analyses and other 
information that are based upon forecasts of future results, estimates of 
amounts not yet determinable and assumptions of management. Such 
forward-looking statements involve known and unknown risks, uncertainties and 
other factors which may cause the actual results, performance or achievements 
of the Company to be materially different from any future results, performance 
or achievements expressed or implied by such forward-looking statements.

In particular, statements (express or implied) contained herein regarding 
filing of the NI 43-101 report on SEDAR, completion of a PEA, and potential for 
phosphates or other minerals on the Bayovar Property should all be viewed as 
forward-looking statements. The presence of phosphates in samples and of 
phosphate resources is not necessarily indicative that phosphates are capable 
of being successfully produced in commercial quantities. There is no assurance 
reserves will be assigned to such phosphate-bearing formations. There is no 
assurance that future holes will be drilled on the Bayovar Property or, if 
drilled, will be successful.

There can be no assurance that such forward-looking statements will prove to be 
accurate as actual results and future events could vary or differ materially 
from those anticipated in such statements. Accordingly, readers should not 
place undue reliance on forward-looking statements contained in this news 
release. The forward-looking statements contained herein are expressly 
qualified by this cautionary statement.

Forward-looking statements are made based on management's beliefs, estimates 
and opinions on the date the statements are made and the Company undertakes no 
obligation to update forward-looking statements and if these beliefs, estimates 
and opinions or other circumstances should change, except as required by 
applicable law.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THE RELEASE.

- 30 -

CONTACT INFO:

Americas Petrogas Inc.
Abby Badwi, P. Geo.
Executive Chairman
+1 587 390 7015
inquiries@americaspetrogas.com
www.americaspetrogas.com

INDUSTRY: Agriculture - Farming, Energy and Utilities - Oil and Gas
SUBJECT: STK - STOCK/OTHER MARKET NEWS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=570731082