Source	Marketwire
Date	06/27/2016
Time	05:02:51 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Reports Final Results from 2016 Exploration Drilling on the 
NW Brodie Trend, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

June 27, 2016

Scorpio Gold Reports Final Results from 2016 Exploration Drilling on the NW 
Brodie Trend, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - June 27, 2016) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports final 
results from 2016 exploration drilling on the NW Brodie trend at its 70% owned 
Mineral Ridge project, located in Nevada.

The NW Brodie trend extends over a 500 meter strike length between the Brodie 
and Bluelite deposits. Exploration drilling in 2014-2015 on the NW Brodie trend 
was based on a geological model of shallow dipping, multiple stacked veins, 
which is consistent with mineralization in the Bluelite and Brodie deposits. 
Inconsistencies in the drilling results prompted a detailed examination of the 
data and an oriented core drilling program. An updated geological model was 
completed in 2016. The mineralization within the NW Brodie trend is now 
interpreted as a corridor of multiple tensional quartz veins with an average 
strike and dip of 255 degrees /-60 degrees. Due to the more steeply dipping 
nature of the mineralization, prior drilling with vertically oriented RC holes 
intersected the mineralization at acute angles, resulting in thicker 
intersections than true widths.

Based on depths to mineralization and current gold prices, the NW Brodie area 
is not considered economic at this time and no further work is currently 
planned in the area.

A drill hole location map is available at: DH Plan

/T/


Table 1. NW Brodie Trend - Significant Drill Results
----------------------------------------------------------------------------
Hole       Azm   Dip   From   To  Width  From    To   Width  Gold  Gold
No.      (deg) (deg)  (ft)  (ft)  (ft)   (m)   (m)    (m)  (OPT) (g/t)
----------------------------------------------------------------------------
MR161936        0   -45   120   125     5  36.58 38.10   1.52 0.059  2.02
----------------------------------------------------------------------------
MR161956-957    180   -45               No Significant Results
----------------------------------------------------------------------------
MR161969        0   -75   145   150     5  44.20 45.72   1.52 0.010  0.34
----------------------------------------------------------------------------
MR161977        0   -75   140   145     5  42.67 44.20   1.52 0.049  1.68
----------------------------------------------------------------------------
MR162037        0   -75    10    15     5   3.05  4.57   1.52 0.026  0.89
----------------------------------------------------------------------------
195   200     5  59.44 60.96   1.52 0.018  0.62
----------------------------------------------------------------------------
MR162043        0   -45               No Significant Results
----------------------------------------------------------------------------
MR162044      180   -45   125   130     5  38.10 39.62   1.52 0.015  0.51
----------------------------------------------------------------------------
MR162045        0   -45   105   110     5  32.00 33.53   1.52 0.030  1.03
----------------------------------------------------------------------------
145   150     5  44.20 45.72   1.52 0.019  0.65
----------------------------------------------------------------------------
MR162047        0   -50   150   155     5  45.72 47.24   1.52 0.072  2.47
----------------------------------------------------------------------------
185   190     5  56.39 57.91   1.52 0.037  1.27
----------------------------------------------------------------------------
MR162048        0   -60   190   195     5  57.91 59.44   1.52 0.011  0.38
----------------------------------------------------------------------------
MR162049        0   -50   145   150     5  44.20 45.72   1.52 0.012  0.41
----------------------------------------------------------------------------
MR162050        0   -50    35    40     5  10.67 12.19   1.52 0.065  2.23
----------------------------------------------------------------------------
125   130     5  38.10 39.62   1.52 0.034  1.17
----------------------------------------------------------------------------
140   145     5  42.67 44.20   1.52 0.026  0.89
----------------------------------------------------------------------------
MR162051        0   -65    10    15     5   3.05  4.57   1.52 0.043  1.47
----------------------------------------------------------------------------
135   140     5  41.15 42.67   1.52 0.020  0.69
----------------------------------------------------------------------------
165   170     5  50.29 51.82   1.52 0.015  0.51
----------------------------------------------------------------------------
180   185     5  54.86 56.39   1.52 0.018  0.62
----------------------------------------------------------------------------
195   200     5  59.44 60.96   1.52 0.030  1.03
----------------------------------------------------------------------------
MR162052        0   -60    85    90     5  25.91 27.43   1.52 0.029  0.99
----------------------------------------------------------------------------
110   120    10  33.53 36.58   3.05 0.103  3.53
----------------------------------------------------------------------------
140   155    15  42.67 47.24  4.572 0.015  0.50
----------------------------------------------------------------------------
165   170     5  50.29 51.82   1.52 0.045  1.54
----------------------------------------------------------------------------
MR162053        0   -50    90    95     5  27.43 28.96   1.52 0.029  0.99
----------------------------------------------------------------------------
120   130    10  36.58 39.62   3.05 0.016  0.53
----------------------------------------------------------------------------
140   145     5  42.67 44.20   1.52 0.118  4.05
----------------------------------------------------------------------------
185   190     5  56.39 57.91   1.52 0.070  2.40
----------------------------------------------------------------------------
MR162054        0   -50   140   160    20  42.67 48.77   6.10 0.023  0.78
----------------------------------------------------------------------------
170   185    15  51.82 56.39   4.57 0.046  1.57
----------------------------------------------------------------------------
195   200     5  59.44 60.96   1.52 0.018  0.62
----------------------------------------------------------------------------
MR162055        0   -45               No Significant Results
----------------------------------------------------------------------------
MR162056      050   -50    60    65     5  18.29 19.81   1.52 0.041  1.41
----------------------------------------------------------------------------
165   175    10  50.29 53.34   3.05 0.021  0.72
----------------------------------------------------------------------------
190   200    10  57.91 60.96   3.05 0.030  1.01
----------------------------------------------------------------------------
245   250     5  74.68 76.20   1.52 0.021  0.72
----------------------------------------------------------------------------
MR162057      310   -50    80    85     5  24.38 25.91   1.52 0.026  0.89
----------------------------------------------------------------------------
180   185     5  54.86 56.39   1.52 0.096  3.29
----------------------------------------------------------------------------
210   220    10  64.01 67.06   3.05 0.024  0.81
----------------------------------------------------------------------------
MR162058        0   -45   200   205     5  60.96 62.48   1.52 0.017  0.58
----------------------------------------------------------------------------
285   290     5  86.87 88.39   1.52 0.061  2.09
----------------------------------------------------------------------------
MR162059      035   -45   195   200     5  59.44 60.96   1.52 0.020  0.69
----------------------------------------------------------------------------
220   225     5  67.06 68.58   1.52 0.055  1.89
----------------------------------------------------------------------------
MR162060      300   -35   275   295    20  83.82 89.92   6.10 0.019  0.63
----------------------------------------------------------------------------
MR162061        0   -75   120   125     5  36.58 38.10   1.52 0.015  0.51
----------------------------------------------------------------------------

/T/

All holes presented in Table 1 were completed by reverse circulation (RC) 
drilling. True width is estimated at 50-70% of downhole width. Scorpio Gold 
utilizes the analytical services of ALS Minerals (Reno, Nevada), an ISO/IEC 
17025:2005 (CAN-P-4E, CAN-P-1579) accredited testing laboratory, and Bureau 
Veritas (Reno, Nevada), an ISO 9001 certified testing laboratory. External 
check assays to verify lab accuracy are routinely completed. Further details 
are presented in the Company's quality assurance and quality control program 
for the Mineral Ridge project, available at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Elevon, LLC (30%). Mineral Ridge is a conventional open pit mining and heap 
leach operation. The Mineral Ridge property is host to multiple gold-bearing 
structures, veins and lenses at exploration, development and production stages. 
Scorpio Gold also holds a 100% interest in the advanced exploration-stage 
Goldwedge property in Manhattan, Nevada, with a fully permitted underground 
mine and 400 ton per day mill facility. The Goldwedge mill facility has been 
placed on a care and maintenance basis and can be restarted immediately when 
needed.

Scorpio Gold's President & CEO, Peter J. Hawley, PGeo,, is a Qualified Person 
as defined by National Instrument 43-101 and has reviewed and approved the 
content of this release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, President & CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Scorpio Gold Corporation
Peter J. Hawley
President & CEO
(819) 825-7618
phawley@scorpiogold.com
www.scorpiogold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=570724510