Source	MARKET NEWS
Date	06/27/2016
Time	07:15:59 AM

Company	 Anfield Resources Inc.
Title	Positive 
Preliminary Economic Assessment on Velv





    CDNX Symbol: ARY











Press Release





ANFIELD RESOURCES INC ("ARY-V;ANLDF-0")
- Positive Preliminary Economic Assessment on Velvet-Wood Uranium
- Project in Utah

Anfield Resources Inc. ("Anfield" or "the Company"), is pleased to
report the results of its Preliminary Economic Assessment ("PEA") with
regard to the Velvet-Wood Uranium Project ("Velvet-Wood"). The
independent PEA was prepared in accordance with National Instrument
43-101 standards of disclosure for mineral properties. Velvet-Wood, as
discussed herein, consists of two mine areas, located in Lisbon Valley,
Utah and the Shootaring Canyon Uranium Mill ("Shootaring Mill"),
located in Ticaboo, Utah.

In the PEA, initial mineral processing will be via conventional
vat or heap leaching methods conducted at Anfield's existing mineral
processing facility, the Shootaring Mill, which lies approximately 180
miles from the Velvet-Wood mine area. Under this scenario, only those
portions of the Shootaring Mill necessary for the final processing of
pregnant leach solutions, from either a vat or heap leach facility,
will be refurbished.

The project area covers approximately 2,425 acres, including
unpatented mining claims and a State of Utah mineral lease related to
the Velvet and Wood mine areas, and the Shootaring Mill.

Highlights include:

--Using a vat leaching recovery option, the PEA shows a pre-tax
project Internal Rate of Return ("IRR") of 41% and a Net Present Value
("NPV") of US$63.0 million, based on a discount rate of 8% and a
uranium price of US$65 per pound.

--Using a heap leaching recovery option, the PEA shows a pre-tax
project Internal Rate of Return ("IRR") of 37% and a Net Present Value
("NPV") of US$53.5 million, based on a discount rate of 8% and a
uranium price of US$65 per pound.

--Under both scenarios, average production would be approximately
663,000 pounds per annum, for total production of 4.6 million pounds
over a seven-year mine life.

--Under both scenarios, total project capex is estimated at
approximately US$46 million.

--Direct operating costs of $10.75 per pound of uranium via vat
leach and $11.39 via heap leach have been estimated.

The PEA completed for Velvet-Wood has been authored by Douglas L.
Beahm, P.E., P.G. Principal Engineer, of BRS Inc., Terence P. (Terry)
McNulty, P.E., D. Sc., of T.P. McNulty and Associates Inc. The purpose
of the PEA is to provide an independent analysis of the potential
economic viability of the mineral resources of the project.

Anfield CEO, Corey Dias, stated, "Anfield continues to add
shareholder value to its undervalued story. In the past eighteen
months, we completed an NI 43-101 mineral resource estimate for the
Velvet-Wood mine. The Velvet-Wood Mine, located in Lisbon Valley, Utah,
includes one of the most advanced conventional uranium deposits in the
U.S. The past-producing, licensed and permitted Velvet deposit and the
Wood deposit both boast rich uranium resources and have significant
exploration upside.

We are extremely satisfied with the outcome of this preliminary
economic assessment as it provides Anfield with evidence of the true
potential of Velvet-Wood. Since our acquisition of Uranium One's
conventional uranium assets, we have been keen to highlight the
economic value of this mine and mill combination. This PEA not only
represents a significant milestone for Anfield but also outlines a path
towards commercial development of Velvet-Wood. Anfield is clearly
well-positioned to benefit from an improving uranium market".

Velvet-Wood Mine

Between 1979 and 1984, Atlas Minerals mined approximately 400,000
tons of ore from the Velvet Deposit at grades of 0.46% U3O8 and 0.64%
VO5, recovering approximately 4 million pounds of U3O8 and 5 million
pounds of V2O5.

The current mineral resources of the combined Velvet and Wood
mines have been estimated to comprise 4.6 million pounds of U3O8 at a
grade of 0.29% U3O8 (measured and indicated resource) and 552,000
pounds of U3O8 at a grade of 0.32% U3O8 (inferred resource). (Source:
Velvet-Wood Mine Uranium Project, San Juan County, Utah USA 43-101
Mineral Reserve and Resource Report, Author: BRS Inc.; Date:
11/14/2014).

The Shootaring Mill was licensed and constructed by Plateau
Resources and operated in 1982 until the uranium price collapsed. U.S.
Energy and Uranium One are also previous owners of the Shootaring Mill.
The mill has not been decommissioned and has been under care and
maintenance since cessation of operations.

Surface Stockpiles

In addition to the estimated mineral resource at Velvet-Wood,
Anfield controls mineralized stockpiles from past mining at two
locations: 1) one stockpile at the Patty Ann mine area near the Velvet
mine; and 2) several stockpiles near the Shootaring mill. The volumes
and uranium content of the stockpiles were estimated from volumetric
surveys and sampling conducted by BRS in March, 2015. In total the
stockpiles are estimated to contain approximately 126,090 tons of
material at an average grade of 0.147% U3O8 and contain approximately
370,000 pounds of uranium. The surface stockpiles have been included as
part of the feed available under both the heap and vat leach scenarios.


Project Economics - Vat Leach

The PEA provides for a two-year pre-production period. The first
year's forecasted capital expenditures of $1.5 million include initial
mill and mine permitting, along with vat facility design. The second
year's capital expenditures, forecasted at $40.7 million (including a
US$4.9 million contingency), include additional mine and mill
permitting and licensing, mine engineering and design, mine facilities
and equipment, plant and vat leach plant construction and engineering.
Total capital for Life of Mine is estimated at $46.4 million.

Direct mine costs via vat leach for Velvet-Wood are estimated at
$10.75 per pound, while total direct costs per pound of recovered
uranium (including mine costs, haulage and handling, processing and
other) are estimated at $29.01 per pound.

The PEA shows a return on investment with a pre-tax IRR ranging
from 29% to 52% with uranium prices ranging from US$55 per pound to
US$75 per pound. The NPV of the Project at an 8% discount rate ranges
from US$37.3 million to US$88.9 million. After-tax IRR ranges between
24% and 43%, while after-tax NPV at an 8% discount rate ranges between
US$25.3 million and US$64.5 million.

Project Economics - Heap Leach

The PEA provides for a two-year pre-production period. The first
year's forecasted capital expenditures of $1.5 million include both
initial mill and mine permitting, along with heap pad design. The
second year's capital expenditures, forecasted at $40.9 million
(including a US$4.9 million contingency), include additional mine and
mill permitting and licensing, mine engineering and design, mine
facilities and equipment, plant and heap leach construction and
engineering. Total capital for Life of Mine is estimated at $46.6
million.

Direct mine costs via heap leach for Velvet-Wood are estimated at
$11.39 per pound, while total direct costs (including mine costs,
haulage and handling, processing and other) are estimated at $30.44 per
pound.

The PEA shows a return on investment with a pre-tax IRR ranging
from 25% to 48% with uranium prices ranging from US$55 per pound to
US$75 per pound. The NPV of the Project at an 8% discount rate ranges
from US$29.1 million to US$77.8 million. After-tax IRR ranges between
20% and 39%, while after-tax NPV at an 8% discount rate ranges between
US$19.1 million and US$56.1 million.

Velvet-Wood Uranium Project economics at 8% discount rate and
US$65 per pound uranium

(img src='https://www.thenewswire.com/client_files/tnwT7VC2t_.png'
/) @ https://www.thenewswire.com/client_files/tnwT7VC2t.png
Click Image To View Full Size     Source: Velvet-Wood PEA

NI 43-101 Disclosure

The PEA completed for Velvet-Wood has been authored by Douglas L.
Beahm, P.E., P.G. Principal Engineer, of BRS Inc., Terence P. (Terry)
McNulty, P.E., D. Sc., of T.P. McNulty and Associates Inc. The authors
have reviewed and approved the technical content of this news release.

A technical report on the Preliminary Economic Assessment will be
published on the System for Electronic Analysis and Retrieval ("SEDAR")
and the Company's website within the 45 days permitted under NI 43-101.


Results of the PEA represent forward-looking information. This
economic assessment is preliminary in nature and it includes inferred
mineral resources that are considered too speculative, geologically, to
have the economic considerations applies to them that would enable them
to be categorized as mineral reserves. There is no certainty that the
preliminary economic assessment will be realized. Conditions and
parameters of the project are subject to change based on the final
filing of the PEA on SEDAR within 45 days of this release. Mineral
resources are not mineral reserves as they do not have demonstrated
economic viability.

About Anfield Resources Inc.

Anfield is an energy metals exploration, development and near-term
production company that is committed to becoming a top-tier
energy-related fuels supplier by creating value through sustainable,
efficient growth in its energy metals assets. Anfield is a
publicly-traded corporation listed on the TSX-Venture Exchange (ARY-V)
and the Frankfurt Stock Exchange (0AD).

On behalf of the Board of Directors

ANFIELD RESOURCES INC.

Corey Dias, Chief Executive Officer

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Contact:

Anfield Resources Inc.
Clive Mostert
Corporate Communications
780-920-5044
info@anfieldresources.com
www.anfieldresources.com

608, 1199 West Pender Street
Vancouver, BC V6E 2R1
Tel: (604) 687-0300
Fax: (604) 687-0151

Safe Harbor Statement

THIS NEWS RELEASE CONTAINS "FORWARD-LOOKING STATEMENTS".
STATEMENTS IN THIS NEWS RELEASE THAT ARE NOT PURELY HISTORICAL ARE
FORWARD-LOOKING STATEMENTS AND INCLUDE ANY STATEMENTS REGARDING
BELIEFS, PLANS, EXPECTATIONS OR INTENTIONS REGARDING THE FUTURE.

EXCEPT FOR THE HISTORICAL INFORMATION PRESENTED HEREIN, MATTERS
DISCUSSED IN THIS NEWS RELEASE CONTAIN FORWARD-LOOKING STATEMENTS THAT
ARE SUBJECT TO CERTAIN RISKS AND UNCERTAINTIES THAT COULD CAUSE ACTUAL
RESULTS TO DIFFER MATERIALLY FROM ANY FUTURE RESULTS, PERFORMANCE OR
ACHIEVEMENTS EXPRESSED OR IMPLIED BY SUCH STATEMENTS. STATEMENTS THAT
ARE NOT HISTORICAL FACTS, INCLUDING STATEMENTS THAT ARE PRECEDED BY,
FOLLOWED BY, OR THAT INCLUDE SUCH WORDS AS "ESTIMATE," "ANTICIPATE,"
"BELIEVE," "PLAN" OR "EXPECT" OR SIMILAR STATEMENTS ARE FORWARD-LOOKING
STATEMENTS. RISKS AND UNCERTAINTIES FOR THE COMPANY INCLUDE, BUT ARE
NOT LIMITED TO, THE RISKS ASSOCIATED WITH MINERAL EXPLORATION AND
FUNDING AS WELL AS THE RISKS SHOWN IN THE COMPANY'S MOST RECENT ANNUAL
AND QUARTERLY REPORTS AND FROM TIME-TO-TIME IN OTHER PUBLICLY AVAILABLE
INFORMATION REGARDING THE COMPANY. OTHER RISKS INCLUDE RISKS ASSOCIATED
WITH SEEKING THE CAPITAL NECESSARY TO COMPLETE THE PROPOSED
TRANSACTION, THE REGULATORY APPROVAL PROCESS, COMPETITIVE COMPANIES,
FUTURE CAPITAL REQUIREMENTS AND THE COMPANY'S ABILITY AND LEVEL OF
SUPPORT FOR ITS EXPLORATION AND DEVELOPMENT ACTIVITIES. THERE CAN BE NO
ASSURANCE THAT THE COMPANY WILL BE ABLE TO COMPLETE THE PROPOSED
TRANSACTION, THAT THE COMPANY'S EXPLORATION EFFORTS WILL SUCCEED OR THE
COMPANY WILL ULTIMATELY ACHIEVE COMMERCIAL SUCCESS. THESE
FORWARD-LOOKING STATEMENTS ARE MADE AS OF THE DATE OF THIS NEWS
RELEASE, AND THE COMPANY ASSUMES NO OBLIGATION TO UPDATE THE
FORWARD-LOOKING STATEMENTS, OR TO UPDATE THE REASONS WHY ACTUAL RESULTS
COULD DIFFER FROM THOSE PROJECTED IN THE FORWARD-LOOKING STATEMENTS.
ALTHOUGH THE COMPANY BELIEVES THAT THE BELIEFS, PLANS, EXPECTATIONS AND
INTENTIONS CONTAINED IN THIS NEWS RELEASE ARE REASONABLE, THERE CAN BE
NO ASSURANCE THOSE BELIEFS, PLANS, EXPECTATIONS OR INTENTIONS WILL
PROVE TO BE ACCURATE. INVESTORS SHOULD CONSIDER ALL OF THE INFORMATION
SET FORTH HEREIN AND SHOULD ALSO REFER TO THE RISK FACTORS DISCLOSED IN
THE COMPANY'S PERIODIC REPORTS FILED FROM TIME-TO-TIME.

THIS NEWS RELEASE HAS BEEN PREPARED BY MANAGEMENT OF THE COMPANY
WHO TAKES FULL RESPONSIBILITY FOR ITS CONTENTS.
__________________________________________________
_______________________________________________
TSX Venture closing price for ARY-V
Date: 2016/06/24
Closing Price: 0.22
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1617800017TS11617801132-06465020160627