Source	MARKET NEWS
Date	06/27/2016
Time	07:15:27 AM

Company	 Scorpio Gold Corporation
Title	Final Results 
From 2016 Exploration Drilling On





    CDNX Symbol: SGN











Press Release





SCORPIO GOLD CORP ("SGN-V;SRCRF-0")
- Final Results From 2016 Exploration Drilling
- On The NW Brodie Trend, Mineral Ridge Project, Nevada

Scorpio Gold Corporation ("Scorpio Gold" or the "Company") reports
final results from 2016 exploration drilling on the NW Brodie trend at
its 70% owned Mineral Ridge project, located in Nevada.

The NW Brodie trend extends over a 500 meter strike length between
the Brodie and Bluelite deposits. Exploration drilling in 2014-2015 on
the NW Brodie trend was based on a geological model of shallow dipping,
multiple stacked veins, which is consistent with mineralization in the
Bluelite and Brodie deposits. Inconsistencies in the drilling results
prompted a detailed examination of the data and an oriented core
drilling program. An updated geological model was completed in 2016.
The mineralization within the NW Brodie trend is now interpreted as a
corridor of multiple tensional quartz veins with an average strike and
dip of 255/-60. Due to the more steeply dipping nature of the
mineralization, prior drilling with vertically oriented RC holes
intersected the mineralization at acute angles, resulting in thicker
intersections than true widths.

Based on depths to mineralization and current gold prices, the NW
Brodie area is not considered economic at this time and no further work
is currently planned in the area.

A drill hole location map is available at: DH Plan

//st
Table 1. NW Brodie Trend - Significant Drill Results
Hole           Azm   Dip From   To Width  From    To Width  Gold  Gold
No.          (deg) (deg) (ft) (ft)  (ft)   (m)   (m)   (m) (OPT) (g/t)
MR161936         0   -45  120  125     5 36.58 38.10  1.52 0.059  2.02
MR161956-957   180   -45                        No Significant Results
MR161969         0   -75  145  150     5 44.20 45.72  1.52 0.010  0.34
MR161977         0   -75  140  145     5 42.67 44.20  1.52 0.049  1.68
MR162037         0   -75   10   15     5  3.05  4.57  1.52 0.026  0.89
195  200     5 59.44 60.96  1.52 0.018  0.62
MR162043         0   -45                        No Significant Results
MR162044       180   -45  125  130     5 38.10 39.62  1.52 0.015  0.51
MR162045         0   -45  105  110     5 32.00 33.53  1.52 0.030  1.03
145  150     5 44.20 45.72  1.52 0.019  0.65
MR162047         0   -50  150  155     5 45.72 47.24  1.52 0.072  2.47
185  190     5 56.39 57.91  1.52 0.037  1.27
MR162048         0   -60  190  195     5 57.91 59.44  1.52 0.011  0.38
MR162049         0   -50  145  150     5 44.20 45.72  1.52 0.012  0.41
MR162050         0   -50   35   40     5 10.67 12.19  1.52 0.065  2.23
125  130     5 38.10 39.62  1.52 0.034  1.17
140  145     5 42.67 44.20  1.52 0.026  0.89
MR162051         0   -65   10   15     5  3.05  4.57  1.52 0.043  1.47
135  140     5 41.15 42.67  1.52 0.020  0.69
165  170     5 50.29 51.82  1.52 0.015  0.51
180  185     5 54.86 56.39  1.52 0.018  0.62
195  200     5 59.44 60.96  1.52 0.030  1.03
MR162052         0   -60   85   90     5 25.91 27.43  1.52 0.029  0.99
110  120    10 33.53 36.58  3.05 0.103  3.53
140  155    15 42.67 47.24 4.572 0.015  0.50
165  170     5 50.29 51.82  1.52 0.045  1.54
MR162053         0   -50   90   95     5 27.43 28.96  1.52 0.029  0.99
120  130    10 36.58 39.62  3.05 0.016  0.53
140  145     5 42.67 44.20  1.52 0.118  4.05
185  190     5 56.39 57.91  1.52 0.070  2.40
MR162054         0   -50  140  160    20 42.67 48.77  6.10 0.023  0.78
170  185    15 51.82 56.39  4.57 0.046  1.57
195  200     5 59.44 60.96  1.52 0.018  0.62
MR162055         0   -45                        No Significant Results
MR162056       050   -50   60   65     5 18.29 19.81  1.52 0.041  1.41
165  175    10 50.29 53.34  3.05 0.021  0.72
190  200    10 57.91 60.96  3.05 0.030  1.01
245  250     5 74.68 76.20  1.52 0.021  0.72
MR162057       310   -50   80   85     5 24.38 25.91  1.52 0.026  0.89
180  185     5 54.86 56.39  1.52 0.096  3.29
210  220    10 64.01 67.06  3.05 0.024  0.81
MR162058         0   -45  200  205     5 60.96 62.48  1.52 0.017  0.58
285  290     5 86.87 88.39  1.52 0.061  2.09
MR162059       035   -45  195  200     5 59.44 60.96  1.52 0.020  0.69
220  225     5 67.06 68.58  1.52 0.055  1.89
MR162060       300   -35  275  295    20 83.82 89.92  6.10 0.019  0.63
MR162061         0   -75  120  125     5 36.58 38.10  1.52 0.015  0.51

//et

All holes presented in Table 1 were completed by reverse
circulation (RC) drilling. True width is estimated at 50-70% of
downhole width. Scorpio Gold utilizes the analytical services of ALS
Minerals (Reno, Nevada), an ISO/IEC 17025:2005 (CAN-P-4E,CAN-P-1579)
accredited testing laboratory, and Bureau Veritas (Reno, Nevada), an
ISO 9001 certified testing laboratory. External check assays to verify
lab accuracy are routinely completed. Further details are presented in
the Company's quality assurance and quality control program for the
Mineral Ridge project, available at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge
gold mining operation located in Esmeralda County, Nevada with joint
venture partner Elevon, LLC (30%). Mineral Ridge is a conventional open
pit mining and heap leach operation. The Mineral Ridge property is host
to multiple gold-bearing structures, veins and lenses at exploration,
development and production stages. Scorpio Gold also holds a 100%
interest in the advanced exploration-stage Goldwedge property in
Manhattan, Nevada, with a fully permitted underground mine and 400 ton
per day mill facility. The Goldwedge mill facility has been placed on a
care and maintenance basis and can be restarted immediately when
needed.

Scorpio Gold's President & CEO, Peter J. Hawley, PGeo,, is a
Qualified Person as defined by National Instrument 43-101 and has
reviewed and approved the content of this release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, President & CEO

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.




Scorpio Gold Corporation
Peter J. Hawley
















TSX Venture closing price for SGN-V
Date: 2016/06/24
Closing Price: 0.10

TEL: (819) 825-7618
E-mail:   phawley@scorpiogold.com
Internet: www.scorpiogold.com
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1617800007TS11617800762-05324820160627