Source	Marketwire
Date	06/29/2016
Time	06:30:59 AM

Company	 AMEX EXPLORATION INC.
Title	2016 Winter Drilling Results at Amex's Perron Property





    CDNX Symbol: AMX











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Amex Exploration Inc.

TSX VENTURE SYMBOL: AMX

June 29, 2016

2016 Winter Drilling Results at Amex's Perron Property


MONTREAL, CANADA--(Marketwired - June 29, 2016) - Amex Exploration Inc. (TSX 
VENTURE:AMX) ("Amex") is pleased to announce that Agnico Eagle Mines Limited  
(TSX:AEM)(NYSE:AEM) ("Agnico Eagle") has recently informed Amex of the 2016 
winter drilling results at Amex's Perron property as scheduled (see 
PR-2016-05-16). This winter work program consisted of nine drill holes (with 
two others holes, ie # 163-16-025 and -032, that were abandoned due to poor 
ground condition) totalling 4,646 metres followed by eight downhole PULSE-EM 
(in holes # 163-16-024, -026, -028 to -031 and -033 to -034; results and 
interpretation still pending). A total of 1,368 samples were taken and analysed 
for their metal content (Au, Ag, Cu, Zn) and 141 others were analysed for 
lithogeochemistry. This latest phase of drilling program was to test the 
Normetal Mine Horizon over a strike length of approximately 3.5 km and also the 
target area located approximately 700 metres to the south inside the Beaupre 
Bloc. Table 1 reports the best drill holes intersects.

Table 1: Best intercepts from the 2016 Winter Drilling Campaign at Perron

/T/

----------------------------------------------------------------------------
Hole              From     To Length (m) Au (g/t) Ag (g/t) Cu (ppm) Zn (ppm)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
163-16-024       333,6  334,3        0,7     4,16      0,3       43        7
----------------------------------------------------------------------------
163-16-024       500,5  504,2        3,7     0,93      0,7       38      520
----------------------------------------------------------------------------
163-16-024 incl  502,4  503,2        0,8     2,28      1,3      120     1825
----------------------------------------------------------------------------
163-16-033       512,1  512,6        0,5        -      5,6      124     1580
----------------------------------------------------------------------------
163-16-033       531,1  534,0        2,9     0,97      0,5      617       80
----------------------------------------------------------------------------
163-16-033 incl  533,5 534,10        0,5     2,11      0,5      696       58
----------------------------------------------------------------------------
163-16-033       539,4  539,9        0,5     1,17      1,0     1035      107
----------------------------------------------------------------------------
163-16-033(i)    546,3  546,8        0,5     0,78      0,1       36       31
----------------------------------------------------------------------------
163-16-033       594,7  597,5        2,8     2,75      0,2      204      166
----------------------------------------------------------------------------
163-16-033 incl  594,7  595,5        0,8     2,41      0,4      184      370
----------------------------------------------------------------------------
163-16-033 incl  597,0  597,5        0,5    11,45      0,5      705      124
----------------------------------------------------------------------------

/T/

Table 1: Geochemical analysis was executed by ALS Chemex Laboratories in Val 
D'Or under Agnico Eagle's QA/QC program and supervision.

(i) 3 points of visible gold in the section.

In the Beaupre bloc area, two drill holes (holes 163-16-024 and -033) 
intersected interesting gold mineralization with values of up to 11,45 g/t Au 
over 0,5 metres (included in a broader zone grading 2,76 g/t Au over 2,8 
metres) in hole 163-16-033. Also of interest in this particular hole 
163-16-033, the only hole drilled at the northern contact between the Beaupre 
bloc Rhyolite and the volcano-sedimentary package of the Normetal Mine Horizon, 
points of visible gold were noted within sulphide bearing stringers cutting the 
cataclased rhyolite confirming again the very important gold potential of the 
Beaupre bloc.

The eight holes targeted to intersect the Normetal Mine Horizon along strike 
successfully hit their target as planned. Most importantly, three of these 
holes encountered intense stratabound hydrothermal alteration zones 
characterized typically by a mineral assemblage of 
Chlorite+Garnet+Biotite+Carbonate (holes # 163-16-026, -029 and -034), of which 
two of them also intersected semi-massive to massive sulfides zones composed 
basically by a combination of Pyrite and Pyrrhotite that enhance the potential 
of finding volcanogenic massive sulphide deposits in the nearby area.

Amex management is pleased with the exploration work done so far by the Agnico 
Eagle exploration team and is waiting for the next program of work to be 
presented for the future development of the Perron property.

Amex Exploration Inc. is a junior mining exploration company listed on the TSX 
Venture Exchange whose primary objective is to develop and bring into 
production viable gold and base metal deposits.

Jacques Marchand, P.Eng., who is a Qualified Persons as defined by Canadian NI 
43-101, has approved the technical information reported in this news release.

Forward-looking statements:

Except for statements of historical facts, all statements in this news release 
regarding, without limitation, future plans and objectives are forward-looking 
statements which involve risks and uncertainties. There can be no assurance 
that such statements will prove to be accurate. Actual results and future 
events could differ materially from those anticipated in such statements.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Jacques Trottier, PhD
President and Chief Executive Officer
(514) 866-8209

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=571003200