Source	MARKET NEWS
Date	06/29/2016
Time	06:44:22 AM

Company	 Amex Exploration Inc.
Title	Amex 
Exploration Announces: 2016 Winter Drilling





    CDNX Symbol: AMX











Press Release





AMEX EXPLORATION INC ("AMX-V")
AGNICO EAGLE MINES LTD ("AEM-TN")
- Amex Exploration Announces: 2016 Winter Drilling Results At
- Amex's Perron Property

Amex Exploration Inc. ("Amex") is pleased to announce that Agnico
Eagle Mines Limited ("Agnico Eagle")has recently informed Amex of the
2016 winter drilling results at Amex's Perron property as scheduled
(see PR-2016-05-16). This winter work program consisted of nine drill
holes (with two others holes, ie # 163-16-025 and -032, that were
abandoned due to poor ground condition) totalling 4,646 metres followed
by eight downhole PULSE-EM (in holes # 163-16-024, -026, -028 to -031
and -033 to -034; results and interpretation still pending). A total of
1,368 samples were taken and analysed for their metal content (Au, Ag,
Cu, Zn) and 141 others were analysed for lithogeochemistry. This latest
phase of drilling program was to test the Normetal Mine Horizon over a
strike length of approximately 3.5 km and also the target area located
approximately 700 metres to the south inside the Beaupre Bloc. Table 1
reports the best drill holes intersects.

Table 1: Best intercepts from the 2016 Winter Drilling Campaign at
Perron

//st
Hole             From     To Length (m) Au (g/t) Ag (g/t) Cu (ppm) Zn (ppm)
163-16-024      333,6  334,3        0,7     4,16      0,3       43        7
163-16-024      500,5  504,2        3,7     0,93      0,7       38      520
163-16-024 incl 502,4  503,2        0,8     2,28      1,3      120     1825
163-16-033      512,1  512,6        0,5        -      5,6      124     1580
163-16-033      531,1  534,0        2,9     0,97      0,5      617       80
163-16-033 incl 533,5 534,10        0,5     2,11      0,5      696       58
163-16-033      539,4  539,9        0,5     1,17      1,0     1035      107
163-16-033*     546,3  546,8        0,5     0,78      0,1       36       31
163-16-033      594,7  597,5        2,8     2,75      0,2      204      166
163-16-033 incl 594,7  595,5        0,8     2,41      0,4      184      370
163-16-033 incl 597,0  597,5        0,5    11,45      0,5      705      124
//et

Table 1: Geochemical analysis was executed by ALS Chemex
Laboratories in Val D'Or under Agnico Eagle's QA/QC program and
supervision.

* 3 points of visible gold in the section.

In the Beaupre bloc area, two drill holes (holes 163-16-024 and
-033) intersected interesting gold mineralization with values of up to
11,45 g/t Au over 0,5 metres (included in a broader zone grading 2,76
g/t Au over 2,8 metres) in hole 163-16-033. Also of interest in this
particular hole 163-16-033, the only hole drilled at the northern
contact between the Beaupre bloc Rhyolite and the volcano-sedimentary
package of the Normetal Mine Horizon, points of visible gold were noted
within sulphide bearing stringers cutting the cataclased rhyolite
confirming again the very important gold potential of the Beaupre bloc.


The eight holes targeted to intersect the Normetal Mine Horizon
along strike successfully hit their target as planned. Most
importantly, three of these holes encountered intense stratabound
hydrothermal alteration zones characterized typically by a mineral
assemblage of Chlorite+Garnet+Biotite+Carbonate (holes # 163-16-026,
-029 and -034), of which two of them also intersected semi-massive to
massive sulfides zones composed basically by a combination of Pyrite
and Pyrrhotite that enhance the potential of finding volcanogenic
massive sulphide deposits in the nearby area.

Amex management is pleased with the exploration work done so far
by the Agnico Eagle exploration team and is waiting for the next
program of work to be presented for the future development of the
Perron property.

Amex Exploration Inc. is a junior mining exploration company
listed on the TSX Venture Exchange whose primary objective is to
develop and bring into production viable gold and base metal deposits.

Jacques Marchand, P.Eng., who is a Qualified Persons as defined by
Canadian NI 43-101, has approved the technical information reported in
this news release.

Forward-looking statements:

Except for statements of historical facts, all statements in this
news release regarding, without limitation, future plans and objectives
are forward-looking statements which involve risks and uncertainties.
There can be no assurance that such statements will prove to be
accurate. Actual results and future events could differ materially from
those anticipated in such statements.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for AMX-V
Date: 2016/06/28
Closing Price: 0.05

TEL:  (514) 866-8209  Jacques Trottier, PhD
President and Chief Executive Officer
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1618000023TS11618000965-06420920160629