Source	MARKET NEWS
Date	06/07/2017
Time	06:38:53 AM

Company	 Mundoro Capital Inc.
Title	Drill 
Program Results From Borsko License In Ser





    CDNX Symbol: MUN











Press Release




[200/News Release]MUNVMUNDORO CAPITAL INCJUN 07 2017  06:35 AMDrill 
Program Results From Borsko License In Serbia --->@NEWS RELEASE
MUNDORO CAPITAL INC ("MUN-V;MUNMF-0")
- Drill Program Results From Borsko License In Serbia

Mundoro Capital Inc. (www.mundoro.com) ("Mundoro" or the "Company")
is pleased to announce the results from drilling at the Borsko Jezero
license ("Borsko"). Borsko is one of the four licenses part of the
JOGMEC-Mundoro option to earn-in agreement announced in August 2016.
Borsko is located directly west of the Serbian state-operated producing
mines, RTB Group's Bor copper porphyry mine and the Veliki Krivelj
copper-gold porphyry mine, all located in the central portion of the
Timok Magmatic Complex ("Timok"). See Figure 1 - Location Map of Borsko
Drill Targets.

Teo Dechev, CEO & President of Mundoro commented, "We are strongly
encouraged by the alteration and mineralization we have intercepted in
the drill core thus far at the Borsko license and that the results to
date from the initial drill holes provide support for the project's
potential to host a copper-gold epithermal and porphyry system. We are
planning, along with our partner JOGMEC, for further drilling at Borsko
in the second half of 2017."

Borsko Drill Program

Overview

The Borsko drill program tested the first two of six targets
generated by the 2016 field program (Figure 1 - Location of Borsko
Drill Targets). For the 2016 field program, Mundoro carried out a soil
sampling program over the central portion of the license to follow up
on high copper-gold stream sediment anomalies which could not be
explained by previous prospecting and rock sampling. The soil sampling
results returned significant copper-gold anomalies which remain open to
the north and south. Follow-up field work revealed association of some
of the soil anomalies with altered dike contacts, discrete quartz
stockwork veinlets and fine grained sulphides related to fault-fracture
zones. Mundoro conducted ground magnetic and CSAMT surveys, structural
analysis and limited trenching over certain soil anomalies.

Geology Interpretation of Borsko License Area

The Borsko license is located in the Timok Magmatic Complex which
is one of the most prolific metallogenic domains in the Tethyan Belt.
The geologic units in this licence area consist of Upper Cretaceous
volcano-sedimentary successions, predominantly andesite and
pyroclastics. Generally considered the most prospective geological
units, the Phase 1 hornblende porphyry andesite occupies the
easternmost boundaries of the Borsko license and dips moderately to
southwest under the andesitic flows and interflow breccias and
pyroclastic rocks of the second phase.

The H1-2017 drillholes are located approximately 2.5 kilometers
west of the Bor group of copper-gold deposits which include high
sulphidation epithermal mineralization such as the historical Tilva
Rosh deposit which has been mined out and reported to have been
intersected in the uppermost 30m meters of the lithocap.

The interpretation of Borsko geology summarized above along with
models of known deposits in the district highlights the uppermost part
of the lithocap, immediately below the less-altered volcanic sequence,
as the prime target for any high-sulphidation copper-gold orebodies of
Bor and &#268;ukaru Peki type. Any such massive and/or stockwork
sulphide bodies are likely to lie within the footprint of the
underlying porphyry copper-gold centre.

The H1-2017 drilling at Borsko shows that an advanced argillic
lithocap underlies 550 m of little-altered andesitic volcanic rocks,
which were in existence at the time the advanced argillic alteration
took place. The lithocap is weakly mineralized but, importantly, the
highest copper and gold assay values lie immediately beneath its top,
which is the equivalent stratigraphic position of the Bor and
&#268;ukaru Peki high-sulphidation copper-gold orebodies with respect
to their associated lithocaps.

Hole BJ-07 exits the lithocap at depth and intersects
pyrite-bearing propylitic alteration, which is interpreted to be the
outer halo of a porphyry copper-gold centre. Additional holes are
planned in order to search for high-sulphidation orebodies at the top
of the Borsko lithocap.

Target 1 - See Figure 2 - Cross Section of Target 1

//st

* Drillhole BJ_06, which tested one of the newly generated drill targets
at
Borsko successfully demonstrated that a potentially mineralised system
exists under overlying andesitic flows. This drill hole targeted an
interpreted blind system at Target 1. Targeting was based on
geophysical
data and geological interpretation. The hole was completed at a depth
of
821.6 m.
* BJ_07: Based on the visual inspection of BJ_06, Mundoro and JOGMEC
determined to extend the drill program to further test Target 1 with a
follow up drill hole, BJ_07, up to 1300 m length.

//et

Target 2 - See Figure 3 - Cross Section of Target 2

//st

* BJ_08: This diamond drill hole was designed to test Target 2 with a
planned depth of 700 m. Based on visual inspection of the core, Mundoro
and JOGMEC determined to extend the drilling to 1,000 m. Target 2 was
based on geophysical data and structural interpretation in relation to
surface geochemistry and hydrothermal alteration.

//et

Table 1: Borsko Drill Holes Observations

//st

Drill   Total    Dip/          Geological description
Hole    Depth    Azimuth
ID

BJ_06   821.6m   -65/246   *   From surface to 585 m, cut through a
EOH                    package of weak but pervasively altered to
chlorite-smectite, lacking pyrite andesitic
flow and interflow breccias;

*   At 585 m the drill hole abruptly entered
advanced argillic mainly kaolinite lithocap
containing disseminated pyrite increasing
at depth.

*   From 625 m to 767 m (142 m) the drill hole
entered pervasively silicified andesite
volcanics containing semi-massive pyrite,
vuggy silica and breccia zones. The
breccias are polymictic and relatively late
stage.

*   From 762.6 m to 767 m such breccia contains
4.4m @0.27 g/t Au, 5.46 g/t Ag; including
0.6m @ 0.8 g/t Au, 24.3 g/t Ag and 0.18%Cu.

*   From 765 m to end of the hole at 821 m, he
drill hole transitioned to advanced
argillic altered partly brecciated
andesitic volcanics containing more ickite
with occasional sericite-pyrite and
semi-massive pyrite implying increased
temperature.

BJ_07   1301.9   -85/66    *   From surface to 580 m, intersected a
m EOH                  package of weak but pervasively altered to
chlorite-smectite, lacking pyrite andesitic
flow and interflow breccias;

*   From 580 m to 1132 m (552 m) the drill hole
entered advanced argillic quartz-kaolinite
lithocap as in drill hole BJ-06.

*   In the lithocap, quartz-kaolinite-pyrite
transitions downwards at around 1100 m to
quartz-kaolinite-dickite-pyrophyllite-pyrite
implying increased temperature. Pyrite is
fine-grained locally sooty (melnikovite)
and occurs in disseminated and semi-massive
pods rather than veinlet form.

*   The lithocap is locally overprinted by 1-5
m intervals of cream-colored silicification
cut by irregular veinlets and patches of
massive pyrite. Vuggy residual quartz and
subsidiary alunite are also observed
locally.

*   From 1032 m enargite-pyrite mineralisation
is observed in an interval 6.2m containing
0.26 g/t Au, 2.6 g/t Ag, 0.2% Cu including
1.4m with 0.6 g/t Au, 0.23% Cu and 0.7 m
with 0.14 g/t Au, 0.6% Cu.

*   From 1132.5 m to the end of the drill hole
at 1302 m, the lithocap is transitional to
propylitic alteration in which magnetite is
preserved and pyrite contents are much
less. The transition zone contains remnant
chlorite but lacks epidote that defines the
underlying propylitic zone.

BJ_08   1002     -75/351   *   From surface to 509 m, drilled through
m EOH                  alternating andesitic agglomerate and
andesite tuff weakly chlorite-smectite
altered.

*   From 509 m to 615 m drill hole continued
through sedimentary package of marl and
conglomerates layered with andesite tuff.

*   From 615 m to 682 m, the drill hole
intersected unaltered coarse-grained
hornblende andesite ('Phase 1 andesite').

*   From 682 m to the end of the drill hole
1002 m, the drill hole continued in weakly
chlorite-smectite altered hornblende
andesite and andesitic breccia with trace
of chalcopyrite-pyrite mineralised clasts
at 695.5 m and 749.6 m.

*   At 942.4m the drill hole cut through
interval with covellite mineralisation
which returned 0.9m @ 0.83 g/t Au and 2.63%
Cu.

//et

Table 2: Assay Results of Borsko Drilling

//st

Drill Hole ID       Total    Dip/        From     To (m)   Interval
Cu      Au       CuEq
Depth    Azimuth     (m)               (m)
(%)1    (g/t)2   (%)3

BJ_06               821.6    -65/246     758.4    767.0    8.6
0.023   0.2      0.17
m EOH

Including   764.6    765.2    0.6
0.18    0.78     0.75

BJ_07               1301.9   -85/66      607.6    609.0    1.4
0.004   1.03     0.76
m EOH

734.0    738.4    4.4
0.01    0.16     0.13

768.3    769.7    1.4
0.008   0.45     0.34

771.9    775.0    3.1
0.006   0.24     0.18

873.0    875.5    2.5
0.27    0.33     0.51

including   875.1    875.5    0.4
0.71    0.65     1.18

989.5    992.5    3.0
0.03    0.15     0.14

1006.0   1013.8   7.8
0.02    0.14     0.12

1032.0   1050.0   18.0
0.07    0.17     0.19

including   1032.0   1035.4   3.4
0.27    0.33     0.51

1130.0   1132.5   2.5
0.03    0.28     0.23

including   1131.8   1132.5   0.7
0.05    0.77     0.61

BJ_08               1002     -75/351     625.0    627.0    2.0
0.1     0.007    0.11
m EOH

942.4    943.3    0.9
2.63    0.83     3.24

1. Analysis by ICP-AES using 0.5 g aliquot for samples containing less
than 1% copper, by
AAS for samples containing 1 - 11% copper, and by ICP-AES using 0.1 g
aliquot for samples
containing )11% copper.

2. Analysis by fire assay with gravimetric finish for samples containing
greater than 3
g/t gold, and by fire assay with AAS finish for samples containing less
than 3 g/t gold.

3.The copper equivalent (CuEq%) is calculated from the formula CuEq =
(%Cu) + [(g/t/AuEq)
x (1/31.1035) x ($/ozAu)] [(22.0462) x ($/lbCu)]

4. The gold equivalent is calculated from the formula AuEq =
(g/t/Au)+[(%Cu) x (22.0462) x
($/lbCu)] [(1/31.1035) x ($/ozAu)].

5. All thicknesses from intersections from drill holes are down-hole
drilled thicknesses.
At this early stage of exploration for a high-sulphidation epithermal and
porphyry system
at depths typical of the Timok, it is not possible at this time to
determine the
orientation of the mineralized zones, or to estimate their true
thickness.

//et

Next Steps

The Company is preparing a follow up drilling program for the
second half of 2017. Based on the data collected in this most recent
drill program and the associated analysis and interpretation, the
Company and its partner JOGMEC, believe that Borsko has strong
potential to host high sulphidation and porphyry style copper-gold
mineralisation. Mostly notably, the prospective lithocap horizon
discovered through this program is directly analogous with the host
horizons at the Bor underground high sulphidation deposits and Cukaru
Peki discovery.

JOGMEC-Mundoro Option to Earn-in Agreement

In July 2016, the Company amended its binding interim agreement
(the "Interim Agreement") with Japan Oil, Gas and Metals National
Corporation ("JOGMEC") and granted to JOGMEC an earn-in option on four
of Mundoro's exploration licenses: Dubrava, Padina, Zeleznik and Borsko
Jezero (the "Timok North Projects") located within the Timok Magmatic
Complex in northeastern Serbia. JOGMEC has the option to earn a 51%
interest in the Timok North Projects by making US$4 million in
expenditures within three years (March 2019) ("Stage One Earn-in").
JOGMEC has completed its commitment to expend US$1 million of this
amount by March 2017. Following the Stage One Earn-in, JOGMEC has aright to 
acquire an additional 24% interest in the Timok North
Projects, for a total of 75% interest, by funding the completion of a
Feasibility Study (up to US$32 million) by the eighth anniversary of
the Interim Agreement (March 2024) ("Stage Two Earn-in"). On completing
the Stage Two Earn-In, JOGMEC will have a right, exercisable for a
period of 60 days, to purchase an additional 5% interest in the Timok
North Projects from Mundoro, for a total of 80% interest.

Qualified Person

Technical information contained in this Press Release has been
reviewed and approved by Mr. G. Magaranov, P. Geo., Qualified Person as
defined by National Instrument 43-101.

QA/QC, Sampling and Analysis

Drillhole orientations were surveyed at approximately 30 m
intervals. Company personnel monitored the drilling, with cores
delivered daily to the Company's core storage facility in the town of
Bor, where it was logged, cut and sampled. Core recovery is recorded as
95-100% in most intervals, with the exception of the more intensely
tectonized sections. The samples were collected in accordance with the
Company's protocols that are compatible with accepted industry
procedures and best practice standards. Most samples through the
mineralized intervals were 1 metre in length, up to a maximum 2 metres.
In sections of poorly mineralized or unaltered and unmineralised rocks
one 2m sample was collected at every 15 meters core. The samples were
submitted to ALS Laboratory in Bor, Serbia, for sample preparation and
analysis. In addition to the laboratory's internal QA/QC procedures,
the Company conducted its own QA/QC with the systematic inclusion of
certified reference materials every 20 samples, blank samples every 20
samples and field duplicates at every 25 samples.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a Canadian mineral exploration and development public
company focused on building value for its shareholders through directly
investing in mineral projects that have the ability to generate future
returns for shareholders. The Company currently holds a diverse
portfolio of projects in two European countries as well as an
investment in a producing gold mine in Bulgaria and a feasibility stage
gold project in China. The Company holds eight 100% owned projects in
Serbia, the four Timok North Projects are in option to JOGMEC, and the
four Timok South Projects are being advanced by Mundoro. Mundoro's
common shares trade on the TSX Venture Exchange under the symbol "MUN".


Caution Concerning Forward-Looking Statements

This News Release contains forward-looking statements.
Forward-looking statements can be identified by the use of
forward-looking words such as "will", "expect", "intend", "plan",
"estimate", "anticipate", "believe" or "continue" or similar words or
the negative thereof, and include the following: completion of the
earn-in expenditures and options by JOGMEC; and completion of a
definitive joint venture agreement by the parties. The material
assumptions that were applied in making the forward looking statements
in this News Release include expectations as to the mineral potential
of the Timok North Properties, the Company's future strategy and
business plan and execution of the Company's existing plans. We caution
readers of this News Release not to place undue reliance on forward
looking statements contained in this News Release, as there can be no
assurance that they will occur and they are subject to a number of
uncertainties and other factors that could cause actual results to
differ materially from those expressed or implied by such
forward-looking statements. These factors include general economic and
market conditions, exploration results, commodity prices, changes in
law, regulatory processes, the status of Mundoro's assets and financial
condition, actions of competitors and the ability to implement business
strategies and pursue business opportunities. The forward-looking
statements contained in this News Release are expressly qualified in
their entirety by this cautionary statement. The forward-looking
statements included in this News Release are made as of the date of
this News Release and the Board undertakes no obligation to publicly
update such forward-looking statements, except as required by law.
Shareholders are cautioned that all forward-looking statements involve
risks and uncertainties and for a more detailed discussion of such
risks and other factors that could cause actual results to differ
materially from those expressed or implied by such forward-looking
statements, refer to the Company's filings with the Canadian securities
regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.



Mundoro Capital Inc.
Teo Dechev




























TSX Venture closing price for MUN-V
Date: 2017/06/06
Closing Price: 0.25

TEL: +1-604-669-8055
Internet: www.mundoro.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1715700024TS11715701219-06354020170607