Source	MARKET NEWS
Date	06/12/2017
Time	06:54:37 AM

Company	 Marlin Gold Mining Ltd.
Title	Intersects 2.73 g/t Gold Over 38.70 Meters, Incl





    CDNX Symbol: MLN











Press Release





Intersects 2.73 g/t Gold Over 38.70 Meters, Including 5.12 g/t GoldOver 14.00 
Meters, --->@NEWS RELEASE
MARLIN GOLD MINING LTD ("MLN-V;MLNGF-0")
- Intersects 2.73 g/t Gold Over 38.70 Meters,
- Including 5.12 g/t Gold Over 14.00 Meters,

Marlin Gold Mining Ltd. ("Marlin" or the "Company") is pleased to
report another round of positive drill results from the Company's
wholly owned La Trinidad gold mine in Sinaloa, Mexico (the "La Trinidad
Mine").

Hole 17TRD52 intersected 2.73 g/t gold over 38.70 meters (16.30
meters true width), including 5.12 g/t gold over 14.00 meters (5.88
meters true width).  17TRD52 was intended to target an area
approximately 25 meters to the north of 17TRD50, which intersected 7.57
g/t gold over 63.35 meters (26.70 meters true width) (see press release
dated May 24, 2017), and approximately 50 meters to the north of
17TRD44, which intersected 15.55 g/t gold over 15.45 meters true width
(see press release dated April 10, 2017).

As is the case with the upper intercepts of holes 17TRD50 and
17TRD44, the upper intercept of 17TRD52 was previously interpreted as
waste, and will likely have a positive impact to the modeled grade and
tonnage in this area of the deposit.  Additionally, there was a
separate and even higher up (approximately 40 meters above the known
depth of the high grade HS Zone) intersection of 1.38 g/t gold over
14.70 meters.  The Company plans to be mining the area around the
highest intercept of 17TRD52 within two months.

A longitudinal section of holes 17TRD52 can be viewed by clicking
HERE.

A cross section of hole 17TRD52 can be viewed by clicking HERE.

A three-dimensional block model of the area around holes 17TRD52,
17TRD50 and 17TRD44 can be viewed by clicking HERE.

Not to be overlooked, holes 17TRD53 and 17TRD56, which are located
over 100 meters to the south of 17TRD52, intersected 2.36 g/t gold over
8.00 meters (4.80 meters true width) and 2.31 g/t gold over 6.17 meters
true width, respectively.

Further drilling is planned to continue refining the current mine
plan, as well as targeting additional areas of mineralization to the
southeast that can extend the mine life of the Taunus pit at the La
Trinidad Mine.

Akiba Leisman, Executive Chairman and Interim CEO states that
"drilling at the Taunus pit is giving us great exploration success.
Areas that were previously modeled as waste are yielding mineralized
intercepts that are multiples of our 0.35 g/t gold cut-off grade.  This
drilling program will add ounces to our mine plan, and we will continue
drilling to the southeast to determine how significant the Taunus pit
can eventually become."

The table below summarizes the significant intercepts.  True
widths of the drilled intercepts are believed to be 42% for 17TRD52 and
60% for 17TRD53.  Drill hole intercepts are believed to be
approximately the true thickness of the zone for holes 17TRD55 and
17TRD56.

//st

Drill Hole(1)   Target Area    From (m)        To (m)   Length     Au
(m)        (g/t)

17TRD51         South HS       No Significant intercepts
Zone

17TRD52(2)      South HS       81.30           96.00    14.70      1.38
Zone

including(3)    South HS       81.30           88.00    6.70       2.16
Zone

17TRD52         South HS       131.30          170.00   38.70      2.73
Zone

including(3)    South HS       134.00          148.00   14.00      5.12
Zone

17TRD52         South HS       184.00          192.00   8.00       1.30
Zone

17TRD53         South HS       88.00           104.00   16.00      1.48
Zone

including(3)    South HS       88.00           96.00    8.00       2.36
Zone

17TRD54         Southeast      No Significant intercepts
Extension

17TRD55         Southeast      0.00            11.20    11.20      0.74
Extension

17TRD56         South HS       60.00           66.17    6.17       2.31
Zone

17TRD56         South HS       76.00           88.00    12.00      1.36
Zone

//et

//st

(1)   Significant intercept defined as a minimum assay of 0.3 g/t Au over
a minimum 6-meter interval with no more than 2 meters of internal
dilution below 0.3 g/t Au.

(2)   Significant intercept criteria for hole 17TRD52 was modified from
all previously reported drill holes to properly account for the
length of the intercept from 131.30 to 170.00 meters. For this
intercept, a 6.6 meter zone of 0.13 g/t Au of internal dilution,
below the cut-off grade of 0.30 g/t Au, was included in the
reported intercept. All other criteria remained the same.

(3)   Significant internal intercept defined as a minimum assay of 2.0
g/t Au over a minimum 6-meter interval with no more than 2 meters
of internal dilution below 0.5 g/t Au.

//et

Dr. Matthew D. Gray. C.P.G., of Resource Geosciences Incorporated,
a Qualified Person under the definitions of CSA NI 43-101, implemented
and supervised industry standard QA/QC protocols for the La Trinidad
drill sampling program including insertion of duplicate and reference
standard samples. Dr. Gray has verified the reliability of the drill
sampling results reported in this press release.

Notes on Sampling and Assaying

Drill core was continuously sampled from inception to termination
of the drill hole.  Sample intervals were typically two meters.  Drill
core diameter was HQ (6.35 centimeters).  Geologic and geotechnical
data was captured into a digital database, core was photographed, then
one half split of the core was collected for analysis and one half was
retained in the core library.  Samples were kept in a secured logging
and storage facility until such time that they were received on site by
representatives of Bureau Veritas Commodities Canada Ltd. ("Bureau
Veritas").  Sample preparation was done in the Durango facilities of
Bureau Veritas and pulps were sent to the Bureau Veritas laboratory in
Vancouver for analysis.  Gold was analyzed by standard fire assay
fusion, 30 gram aliquot, AAS finish, with samples reporting greater
than 10 grams per tonne gold re-assayed by fire assay fusion with
gravimetric finish.  Controls samples consisting of duplicates,
standards, and blanks were inserted into the sample stream and
analytical results of control samples confirmed reliability of the
assay data.

About Marlin Gold

Marlin is a growth-oriented gold and silver mining company focused
on the Americas.  The company owns two properties located in Sinaloa,
Mexico and Arizona, USA and a portfolio of royalties.  Marlin's
priority is to advance its properties toward commercial production and
enhance shareholder value through the growth of its wholly owned
subsidiary, Sailfish Royalty Corp.  Marlin is backed by a well-funded
investor with a successful track record in the resources sector.  The
La Trinidad Mine in Sinaloa, Mexico declared commercial production on
November 1, 2014 and is one of the highest-grade open pit heap leach
gold mines in Mexico.  A NI 43-101 mineral resource estimate and
preliminary economic assessment for the La Trinidad Mine and
Commonwealth Project can be found at www.sedar.com or at
www.marlingold.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as the term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Cautionary statement regarding forward-looking information

This news release contains 'forward-looking statements' within the
meaning of applicable securities laws. Forward-looking statements are
statements that are not historical facts and are generally, but not
always, identified by words such as the following: expects, plans,
anticipates, believes, intends, estimates, projects, assumes, potential
and similar expressions. Forward-looking statements also include
reference to events or conditions that will, would, may, could or
should occur, including, without limitation, the intended use of
proceeds. These forward-looking statements are necessarily based upon a
number of estimates and assumptions that, while based on management's
expectations and considered reasonable at the time they are made, are
inherently subject to a variety of risks and uncertainties which could
cause actual events or results to differ materially from those
reflected in the forward-looking statements, including, without
limitation: the risk that the anticipated effects of the equity
financing may not result in the outcomes predicted by management,
uncertainties related to raising sufficient financing to fund planned
work in a timely manner and on acceptable terms; changes in planned
work resulting from logistical, technical or other factors; the
possibility that results of work will not fulfill
projections/expectations and realize the perceived potential of the
Company's projects; uncertainties involved in the interpretation of
drilling results and other tests and the estimation of gold resources;
risk of accidents, equipment breakdowns and labour disputes or other
unanticipated difficulties or interruptions; the possibility of
environmental issues at the Company's projects; the possibility of cost
overruns or unanticipated expenses in work programs; the need to obtain
permits and comply with environmental laws and regulations and other
government requirements; fluctuations in the price of gold and other
risks and uncertainties, including those described in the Company's
current Annual Information Form filed on SEDAR at www.sedar.com. As a
result, readers are cautioned not to place undue reliance on these
forward-looking statements. The forward-looking statements contained in
this news release are made as of the date of this release. Unless
required by law, Marlin has no intention to and assumes no obligation
to update or revise any forward-looking statements, whether as a result
of new information, future events or otherwise.

NOT FOR DISTRIBUTION TO U.S. NEWSWIRE SERVICES OR FOR RELEASE OR
DISSEMINATION DIRECTLY, OR INDIRECTLY, IN WHOLE OR IN PART, IN OR INTO
THE UNITED STATES



For further information:  Akiba Leisman, Executive Chairman and
Interim CEO, Marlin Gold Mining Ltd., Telephone: 203-862-7059, E-mail:
aleisman@marlingold.com

______________________________
_______________________________________________
TSX Venture closing price for MLN-V
Date: 2017/06/09
Closing Price: 0.82
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1716200020TS11716201009-06111620170612