Source	MARKET NEWS
Date	06/13/2017
Time	09:45:49 AM

Company	 Cascadero Copper Corporation
Title	Exploration 
Highlights Santa Rosa I Sampling





    CDNX Symbol: CCD











Press Release





CASCADERO CORP ("CCD-V")
- Exploration Highlights - Santa Rosa I Sampling

In February Cascadero sent geological staff to Argentina to be on
sight for the drilling of its Taron property. Due to severe weather
conditions, the drilling was delayed. It was thus decided that the
geological staff would sample, prospect and map Cascadero's, Santa Rosa
property to follow up on work done in late 2016. Drilling on the Taron
property has now finished and all samples from the 35 holes have been
delivered to Bureau Veritas' Mendoza laboratory for preparation of
pulps for shipment to the Bureau Veritas Laboratory in Vancouver for
assay. The Company will wait for the Taron results. As noted in prior
release, the Company has decided to receive all assays and data on the
Taron program to enable the preparation of an NI 43-101 Preliminary
Economic Analysis (PEA) Report.

In 2016 Cascadero Copper initiated an exploration and geochemistry
program on the Santa Rosa I property, located in Salta Province,
Argentina. Cascadero acquired a 100% interest in Santa Rosa I in 2004
and it is the only company that has worked on the property since then.
The 2016 geochem work was done to get fresh data on the property that
is known, based on previous work by Cascadero, to host gold and silver
mineralized veins. The Company recently sold a 30% interest in the
property in order to raise sufficient funds to begin work on the
property.

The Santa Rosa property under claim encompasses 2,987 hectares and
the mapping and sampling program was conducted by Cascadero's
prospectors R. Bilquist and R. Lera in 2016.  Assay work was completed
in 2017.  This new work was targeted at defining areas with large
quartz veins as well as possible concentrations of "sheeted" veins and
vein stockworks in large areas of alteration.  A total of 46 chip and
grab samples were taken for analysis. The grab samples are selected
samples and may not be representative of the mineralization on the
property. Most of these samples were taken in the northern area of the
project; an underexplored area with some single sample anomalies, while
only five samples were taken from the south area with a focus put on
reconnaissance mapping.

In general, the Santa Rosa I property can be divided into a
Northern area and a Southern area, which itself is divisible into 9
smaller showings that were sampled. Forty Six (46) samples were taken
from both areas returned a weighted average of 3.979 g/tn gold, 11.08
g/tn silver and 0.64% lead. Other base metals were very anomalous with
zinc at 0.16%, and copper at 0.379%.  The 46 assays range from .005
g/tn to 20 g/tn with the median value for gold 0.265 g/t, for lead
41.63 ppm, for silver 0.249 g/tn.

Following are excerpts from Bilquist's report:

"Geologically, the veins and vein concentrations are hosted in a
sedimentary package of rocks comprised of calcareous
sandstone-siltstone and finely laminated siltstone to mudstone.    The
siltstone to mudstone is the dominate host of the veins while the more
resistant sandstone-siltstone acts as a "trap" and conduit for the
mineralizing solutions resulting in the veins mostly being confined to
bedding.  The auriferous veins are often found within thin "envelopes"
of argillic altered material, all of which is generally within a
"regional", propylitic alteration (chlorite) halo".

Highlights of sampling of the various areas include:

Northern Area - A new zone was discovered in the northern area of
the project in the vicinity of some ancient Jesuit workings.   A
"single point" anomaly of three samples gave values of 2.09, 52.6 and
25 Au g/tn.  Follow up work with fifteen samples taken, gave results of
greater than 0.5 g/tn Au; eight of which are greater than 3 g/tn Au,
and 12 g/tn Au.   Anomalous silver values were coincident with the
higher gold values with six samples giving a range of results from 13.8
to 22.7 g/tn Ag. The program was reconnaissance in nature and the type
of sample in the Northern and Southern area are rock outcrop samples
with no clear orientation and no sample was a chip sample taken
perpendicular to the strike of the vein and the outcrop samples were
taken within veins. The average weight of all samples was 1.308 kgs
ranging from a high of 1.9 kgs to a low of 0.7 kgs and a median value
of 1.3 kgs.

Within approximately 200 metres all samples showed anomalous gold
with values ranging between 0.57 g/tn Au to highs of 17 and 20 g/tn Au.
High silver values of 15.1, 27.8 and 86.1 g/tn Ag were coincident with
the highest gold values.

Southern Area - Previous work in the southern area had defined
several relatively large areas that host highly anomalous quartz veins
and veinlets with intense argillic alteration.

Park Zone:  No samples were taken during 2016 but gold values from
historic sampling gave many "multi gram" samples with one sample
returning 49.5 g/tn Au and 70 g/tn Ag .

Spectacle Zone: No sampling was carried out in this zone in 2016
but, in historic sampling sixty nine grab and chip samples returned
thirty samples greater than 1 g/tn Au with coincidently anomalous
silver.  The highest gold numbers include seven samples greater than 30
g/tn Au with a high of 52.2 g/tn Au and 119.3 g/tn Ag at this site.

Ron Zone: No samples were taken here in 2016 and the only work
done consisted of some mapping to determine the extent of the
alteration area. In previous sampling 9 samples showed anomalous gold;
4 samples returned values of 3.10, 9.65, 8.25 and 8.99 g/tn Au.

JB Zone:  The JB Zone covers a fairly large area where thirty
eight samples with highly anomalous gold were taken on previous
programs.  Of these samples six were less than 1 g/tn Au, 14 samples
were greater than 10 g/tn  Au g/tn and 7 were greater than 30 g/tn Au
with the high being 39.6 g/tn Au. Ag samples were generally anomalous
with the highest being 139.5 g/tn Ag.  In 2016, work consisted
primarily of geological mapping with only one sample being taken which
returned values of 16.2 g/tn Au.

Subzone 4a:  This area is in the extreme north of the JB Zone.
Six samples, all anomalous in gold, were taken from this location on
previous programs. These samples returned values of 2.3, 4.3, 3.2, 3.5,
1.12 g/t Au and 5.7 g/tn Ag.

Subzone 4b: This area, approximately 240 by 250 metres is in the
south west of the JB Zone and has very anomalous gold values from
eighteen samples assaying greater than 1 g/tn Au., 14 of these assayed
greater than 10 g/tn Au and 8 samples exceeded 31 g/tn Au. The highest
sample assayed 39.6 g/tn Au and one sample assayed, returned 16.2 Au
g/tn from the 2016 program.

AL 87 Zone:  The "Discovery" sample for the AL87 Zone, taken from
a large quartz vein in argillic altered siltstone-mudstone assayed
88.597 g/tn Au with 86.6 g/tn Ag. Two areas for follow up in this
region have been delineated so far and occur to the north and south
along the same trend as the AL87 Vein.

Subzone 5a:  The first area includes the AL87 Vein and extends
approximately 200 metres to the south of the Discovery sample.  This
entire zone measures about 200 metres by 275 and includes a number of
samples from the AL 87 vein system.  In this area historic sampling
included 1 sample with a value of 1.325 g/tn Au and 4 samples which
returned values of 44.2, 0.7, 0.65 and 15.6 g/tn Au.  Samples taken in
2016 program included values of (0.005, 5.67, 15.6, and 15.586 g/tn Au.


Subzone 5b:  The second prospective area within the AL 87 Vein
zone covers an area approximately 140 by 260 metres.  No samples were
taken during 2016 but during previous programs 15 samples were taken.
8 of these samples returned values of 1.89, 2.23, 11.08, 5.76, 3.69,
10, 32.55 and 18.59 g/tn Au. The two highest silver values were 46.3
and 54.9 g/tn Ag.

All samples were prepared at the Bureau Veritas (BV) Laboratory in
Mendoza, Argentina and then assayed by BV's facility in Vancouver,
Canada. Assay methods included BV's Multi Acid (MA) 250 procedure, with
gold by Fire Assay (FA) 450, with those samples exceeding 10 g/tn Au
being processed by BV's FA 550.

The Company has now completed a second and much larger sampling
and mapping program on Santa Rosa, consisting 275 rock samples which
include some areas that were chip sampled.  Results of this work are
being compiled and will be the subject of a release, shortly.

The Chairman, Bill McWilliam says, "The Company is very excited
about the Santa Rosa results as gold and silver values occur in outcrop
over the majority of the system's seven (7) kilometre strike length.
Santa Rosa presents an excellent exploration target that has a
combination of good grades of gold and silver that are present in a
coherent system that has size potential."

This release and its technical content has been read and approved
by Dr. David Trueman, Ph.D., P.Geo who is a director of the Company and
is a qualified person acting for the Company.

Bill McWilliam
Chairman
Email = bill@cascadero.com
O = 604.924.5504
C = 604.999.0391

Neither the TSX Venture Exchange nor its Regulation Service
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release
______________________________________
_______________________________________________
TSX Venture closing price for CCD-V
Date: 2017/06/12
Closing Price: 0.12
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1716300042TS11716302061-09450020170613