Source	Marketwire
Date	06/14/2017
Time	04:01:03 AM

Company	 TERRAX MINERALS INC.
Title	TerraX extends strike at Sam Otto Zone from 350 m to 750 m and depth to 
300 m; highlights include 123.5 m @ 0.59 g/t Au, inclusive of 25.07 m @ 1.38 
g/t Au





    CDNX Symbol: TXR











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: TerraX Minerals Inc.

TSX VENTURE SYMBOL: TXR
FRANKFURT SYMBOL: TX0
OTC PINK SYMBOL: TRXXF

June 14, 2017

TerraX extends strike at Sam Otto Zone from 350 m to 750 m and depth to 300 m; 
highlights include 123.5 m @ 0.59 g/t Au, inclusive of 25.07 m @ 1.38 g/t Au


VANCOUVER, BRITISH COLUMBIA--(Marketwired - June 14, 2017) - TerraX Minerals 
Inc. (TSX VENTURE:TXR)(FRANKFURT:TX0)(OTC PINK:TRXXF) is pleased to announce 
the final assay results from the 2017 winter drill program at the Yellowknife 
City Gold Project ("YCG") in the Northwest Territories. Included in the assays 
reported today are 9 holes (3,713 m) at Sam Otto, located at the Northbelt 
property, that have more than doubled the strike length, intersected multiple 
zones of mineralization parallel to the main system, and extended the depth of 
gold mineralization to greater than 300 metres. Highlights include:

/T/

--  123.50 m @ 0.59 g/t Au including 25.07 m @ 1.38 g/t Au in hole TSO17-026
--  143.00 m @ 0.48 g/t Au including 34.50 m @ 1.10 g/t Au in hole TSO17-028
--  97.17 m @ 0.45 g/t Au including 24.00 m @ 1.15 g/t Au in hole TSO17-031
--  77.50 m @ 0.51 g/t Au including 23.75 m @ 1.02 g/t Au in hole TSO17-023

/T/

The drilling at Sam Otto also intersected multiple narrower horizons parallel 
to the main Sam Otto structure with significant zones of gold mineralization, 
particularly in the hanging wall of the Main Zone. These include:

/T/

--  5.50 m @ 1.29 g/t Au in hole TSO17-021
--  5.80 m @ 0.98 g/t Au in hole TSO17-023
--  8.00 m @ 1.07 g/t Au in hole TSO17-024
--  6.55 m @ 2.31 g/t Au in hole TSO17-025
--  5.05 m @ 1.51 g/t Au in hole TSO17-028
--  2.00 m @ 2.91 g/t Au in hole TSO17-031

/T/

Sam Otto is considered a bulk tonnage, low grade target with very uniform grade 
distribution across the zone, however some intersections encountered higher 
grade zones including:

/T/

--  7.17 m @ 3.24 g/t Au in hole TSO17-031
--  1.80 m @ 5.07 g/t Au in hole TSO17-027a

/T/

Joseph Campbell, CEO of TerraX, stated, "The consistency of wide gold 
intersections at Sam Otto along the north-south strike of 750 metres and to a 
depth of 300 metres confirms the existence of a bulk tonnage target with 
considerable upside potential. Open in all directions, Sam Otto also hosts the 
Dave's Pond structure of classic high grade lode gold targets 300 metres to the 
west and high grade zones at Mispickel, 1 km to the northeast. We believe Sam 
Otto has potential to host a large, high grade deposit similar to the past 
producing Con mine to the south. This area is a priority target for generating 
future mineral resources."

/T/

---------------------------------------------------------------------------
Sam Otto Zone
---------------------------------------------------------------------------
Drill
Hole   Dip Azimuth   UTM Location            From      To  Interval     Au
-----------------
Easting Northing           (m)     (m)       (m)    g/t
---------------------------------------------------------------------------
TSO17-  -50     270  639856  6944994
021                                         83.70   89.20      5.50   1.29
---------------------------------------
and  145.00  162.90     17.90   1.19
---------------------------------------
incl.  155.50  158.80      3.30   2.33
---------------------------------------------------------------------------

---------------------------------------------------------------------------
TSO17-  -50     270  639765  6944456
022a                                        58.00  123.50     65.50   0.46
---------------------------------------
incl.   83.00   98.24     15.24   1.02
---------------------------------------
incl.   92.00   95.25      3.25   2.83
---------------------------------------------------------------------------

---------------------------------------------------------------------------
TSO17-  -50     270  639823  6944685
023                                          4.20   10.00      5.80   0.98
---------------------------------------
and   82.00  159.50     77.50   0.51
---------------------------------------
incl.  111.35  135.10     23.75   1.02
---------------------------------------
incl.  111.35  116.50      5.15   1.81
---------------------------------------
incl.  126.60  135.10      8.50   1.51
---------------------------------------------------------------------------

---------------------------------------------------------------------------
TSO17-  -55     270  639849  6944694
024                                         50.00   58.00      8.00   1.07
---------------------------------------
and  119.00  197.50     78.50   0.42
---------------------------------------
incl.  170.00  180.50     10.50   1.17
---------------------------------------------------------------------------

---------------------------------------------------------------------------
TSO17-  -45     270  639860  6944902
025                                        114.50  144.00     29.50   0.78
---------------------------------------
incl.  128.45  135.00      6.55   2.31
---------------------------------------
and  157.00  175.50     18.50   0.56
---------------------------------------
incl.  161.96  165.57      3.61   2.09
---------------------------------------------------------------------------

---------------------------------------------------------------------------
TSO17-  -65     270  639904  6944604
026                                        205.00  328.50    123.50   0.59
---------------------------------------
incl.  258.50  271.09     12.59   1.33
---------------------------------------
incl.  265.00  271.09      6.09   2.11
---------------------------------------
and
incl.  289.93  315.00     25.07   1.38
---------------------------------------
incl.  300.00  310.81     10.81   2.19
---------------------------------------------------------------------------

---------------------------------------------------------------------------
TSO17-  -65     270  639899  6944551
027a                                       192.00  197.00      5.00   1.95
---------------------------------------
and  308.60  344.60     36.00   0.57
---------------------------------------
incl.  310.00  312.00      2.00   2.68
---------------------------------------
and
incl.  331.15  337.15      6.00   1.03
---------------------------------------------------------------------------
TSO17-  -58     270  639861  6944800
028                                         43.00   55.02     12.02   0.75
---------------------------------------
incl.   50.00   52.70      2.70   2.14
---------------------------------------
and   94.00  237.00    143.00   0.48
---------------------------------------
incl.  107.50  142.00     34.50   1.10
---------------------------------------
incl.  130.88  137.88      7.00   2.07
---------------------------------------------------------------------------
TSO17-  -50     270  639858  6944852
031                                         59.00   61.00      2.00   2.91
---------------------------------------
and   90.50  187.67     97.17   0.45
---------------------------------------
incl.  119.00  143.00     24.00   1.15
---------------------------------------
incl.  135.00  142.17      7.17   3.24
---------------------------------------------------------------------------

/T/

The Sam Otto zone includes the Dave's Pond structure, where 2 holes totaling 
804 metres intersected 24.52 m @ 1.60 g/t Au including 6.05 m @ 3.52 g/t Au in 
the higher grade core in hole TSO17-029 and 2.50 m @ 1.47 g/t Au in hole 
TSO17-030. These are infill holes between TSO16-005 (2.40 m @ 9.89 g/t Au 
reported Jan11, 2017) and TSO17-019 (1.90 m @ 13.96 g/t Au reported May 2, 
2017) and confirm the excellent continuity of the Dave's Pond Structure over 
400 metres of strike and 150 metres of depth, with the mineralized zone 
remaining open in both directions.

/T/

----------------------------------------------------------------------------
Dave's Pond Structure
----------------------------------------------------------------------------
Drill
Hole   Dip Azimuth   UTM Location             From      To  Interval     Au
------------------
Easting  Northing           (m)     (m)       (m)    g/t
----------------------------------------------------------------------------
TSO17-  -50     270  639611   6945103
029                                         101.30  125.82     24.52   1.60
---------------------------------------
incl.  101.30  104.30      3.00   3.20
---------------------------------------
and  116.25  122.30      6.05   3.52
---------------------------------------
incl.  119.30  122.30      3.00   5.78
----------------------------------------------------------------------------

----------------------------------------------------------------------------
TSO17-  -50     270  639664   6945119
030                                          22.50   24.00      1.50   0.91
---------------------------------------
and   46.92   47.70      0.78   1.07
---------------------------------------
and  145.25  147.75      2.50   1.47
----------------------------------------------------------------------------

/T/

All holes were drilled approximately normal to projected strike and dip of the 
zones of mineralization and are interpreted to be 75-95% of true thickness. A 
drill map showing the location of the drill holes reported above from the Sam 
Otto area, along with a cross section and long section, are available by 
clicking here.

Assay results were also received from our Banting Lake target (3 holes totaling 
698 metres) on the Northbelt property. Results from the three drill holes were 
all sub gram. A single hole drilled on a due east azimuth east of the Jackson 
Lake formation encountered a mixed geology of felsic intrusives, felsic to 
intermediate volcanics and sediments, but did not intersect mineralized 
structures.

Initial drilling at our Southbelt property was comprised of 6 holes totaling 
1,535 metres. Five holes tested the southern extension of the Con structure 
from the Con Mine over approximately 850 metres of strike. All holes 
intersected the Con structure and assays were 0.49 g/t Au to 1.03 g/t Au over 
2.30 - 5.30 metre intersections. TerraX is encouraged by the demonstrated 
continuity of the Con shear and we will conduct further surface exploration 
this summer to better define potential higher grade zones along this 5 km long 
structure. Terrax was only able to drill a single hole on the New Vein 
structure at Southbelt due to an early spring breakup making drilling 
conditions unsafe. More drilling will be done on this structure in the summer. 
The single hole intersected the New Vein structure and assayed 0.65 g/t Au over 
2.47 metres. Detailed surface exploration will be carried out along this 
greater than 1.5 km structure to define controls on higher grade areas observed 
in initial surface work (up to 95 g/t Au in grabs).
For the 21 holes reported today TerraX collected 4,629 samples for assay. 
Results ranged from below detection to 9.55 g/t Au. Drill hole collar locations 
were surveyed to sub-metre accuracy. Down hole surveying (Reflex Gyro) was 
completed on all holes. TerraX inserts certified standards and blanks into the 
sample stream as a check on laboratory QC. Drill core samples are cut by 
diamond saw at TerraX's core facilities in Yellowknife. A halved core sample is 
left in the core box. The other half core is sampled and transported by TerraX 
personnel in securely sealed bags to ALS Chemex's (ALS) preparation laboratory 
in Yellowknife. After sample preparation, samples are shipped to ALS's 
Vancouver facility for gold and ICP analysis. Gold assays of greater than 3 g/t 
are re-assayed on a 30 g split by fire assay with a gravimetric finish. ALS is 
a certified and accredited laboratory service. ALS routinely inserts certified 
gold standards, blanks and pulp duplicates, and results of all QC samples are 
reported.

The technical information contained in this news release has been approved by 
Joseph Campbell, the Chief Executive Officer of TerraX, who is a Qualified 
Person as defined in "National Instrument 43-101, Standards of Disclosure for 
Mineral Projects."

About the Yellowknife City Gold Project

Yellowknife City Gold ("YCG") encompasses 418 sq km of contiguous land 
immediately north and south of the City of Yellowknife in the Northwest 
Territories. Through a series of acquisitions, TerraX controls one of the six 
major high-grade gold camps in Canada. Being within 15 km of the City of 
Yellowknife, the YCG is close to vital infrastructure, including 
transportation, service providers, hydro-electric power and skilled 
tradespeople.

The YCG lies on the prolific Yellowknife greenstone belt, covering 45 km of 
strike length along the main mineralized break in the Yellowknife gold 
district, including the southern and northern extensions of the shear system 
that hosted the high-grade Con and Giant gold mines. The project area contains 
multiple shears that are the recognized hosts for gold deposits in the 
Yellowknife gold district, with innumerable gold showings and recent high grade 
drill results that serve to indicate the project's potential as a world-class 
gold district.

For more information on the YCG project, please visit our web site at 
www.terraxminerals.com.

On behalf of the Board of Directors

"JOSEPH CAMPBELL"

Joe Campbell, CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release contains forward-looking information, which involves known 
and unknown risks, uncertainties and other factors that may cause actual events 
to differ materially from current expectation. Important factors - including 
the availability of funds, the results of financing efforts, the completion of 
due diligence and the results of exploration activities - that could cause 
actual results to differ materially from the Company's expectations are 
disclosed in the Company's documents filed from time to time on SEDAR (see 
www.sedar.com). Readers are cautioned not to place undue reliance on these 
forward-looking statements, which speak only as of the date of this press 
release. The company disclaims any intention or obligation, except to the 
extent required by law, to update or revise any forward-looking statements, 
whether as a result of new information, future events or otherwise.

- 30 -

CONTACT INFO:

TerraX Minerals Inc.
Samuel Vella
Manager of Corporate Communications
604-689-1749 / Toll-Free: 1-855-737-2684
svella@terraxminerals.com
www.terraxminerals.com

or

Paradox Public Relations Inc.
514-341-0408
Toll-Free: 1-866-460-0408
info@paradox-pr.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=594950389