Source	MARKET NEWS
Date	06/14/2017
Time	06:09:54 AM

Company	 Terrax Minerals Inc.
Title	Extends 
Strike At Sam Otto Zone From 350 M To 75





    CDNX Symbol: TXR











Press Release





TERRAX MINERALS INC ("TXR-V;TRXXF-0")
- Extends Strike At Sam Otto Zone From 350 M To 750 M And
- Depth To 300 M; Highlights Include 123.5 M @ 0.59 G/t Au, Inclusive
- Of 25.07 M @ 1.38 G/t Au

TerraX Minerals Inc. is pleased to announce the final assay results
from the 2017 winter drill program at the Yellowknife City Gold Project
("YCG") in the Northwest Territories. Included in the assays reported
are 9 holes (3,713 m) at Sam Otto, located at the Northbelt property,
that have more than doubled the strike length, intersected multiple
zones of mineralization parallel to the main system, and extended the
depth of gold mineralization to greater than 300 metres. Highlights
include:

//st

* 123.50 m @ 0.59 g/t Auincluding 25.07 m @ 1.38 g/t Au in hole TSO17-026
* 143.00 m @ 0.48 g/t Auincluding 34.50 m @ 1.10 g/t Au in hole TSO17-028
* 97.17 m @ 0.45 g/t Au including 24.00 m @ 1.15 g/t Au in hole TSO17-031
* 77.50 m @ 0.51 g/t Auincluding 23.75 m @ 1.02 g/t Au in hole TSO17-023

//et

The drilling at Sam Otto also intersected multiple narrower
horizons parallel to the main Sam Otto structure with significant zones
of gold mineralization, particularly in the hanging wall of the Main
Zone. These include:

//st

* 5.50 m @ 1.29 g/t Auin hole TSO17-021
* 5.80 m @ 0.98 g/t Auin hole TSO17-023
* 8.00 m @ 1.07 g/t Au in hole TSO17-024
* 6.55 m @ 2.31 g/t Au in hole TSO17-025
* 5.05 m @ 1.51 g/t Au in hole TSO17-028
* 2.00 m @ 2.91 g/t Au in hole TSO17-031

//et

Sam Otto is considered a bulk tonnage, low grade target with very
uniform grade distribution across the zone, however some intersections
encountered higher grade zones including:

//st

* 7.17 m @ 3.24 g/t Au in hole TSO17-031
* 1.80 m @ 5.07 g/t Auin hole TSO17-027a

//et

Joseph Campbell, CEO of TerraX, stated, "The consistency of wide
gold intersections at Sam Otto along the north-south strike of 750
metres and to a depth of 300 metres confirms the existence of a bulk
tonnage target with considerable upside potential. Open in all
directions, Sam Otto also hosts the Dave's Pond structure of classic
high grade lode gold targets 300 metres to the west and high grade
zones at Mispickel, 1 km to the northeast. We believe Sam Otto has
potential to host a large, high grade deposit similar to the past
producing Con mine to the south. This area is a priority target for
generating future mineral resources."

//st

Sam Otto Zone

Drill Hole Dip Azimuth   UTM Location From  To     Interval Au

Easting Northing   (m)   (m)    (m)      g/t

TSO17-021  -50 270 639856  6944994   83.70  89.20  5.50     1.29

and     145.00 162.90 17.90    1.19

incl.   155.50 158.80 3.30     2.33

TSO17-022a -50 270 639765  6944456   58.00  123.50 65.50    0.46

incl.   83.00  98.24  15.24    1.02

incl.   92.00  95.25  3.25     2.83

TSO17-023  -50 270 639823  6944685   4.20   10.00  5.80     0.98

and     82.00  159.50 77.50    0.51

incl.   111.35 135.10 23.75    1.02

incl.   111.35 116.50 5.15     1.81

incl.   126.60 135.10 8.50     1.51

TSO17-024  -55 270 639849  6944694   50.00  58.00  8.00     1.07

and     119.00 197.50 78.50    0.42

incl.   170.00 180.50 10.50    1.17

TSO17-025  -45 270 639860  6944902   114.50 144.00 29.50    0.78

incl.   128.45 135.00 6.55     2.31

and     157.00 175.50 18.50    0.56

incl.   161.96 165.57 3.61     2.09

TSO17-026  -65 270 639904  6944604   205.00 328.50 123.50   0.59

incl.   258.50 271.09 12.59    1.33

incl.   265.00 271.09 6.09     2.11

and     289.93 315.00 25.07    1.38
incl.

incl.   300.00 310.81 10.81    2.19

TSO17-027a -65 270 639899  6944551   192.00 197.00 5.00     1.95

and     308.60 344.60 36.00    0.57

incl.   310.00 312.00 2.00     2.68

and     331.15 337.15 6.00     1.03
incl.

TSO17-028  -58 270 639861  6944800   43.00  55.02  12.02    0.75

incl.   50.00  52.70  2.70     2.14

and     94.00  237.00 143.00   0.48

incl.   107.50 142.00 34.50    1.10

incl.   130.88 137.88 7.00     2.07

TSO17-031  -50 270 639858  6944852   59.00  61.00  2.00     2.91

and     90.50  187.67 97.17    0.45

incl.   119.00 143.00 24.00    1.15

incl.   135.00 142.17 7.17     3.24

//et

The Sam Otto zone includes the Dave's Pond structure, where 2 holes
totaling 804 metres intersected 24.52 m @ 1.60 g/t Auincluding 6.05 m @
3.52 g/t Au in the higher grade core in hole TSO17-029 and 2.50 m @
1.47 g/t Auin hole TSO17-030. These are infill holes between TSO16-005
(2.40 m @ 9.89 g/t Au reported Jan11, 2017) and TSO17-019 (1.90 m @
13.96 g/t Au reported May 2, 2017) and confirm the excellent continuity
of the Dave's Pond Structure over 400 metres of strike and 150 metres
of depth, with the mineralized zone remaining open in both directions.

//st

Dave's Pond Structure

Drill Hole Dip Azimuth   UTM Location From  To     Interval Au

Easting Northing   (m)   (m)    (m)      g/t

TSO17-029 -50  270 639611  6945103   101.30 125.82 24.52    1.60

incl.  101.30 104.30 3.00     3.20

and    116.25 122.30 6.05     3.52

incl.  119.30 122.30 3.00     5.78

TSO17-030 -50  270 639664  6945119   22.50  24.00  1.50     0.91

and    46.92  47.70  0.78     1.07

and    145.25 147.75 2.50     1.47

//et

All holes were drilled approximately normal to projected strike and
dip of the zones of mineralization and are interpreted to be 75-95% of
true thickness. A drill map showing the location of the drill holes
reported above from the Sam Otto area, along with a cross section and
long section, are available by clicking here.

Assay results were also received from our Banting Lake target (3
holes totaling 698 metres) on the Northbelt property. Results from the
three drill holes were all sub gram. A single hole drilled on a due
east azimuth east of the Jackson Lake formation encountered a mixed
geology of felsic intrusives, felsic to intermediate volcanics and
sediments, but did not intersect mineralized structures.

Initial drilling at our Southbelt property was comprised of 6
holes totaling 1,535 metres. Five holes tested the southern extension
of the Con structure from the Con Mine over approximately 850 metres of
strike. All holes intersected the Con structure and assays were 0.49
g/t Au to 1.03 g/t Au over 2.30 - 5.30 metre intersections. TerraX is
encouraged by the demonstrated continuity of the Con shear and we will
conduct further surface exploration this summer to better define
potential higher grade zones along this 5 km long structure. Terrax was
only able to drill a single hole on the New Vein structure at Southbelt
due to an early spring breakup making drilling conditions unsafe. More
drilling will be done on this structure in the summer. The single hole
intersected the New Vein structure and assayed 0.65 g/t Au over 2.47
metres. Detailed surface exploration will be carried out along this
)1.5 km structure to define controls on higher grade areas observed in
initial surface work (up to 95 g/t Au in grabs).

For the 21 holes reported TerraX collected 4,629 samples for
assay. Results ranged from below detection to 9.55 g/t Au. Drill hole
collar locations were surveyed to sub-metre accuracy. Down hole
surveying (Reflex Gyro) was completed on all holes. TerraX inserts
certified standards and blanks into the sample stream as a check on
laboratory QC. Drill core samples are cut by diamond saw at TerraX's
core facilities in Yellowknife. A halved core sample is left in the
core box. The other half core is sampled and transported by TerraX
personnel in securely sealed bags to ALS Chemex's (ALS) preparation
laboratory in Yellowknife. After sample preparation, samples are
shipped to ALS's Vancouver facility for gold and ICP analysis. Gold
assays of )3 g/t are re-assayed on a 30 g split by fire assay with a
gravimetric finish. ALS is a certified and accredited laboratory
service. ALS routinely inserts certified gold standards, blanks and
pulp duplicates, and results of all QC samples are reported.

The technical information contained in this release has been
approved by Joseph Campbell, the Chief Executive Officer of TerraX, who
is a Qualified Person as defined in "National Instrument 43-101,
Standards of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

Yellowknife City Gold ("YCG") encompasses 418 sq km of contiguous
land immediately north and south of the City of Yellowknife in the
Northwest Territories. Through a series of acquisitions, TerraX
controls one of the six major high-grade gold camps in Canada. Being
within 15 km of the City of Yellowknife, the YCG is close to vital
infrastructure, including transportation, service providers,
hydro-electric power and skilled tradespeople.

The YCG lies on the prolific Yellowknife greenstone belt, covering
45 km of strike length along the main mineralized break in the
Yellowknife gold district, including the southern and northern
extensions of the shear system that hosted the high-grade Con and Giant
gold mines. The project area contains multiple shears that are the
recognized hosts for gold deposits in the Yellowknife gold district,
with innumerable gold showings and recent high grade drill results that
serve to indicate the project's potential as a world-class gold
district.

For more information on the YCG project, please visit our web site
at www.terraxminerals.com.

On behalf of the Board of Directors

"JOSEPH CAMPBELL"

Joe Campbell, CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This release contains forward-looking information, which involves
known and unknown risks, uncertainties and other factors that may cause
actual events to differ materially from current expectation. Important
factors - including the availability of funds, the results of financing
efforts, the completion of due diligence and the results of exploration
activities - that could cause actual results to differ materially from
the Company's expectations are disclosed in the Company's documents
filed from time to time on SEDAR (see www.sedar.com). Readers are
cautioned not to place undue reliance on these forward-looking
statements, which speak only as of the date of this press release. The
company disclaims any intention or obligation, except to the extent
required by law, to update or revise any forward-looking statements,
whether as a result of new information, future events or otherwise.

Contact Information:

TerraX Minerals Inc.
Samuel Vella
Manager of Corporate Communications
604-689-1749 / Toll-Free: 1-855-737-2684
svella@terraxminerals.com
www.terraxminerals.com

Paradox Public Relations Inc.
514-341-0408
Toll-Free: 1-866-460-0408
info@paradox-pr.ca
______________________________
_______________________________________________
TSX Venture closing price for TXR-V
Date: 2017/06/13
Closing Price: 0.55
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1716400015TS11716401064-06072220170614


[200/News Release]TXRVTERRAX MINERALS INCJUN 14 2017  06:07 AMExtends 
Strike At Sam Otto Zone From 350 M To 750 M And Depth To 300M; Highlights 
Include 123.5 M @ 0.59 G/t Au, Inclusive Of 25.07 M @1.38 G/t Au --->@NEWS 
RELEASE
TERRAX MINERALS INC ("TXR-V;TRXXF-0")
- Extends Strike At Sam Otto Zone From 350 M To 750 M And
- Depth To 300 M; Highlights Include 123.5 M @ 0.59 G/t Au, Inclusive
- Of 25.07 M @ 1.38 G/t Au

TerraX Minerals Inc. is pleased to announce the final assay results
from the 2017 winter drill program at the Yellowknife City Gold Project
("YCG") in the Northwest Territories. Included in the assays reported
are 9 holes (3,713 m) at Sam Otto, located at the Northbelt property,
that have more than doubled the strike length, intersected multiple
zones of mineralization parallel to the main system, and extended the
depth of gold mineralization to greater than 300 metres. Highlights
include:

//st

* 123.50 m @ 0.59 g/t Auincluding 25.07 m @ 1.38 g/t Au in hole TSO17-026
* 143.00 m @ 0.48 g/t Auincluding 34.50 m @ 1.10 g/t Au in hole TSO17-028
* 97.17 m @ 0.45 g/t Au including 24.00 m @ 1.15 g/t Au in hole TSO17-031
* 77.50 m @ 0.51 g/t Auincluding 23.75 m @ 1.02 g/t Au in hole TSO17-023

//et

The drilling at Sam Otto also intersected multiple narrower
horizons parallel to the main Sam Otto structure with significant zones
of gold mineralization, particularly in the hanging wall of the Main
Zone. These include:

//st

* 5.50 m @ 1.29 g/t Auin hole TSO17-021
* 5.80 m @ 0.98 g/t Auin hole TSO17-023
* 8.00 m @ 1.07 g/t Au in hole TSO17-024
* 6.55 m @ 2.31 g/t Au in hole TSO17-025
* 5.05 m @ 1.51 g/t Au in hole TSO17-028
* 2.00 m @ 2.91 g/t Au in hole TSO17-031

//et

Sam Otto is considered a bulk tonnage, low grade target with very
uniform grade distribution across the zone, however some intersections
encountered higher grade zones including:

//st

* 7.17 m @ 3.24 g/t Au in hole TSO17-031
* 1.80 m @ 5.07 g/t Auin hole TSO17-027a

//et

Joseph Campbell, CEO of TerraX, stated, "The consistency of wide
gold intersections at Sam Otto along the north-south strike of 750
metres and to a depth of 300 metres confirms the existence of a bulk
tonnage target with considerable upside potential. Open in all
directions, Sam Otto also hosts the Dave's Pond structure of classic
high grade lode gold targets 300 metres to the west and high grade
zones at Mispickel, 1 km to the northeast. We believe Sam Otto has
potential to host a large, high grade deposit similar to the past
producing Con mine to the south. This area is a priority target for
generating future mineral resources."

//st

Sam Otto Zone

Drill Hole Dip Azimuth   UTM Location From  To     Interval Au

Easting Northing   (m)   (m)    (m)      g/t

TSO17-021  -50 270 639856  6944994   83.70  89.20  5.50     1.29

and     145.00 162.90 17.90    1.19

incl.   155.50 158.80 3.30     2.33

TSO17-022a -50 270 639765  6944456   58.00  123.50 65.50    0.46

incl.   83.00  98.24  15.24    1.02

incl.   92.00  95.25  3.25     2.83

TSO17-023  -50 270 639823  6944685   4.20   10.00  5.80     0.98

and     82.00  159.50 77.50    0.51

incl.   111.35 135.10 23.75    1.02

incl.   111.35 116.50 5.15     1.81

incl.   126.60 135.10 8.50     1.51

TSO17-024  -55 270 639849  6944694   50.00  58.00  8.00     1.07

and     119.00 197.50 78.50    0.42

incl.   170.00 180.50 10.50    1.17

TSO17-025  -45 270 639860  6944902   114.50 144.00 29.50    0.78

incl.   128.45 135.00 6.55     2.31

and     157.00 175.50 18.50    0.56

incl.   161.96 165.57 3.61     2.09

TSO17-026  -65 270 639904  6944604   205.00 328.50 123.50   0.59

incl.   258.50 271.09 12.59    1.33

incl.   265.00 271.09 6.09     2.11

and     289.93 315.00 25.07    1.38
incl.

incl.   300.00 310.81 10.81    2.19

TSO17-027a -65 270 639899  6944551   192.00 197.00 5.00     1.95

and     308.60 344.60 36.00    0.57

incl.   310.00 312.00 2.00     2.68

and     331.15 337.15 6.00     1.03
incl.

TSO17-028  -58 270 639861  6944800   43.00  55.02  12.02    0.75

incl.   50.00  52.70  2.70     2.14

and     94.00  237.00 143.00   0.48

incl.   107.50 142.00 34.50    1.10

incl.   130.88 137.88 7.00     2.07

TSO17-031  -50 270 639858  6944852   59.00  61.00  2.00     2.91

and     90.50  187.67 97.17    0.45

incl.   119.00 143.00 24.00    1.15

incl.   135.00 142.17 7.17     3.24

//et

The Sam Otto zone includes the Dave's Pond structure, where 2 holes
totaling 804 metres intersected 24.52 m @ 1.60 g/t Auincluding 6.05 m @
3.52 g/t Au in the higher grade core in hole TSO17-029 and 2.50 m @
1.47 g/t Auin hole TSO17-030. These are infill holes between TSO16-005
(2.40 m @ 9.89 g/t Au reported Jan11, 2017) and TSO17-019 (1.90 m @
13.96 g/t Au reported May 2, 2017) and confirm the excellent continuity
of the Dave's Pond Structure over 400 metres of strike and 150 metres
of depth, with the mineralized zone remaining open in both directions.

//st

Dave's Pond Structure

Drill Hole Dip Azimuth   UTM Location From  To     Interval Au

Easting Northing   (m)   (m)    (m)      g/t

TSO17-029 -50  270 639611  6945103   101.30 125.82 24.52    1.60

incl.  101.30 104.30 3.00     3.20

and    116.25 122.30 6.05     3.52

incl.  119.30 122.30 3.00     5.78

TSO17-030 -50  270 639664  6945119   22.50  24.00  1.50     0.91

and    46.92  47.70  0.78     1.07

and    145.25 147.75 2.50     1.47

//et

All holes were drilled approximately normal to projected strike and
dip of the zones of mineralization and are interpreted to be 75-95% of
true thickness. A drill map showing the location of the drill holes
reported above from the Sam Otto area, along with a cross section and
long section, are available by clicking here.

Assay results were also received from our Banting Lake target (3
holes totaling 698 metres) on the Northbelt property. Results from the
three drill holes were all sub gram. A single hole drilled on a due
east azimuth east of the Jackson Lake formation encountered a mixed
geology of felsic intrusives, felsic to intermediate volcanics and
sediments, but did not intersect mineralized structures.

Initial drilling at our Southbelt property was comprised of 6
holes totaling 1,535 metres. Five holes tested the southern extension
of the Con structure from the Con Mine over approximately 850 metres of
strike. All holes intersected the Con structure and assays were 0.49
g/t Au to 1.03 g/t Au over 2.30 - 5.30 metre intersections. TerraX is
encouraged by the demonstrated continuity of the Con shear and we will
conduct further surface exploration this summer to better define
potential higher grade zones along this 5 km long structure. Terrax was
only able to drill a single hole on the New Vein structure at Southbelt
due to an early spring breakup making drilling conditions unsafe. More
drilling will be done on this structure in the summer. The single hole
intersected the New Vein structure and assayed 0.65 g/t Au over 2.47
metres. Detailed surface exploration will be carried out along this
)1.5 km structure to define controls on higher grade areas observed in
initial surface work (up to 95 g/t Au in grabs).

For the 21 holes reported TerraX collected 4,629 samples for
assay. Results ranged from below detection to 9.55 g/t Au. Drill hole
collar locations were surveyed to sub-metre accuracy. Down hole
surveying (Reflex Gyro) was completed on all holes. TerraX inserts
certified standards and blanks into the sample stream as a check on
laboratory QC. Drill core samples are cut by diamond saw at TerraX's
core facilities in Yellowknife. A halved core sample is left in the
core box. The other half core is sampled and transported by TerraX
personnel in securely sealed bags to ALS Chemex's (ALS) preparation
laboratory in Yellowknife. After sample preparation, samples are
shipped to ALS's Vancouver facility for gold and ICP analysis. Gold
assays of )3 g/t are re-assayed on a 30 g split by fire assay with a
gravimetric finish. ALS is a certified and accredited laboratory
service. ALS routinely inserts certified gold standards, blanks and
pulp duplicates, and results of all QC samples are reported.

The technical information contained in this release has been
approved by Joseph Campbell, the Chief Executive Officer of TerraX, who
is a Qualified Person as defined in "National Instrument 43-101,
Standards of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

Yellowknife City Gold ("YCG") encompasses 418 sq km of contiguous
land immediately north and south of the City of Yellowknife in the
Northwest Territories. Through a series of acquisitions, TerraX
controls one of the six major high-grade gold camps in Canada. Being
within 15 km of the City of Yellowknife, the YCG is close to vital
infrastructure, including transportation, service providers,
hydro-electric power and skilled tradespeople.

The YCG lies on the prolific Yellowknife greenstone belt, covering
45 km of strike length along the main mineralized break in the
Yellowknife gold district, including the southern and northern
extensions of the shear system that hosted the high-grade Con and Giant
gold mines. The project area contains multiple shears that are the
recognized hosts for gold deposits in the Yellowknife gold district,
with innumerable gold showings and recent high grade drill results that
serve to indicate the project's potential as a world-class gold
district.

For more information on the YCG project, please visit our web site
at www.terraxminerals.com.

On behalf of the Board of Directors

"JOSEPH CAMPBELL"

Joe Campbell, CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This release contains forward-looking information, which involves
known and unknown risks, uncertainties and other factors that may cause
actual events to differ materially from current expectation. Important
factors - including the availability of funds, the results of financing
efforts, the completion of due diligence and the results of exploration
activities - that could cause actual results to differ materially from
the Company's expectations are disclosed in the Company's documents
filed from time to time on SEDAR (see www.sedar.com). Readers are
cautioned not to place undue reliance on these forward-looking
statements, which speak only as of the date of this press release. The
company disclaims any intention or obligation, except to the extent
required by law, to update or revise any forward-looking statements,
whether as a result of new information, future events or otherwise.

Contact Information:

TerraX Minerals Inc.
Samuel Vella
Manager of Corporate Communications
604-689-1749 / Toll-Free: 1-855-737-2684
svella@terraxminerals.com
www.terraxminerals.com

Paradox Public Relations Inc.
514-341-0408
Toll-Free: 1-866-460-0408
info@paradox-pr.ca
______________________________
_______________________________________________
TSX Venture closing price for TXR-V
Date: 2017/06/13
Closing Price: 0.55
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1716400015TS11716401064-06072220170614