Source	MARKET NEWS
Date	06/15/2017
Time	05:10:00 AM

Company	 Algold Resources Ltd.
Title	Further 
Defines and Extends the High Grade Miner





    CDNX Symbol: ALG











Press Release





ALGOLD RESOURCES LTD ("ALG-V;ALGDF-0")
- Further Defines and Extends the High-Grade Mineralization at
- Tijirit

ALGOLD RESOURCES LTD. ("Algold" or the "Corporation") announced
more assay results from the diamond ("DDH") and reverse-circulation
("RC") drilling carried out on its Tijirit property ("Tijirit") in
Mauritania, as part of the Corporation's Phase III 25,000-meter
drilling campaign. The results continue to demonstrate the high-grade
nature of the mineralization, both near surface and at depth over the
3.4-kilometer strike length of the Eleonore zone.

Highlights

//st

* Hole T17DD011 (Eleonore Central) - 3 m @ 16.16 g/t Au, approximately 55
meters below the surface (Figure 1) (Photo)
* Hole T16RD041 (Eleonore South) - 1 m @ 36.09 g/t Au, including 0.5 m @
65.0 g/t Au approximately 126 meters below the surface and 1.25 m @
5.68
g/t Au, approximately 133 meters below the surface (Figure 2)
* Hole T17RD064 (Eleonore South) - 1.10 m @ 44.02 g/t Au, approximately
69
meters below the surface (Figure 2)
* Hole T17RD068 (Eleonore North) - 4.58 m @ 1.55 g/t Au, approximately 28
meters below the surface (Figure 3)

//et

These new results, combined with the structural and lithological
information gathered from the drill core, further increase Algold's
level of confidence with regard to the potential of the three main
Eleonore zones. All three zones remain open along strike and at depth.

In hole T17DD011 (section 8960), the shear structure hosting the
mineralization was well developed with a sub-1-g/t-Au mineralization
occurring at 63.9 meters to a 16.16 g/t Au high-grade zone at 78
meters. Visible gold was noted in the intersections corresponding to
the highest assay values.

Hole T16RD041 (section 8400) was a re-entry of an RC hole drilled
in 2016, designed to test the mineralization at depth (100 meters
vertically below hole T16RC109). Coarse visible gold was observed
within the high strain shear zone.

Hole T17RD064 (section e7730) was sited to intersect
mineralization 50 meters between RC holes T16RC133 and T16RC139 and 50
meters below ground level. An alteration halo of disseminated
pyrrhotite occurred from 62 to 73 meters down the hole. This surrounds
the main mineralized zone, which is comprised of smoky quartz veining
with associated pyrite and biotite alteration. Both coarse and
fine-grained visible gold was observed within the vein.

Hole T17RD068 (section 9800) intersected a 6.2-meter-wide shear
zone with abundant biotite and quartz stringers. No VG was noted. This
was an infill hole, drilled along strike between T16RC045 (7.45 g/t Au
over 5 m, 40 meters southwest), and T16RC088 (1.43 g/t Au over 1 m, 50
meters northeast). Hole T17RD068 served to confirm the mineralization
between the two section lines.

The Phase III 20,000-meter RC and 5,000-meter DDH drilling program
was initiated on February 1, 2017 with the objective to further
delineate the high-grade gold deposit. As of June 5, 2017, 117 RC
holes, 16 DDH and 18 RC pre-collar/diamond tails were completed for
14,944 meters of RC and 4,053 meters of diamond drilling.

As of June 5, 2017, 6,945 samples (excluding QA/QC and re-assays)
from the Phase III drilling program were sent to the SGS Bamako lab
facility for analysis. To date, the Corporation is in receipt of 5,821
RC and 772 DDH results, with assays still pending for 221 RC and 111
DDH samples (with further samples being processing in Nouakchott for
export). The Phase III drilling program remains ongoing and is expected
to be completed by the end of the second quarter 2017.

//st

Table 1: Assay Results Highlights - Phase III Drilling Program

Hole ID  Prospect   East    North   From    To      Vertical  Grade** Width
Local   Local   (m)     (m)     Depth*(m)   (g/t  ***(m)
Au)

T17RD068 Eleonore   9568    9801    44.9    49.5    28          1.55   4.58
N

T17DD011 Eleonore   9804    8962    78.0    81.0    55          16.16  3.00
C

T17RD064 Eleonore   9847    7729    73.2    74.3    69          44.02  1.10
S

T16RD041 Eleonore   10096   8402    166.0   167.0   126         36.09  1.00
S

175.3   176.5   133         5.68   1.25

T17RC076 Eleonore   10014   7679    126.0   136.0   104         1.58  10.00
S

//et

//st

*Vertical depth of intersection below RL collar.

**Weighted average grade, composite based on a minimum grade of 0.3 g/t
Au with an internal dilution of 0.005 g/t Au over 2 m and an edge grade
of 0.25 g/t Au permitted.

***Down-hole length (believed to be close to true width)

No capping of higher values has been applied.

//et

Note: Complete assay results are available on Algold's website
(www.algold.com)

Filing of a Technical ReportAlgold will filed a technical report
entitled "Tijirit Property NI 43-101 Technical Report with Resource
Estimate Update, Tijirit, Mauritania" dated June 15, 2017 (the
"Report"), which was prepared by Yann Camus, P.Eng., SGS Geostat,
Blainville, Canada an independent Qualified Person (as defined in NI
43-101). The Report supports the Corporation's disclosure in its news
release issued on May 1, 2017, entitled "Algold More Than Doubles
Inferred Mineral Resources at Tijirit, Gold Grade up by 25%". The
Report will be filed today on SEDAR (www.sedar.com) and also made
available on the Corporation's website (www.algold.com).

Quality Assurance / Quality Control (QA/QC)Analytical work for
drill core and chips, geochemical samples and rock chip samples is
being carried out at the independent SGS Laboratories Ltd. in Bamako,
Mali. The 50 g fire assay with ASS finish analytical services are
accredited by SANAS and are carried out with a quality assurance
protocol in line with ISO 17025:2005. Samples are stored at the
Corporation's field camps and put into sealed bags until delivered by a
geologist on behalf of Algold to the laboratory in Bamako, Mali, where
samples are prepared and analyzed. Until the end of 2016, samples were
analyzed at ALS's facility in Loughrea, Ireland. Beginning in 2017,
samples are analyzed at SGS Laboratory, Bamako. Samples are logged in
the tracking system, weighed, dried and finely crushed to better than
70%, passing a 2 mm (Tyler 9 mesh, US Std. No.10) screen. A split of up
to 1,000 g is taken and pulverized to better than 85%, passing a
75-micron (Tyler 200 mesh) screen, and a 50-gram split is analyzed by
fire assay with an AA finish. Anomalous samples greater than 5 g/t Au
are re-analyzed by 50 g fire assay with gravimetric finish. Selected
samples may be re-analyzed using a 1 kg cyanide leach (Bottle Roll)
using "LeachWELL" or the 1 kg screen fire assay method. Blanks,
duplicates and certified reference material (standards) are inserted to
monitor laboratory performance during the analysis.
This press release has been reviewed for accuracy and compliance
under National Instrument 43-101 by Andre Ciesielski, DSc., PGeo.,
Algold Resources Ltd Lead Consulting Geologist and Qualified Person,
and Alastair Gallaugher, C.Geo. (Chartered Geologist and Fellow of the
Geological Society of London), BSc. Geology, Algold's Exploration
Manager in Mauritania, Qualified Persons as defined by NI 43-101
Standards of Disclosure for Mineral Projects. Andre Ciesielski, Dsc.,
PGeo., has further approved the scientific and technical disclosure in
the news release.

ABOUT ALGOLDAlgold Resources Ltd is focused on the exploration and
development of gold deposits in West Africa. The board of directors and
management team are seasoned resource industry professionals with
extensive experience in the exploration and development of world-class
gold projects in Africa.

FORWARD-LOOKING INFORMATION

This press release contains and refers to forward-looking
information based on current expectations. All other statements other
than statements of historical fact included in this release are
forward-looking statements (or forward-looking information). The
Corporation's plans involve various estimates and assumptions and its
business is subject to various risks and uncertainties. For more
details on these estimates, assumptions, risks and uncertainties, see
the Corporation's most recent Management Discussion and Analysis on
file with the Canadian provincial securities regulatory authorities on
SEDAR at www.sedar.com. These forward-looking statements are made as of
the date hereof and there can be no assurance that such statements will
prove to be accurate. Forward-looking statements are subject to
significant risks and uncertainties, and actual results and future
events could differ materially from those anticipated in such
statements. Accordingly, readers should not place undue reliance on
forward-looking statements that are included herein, except in
accordance with applicable securities laws.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Algold Resources Ltd.

Internet: www.algold.com

Francois Auclair M.Sc., PGeo, President & Chief Executive Officer
E-mail: f.auclair@algold.com
TEL: +1 (514) 889 5089

Alex Ball, Executive VP, Finance and Corporate Development


























TSX Venture closing price for ALG-V
Date: 2017/06/14
Closing Price: 0.20

TEL: +1 (647) 919 2227
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1716500003TS11716500613-05073820170615