Source	MARKET NEWS
Date	06/19/2017
Time	08:07:40 AM

Company	 Riverside Resources Inc.
Title	Riverside And Centerra Complete Pitaya Target Dr





    CDNX Symbol: RRI











Press Release





Riverside And Centerra Complete Pitaya Target Drilling At The GlorGold Project 
In Sonora, Mexico --->@NEWS RELEASE
RIVERSIDE RESOURCES INC ("RRI-V;RVSDF-0")
CENTERRA GOLD INC ("CG-T;CAGDF-0")
- Riverside And Centerra Complete Pitaya Target Drilling
- At The Glor Gold Project In Sonora, Mexico

Riverside Resources Inc. ("Riverside" or the "Company") has
completed an initial nine-hole diamond core drilling program at the 4
km2 Pitaya Target within the 36 km Glor Gold Project (the "Project"),
which is being explored with funding by partner, Centerra Gold Inc.
("Centerra"). The Project hosts five key target areas and is located
approximately 8 km west of Alamos Gold's El Chanate Mine in Sonora,
Mexico. The recently completed drill program focused on the Pitaya
Target located in the north-eastern sector of the Project, which had
been defined by partner-funded soil geochemistry and induced
polarization geophysical surveys and then further investigated with
mechanical trenching and chip-channel sampling (see Company press
releases issued on February 15 and April 17, 2017).

Assay results have now been received for all nine drill-holes,
which together total 1,942 metres in length. The longest hole was 285
metres. Drill-hole GL17-002D yielded the best intersection of gold
mineralization of the campaign: 11.0 metres averaging 0.591 grams gold
per tonne (g/t Au) starting at 122 metres down the inclined drill-hole.
The highest gold value included in this assay interval is 1.415 g/t Au
over 1.0 metre of core. The other eight drill-holes intersected
sporadic thin zones of gold mineralization that generally graded less
than 0.4 g/t Au across 1.0 metre, with the best of these intercepts
being a 2.0 metre interval in GL17-004D that averaged 0.466 g/t Au.

Riverside's President and CEO, John-Mark Staude, stated: "Given
the trench sampling intervals gave disseminated gold values in the
range of 0.5-1 g/t Au at the Pitaya Target, we are surprised that this
initial drill campaign didn't manage to replicate these results. We've
been mapping and sampling the larger Glor tenement finding numerous
areas with gold and remain positive on the Project's potential. So far
we've developed five target areas and have only trenched and drilled
one. The four additional target areas will be field sampled and worked
on in the coming months to determine if another drill program will be
pursued."

Figure 1 below displays the location of the Pitaya Target in
relation to the other four target areas that remain undrilled at the
Glor Project. Figure 2 is an enlargement of the Pitaya Target area
showing the locations of drill-hole collars and surface traces with
respect to the trenches that were excavated and sampled just prior to
the commencement of drilling.

To view Figure 1: Map of the 5 Target Areas at the Glor
Project,please visit the following link:
http://media3.marketwire.com/docs/1097525_Figure1.pdf

Additional Drill Program Details:

The gold assay results for the 9-hole drilling campaign are in
general weaker than the assay results that were obtained from the
chip-channel samples collected from the trenches in the immediate area
of the Pitaya drill-holes. A possible explanation for the discrepancy
between the drilling and trench sampling results is that the extensive
mineralization sampled on surface transect in trenches Tr-01 and Tr-02
occurs in a zone of altered andesite that is exposed along an easterly
inclined dip-slope in the local topography. (Drill-hole G17-002D
appears to have perpendicularly intersected the subsurface down-dip
continuation of this zone of gold mineralization (see Figure 2)
indicating a true thickness of approximately 11 meters.

To view Figure 2: Compilation map of the north-eastern
sector of the Glor Project showing Au-in-soil anomaly, drill holes and
trenches completed at the Pitaya Target,please visit the following
link: http://media3.marketwire.com/docs/1097525_Figure2.pdf

There is a spatial relationship between gold and arsenic (As) at
the Pitaya Target, where core samples having gold concentrations
greater than 0.3 g/t Au are seen to have As contents of 5,000 ppm and
greater. The drill-hole sample containing 1.415 g/t Au showed an As
content of )10,000 ppm As. This feature is similar to other orogenic
gold systems in north-western, Sonora and indicates the district is the
type of region that could be fertile for a new gold discovery.

Although the drilling of the Pitaya target area did not produce an
economically significant discovery, much has been improved in the
understanding of controls on gold mineralization, which are now being
applied to the overall Glor Project. Project geologists are in the
field investigating other geochemical survey anomalies on the Project
with the objective of refining existing target areas and defining new
high-potential drill targets. Particular attention will be given to the
rock and soil geochemistry, structural geology, ground magnetic data
and utilizing induced polarization as a tool to refine the targets.
Fieldwork will continue to be funded by Centerra through the next
quarter and, if sufficiently prospective gold targets are generated, a
second round of drilling will possibly be completed before the end of
the year.

Qualified Person and QA/QC:

The scientific and technical data contained in this news release
pertaining to the Glor Project was reviewed and prepared under the
supervision of Locke Goldsmith, P. Eng., P. Geo., a non-independent
qualified person to Riverside Resources who is responsible for ensuring
that the geologic information provided in this news release is accurate
and acts as a "qualified person" under National Instrument 43-101
Standards of Disclosure for Mineral Projects.

All drill cores were photographed, geologically logged and then
sawed in half to provide samples for gold assaying and multi-element
ICP mass spectrometry analysis, which was done by Bureau Veritas'
laboratories in Hermosillo, Mexico and Vancouver, Canada, respectively.
A total of 1,246 core samples were analysed, with individual samples
having core lengths of 1.0 m or 3.0 m, depending on the presence or
absence of visible hydrothermal alteration. For quality assurance and
control purposes 48 non-mineralized 'blank' samples and 83 standard
samples were included with the batches of core samples that were
analysed.

About Riverside Resources Inc.:

Riverside is a well-funded prospect generator exploration company
with over $5,000,000 in the bank and a tight share structure with fewer
than 45M shares issued. Riverside leverages its 77,000 location Mexico
mineral database, highly experienced and dedicated technical team and
partnership network to acquire and develop high-potential projects. The
Company increases the chances of discovery by advancing multiple assets
simultaneously through partnerships, allowing Riverside to mitigate
risk and conserve capital. Riverside has a diverse portfolio of gold,
silver and copper properties throughout North America. Riverside has
additional properties available for option with more information
available on the Company's website at www.rivres.com.

ON BEHALF OF RIVERSIDE RESOURCES INC.

Dr. John-Mark Staude, President & CEO

Certain statements in this press release may be considered
forward-looking information. These statements can be identified by the
use of forward looking terminology (e.g., "expect"," estimates",
"intends", "anticipates", "believes", "plans"). Such information
involves known and unknown risks -- including the availability of
funds, the results of financing and exploration activities, the
interpretation of exploration results and other geological data, or
unanticipated costs and expenses and other risks identified by
Riverside in its public securities filings that may cause actual events
to differ materially from current expectations. Readers are cautioned
not to place undue reliance on these forward-looking statements, which
speak only as of the date of this press release.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.




Riverside Resources Inc.
John-Mark Staude
President & CEO
TEL: (778) 327-6671
FAX: (778) 327-6675
E-mail: info@rivres.com
Internet: www.rivres.com

Riverside Resources Inc.
Raffi Elmajian
























TSX Venture closing price for RRI-V
Date: 2017/06/16
Closing Price: 0.40

TEL: (778) 327-6671 / TF: (877) RIV-RES1
E-mail: relmajian@rivres.com
Internet: www.rivres.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1716900042TS11716901671-08061220170619