Source	MARKET NEWS
Date	06/19/2017
Time	10:52:34 AM

Company	 Newrange Gold Corp.
Title	Drills 6.1 
Meters Of 98 G/t Au, Discovers New Zo





    CDNX Symbol: NRG











Press Release





NEWRANGE GOLD CORP ("NRG-V;CMBPF-0")
- Drills 6.1 Meters Of 98 G/t Au, Discovers New Zone At Pamlico Gold
- Project, Nevada

Newrange Gold Corp. ("Newrange" or the "Company") is pleased to
report drilling results for the first 10 holes of the recently
completed 19 hole Reverse Circulation (RC) Phase I drilling program
focused on the Merritt Zone of the Pamlico gold project.

Highlights for these results:

//st

* Results from the first 10 holes were highly successful, supporting the
continuity of gold mineralization in the vicinity of the Merritt decline
(see prior news releases on underground channel sampling results by
Newrange Gold) and historic high-grade drill intercepts in the Merritt
Zone by prior operators. Work to date in the Merritt area indicate a
mineralized zone approximately 100 to 130 meters wide that is presently
open ended along strike.
* Hole P17-03 drill tested the projection of high-grade gold mineralization
east of the decline and south of the Merritt Zone intersecting 1.5 meters
of 51 grams gold per metric tonne (g/T Au).
* Holes P17-04 and P17-05 were drilled in a fan to confirm the presence of
high-grade gold mineralization and test lateral and up dip projections of
mineralization reported in historic holes PRC36, M10-04 and M10-17. Hole
P17-04 intersected 1.5 meters of near surface mineralization assaying
9.40 g/T Au. Hole P17-05 intersected 1.6 meters assaying 17.9 g/T Au.
Importantly, these holes confirm the presence of high-grade gold bearing
structures and indicate good lateral and vertical continuity of
mineralization near the surface in this area.
* Holes P17-08, 09 and 10 are interpreted to have discovered a new zone of
near surface high-grade gold mineralization approximately 50 meters south
of the end of the decline. Drilling tested favorable structural
projections beneath an area of shallow alluvial cover. Holes P17-08 and
09 were drilled from the same site and P17-10 was drilled approximately
15 meters to the northwest. P17-08 intersected a mineralized zone
averaging 13.67 g/T Au over 21.3 meters, including a higher grade
sub-zone averaging 27.8 g/T Au over 9.1 meters with a high-grade interval
averaging 84.90 g/T Au over 1.5 meters. Hole P17-09 is interpreted to
have been drilled over the top of, and sub-parallel to the structure
intersected in P17-08 and returned 9.5 g/T Au over 1.5 meters and 6.82
g/T Au over 1.5 meters. Hole P17-10 intersected 49.49 g/T Au over 12.2
meters with a higher grade sub-zone averaging 97.94 g/T Au over 6.1
metersincluding an interval of 340.9 g/T Au over 1.5 meters.

//et

Robert G. Carrington, CEO made the following comments: "These
initial results indicate that Pamlico is a unique high potential
opportunity for Newrange Gold. The extremely rich Merritt Zone where we
are focusing our initial exploration efforts right now is one of five
similar target areas, covering only 1/2 of 1% of this property and less
than 1/10 of 1% of the combined strike extent of the more than 300
known veins and mineralized structures on the property. The knowledge
gained in this area will guide future exploration for several similar
target areas elsewhere on the property including the Gold Box, Central
and Sunset Mine Zones. I look forward to the receipt of assays for the
remaining 9 holes of the Phase I Drill Program and for more information
that will come from ongoing exploration work underway at Pamlico. We
are truly excited by what we are seeing develop here."

Phase I Drill Results -- First 10 holes

//st

Hole             Inclination/Azimuth   Total      From   To    Length g/T Au
Depth(m)   (m)    (m)    (m)

P17-02           -90/0               122.0      21.3   25.9   4.6     1.91

And                                      42.7   64.0   21.3    1.27

Incl.                                    61.0   64.0   3.0     6.27

P17-03           -90/0               106.7      62.5   64.0   1.5    51.00

P17-04           -85/5               106.7      7.6    16.8   9.2     1.89

Incl.                                    9.2    10.7   1.5     9.40

P17-05           -65/5               112.8      21.3   22.8   1.5    17.90

P17-08           -85/0               106.7      30.5   51.8   21.3   13.67

Incl.                                    30.5   39.6   9.1    27.80

Incl.                                    35.1   36.6   1.5    84.90

P17-09           -50/0               122.0      16.8   50.3   33.5    1.10

Incl.                                    18.3   19.8   1.5     4.23

Incl.                                    39.6   41.1   1.5     9.50

And                                      65.6   67.1   1.5     6.82

P17-10           -85/170             61.0       18.3   19.8   1.5     6.44

And                                      25.9   38.1   12.2   49.49

Incl.                                    27.4   33.5   6.1    97.94

Incl.                                    27.4   28.9   1.5   340.90

//et

All results reported are length-weighted averages with no grade
capping applied. Lengths of drill intercepts are for the actual drilled
intercept length and may not represent true widths. Insufficient data
currently exists to estimate true width.

Exploration Guidance

The Company plans to aggressively pursue exploration at Pamlico
during the coming months.

Planned work will include:

//st

* Continuation of the ongoing program of surface and underground mapping
and sampling currently underway.
* Finalizing arrangements to complete a property-wide airborne geophysical
survey consisting of high resolution airborne magnetometry and
radiometrics.
* Selection of suitable composite sample for preliminary metallurgical
study once the Company has the results for all 19 holes of the current
Phase I drilling program.
* Finalizing plans for a large diameter PQ diamond core drilling program.
* Expanding program of RC drilling.
* Assessing potential to initiate program of bulk sampling / test mining
utilizing the existing decline and infrastructure.

//et

Terms of Reference

In this release, all references to grams per tonne (denoted g/T Au)
are grams per metric ton of 1,000 kilograms (2,204.62 pounds). All
references to ounces per ton (denoted oz/t Au) are troy ounces per
short ton of 2,000 pounds.

Quality Assurance/Quality Control

Mr. Robert G. Carrington, P. Geo, a Qualified Person as defined by
National Instrument 43-101, the President and CEO of the Company, has
reviewed, verified and approved for disclosure the technical
information contained in this news release. All drilling was by Reverse
Circulation (RC) methods using a six inch diameter center recovery bit.
All drilling was supervised by professional geologists. Drill samples
were collected on 1.5 meter intervals, and riffel split in a three
tiered jones type splitter generating an average sample weight of
approximately 4.9 kilograms per meter. Samples were then securely
delivered to Inspectorate -- Bureau Veritas in Sparks, Nevada for
sample preparation and analysis. Samples are stage crushed to 80%
passing 10 mesh. A 1,000 gram sub-sample was then split out and
pulverized to 140 mesh from which 50 gram samples were split for
analysis by fire assay (FA) with a gravimetric finish. All samples
assaying more than 10 grams are checked and re-assayed using 50 gram FA
with gravimetric finish. In addition to the QA -- QC included by the
laboratory, the Company inserts blanks, standards and certified
reference material (CRM) at a rate of not less than 1 in 30.

About Pamlico

Located 12 miles southeast of Hawthorne, Nevada, along US Highway
95, the project has excellent access and infrastructure, a mild,
year-round operating climate and strong political support from Mineral
County, one of the most pro-mining counties in the pro-mining state of
Nevada. The Pamlico project covers the historic Pamlico group of mines,
as well as the nearby Good Hope, Central, Gold Bar and Sunset mines.

Discovered about 1884, the district rapidly gained a reputation as
being one of Nevada's highest grade districts. Held by private
interests for most of its history, the property remains very
underexplored in terms of modern exploration.

About Newrange Gold Corp.

Newrange is an aggressive exploration and development company
focused on near to intermediate term production opportunities in
favorable jurisdictions including Nevada, Colorado and Colombia.
Focused on developing shareholder value through exploration and
development of key projects, the Company is committed to building
sustainable value for all stakeholders. Further information can be
found on our website at www.newrangegold.com.

Signed: "Robert G. Carrington"

President & CEO

Neither the TSX Venture Exchange nor the Investment Industry Regulatory
Organization of Canada accepts responsibility for the adequacy or accuracy
of this release.

Forward-Looking Statement:

Some of the statements in this news release contain forward-looking
information that involves inherent risk and uncertainty affecting the
business of Newrange Gold Corp. Actual results may differ materially
from those currently anticipated in such statements.

ENQUIRIES:
Sharon Hebgin
Corporate Communications
Phone: 760-898-9129
Email: info@newrangegold.com

Dave Cross
Chief Financial Officer and Corporate Secretary
Phone: 604-669-0868
Email: dcross@crossdavis.com

Website: www.newrangegold.com
______________________________
_______________________________________________
TSX Venture closing price for NRG-V
Date: 2017/06/16
Closing Price: 0.45
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1716900046TS11716902089-10495220170619