Source	Marketwire
Date	06/26/2017
Time	09:01:19 PM

Company	 ML GOLD CORP.
Title	ML Gold Reports Drilling Results at Palmetto - Northwest Zone Expanding





    CDNX Symbol: MLG











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: ML Gold Corp.

TSX VENTURE SYMBOL: MLG
FRANKFURT SYMBOL: XOVN.F

June 27, 2017

ML Gold Reports Drilling Results at Palmetto - Northwest Zone Expanding


VANCOUVER, BRITISH COLUMBIA--(Marketwired - June 27, 2017) - ML Gold Corp. (TSX 
VENTURE:MLG)(FRANKFURT:XOVN.F) ("ML Gold" or the "Company") reports results 
from an additional 4 holes of the phase I drill program at its wholly owned 
Palmetto Gold Project in Nevada, where a first ever gold resource is being 
calculated. Drilling by ML Gold has seen a high success ratio with almost all 
holes encountering significant mineralization, resulting in the extension of 
known zones well beyond historically identified limits. Mineralization in the 
Northwest and Discovery Zones remains open along strike, west and east, and at 
depth.

Further drilling in the Northwest Zone stepped out an additional 50 metres from 
ML Gold's previously reported holes and returned a wide mineralized intercept 
outlining a thick consistently mineralized horizon which remains open to the 
east and west. Drill hole PAL-17R10, the most western hole to date in the 
Northwest Zone reports 21.3 metres of 0.93 grams per tonne ("gpt") gold, 
including 7.6 metres grading 2.26 gpt. This gold mineralization is disseminated 
within the sediments and is likely related to a high grade feeder/breccia zone.

Additional drilling in the Discovery Zone ended in high grade gold 
mineralization with drill hole PAL-17R13 ending in 6.1 metres of 1.82 gpt at 
237 metres (end of hole or "EOH") below surface, leaving the zone open to 
depth. This highlights the depth potential and need for the phase II drilling 
program to further test the depth extent of mineralization. Drilling also 
confirms consistent gold mineralization surrounding the intense breccia and 
stock work zones that form the higher grade core(s) of mineralization. Past 
metallurgical studies conducted by previous operators on the Discovery Zone 
show that the material is amenable to heap leaching. Further metallurgical 
studies will be carried out as part of the phase II drilling program following 
the completion of the maiden resource estimate and 43-101 technical report on 
the Palmetto Gold Project.

The table below outlines the results from four additional holes at ML Gold's 
Palmetto Gold Project in Nevada.

/T/

----------------------------------------------------------------------------
Northwest Zone
----------------------------------------------------------------------------
Hole ID                                        Interval             Silver
Azimuth  Dip From (m) To (m)     (m)   Gold (g/t)   (g/t)
----------------------------------------------------------------------------
PAL-17R07          10     -60   182.9   196.6    15.2       0.3      8.08
----------------------------------------------------------------------------
incl.                           182.9   185.9      3       0.82      22.13
----------------------------------------------------------------------------

----------------------------------------------------------------------------
PAL-17R10           0     -65   111.3   141.7    30.5       0.7      5.21
----------------------------------------------------------------------------
incl.                           111.3   132.6    21.3      0.93      7.06
----------------------------------------------------------------------------
incl.                           120.4    128      7.6      2.26      14.7
----------------------------------------------------------------------------
175.3   190.5    15.2       0.2      2.59
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Discovery Zone
----------------------------------------------------------------------------
Hole ID                                        Interval             Silver
Azimuth  Dip From (m) To (m)     (m)   Gold (g/t)   (g/t)
----------------------------------------------------------------------------
PAL-17R11           0     -85   100.6   108.2     7.6      0.23      8.03
----------------------------------------------------------------------------
123.4   137.2    13.8      0.24      4.87
----------------------------------------------------------------------------

----------------------------------------------------------------------------
PAL-17R13           0     -90   138.7   143.3     4.6      0.34      1.49
----------------------------------------------------------------------------
166.1   208.8    42.7       0.3      7.88
----------------------------------------------------------------------------
incl.                           179.8   199.6    19.8      0.45      14.64
----------------------------------------------------------------------------
incl.                            189     192       3       1.26      5.88
----------------------------------------------------------------------------
237.7(EO
222.5    H)      15.2      0.85      2.09
----------------------------------------------------------------------------
incl.                                 237.7(EO
231.6    H)       6.1      1.82      2.98
----------------------------------------------------------------------------

/T/

Based on the highly successful phase I drilling program, ML Gold anticipates a 
phase II program to expand the existing zones and locate additional zones. 
Phase II will focus on areas north and northwest of the Discovery and Northwest 
zones along the Palmetto Gold Trend. As this trend is primarily under cover, 
the Northwest Zone was interpreted and discovered through structural analysis 
and detailed structural mapping. Similarly, new zones have been identified 
within the trend and warrant drilling in the phase II program.

Adrian Smith, President of ML Gold comments "We are grateful to everyone 
involved in this project and their hard work and support which has enabled us 
to rapidly advance the project to a resource stage. We look forward to seeing a 
large initial resource that will propel ML Gold into the phase II program, 
expanding and building the global ounces within the newly developing Palmetto 
Gold Trend."

ML Gold Corp. has an option to acquire a 100% right, title and interest to the 
Palmetto project (see news release dated October 18, 2016). The Palmetto 
Project is located in Esmeralda County, Nevada, within the southern portion of 
the Walker Lane Gold Trend.

Quality Assurance/Quality Control

Sample preparation and analyses for this program were completed at ALS Minerals 
Lab in Reno Nevada. Gold was determined by 30g Fire Assay with Atomic 
Absorption Spectrophotometry (AAS) finish. Other elements were determined by 
Ultra Trace Aqua Regia digestion with Inductively Coupled Plasma Mass 
Spectrometry (ICP-MS) finish.

A comprehensive quality assurance/quality control program including duplicate 
samples, blanks and standards form part of ML Gold's sampling protocol in 
addition to the laboratory's own quality assurance program. The field program 
was supervised by ML Gold staff and contractors and the technical information 
in this news release has been prepared in accordance with Canadian regulatory 
requirements as set out in National Instrument 43-101, and reviewed by Adrian 
Smith, Director, and a Qualified Person as that term is defined in NI 43-101.

ABOUT ML GOLD CORP.

ML Gold Corp. is a Canadian listed Company, focused on creating shareholder 
value through discoveries and strategic development of mineral properties in 
Canada and the United States.

For additional information please visit the Company's website at 
www.mlgoldcorp.com.

ML GOLD CORP.

Andrew Bowering, Chairman

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

This news release may contain certain "Forward-Looking Statements" within the 
meaning of the United States Private Securities Litigation Reform Act of 1995 
and applicable Canadian securities laws. When or if used in this news release, 
the words "anticipate", "believe", "estimate", "expect", "target, "plan", 
"forecast", "may", "schedule" and similar words or expressions identify 
forward-looking statements or information. These forward-looking statements or 
information may relate to future prices of commodities, accuracy of mineral or 
resource exploration activity, reserves or resources, regulatory or government 
requirements or approvals, the reliability of third party information, 
continued access to mineral properties or infrastructure, currency risks 
including the exchange rate of US$ for CDN$, changes in exploration costs and 
government royalties or taxes in Canada, the United States or other 
jurisdictions and other factors or information. Such statements represent the 
Company's current views with respect to future events and are necessarily based 
upon a number of assumptions and estimates that, while considered reasonable by 
the Company, are inherently subject to significant business, economic, 
competitive, political and social risks, contingencies and uncertainties. Many 
factors, both known and unknown, could cause results, performance or 
achievements to be materially different from the results, performance or 
achievements that are or may be expressed or implied by such forward-looking 
statements. The Company does not intend, and does not assume any obligation, to 
update these forward-looking statements or information to reflect changes in 
assumptions or changes in circumstances or any other events affections such 
statements and information other than as required by applicable laws, rules and 
regulations.

- 30 -

CONTACT INFO:

ML Gold Corp.
Investor Relations
(604) 669-2279
info@mlgoldcorp.com
www.mlgoldcorp.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=595752168