Source	MARKET NEWS
Date	06/29/2017
Time	06:03:00 AM

Company	 Oceanus Resources Corporation
Title	Mobilizes Team to Evaluate and Drill the High Gr





    CDNX Symbol: OCN











Press Release





Mobilizes Team to Evaluate and Drill the High Grade Protectora Veinat the El 
Tigre Property in Sonora, Mexico --->@NEWS RELEASE
OCEANUS RESOURCES CORP ("OCN-V;OCNSF-0")
- Mobilizes Team to Evaluate and Drill the High Grade
- Protectora Vein at the El Tigre Property in Sonora, Mexico

Oceanus Resources Corporation ("Oceanus" or the "Company") reports
it has received the final assay results for step-out drill hole
ET-17-144. As previously released, this hole returned 0.85 meters of
135.1 g/t gold equivalent consisting of 37.2 g/t gold and 7,338.9 g/t
silver.  Oceanus now reports the base metal results for drill hole 144.
Drill hole ET-17-144 returned 0.85 meters of 2.84% copper, 4.06% zinc
and 1.38% lead.  The mineralized zone consists of several vuggy quartz
veins and veinlets carrying galena, sphalerite, chalcopyrite,
stromeyerite and pyrite within a strongly silicified and kaolinized
alteration zone.  The true width of the vein is estimated to be 0.80
meters and the gold equivalent ratio is based on a gold-to-silver ratio
of 75:1.

Hole ET-17-144 was designed to test the Protectora vein at a
vertical depth of 50 metres below surface approximately 800 metres to
the north of the El Tigre mine workings (see attached Appendix A).
Near drill hole 144 the Protectora vein was partially explored in the
1920s by four exploration tunnels on several levels.  As Mishler (1920)
reported these exploration tunnels, known as Palomitas, exposed the
Protectora vein for a length of approximately 150 feet, a vertical
height of 50 feet and a width of 3.5 feet (45m L x 15m V x 1.1m W).
This exposed oxidized vein assayed 0.11 ounces per ton gold (3.77 g/t
Au) and 50 ounces per ton silver (1714.3 g/t Ag).

A second underground exploration tunnel is located approximately
950 meters north of Palomitas and drill hole ET-17-144 on the
Protectora vein. Here, the exploration tunnel follows the Protectora
vein for a length of 1000 feet (305m L) over a vertical height of 350
feet (106m V).  Mishler (1920) reports the vein averages 2 feet (61cm)
in width.  The mineralized zone consists of several vuggy quartz veins
and veinlets carrying galena, sphalerite, chalcopyrite, stromeyerite
and pyrite.

At Protectora the Oceanus exploration team is currently mapping
and sampling on surface and in the underground exploration tunnels.
Oceanus intends to start a new drill program this summer at Protectora.


Glenn Jessome, President and CEO of Oceanus reports, "The bonanza style
high grade gold-silver-base metal mineralization in the Protectora vein is
an exciting new discovery on the El Tigre property.  This could be a new
clavos along the El Tigre structure and our exploration team are mapping
and sampling the underground workings in advance of drilling this new
discovery this summer."

El Tigre Drilling Program and Resource Estimate

Oceanus has completed the 2016-17 infill drilling program at El
Tigre with a total of 62 diamond drill holes totalling 11,923.1 meters.
The purpose of this drill program was to support a NI 43-101 resource
estimation for the El Tigre Property.  The results from the Oceanus
drilling, prior drilling and other data will be incorporated into the
resource estimate to be released in July, 2017.

El Tigre Property

The El Tigre Property lies at the northern end of the Sierra Madre
gold belt which hosts many of the larger multi-million ounce epithermal
gold and silver deposits including Ocampo, Pinos Altos, Dolores and
Palmarejo.  In 1896, gold was first discovered on the property in the
Gold Hill area and mining started with the Brown Shaft in 1903.  The
focus soon changed to mining high-grade silver veins in the area with
the majority of the production coming from the El Tigre vein.
Underground mining on the El Tigre vein extended 1,450 meters along
strike and mined on 14 levels to a depth of 450 meters.   By the time
the mine closed in 1938, it is reported to have produced a total of
353,000 ounces of gold and 67.4 million ounces of silver from 1.87
million tons (Craig, 2012).

The El Tigre Property is approximately 35 kilometers long and
comprises 21,842.78 hectares. The El Tigre gold and silver deposit is
related to a series of high-grade epithermal veins controlled by a
north-south trending structure cutting across the andesitic and
rhyolitic tuffs of the Sierra Madre Volcanic Complex within a broad
gold and silver mineralized prophylitic alternation zone. The veins dip
steeply to the west and are typically 1 meter wide but locally can be
up to 5 meters in width. The veins, structures and mineralized zones
outcrop on surface and have been traced for a distance of 5.3
kilometers along strike.  Historical mining and exploration activities
focused on a 1.5 kilometer portion of the southern end of the deposits,
principally on the El Tigre, Seitz Kelly and Sooy veins. Four veins in
the north (Aguila, Escondida, Fundadora and Protectora) were explored
with only limited amounts of production.

Lab Preparation and Assay

The diamond drill core (HQ size) is geologically logged,
photographed and marked for sampling. When the sample lengths are
determined, the full core is sawn with a diamond blade core saw with
one-third of the core being bagged and tagged for assay. The remaining
two-thirds portion is returned to the core trays for storage and/or for
metallurgical test work.

The sealed and tagged sample bags are transported to the ActLabs
facility in Zacatecas, Mexico. ActLabs crushes the samples and prepares
200-300 gram pulp samples with ninety percent passing Tyler 150 mesh
(106m). The pulps are assayed for gold using a 50 gram charge by fire
assay (Code 1A2-50) and over limits greater than 10 grams per tonne are
re-assayed using a gravimetric finish (Code 1A3-50). Silver and
multi-element analysis is completed using 4 acid total digestion (Code
1F2 Total Digestion ICP).  Over limits greater than 100 grams per tonne
silver are re-assayed using a gravimetric finish (Code 8-Ag FA-GRAV
Ag).  Over limits greater than 10,000 ppm for copper, lead and zinc are
re-assayed using 4 acid total digestion (Code 8-4A AAS) and reported in
percent.

Quality Assurance / Quality Control and Data Verification

Quality assurance and quality control ("QA/QC") procedures monitor
the chain-of-custody of the samples and includes the systematic
insertion and monitoring of appropriate reference materials (certified
standards, blanks and duplicates) into the sample strings. The results
of the assaying of the QA/QC material included in each batch are
tracked to ensure the integrity of the assay data.  All results stated
in this announcement have passed Oceanus' QA/QC protocols.

Qualified Person

David R. Duncan, P. Geo., V.P. Exploration of the Company, is the
Qualified Person for Oceanus as defined under National Instrument
43-101. Mr. Duncan has reviewed and approved the scientific and
technical information in this press release and has reviewed the
Technical Report.

About Oceanus Resources Corporation

Oceanus Resources Corporation is a gold exploration company
operating in Mexico. Oceanus is managed by a team of mine finders with
extensive experience in exploring and developing large hydrothermal
gold projects in Mexico.  Oceanus is currently drilling and exploring
the El Tigre Property in the Sierra Madre Occidental.

CAUTIONARY STATEMENT: Neither TSX Venture Exchange nor its
Regulation Services Provider (as that term is defined in the policies
of the TSX Venture Exchange) accepts responsibility for the adequacy or
accuracy of this release. This News Release includes certain
"forward-looking statements".  All statements other than statements of
historical fact included in this release, including, without
limitation, statements regarding potential mineralization, resources
and reserves, the ability to convert inferred resources to indicated
resources, the ability to complete future drilling programs and infill
sampling, the ability to extend resource blocks, the similarity of
mineralization at El Tigre to the Ocampo mine, exploration results, and
future plans and objectives of Oceanus, are forward-looking statements
that involve various risks and uncertainties. Forward-looking
statements are frequently characterized by words such as "may", "is
expected to", "anticipates", "estimates", "intends", "plans",
"projection", "could", "vision", "goals", "objective" and "outlook" and
other similar words. Although Oceanus believes the expectations
expressed in such forward-looking statements are based on reasonable
assumptions, there can be no assurance that such statements will prove
to be accurate and actual results and future events could differ
materially from those anticipated in such statements.  Important
factors that could cause actual results to differ materially from
Oceanus's expectations include risks and uncertainties related to
exploration, development, operations, commodity prices and global
financial volatility, risk and uncertainties of operating in a foreign
jurisdiction as well as additional risks described from time to time in
the filings made by Oceanus with securities regulators.

Glenn Jessome
President and CEO
902 492 0298
jessome@oceanusresources.ca
______________________________________
_______________________________________________
TSX Venture closing price for OCN-V
Date: 2017/06/28
Closing Price: 0.25
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1717900020TS11717900969-06020320170629