Source	MARKET NEWS
Date	07/05/2018
Time	11:01:30 AM

Company	 Monument Mining Limited
Title	Update on 
FEED study of Selinsing Gold Sulphide





    CDNX Symbol: MMY











Press Release





MONUMENT MINING LTD ("MMY-V;MMTMF-0")
- Update on FEED study of Selinsing Gold Sulphide Plant Upgrade

Monument Mining Limited "Monument" or the "Company" reports on
progress made with the basic gold processing plant design and the Front
End Engineering Design ("FEED") for its Selinsing Gold Sulphide Project
("SGSP") in Malaysia. Additional testwork programs from independent
consultants have pushed out the completion date which is now aimed for
mid-August, 2018.

Process and Engineering Design

The basic gold processing plant design and FEED form a major part
of the Feasibility Study. It is aimed to convert the existing oxide
gold treatment processing plant to a sulphide treatment gold processing
plant. As a result, it would allow additional flotation process and
BIOX(R) process to be added to the existing plant with certain
alterations to the existing process. To date both design packages have
been delivered for Monument's review, subject to further optimization
should it be required upon additional flotation test work.

Basic Metallurgical Process Design

The design of the new processing facilities featuring: flotation,
BIOX(R) oxidation, counter current decantation, neutralisation and
conventional CIL processing has now been completed by Orway Mineral
Consultants ("Orway") and delivered to Monument for review. CIL
tailings will undergo conventional cyanide detoxification prior to the
Activated Sludge Tailings Effluent Remediation ("ASTER(TM)") process. A
water recovery thickener will recover the bulk of process water from
flotation tailings, neutralisation and ASTER(TM) discharge. The
thickener underflow will be pumped to the existing tailings storage
facility ("TSF").

The BIOX(R) process is a patented technology for pre-treatment of
sulphide-based refractory ores and concentrates ahead of a conventional
cyanide leach for gold recovery.  Outotec, the owner of the patent has
produced an ASTER(TM) process design package for the biological
destruction of residual cyanide and thiocyanate. Operation of the
ASTER(TM) process, as successfully practised at the Runruno BIOX(R)
plant in the Philippines, will provide clean water for milling and
flotation and prevent the poisoning of the BIOX(R) microbes by cyanide
compounds.

FEED

Contromation Energy Services ("CES") has submitted the engineering
design of the new processing facilities. The 3D model of the new
processing plant has been incorporated into the available space around
the process plant while minimizing the loss of existing infrastructure.
Best use has been made of the local topography with the BIOX(R) cooling
towers located at an elevated position. CES has also provided: major
equipment data sheets and specifications; material take-offs for
earthworks, civils, structural steel, platework and piping; also the
specifications for medium voltage switchgear and low voltage motor
control centres, cabling and instrumentation requirements.

SRK Consulting ("SRK") has provided a scoping level design
confirming the feasibility to expand the existing TSF. Detailed design
will be carried out following further geotechnical investigations and
testing of suitable materials from borrow pits and open pit cutbacks.

Perth based geotechnical specialists, Peter O'Bryan and Associates
("POB"), has completed the slope stability studies for both the
Selinsing and Buffalo Reef pits, providing recommendations for new
slope angles that will provide a safe working environment for the
development of these pits.

Metallurgical Testwork

Bioleach Variability Testwork

Following the announcement of bioleaching test results in February
2018, additional bioleaching variability testwork has been conducted by
SGS Johannesburg under the supervision of Outotec to determine the
metallurgical response of other ore sources to be processed in the
first two years of production. The testwork results have shown
excellent bioleaching kinetics with 98-99% sulphide sulphur oxidation
achieved within 18 days. Cyanide leaching of the BIOX(R) residues
achieved gold dissolution of 94-99% in the standard 24-hour tests. It
has confirmed the process being selected is most suitable for Selinsing
and Buffalo Reef ore. No more testwork is required.

Iron to arsenic solution grades indicated that the formation of a
stable ferric arsenate compound would result and toxicity
characteristic leaching procedure ("TCLP") testwork confirmed
compliance with the USA Environmental Protection Agency requirements.

The latest testwork included the testing of Selinsing Pit 5
hanging wall limestone for its acid neutralisation capacity and
potential use in the BIOX(R) reactors and the neutralisation tanks. The
limestone was found to have excellent neutralisation characteristics
and could be used for pH control in the BIOX(R) reactor tanks and for
neutralisation of the effluent solution and BIOX(R) residue. Quotations
have been sought for suitable crushing and milling equipment both
locally and overseas to produce milled limestone slurry.

Flotation Optimization Testwork

Additional flotation testwork has been commissioned at the Bureau
Veritas laboratory in Perth on further samples of drill core from
Buffalo Reef. The aim of the testwork is to provide independent
verification of the flotation conditions reported by the in house R&D
team that achieved better recovery rate of gold to the flotation
concentrate while maintaining the design sulphur grade and mass pull.
The Bureau Veritas testwork will be supervised by Orway.

Feasibility Study and Project Execution Plan

The equipment specifications and data sheets produced by CES have
been used by Monument to solicit quotations from appropriate equipment
vendors. The quotations received have been combined with the material
take-offs and schedules of rates to produce initial capital cost
("Capex") estimates. Quotations have been received for specialist
BIOX(R) and ASTER(TM) nutrients, flotation chemicals and flocculants
towards compiling the operating cost ("Opex") estimate. Both Capex and
Opex are under review and will be used for economic assessment in the
Feasibility Study. Geological modelling and mine plan review and update
are in progress to complete the internal Feasibility Study that will
deliver the Sulphide Project Execution Plan, which is also in progress
to complete. The delay is primarily caused by external laboratory work,
targeting completion in mid-August, 2018.

Michael John Kitney, Ass. Met, M.Sc., MAusIMM has reviewed and
approved the scientific and technical disclosure in the news release as
a Qualified Person under NI43-101 standards.

About Monument

Monument Mining Limited (TSX-V: MMY, FSE: D7Q1) is an established
Canadian gold producer that owns and operates the Selinsing Gold Mine
in Malaysia. Its experienced management team is committed to growth and
is advancing several exploration and development projects including the
Mengapur Copper and Iron Project, in Pahang State of Malaysia, and the
Murchison Gold Projects comprising Burnakura, Gabanintha and Tuckanarra
in the Murchison area of Western Australia. The Company employs
approximately 190 people in both regions and is committed to the
highest standards of environmental management, social responsibility,
and health and safety for its employees and neighboring communities.

Cathy Zhai, President and CEO Monument Mining Limited Suite 1580
-1100 Melville Street
Vancouver, BC V6E 4A6

FOR FURTHER INFORMATION visit the company web site at
www.monumentmining.com or

Contact Information:

contact:

Richard Cushing, MMY Vancouver                T: +1-604-638-1661
x102 rcushing@monumentmining.com Wolfgang Seybold, Axino GmbH
T: +49 711-82-09-7211 wolfgang.seybold@axino.com

"Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release."

Forward-Looking Statement

This news release includes statements containing forward-looking
information about Monument, its business and future plans
("forward-looking statements"). Forward-looking statements are
statements that involve expectations, plans, objectives or future
events that are not historical facts and include the Company's plans
with respect to its mineral projects and the timing and results of
proposed programs and events referred to in this news release.
Generally, forward-looking information can be identified by the use of
forward-looking terminology such as "plans", "expects" or "does not
expect", "is expected", "budget", "scheduled", "estimates",
"forecasts", "intends", "anticipates" or "does not anticipate", or
"believes", or variations of such words and phrases or state that
certain actions, events or results "may", "could", "would", "might" or
"will be taken", "occur" or "be achieved". The forward-looking
statements in this news release are subject to various risks,
uncertainties and other factors that could cause actual results or
achievements to differ materially from those expressed or implied by
the forward-looking statements.  These risks and certain other factors
include, without limitation: risks related to general business,
economic, competitive, geopolitical and social uncertainties;
uncertainties regarding the results of current exploration activities;
uncertainties in the progress and timing of development activities;
foreign operations risks; other risks inherent in the mining industry
and other risks described in the management discussion and analysis of
the Company and the technical reports on the Company's projects, all of
which are available under the profile of the Company on SEDAR at
www.sedar.com.  Material factors and assumptions used to develop
forward-looking statements in this news release include: expectations
regarding the estimated cash cost per ounce of gold production and the
estimated cash flows which may be generated from the operations,
general economic factors and other factors that may be beyond the
control of Monument; assumptions and expectations regarding the results
of exploration on the Company's projects; assumptions regarding the
future price of gold of other minerals; the timing and amount of
estimated future production; the expected timing and results of
development and exploration activities; costs of future activities;
capital and operating expenditures; success of exploration activities;
mining or processing issues; exchange rates; and all of the factors and
assumptions described in the management discussion and analysis of the
Company and the technical reports on the Company's projects, all of
which are available under the profile of the Company on SEDAR at
www.sedar.com.  Although the Company has attempted to identify
important factors that could cause actual results to differ materially
from those contained in forward-looking statements, there may be other
factors that cause results not to be as anticipated, estimated or
intended. There can be no assurance that such statements will prove to
be accurate, as actual results and future events could differ
materially from those anticipated in such statements. Accordingly,
readers should not place undue reliance on forward-looking statements.
The Company does not undertake to update any forward-looking
statements, except in accordance with applicable securities laws.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1818500051TS11818501143-10590520180705