Source	CANADA NEWSWIRE
Date	06/12/2019
Time	03:03:07 AM

Company	 BonTerra Resources Inc.
Title	Bonterra Intersects 101.1 g/t Au over 3.9 m at Gladiator and 12.8 g/t Au
over 5.6 m at Moroy





    CDNX Symbol: BTR











Press Release




" BC-BonterraGladiatorMoro   06-12 0912
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.306225:
^Bonterra Intersects 101.1 g/t Au over 3.9 m at Gladiator and 12.8 g/t Au
over 5.6 m at Moroy@

VAL-D'OR, QC, June 12, 2019 /CNW/ - Bonterra Resources Inc. (TSX-V: BTR,
OTCQX: BONXF, FSE: 9BR1) ("Bonterra" or the "Company") is pleased to announce
drill results from the ongoing exploration campaign at its 100%-owned
Gladiator, Moroy and Barry projects. The objective of the current drilling
campaign is to step out from known mineralization included in the Company's
recently released mineral resource estimate on the three projects.
Gladiator
The current drilling at Gladiator extends gold mineralization on both the
Barbeau and North Zones. Drill hole BA-19-40 intersected 101.1 g/t Au over 3.9
m on the Barbeau zone, approximately 50 m down-plunge of the known
mineralization. Drill hole BA-19-37 intersected 8.1 g/t Au over 1.8 m on the
North Zone, approximately 50 m down-plunge of the known mineralization. See
section for location.
Moroy
Ongoing exploration at the Moroy project includes both underground and
surface drilling. Drill hole MY-19-155 intersected 12.8 g/t Au over 5.6 m and
drill hole MY-19-158 intersected 12.2 g/t Au over 5.4 m. This drilling has
extended the known mineralization by 150 m in the down-plunge direction.
Surface drilling also succeeded to extend the mineralization by 150 m
up-plunge with hole MO-19-227 that intersected 3.6 g/t Au over 2.3 m. The
Moroy Deposit remains open at depth and along strike. See section for holes
locations.
Barry
The current drilling campaign has extended known mineralization along
strike and at depth on multiples zones. Hole MB-19-209 intersected 8.7 g/t Au
over 1.5 m and 6.1 g/t Au over 2.0 m on zone H1, approximately 75 m deeper
than known mineralization. In the same zone, Hole MB-19-211 extended H1 zone
at depth by 250 m with 6.3 g/t Au over 1.5 m. Hole MB-19-206 also extended
mineralization by 200 m at depth with 5.9 g/t Au over 1.5 m. See sections for
location.
Drilling highlights:
Project

Drillhole   From    To

Length (m)(x)         Au (g/t)

---                                                                       ---

Gladiator

BA-19-37  440.0  441.8                 1.8              8.1

---                                                                             
   ---

BA-
19-
39                           366.0  367.5    1.5                 5.5

---

BA-
19-
40                      570.1  574.0    3.9               101.1

---





Barry
MB-19-206       283.5  285.4                 1.9              3.1

---                                                                             
   ---

MB-
19-
206                           341.1  342.9    1.8                 3.5

---

MB-
19-
206                           592.9  594.4    1.5                 5.9

---

MB-
19-
207                           154.3  155.9    1.6                4.15

---

MB-
19-
209                           118.7  120.2    1.5                 8.7

---

MB-
19-
209                           137.8  139.8    2.0                 6.1

---

MB-
19-
209                     206.7  210.9    4.2                 5.1

---

MB-
19-
211                           453.7  455.2    1.5                 6.3

---



Moroy
MO-19-227       306.5  308.8                 2.3              3.6

---                                                                             
   ---

MY-
19-
155                     256.3  261.9    5.6                12.8

---

MY-
19-
158                      70.5   75.9    5.4                12.2

---


(x)Stated lengths are core width
as drilled, true widths vary
and average between 60 and 80
percent of drilled widths.
Core axis angles of the
intersection contacts and
surrounding rock units average
55 to 70 degrees.

Greg Gibson, Chairman and Interim CEO commented: "These recent
encouraging drill results bode well for the expansion of the current resource.
The Company now has five drill rigs working on the current
exploration-drilling program on its three projects with multiple targets
currently being tested to expand the gold mineralization footprint."
Bonterra Resources Quick Facts:
<<

--  Control of three high-grade gold deposits (Gladiator, Barry and Moroy)
and significant regional targets
--  100% ownership of the Urban-Barry Mill, the only permitted gold mill in
the region
--  Strong shareholder base including Wexford, Eric Sprott and Kirkland Lake
Gold
--  Property-wide NI 43-101 Mineral Resource Estimate recently updated with
a combined resource of 55,000 Oz Au Measured, 643,000 Oz Au Indicated
and 1,405,000 oz Au Inferred.
<>>
Quality Control and Reporting Protocols
Bonterra estimates that the actual thicknesses of the mineralized
intersections are between 65% and 80% of the core lengths. No capping grade is
used at this stage. The Company uses a rigorous QA-QC analytical program
according to industry standards. The analytical results were done by
pyroanalysis (A.A.) at the mine laboratory. Blanks, duplicates and certified
reference standards are inserted into the sample stream to monitor laboratory
performance. The company's QA-QC analytical verification program requires that
a minimum of 5% of the samples be audited at an independent laboratory. These
audit assays were sent to ALS laboratory located in Val-d'Or, Quebec. The
results of the audits are consistent with those obtained.
Qualified Person
Pascal Hamelin, P.Eng. has approved the information contained in this
release. Mr. Hamelin, Bonterra's VP Operations, is a Qualified Person as
defined by NI 43-101.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary and Forward-Looking Statements
This press release contains "forward-looking information" that is based
on Bonterra's current expectations. The words "will", "anticipated", "plans"
or other similar words and phrases are intended to identify forward-looking
information. This forward-looking information includes namely, information
with respect to the legal proceedings and Bonterra's successful contest
thereof. Forward-looking information is subject to known and unknown risks,
uncertainties and other factors that may cause Bonterra's actual achievements
to be materially different from those expressed or implied by such
forward-looking information. Such factors include but are not limited to
uncertainties of the outcome of legal proceedings. This list is not exhaustive
of the factors that may affect our forward-looking information. These and
other factors should be considered carefully and readers should not place
undue reliance on such forward-looking information. Bonterra disclaims any
intention or obligation to update or revise forward-looking information,
whether as a result of new information, future events or otherwise.
View original content to download
multimedia:http://www.prnewswire.com/news-releases/bonterra-intersects-101-1-g
t-au-over-3-9-m-at-gladiator-and-12-8-gt-au-over-5-6-m-at-moroy-300866056.html
SOURCE Bonterra Resources Inc.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/June2019/12/c8857.html

-0-                           06/12/2019
/For further information: Interim Chief Executive Officer: Greg Gibson,
819-825-8678 | ir(at)btrgold.com, 2872 Sullivan Road, Suite 2, Val d'Or, Quebec
J9P 0B9, 819-825-8678, Website: www.btrgold.com/
/Web Site: http://www.bonterraresources.com /
(BONXF BTR.)

CO:  Bonterra Resources Inc.
ST:  Quebec
IN:  MNG OTC
SU:

-30-