Source	CANADA NEWSWIRE
Date	06/18/2019
Time	04:03:15 AM

Company	 Bemetals Corp.
Title	BeMetals identifies priority targets and designs underground drilling
program for the high-grade, South Mountain zinc-silver project in Idaho





    CDNX Symbol: BMET











Press Release




" BC-BeMetals-SouthMtn   06-18 1853
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.342483:
^BeMetals identifies priority targets and designs underground drilling
program for the high-grade, South Mountain zinc-silver project in Idaho@

TSXV: BMET
VANCOUVER, June 18, 2019 /CNW/ - BeMetals Corp. (TSXV: BMET) ("BeMetals"
or the "Company") is pleased to announce it has identified a series of
significant priority high-grade target zones at its South Mountain Project
("South Mountain" or the "Property") in southwestern Idaho, U.S.A. The target
zones have been determined from the compilation and modelling of historical
geological and sampling information from two levels of existing underground
development, including areas of previous mine stoping. In addition, all
existing underground and surface drilling data have been included in the
targeting study. An important data set in identifying the priority target
zones were the results from previous underground channel sampling of the
Sonneman Level ribs at South Mountain.
Highlights from Rib-Sampling Program
<<

--  DMEA Zones 1/2/3; 39.62m (at) 16.76% Zinc ("Zn"), 140.91 grams per tonne
("g/t") Silver ("Ag"), 3.08 g/t Gold ("Au"), 0.78% Copper ("Cu") and
0.38% Lead ("Pb")
--  Muck Bay (number sign)4 Zone; 7.01m (at) 14.69% Zn, 246.17 g/t Ag, 0.34% Cu 
and 0.65%
Pb
--  Laxey Zone; 12.19m (at) 16.44% Zn, 478.97 g/t Ag, 0.68 g/t Au, 0.70% Cu and
0.86% Pb
<>>
The rib-sampling results indicate the high-grade and polymetallic nature
of the South Mountain deposit, as illustrated in Table 1 below, across a
number of currently identified, closely spaced, mineralized bodies forming the
deposit. Orientations of these samples are predominantly from the rib along
the length of the drift, which is approximately along strike of the deposit,
or from the ribs of the cross-cuts adjacent to the drift. Figures 1 and 2
illustrate the location of the rib-sampling program results conducted in 2013
and 2014.
John Wilton, President and CEO of BeMetals, commented, "As we continue to
work through the historical information at South Mountain, with input from
Thunder Mountain Gold Inc., the Optionees, the full extent and exciting upside
of the project is becoming more apparent. The underground rib-sampling of the
Sonneman Level demonstrates the significant, high-grade, nature of the
polymetallic mineralization.
Select targets will be tested through the completion of a 2,500m
underground core-drilling program in 2019. The drilling program is expected to
start upon site re-establishment and modest amounts of re-equipping at the
Sonneman Level development."
UNDERGROUND RIB-SAMPLING AND PRORITY TARGET LOCATIONS
Table 1 below shows the results of the 2013-2014 rib-sampling program
that provides four initial priority targets for underground drill testing. The
sampled mineralized zones are characterised by high-grade zinc and silver
grades with additional copper and lead values.
Table 1: Sonneman Level Channel Sampling Results at South Mountain
Deposit, 2012-2013
Zone

Sample    From   Length   Zinc   Silver    Gold         Copper      Lead
Name


Series  Station (metres)    %      g/t     g/t

%           %
ID
(feet)

(equal sign)(equal sign)(equal sign)

DMEA 1/2/3

OGT1616    30.0     39.62  16.76    140.91     3.08            0.78      0.38
71-02

---

MUCK BAY (number sign)4

OGT1617     9.0      7.01  14.69    246.17     0.34            1.17      0.65
(Sonneman                14-22
Drift)

---

MUCK BAY (number sign)4

OGT1617    76.9      4.60  14.04    282.51     0.34            2.30      0.59
14-22
(Refuge Bay)

---

MUCK BAY (number sign)3

OGT1617     0.0     12.19   5.63    198.85     0.00            0.28      2.83
24-30

---

LAXEY

OGT1617     0.0     12.19  16.44    478.97     0.68            0.70      0.86
35-9
MUCK BAY (number sign)1

(equal sign)(equal sign)(equal sign)

Figure 1 below illustrates the location of the historical rib-sampling
zones on a plan view of the Sonneman and Laxey underground developments. These
four priority target zones are further supported by the integration of
underground geological mapping and resource modelling of existing drilling
data. In addition to these zones the Texas target provides another priority
for drill testing based upon historical surface and underground drilling
compilations.
Figure 2 is a long section through the South Mountain deposit showing;
the location of the rib-sampling, related priority targets, the Texas Zone
target and planned boreholes to test the mineralization. The planned drilling
is principally designed as a series of fans to test the down plunge extension
potential of the deposit, and to scope the optimum borehole spacing that may
be required to expand the current resource. A number of other valid targets
have also been identified, in close proximity to the priority targets, and
these will be scheduled for drill testing, partially guided, by results of the
initial drilling.
THE SOUTH MOUNTAIN PROJECT
South Mountain is a polymetallic development project focused on
high-grade zinc and is located approximately 70 miles southwest of Boise,
Idaho (see Figure 3). The Project was intermittently mined from the late 1800s
to the late 1960's and its existing underground workings remain intact and
well maintained. Historic production at the Project has largely come from
skarn-hosted and high-grade massive sulphide bodies that remain open at depth
and along strike. According to historical smelter records, approximately
53,642 tons of ore have been mined to date. These records also indicate
average grades; 14.5% Zn, 363.42 g/t Ag, 1.98 g/t Au, 2.4% Pb, and 1.4% Cu
were realised.
The Project is largely on and surrounded by private surface land, and as
such, the permitting and environmental aspects of the Project are expected to
be straightforward. Permits are in place for underground exploration
activities and BeMetals does not anticipate significant barriers to any future
development at the Project.
Since 2008, the Optionees of the project have completed some 27 drill
holes for a total of 5,500 metres on the Property. Thus far, drill results
have been encouraging and significant potential exists to increase the known
mineral resource with additional drilling, as well as to expand the existing
measured and indicated mineral resource classifications with in-fill drilling.
Table 2. NI 43-101 Mineral Resource Statement for the South Mountain
Project - April 1, 2019



Mineral Resources at 6.04% ZnEq Cut-off

---

Classification                    Zinc Equivalent Resource


Contained Metal

---

Short
Tons     ZnEq lbs     ZnEq %                         Zn lbs    Zn%          Ag 
oz                                         Ag opt           Au 
oz                       Au opt       Pb lbs   Pb %         Cu lbs Cu %

---

x1000            x1000                                    
x1000                                  
x1000                                                  
x1000                       x1000                x1000

---

Measured        63.2      22,200                            17.57  
14,700            11.64                                            
237           3.745                         4.0         0.063    600            
0.483   700 0.566

---

Indicated      106.7      37,800                            17.72  
21,500            10.08                                            
576           5.398                         7.0         0.066  2,100            
0.983 1,600 0.766

---

Measured +      169.9      60,000                            17.66  
36,200            10.66                                            
813           4.783                        11.0         0.065  2,700            
0.797 2,300 0.692
Indicated

---

Inferred       363.2     120,800                            16.63  
70,500             9.70                                          
2,029           5.585                        16.3         0.045  
8,700            1.202 5,200 0.696

---

<<

1. The effective date of the mineral resource estimate is April 1, 2019. The
QP for the estimate is Mr. Randall K. Martin of Hard Rock Consulting, LLC,
is independent of BeMetals Corp.
2. Mineral resources that are not mineral reserves do not have demonstrated
economic viability. Inferred mineral resources that are part of the mineral
resource for which quantity and grade or quality are estimated on the basis
of limited geologic evidence and sampling, which is sufficient to imply but
not verify grade or quality and continuity. Inferred mineral resources may
not be converted to mineral reserves. It is reasonably expected, though not
guaranteed, that the majority of Inferred mineral resources could be
upgraded to Indicated mineral resources with continued exploration.
3. The mineral resource is reported at an underground mining cutoff of 6.04%
Zinc Equivalent ("ZnEq") within coherent wireframe models. The ZnEq
calculation and cutoff is based on the following assumptions: an Au price
of US$1,231/oz, Ag price of US$16.62/oz, Pb price of US$0.93/lb., Zn price
of US$1.10/lb. and Cu price of $2.54/lb.; metallurgical recoveries of 75%
for Au, 70% for Ag, 87% for Pb, 96% for Zn and 56% for Cu, assumed mining
cost of US$70/ton, process costs of US$25/ton, general and administrative
costs of US$7.50/ton, smelting and refining costs of US$25/ton. Based on
the stated prices and recoveries the ZnEq formula is calculated as follows;
ZnEq (equal sign) (Au grade (x) 43.71) + (Ag grade (x) 0.55) + (Pb grade (x) 
0.77) + (Cu
grade (x) 1.35) + (Zn grade).
4. Rounding may result in apparent differences when summing tons, grade and
contained metal content. Tonnage and grade measurements are in imperial
units.
<>>
About BEMETALS CORP.
BeMetals' founding Directors include Clive Johnson, Roger Richer, Tom
Garagan and John Wilton. BeMetals is a new base metals exploration and
development company focused on becoming a significant base metal producer
through the acquisition of quality exploration, development and potentially
production stage base metals projects. The Company's growth strategy is led by
a strong Board, key members of which have an extensive proven record of
accomplishment in delivering considerable value in the mining sector through
the discovery, construction and operation of mines around the world. The
Board, its Advisors, and senior management also provide outstanding deal flow
of projects to BeMetals based upon their extensive network of contacts in the
international minerals business.
The technical information in this news release for BeMetals, has been
reviewed and approved by John Wilton, CGeol FGS, CEO and President of
BeMetals, and a "Qualified Person" as defined under National Instrument
43-101.
ON BEHALF OF BEMETALS CORP.
"John Wilton"
John WiltonPresident, CEO and Director
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary Note Regarding Forward-Looking Statements
This news release contains "forward-looking statements" and "forward
looking information" (as defined under This news release contains
"forward-looking statements" and "forward looking information" (as defined
under applicable securities laws), based on management's best estimates,
assumptions and current expectations. Such statements include but are not
limited to, statements with respect to future exploration and development of
the South Mountain Project and plans for the identification and acquisition of
additional base metal projects. Although the Company has attempted to identify
important factors that could cause actual results to differ materially from
those contained in forward-looking statements, there may be other factors that
cause results not to be as anticipated, estimated or intended. These
statements should not be read as guarantees of future performance or results.
There can be no assurance that such statements will prove to be accurate, as
actual results and future events could differ materially from those
anticipated in such statements. Such statements involve known and unknown
risks, uncertainties and other factors that may cause actual results,
performance or achievements to be materially different from those expressed or
implied by such statements. Important factors that could cause actual results
to differ materially from expectations include, without limitation, the actual
results of exploration activities, the availability of financing and/or cash
flow to fund the current and future plans and expenditures, the ability of the
Company to satisfy the conditions of the option agreements for the South
Mountain Project and/or the Pangeni Copper Project, and changes in the world
commodity markets or equity markets. Please refer to the Company's most recent
filings under its profile at www.sedar.com for further information respecting
the risks affecting the Company and its business. The forward-looking
statements and forward looking information are made as of the date hereof and
are qualified in their entirety by this cautionary statement. The Company
disclaims any obligation to revise or update any such factors or to publicly
announce the result of any revisions to any forward-looking statements or
forward looking information contained herein to reflect future results, events
or developments, except as require by law. Accordingly, readers should notplace 
undue reliance on forward-looking statements and information.
SOURCE BeMetals Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/June2019/18/c0615.html

-0-                           06/18/2019
/For further information: about BeMetals please visit our website at
www.bemetalscorp.com and sign-up to our email list to receive timely updates,
or contact: Derek Iwanaka, Vice President, Investor Relations & Corporate
Development, Telephone: 604-609-6141, Email: diwanaka(at)bemetalscorp.com/
(BMET.)

CO:  BeMetals Corp.
ST:  British Columbia
IN:  MIN MNG
SU:

-30-