Source	CANADA NEWSWIRE
Date	06/24/2021
Time	04:02:33 AM

Company	 Golden Arrow Resources Corporation
Title	Golden Arrow Identifies Drill Targets and Expands Tenements at Rosales
Copper Project, Chile





    CDNX Symbol: GRG











Press Release




" BC-GoldenArrow-Rosales   06-24 1931
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.290083:
^Golden Arrow Identifies Drill Targets and Expands Tenements at Rosales
Copper Project, Chile@

TSX Venture Exchange (TSX-V): GRGFrankfurt Stock Exchange (FSE): G6AOTCQB
Venture Market (OTCQB): GARWF
VANCOUVER, BC, June 24, 2021 /CNW/ - Golden Arrow Resources Corporation
(TSXV: GRG) (FSE: G6A) (OTCQB: GARWF), ("Golden Arrow" or the "Company") is
pleased to report that the Transient Electromagnetic (TEM) surface geophysical
survey at the Rosales Copper Project has identified large, near-surface
conductive anomaly targets and prompted the Company to plan its first drill
campaign at the project. Furthermore, based on the results to date the Company
has applied for an additional 900 hectares of concessions adjacent to the
southern boundaries of the project area (See Figure 1:
https://bit.ly/3gMWFmC).
"The TEM survey has performed even better than expected, and we are
excited to have identified significant areas with near-surface anomalies that
are prospective for sulphide copper mineralization," stated Brian McEwen,
Golden Arrow VP Exploration and Development. "Drill testing these is now our
priority and we plan to start that imminently."
The highest priority target based on size, strong conductivity and
correlation with high-copper values in surface rock-chip samples is a
conductive area of 850 by 500 metres that may include several conductive zones
("G1", see Figure 2a: https://bit.ly/3xNtSE5). The shallowest part of anomaly
is estimated to be at approximately 100 metres below surface with the depth
extent still to be determined. A second large conductive anomaly is situated
approximately 500 metres to the southeast, ("G-2" see Figure 2b:
https://bit.ly/3xNtSE5) with dimensions of 600 by 400 metres, and it is open
to the south. The upper reaches of this anomaly are also interpreted to be
within 100 metres of surface. A third conductive target has been identified
2650 metres to the northwest of G1.
Following the TEM survey, Golden Arrow engaged Quantec to complete a 440
line-kilometre ground magnetic survey at 100-metre line separation to provide
additional detailed geophysical information throughout the entire project area
and to detect possible porphyry targets at depth. The new survey is underway
and expected to be completed by approximately the end of June.
Compiled interpretation of both surveys will allow final targets to be
refined for drill testing. A tender for reverse circulation (RC) drilling of
up to 2,000 metres has been put out for bid, with a plan to commence drilling
in August.
Rosales Project and Program DetailsThe Rosales Project currently includes
3444 hectares of 100% held mineral claims (not including 900 additional
hectares under application). The project is road-accessible and is situated
less than 90 kilometres from the mining centre of Copiapo, with world-class
exploration and mining infrastructure readily available. The Project is
situated in the Atacama Region, a prolific mining region that hosts multiple
large precious and base metal mines.
The initial reconnaissance program at Rosales identified two general
areas of prospective mineralization: The Margarita Mine trend (MMT), and the
NW Target. The MMT is a 3.5-kilometre-long structural corridor, oriented
northeast-southwest, mainly defined by felsic dykes. Chalcocite and
chrysocolla were identified in outcrop in an area covering 350 by 400 metres,
and samples from this area averaged 1.74% copper with a highest value of 4.37%
copper hosted in andesitic volcanoclastic rocks and andesites (See News
Release dated July 20, 2020 filed on SEDAR). This mineralization is coating
fractures and disseminated in the matrix of the volcanoclastic host rock.
There are also indications manto-type mineralization two to four metres thick
in this zone.
The NW Target is located 2.7 kilometres to the northwest of the MMT. It
includes outcrop with veinlets and fractures hosting quartz-chalcocite-copper
oxides within an area measuring 1,500 by 400 metres. This mineralization is
hosted by porphyritic andesite and dacite, which may represent a dome complex.
Eight chip samples averaged 3.19% Cu and 13.9 g/t Ag with a highest value of
5.74% Cu and 37.1 g/t Ag (See News Release dated July 20, 2020 filed on
SEDAR).
The goal of the geophysical program announced on April 29, 2021, was to
detect and delineate prospective electromagnetic conductor responses
consistent with near-surface copper stockwork mineralization, potentially
related to larger copper systems at depth, and associated with surface
anomalies in the MMT and NW target areas described above. Quantec Geoscience
Chile Ltda. ("Quantec") was awarded the contract for completing the survey.
Golden Arrow also engaged independent geophysical consultant Miles Rideout to
guide the program, provide additional interpretations of the data, and
recommendations for next steps.
The survey utilized a Geonics Ltd. 'Protem' geophysical system operated
with an in-loop profiling configuration, transmitting 25 Hz current in
overlapping 800 m x 800 m transmitter loops and covering a total of 850
hectares. Three-component receiver measurements were acquired at 50 metre
intervals along east-west lines spaced with 100 metre line separation.
Transient or time-domain electromagnetic profiling is one of the best
proven geophysical techniques for the detection of conductive sulphide
minerals. TEM was originally developed in Canada and has been credited with
many mining discoveries over five decades. Unlike Induced Polarization
surveys, TEM data are largely unaffected by disseminated pyrite mineralization
and can detect and delineate conductive sulphide bodies within larger
disseminated formations. Additionally, sulphide minerals associated with weak
induced polarization response can present excellent TEM conductors as long as
the sulphide grains form continuous paths of electrical conductivity. This is
the reason that TEM surveys are preferentially sensitive to high-grade and
massive sulphide bodies.
TEM profile data presents decay intervals from earliest interval (channel
1) to the latest interval (channel 20). Current in the TEM transmit loop
induces secondary eddy current in the ground, from near surface to depths of
hundreds of metres. Eddy currents attenuate fastest in areas with poor
conductivity but persist for relatively long periods in good electrical
conductors. The relative electrical conductivity of target features is often
discriminated by which channels present strong anomalous response. Early-time
gates typically show poor conductors such as clays or water-saturated
sediment. Late-time gates only respond to the best-quality conductors, which
often represent zones of metallic conductivity as found in many sulphide
minerals. Better conductivity is usually attributable to more massive textures
and greater conductor thickness. Chalcocite, bornite and chalcopyrite are
copper sulphides often associated with high-conductivity TEM responses.
Historic investigation in the Copiapo district has demonstrated that pyrite is
rarely associated TEM anomalies, attributable to pyrite's predominant tendency
to form discontinuous grains, which do not facilitate electrical conduction.
In the MMT target two anomalous zones were detected; one with the highest
conductivity and very strong responses to channel 20 (G-1 in Figure 2a). The
dimensions of this target are 850 by 500 metres, though the target may
comprise multiple conductive zones. Interpretation of the TEM profiles
indicates the shallowest portions of this target are approximately 100 metres
below surface. The depth extent of this target has not yet been determined.
This conductive target is the highest priority target for drilling due to its
size, excellent conductivity and correlation with high-copper values in
surface rock-chip samples.
At 500 metres to the southeast, a second large conductive zone (G-2-
Figure 2b) has been detected with dimensions 600 by 400 metres in channel 14
response. This zone remains open to the south, to the southern border of the
project, and Golden Arrow has applied for three additional concessions of 300
hectares each to cover the extension of the anomaly in this area. This
southeast target is somewhat less conductive than the central target, with the
TEM response attenuating significantly beyond channel 17. This earlier
response suggests more disseminated textures or different composition.
Interpretation of TEM profiles indicates the upper portions of this target are
less than 100 metres below surface. Due to its earlier-time anomalous
response, this is the second priority area for drilling.
At the NW target a third conductive zone has been identified at the
northern limit of the TEM survey coverage (G3 in Figure 2, 2650 metres NNW of
G-1 in Figure 2a). A very broad early and mid-time response resolves to a
narrow, highly conductive lineament in channel 20. This zone is approximately
100 metres wide, and has been delineated over 400 metres length, and it
remains open to the north. Considering the setting this response is consistent
with a highly conductive structure located below a relatively thin unit of
conductive sediment. This is the third priority target. Geochemical sampling
shows positive copper values at all three TEM targets, thus the Company
considers all three to be highly prospective.
Golden Arrow's geophysical consultant Miles Rideout stated "We chose the
TEM profiling technique as an expedient method to directly detect high-quality
sulphide targets. The observed TEM responses show broader conductors
consistent with manto deposits and strong narrow features consistent with
feeder structures. It is easy to recommend drilling based on these very
positive results."
Qualified Persons
The technical portions of this news release have been reviewed and
approved by Brian McEwen, P.Geol., VP Exploration and Development to the
Company and a Qualified Person as defined in National Instrument 43-101.
About Golden Arrow:
Golden Arrow Resources Corporation is a mining exploration company with a
successful track record of creating value by making precious and base metal
discoveries and advancing them into exceptional deposits. The Company is well
leveraged to the price of gold, having monetized its Chinchillas silver
discovery into a significant holding in precious metals producer SSR Mining
Inc.
Golden Arrow is actively exploring a portfolio that includes a new
epithermal gold project in Argentina, a district-scale frontier gold
opportunity in Paraguay, a base-metal project in the heart of a leading mining
district in Chile and more than 180,000 hectares of properties in Argentina.
The Company is a member of the Grosso Group, a resource management group
that has pioneered exploration in Argentina since 1993.
ON BEHALF OF THE BOARD
"Joseph Grosso" _______________________________Mr. Joseph Grosso,
Executive Chairman, President and CEO
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release may contain forward-looking statements. Forward-looking
statements address future events and conditions and therefore involve inherent
risks and uncertainties. All statements, other than statements of historical
fact, that address activities, events or developments the Company believes,
expects or anticipates will or may occur in the future, including, without
limitation, statements about the Company's plans for its mineral properties;
the Company's business strategy, plans and outlooks; the future financial or
operating performance of the Company; and future exploration and operating
plans are forward-looking statements.
Forward-looking statements are subject to a number of risks and
uncertainties that may cause the actual results of the Company to differ
materially from those discussed in the forward-looking statements and, even if
such actual results are realized or substantially realized, there can be no
assurance that they will have the expected consequences to, or effects on, the
Company. Factors that could cause actual results or events to differ
materially from current expectations include, among other things: the impact
of COVID-19; risks and uncertainties related to the ability to obtain, amend,
or maintain licenses, permits, or surface rights; risks associated with
technical difficulties in connection with mining activities; and the
possibility that future exploration, development or mining results will not be
consistent with the Company's expectations. Actual results may differ
materially from those currently anticipated in such statements. Readers are
encouraged to refer to the Company's public disclosure documents for a more
detailed discussion of factors that may impact expected future results. The
Company undertakes no obligation to publicly update or revise any
forward-looking statements, unless required pursuant to applicable laws.
View original content to download
multimedia:http://www.prnewswire.com/news-releases/golden-arrow-identifies-dri
ll-targets-and-expands-tenements-at-rosales-copper-project-chile-301319165.htm
l
SOURCE Golden Arrow Resources Corporation



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/June2021/24/c8143.html

-0-                           06/24/2021
/For further information: Corporate Communications, Tel: 1-604-687-1828,
Toll-Free: 1-800-901-0058, Email: info(at)goldenarrowresources.com/
(GARWF GRG. G6A)

CO:  Golden Arrow Resources Corporation
ST:  British Columbia
IN:  MIN MNG OTC PRM
SU:

-30-