Source	CANADA NEWSWIRE
Date	06/09/2021
Time	06:34:52 AM

Company	 Neo Lithium Corp.
Title	Neo Lithium Updates 3Q Project with 125% Increase of Measured and
Indicated Resources in the High-Grade Zone





    CDNX Symbol: NLC











Press Release




" BC-NeoLithium-3Q-Project   06-09 3174
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.265177:
^Neo Lithium Updates 3Q Project with 125% Increase of Measured and
Indicated Resources in the High-Grade Zone@

<<

--  Significant increase in northern high-grade mineral resource estimate at
800 mg/l lithium cut-off:
o Measured and indicated resource estimate of 1,682,000 tonnes of lithium
carbonate equivalent at an average grade of 926 mg/l Lithium
--  Significant increase of central and southern medium-grade resource
estimate at 400 mg/l Lithium cut-off:
o Measured and indicated resource estimate 5,304,000 tonnes of lithium
carbonate equivalent at an average grade of 636 mg/l Lithium
--  Average combined impurities for Magnesium/Lithium and Sulphate/Lithium
continue to be lowest in industry
o High grade resource with 800 mg/l cut off: Mg/Li(equal sign)1.66 and 
Sulfate/Li(equal sign)0.49
--  Potential for resource expansion continues to exist at depth, and off
strike on the eastern border of the 3Q Project under the alluvial cones.
<>>
TORONTO, June 9, 2021 /CNW/ - Neo Lithium Corp. ("Neo Lithium" or the
"Company") (TSXV: NLC) (OTCQX: NTTHF) (FSE: NE2) is pleased to announce an
updated resource estimate for the Tres Quebradas lithium brine project in
Catamarca Province, Argentina ("3Q Project"). This updated mineral resource
estimate has been completed under the supervision of Canadian-based
Groundwater Insight, Inc., which is independent of the Company.
Based on this updated mineral resource estimate, the 3Q Project deposit
continues to improve, confirming that it is one of the largest and
highest-grade lithium brine deposits in the world.
Since the completion of the previous mineral resource estimate in July
2018, the Company has continued drilling and has revised the statistical
criteria to define measured, indicated, and inferred resources. Using the new
drill holes (see news release dated May 27, 2021 for further information) and
the revised statistical criteria, the measured and indicated mineral resource
categories have increased by 125% at the 800 mg/l lithium cut-off, and by 33%
at 400 mg/l lithium cut-off, when compared to the July 2018 estimate. Similar
average grades and impurities were observed.
The updated lithium resource estimate is summarized in Tables 1 and 2,
for the 800 and 400 mg/l cut-offs, respectively, with comparison to the July
2018 results.
Table 1 - in situ Lithium Resource at 800 mg/L Lithium cut-off


Average        Brine Volume   Mass Cumulated

Comparison
Concentration                                                     with 2018
Resource





Li (mg/l)     (Millions m(3))    Li (tonne)

Li2CO3

Li2CO3
(tonne)


(%)



Measured                            928              188          
175,000                      930,000                281%

---

Indicated                            923              153          
141,000                      752,000                 50%

---

Total M & I                          926              341          
316,000                    1,682,000                125%

---

Inferred                            918               33           
31,000                      163,000                -12%

---
Table 2 - in situ Lithium Resource at 400 mg/l Lithium cut-off


Average      Brine Volume   Mass Cumulated

Comparison
Concentration                                                     with 2018
Resource





Li (mg/l)   (Millions m(3))    Li (tonne)

Li2CO3

Li2CO3
(tonne)


(%)



Measured                           790              437          
346,000                     1,839,000                223%

---

Indicated                           576            1,131          
651,000                     3,465,000                  1%

---

Total M & I                          636            1,568          
996,000                     5,304,000                 33%

---

Inferred                           561              757          
425,000                     2,261,000                -22%

---
Note: The tonnage values in
Tables 1 and 2 are
expressed as total
contained metals and have
been rounded to the
nearest thousand.

---
Average density for the brine is 1.217. The low magnesium and sulfate
content of the mineral resource is consistent with the previous mineral
resource estimate. Table 3 summarizes the main impurities ratios for magnesium
and sulfate.
Table 3 - 3Q Project Impurity Ratios at 800 mg/l Lithium Cut-off
Impurity Ratio

Magnesium/Lithium

Sulfate/Lithium

---





Measured                            1.66                  0.49

---



Indicated                           1.66                  0.48

---



Total M & I                         1.66                  0.49

---



Inferred                            1.67                  0.41

---
"These updated results confirm that 3Q Project is one of the most
significant lithium brine discoveries in recent history" said Dr. Perez,
President and CEO of Neo Lithium. "We continue to add high quality resources
to the 3Q Project and there is still incremental value and growth at this
world-class high-grade resource."
Neo Lithium's wholly-owned 3Q Project is within an elongated salar, 28 km
in length that contains a high-grade resource in the northern third of the
salar, roughly defined by the 800 mg/l cut off, and a medium-grade resource in
the southern two thirds of the salar, within the 400 mg/l cut off. The
high-grade resource is strategically important because it requires smaller
evaporation ponds to put the project into production. Since the pond size is
geometrically related to grade, increases in grade have a significant impact
in decreasing capital costs of pond construction. Ponds can represent up to
50% of the capital cost of an evaporative lithium brine project. Therefore, an
important design goal of the project is to minimize pond size.
"We are very pleased with these updated results, which highlight further
upside at the 3Q Project. However, this development does not take away focus
from our ongoing work toward the completion of the Feasibility Study in Q3,"
said Gabriel Pindar, COO of Neo Lithium. "These results emphasize the
potential for further expansion, even beyond what we originally thought."
Feasibility Study Update
The Company is working with Worley on the Feasibility Study for the 3Q
Project. The current larger mineral resource estimate is not expected to
negatively impact the new reserve estimation and mine plan that will be
delivered as part of the Feasibility Study. The Company does not expect
mineral extraction methods to change as a result of the increased mineral
resource estimates, as the grade and location of the mineral resource remains
substantially the same. Accordingly, the "Preliminary Feasibility Study
("PFS") - 3Q Project, NI 43-101 Technical Report Catamarca, Argentina" with an
effective date of May 7, 2019 and amended as of May 8, 2019, and subsequently
amended April 1, 2021 is still relevant and valid as a preliminary indication
of the economic potential of the 3Q Project.
A new reserve estimate will be issued along with the Feasibility Study,
to be completed by Worley at the end of Q3 - beginning of Q4 2021. We have
completed all base engineering work and issued proposals to receive vendor
budgetary quotes to start compiling the Feasibility Study Capex estimate. At
this stage we remain within the parameters of the PFS Capex and we do not
expect major changes or deviations from it beyond the accuracy of the PFS
estimate.
Our expanded pilot ponds have been commissioned and are fully
operational. We will be reconfiguring the pilot plant to reflect continuous
operation as part of our operational testing procedure. Both systems have
provided valuable information in support of the Feasibility Study and are
serving as training grounds for our team in Argentina. We are proud to
announce that we have now reached 20% of our future permanent staff, in full
compliance with our Environmental, Social and Governance (ESG) goals,
providing training and work opportunities to local people, and thus
strengthening the relationship with our local community.
Resource Estimate Methodology
The mineral resource estimate was prepared in accordance with best
practice methods specific to brine resources. The approach includes a reliance
on drilling and sampling methods that yield depth-specific chemistry and
drainable porosity measurements of the brine host rock.
The mineral resource calculation is based on four drilling and sampling
campaigns, which included the following:
<<

--  Completion of 10,523.65m of drilling (6,145.75m of diamond drill and
4,377.90m of rotary holes) divided in 56 drill holes.
--  The deepest hole was 647m.
--  The rotary wells were completed with 8 or 10 inch PVC or iron piping.
They were pumped for over 48 hours to ensure the brine flowed from the
aquifer and that all remaining traces of drill mud was removed. Outflow
was typically sampled at six-hour intervals. All samples were averaged
(typically 6 to 10 samples were collected in each well) and the sample
concentration was attributed to the gravel pack interval of the well.
--  The diamond drill holes were cored with HQ triple tube.
--  Of the 56 holes used for the mineral resource estimate, nine reached the
basement at depths ranging from 50m (in the western boundary of the
salar) to 647m in the eastern border of the salar. All others were
terminated after reaching target depth or due to drill limitations.
--  The total thickness of the basin exceeds 650m on the eastern side, and
brine saturated sediments are present throughout the majority of the
sequence; the exception is relatively fresher-water zones where surface
inflows occur.
--  A total of 230 brine samples plus 74 QA/QC samples were collected from
the drill holes during drilling and from completed wells; and 45 surface
samples were collected from the 3Q and Verde lagunas. Repeat samples
were averaged resulting in 184 unique sample locations, that were used
to calculate the resource estimate.
--  Brine samples were collected from the diamond drill holes during
drilling, using a standard packer technique (both single and double
packer) to obtain samples from discrete levels of the formation.
Fluorescein dye was used to ensure that the samples were representative
of the collection interval. Sampling intervals range from 2m to 50m,
depending on the hole.
--  Brine was sampled (and bathymetry conducted) in Laguna 3Q and Laguna
Verde, located at the north and south ends of the salar, respectively.
Extensive sampling indicates that the brine composition in these lagunas
is essentially continuous with the brine under the salar crust.
--  Brine samples interpreted to reflect the influence of freshwater inflows
(Rio Salado, Rio Nacimiento, and Rio 3Q) were removed from the data set
prior to interpolation. Similarly, volumes of the subsurface associated
with fresher water were also removed from the salar volume for resource
estimation.
<>>
The previous (2018) mineral resource estimate used a search radius
criteria technique to classify measured, indicated and inferred resources. In
the current estimate the approach was revised to a borehole density method.
Both methods are widely used in both brine and hard rock resource estimation.
The borehole density method was considered more appropriate based on an
increasing body of site data, which continue to support spatially predictable
geology and brine trends.
Geology and Brine Model
Geology and brine models were assembled in the numerical modeling
software FEFLOW. Geology was interpreted from surface mapping, diamond
drilling core and rotary borehole logging. Eight primary geological units were
identified:
<<

--  Brine lakes: standing bodies of surface brine at the north and south
ends of the salar complex (Laguna 3Q and Laguna Verde, respectively);
--  Hyper-Porous Halite: karstic, near surface halite (typically less than
50m depth);
--  Upper Sediments: formed by sand, silt and conglomerates located at
surface or near surface;
--  Porous Halite: formed by halite with moderate porosity that is readily
identified by visual methods;
--  Massive Halite: this unit generally occurs as labelled, but often
contains interbedded layers of clay, volcaniclastics, and halite with
greater visible porosity. Consistent with this observation, a range of
tests have indicated potentially important porosity in this unit.
--  Lower Sediments: well rounded sand, silt and minor conglomerates hosted
below the Massive Halite (typically 300m to 500 m deep);
--  Fanglomerates: sedimentary polymictic angular breccia with sand matrix
located below the Lower Sediments and above the Basement, typically
below 500 m depth; and
--  Hydrostratigraphic Basement: Permian andesites and dacites; generally
considered to have negligible or low drainable porosity.
<>>Core samples were packed in Lexan tubing and shipped to Daniel B.
Stephens & Associates Inc. ("DBS"), Inc., a laboratory in the U.S., to measure
Relative Brine Release Capacity (RBRC). This method of porosity determination
is designed to estimate Specific Yield, which is the portion of the total
porosity that can reasonably be expected to drain through pumping. General
porosity trends were consistent with geology, with considerable variability
also noted within geological units.
RBRC was measured in 307 core samples (across all drilling campaigns), to
estimate the Specific Yield of each geological unit. Pumping tests were also
completed in the Hyper-Porous Halite, Upper Sediments and Porous Halite.
A summary of the RBRC measurements and the percentage of the resource in
each unit is provided in Table 4.
Table 4 - RBRC Results and the Distribution of the Resource between the
Primary Geological Units
Hydrostratigraphic         (number sign) of          Average           % of the
Units                   Samples      Specific          Resource
Yield

---





Brine Lakes                                                               1

---

Hyper-Porous Halite(x)                 66             14.74                  11

---



Upper Sediments(x)                     14              9.12                  22

---



Porous Halite(x)                       97              6.33                  16

---



Massive Halite                       84              3.85                  15

---



Lower Sediments                      12              5.18                  11

---



Fanglomerate                         33             11.23                  24

---

Hydrological Basement                 1              1.73                   0

---
(x)Units evaluated with
Pumping Tests
The Hyper-Porous Halite hosts 11% of the resource. A pumping test was
completed in this unit that included the use of fluorescein dye, which enabled
estimation of Effective Porosity, a parameter that is closely related to
Specific Yield. The test provided an Effective Porosity value of 15%, which is
consistent with the average RBRC value for the unit.
The Lower Sediments and Fanglomerates host a combined 35% of the total
resource (almost entirely classified as inferred resource, due to depth and
lower borehole density). Only 13 boreholes penetrate to these units, and only
two completely penetrate the units. Further exploration is required at depth
along the entire salar complex with the objective of converting these inferred
resources into the measured and indicated categories.
The brine data were interpolated directly within FEFLOW, to minimize the
potential for errors in transferring distributions be

" BC-NeoLithium-3Q-Project   06-09 3174
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.265177:
^Neo Lithium Updates 3Q Project with 125% Increase of Measured and
Indicated Resources in the High-Grade Zone@

<<

--  Significant increase in northern high-grade mineral resource estimate at
800 mg/l lithium cut-off:
o Measured and indicated resource estimate of 1,682,000 tonnes of lithium
carbonate equivalent at an average grade of 926 mg/l Lithium
--  Significant increase of central and southern medium-grade resource
estimate at 400 mg/l Lithium cut-off:
o Measured and indicated resource estimate 5,304,000 tonnes of lithium
carbonate equivalent at an average grade of 636 mg/l Lithium
--  Average combined impurities for Magnesium/Lithium and Sulphate/Lithium
continue to be lowest in industry
o High grade resource with 800 mg/l cut off: Mg/Li(equal sign)1.66 and 
Sulfate/Li(equal sign)0.49
--  Potential for resource expansion continues to exist at depth, and off
strike on the eastern border of the 3Q Project under the alluvial cones.
<>>
TORONTO, June 9, 2021 /CNW/ - Neo Lithium Corp. ("Neo Lithium" or the
"Company") (TSXV: NLC) (OTCQX: NTTHF) (FSE: NE2) is pleased to announce an
updated resource estimate for the Tres Quebradas lithium brine project in
Catamarca Province, Argentina ("3Q Project"). This updated mineral resource
estimate has been completed under the supervision of Canadian-based
Groundwater Insight, Inc., which is independent of the Company.
Based on this updated mineral resource estimate, the 3Q Project deposit
continues to improve, confirming that it is one of the largest and
highest-grade lithium brine deposits in the world.
Since the completion of the previous mineral resource estimate in July
2018, the Company has continued drilling and has revised the statistical
criteria to define measured, indicated, and inferred resources. Using the new
drill holes (see news release dated May 27, 2021 for further information) and
the revised statistical criteria, the measured and indicated mineral resource
categories have increased by 125% at the 800 mg/l lithium cut-off, and by 33%
at 400 mg/l lithium cut-off, when compared to the July 2018 estimate. Similar
average grades and impurities were observed.
The updated lithium resource estimate is summarized in Tables 1 and 2,
for the 800 and 400 mg/l cut-offs, respectively, with comparison to the July
2018 results.
Table 1 - in situ Lithium Resource at 800 mg/L Lithium cut-off


Average        Brine Volume   Mass Cumulated

Comparison
Concentration                                                     with 2018
Resource





Li (mg/l)     (Millions m(3))    Li (tonne)

Li2CO3

Li2CO3
(tonne)


(%)



Measured                            928              188          
175,000                      930,000                281%

---

Indicated                            923              153          
141,000                      752,000                 50%

---

Total M & I                          926              341          
316,000                    1,682,000                125%

---

Inferred                            918               33           
31,000                      163,000                -12%

---
Table 2 - in situ Lithium Resource at 400 mg/l Lithium cut-off


Average      Brine Volume   Mass Cumulated

Comparison
Concentration                                                     with 2018
Resource





Li (mg/l)   (Millions m(3))    Li (tonne)

Li2CO3

Li2CO3
(tonne)


(%)



Measured                           790              437          
346,000                     1,839,000                223%

---

Indicated                           576            1,131          
651,000                     3,465,000                  1%

---

Total M & I                          636            1,568          
996,000                     5,304,000                 33%

---

Inferred                           561              757          
425,000                     2,261,000                -22%

---
Note: The tonnage values in
Tables 1 and 2 are
expressed as total
contained metals and have
been rounded to the
nearest thousand.

---
Average density for the brine is 1.217. The low magnesium and sulfate
content of the mineral resource is consistent with the previous mineral
resource estimate. Table 3 summarizes the main impurities ratios for magnesium
and sulfate.
Table 3 - 3Q Project Impurity Ratios at 800 mg/l Lithium Cut-off
Impurity Ratio

Magnesium/Lithium

Sulfate/Lithium

---





Measured                            1.66                  0.49

---



Indicated                           1.66                  0.48

---



Total M & I                         1.66                  0.49

---



Inferred                            1.67                  0.41

---
"These updated results confirm that 3Q Project is one of the most
significant lithium brine discoveries in recent history" said Dr. Perez,
President and CEO of Neo Lithium. "We continue to add high quality resources
to the 3Q Project and there is still incremental value and growth at this
world-class high-grade resource."
Neo Lithium's wholly-owned 3Q Project is within an elongated salar, 28 km
in length that contains a high-grade resource in the northern third of the
salar, roughly defined by the 800 mg/l cut off, and a medium-grade resource in
the southern two thirds of the salar, within the 400 mg/l cut off. The
high-grade resource is strategically important because it requires smaller
evaporation ponds to put the project into production. Since the pond size is
geometrically related to grade, increases in grade have a significant impact
in decreasing capital costs of pond construction. Ponds can represent up to
50% of the capital cost of an evaporative lithium brine project. Therefore, an
important design goal of the project is to minimize pond size.
"We are very pleased with these updated results, which highlight further
upside at the 3Q Project. However, this development does not take away focus
from our ongoing work toward the completion of the Feasibility Study in Q3,"
said Gabriel Pindar, COO of Neo Lithium. "These results emphasize the
potential for further expansion, even beyond what we originally thought."
Feasibility Study Update
The Company is working with Worley on the Feasibility Study for the 3Q
Project. The current larger mineral resource estimate is not expected to
negatively impact the new reserve estimation and mine plan that will be
delivered as part of the Feasibility Study. The Company does not expect
mineral extraction methods to change as a result of the increased mineral
resource estimates, as the grade and location of the mineral resource remains
substantially the same. Accordingly, the "Preliminary Feasibility Study
("PFS") - 3Q Project, NI 43-101 Technical Report Catamarca, Argentina" with an
effective date of May 7, 2019 and amended as of May 8, 2019, and subsequently
amended April 1, 2021 is still relevant and valid as a preliminary indication
of the economic potential of the 3Q Project.
A new reserve estimate will be issued along with the Feasibility Study,
to be completed by Worley at the end of Q3 - beginning of Q4 2021. We have
completed all base engineering work and issued proposals to receive vendor
budgetary quotes to start compiling the Feasibility Study Capex estimate. At
this stage we remain within the parameters of the PFS Capex and we do not
expect major changes or deviations from it beyond the accuracy of the PFS
estimate.
Our expanded pilot ponds have been commissioned and are fully
operational. We will be reconfiguring the pilot plant to reflect continuous
operation as part of our operational testing procedure. Both systems have
provided valuable information in support of the Feasibility Study and are
serving as training grounds for our team in Argentina. We are proud to
announce that we have now reached 20% of our future permanent staff, in full
compliance with our Environmental, Social and Governance (ESG) goals,
providing training and work opportunities to local people, and thus
strengthening the relationship with our local community.
Resource Estimate Methodology
The mineral resource estimate was prepared in accordance with best
practice methods specific to brine resources. The approach includes a reliance
on drilling and sampling methods that yield depth-specific chemistry and
drainable porosity measurements of the brine host rock.
The mineral resource calculation is based on four drilling and sampling
campaigns, which included the following:
<<

--  Completion of 10,523.65m of drilling (6,145.75m of diamond drill and
4,377.90m of rotary holes) divided in 56 drill holes.
--  The deepest hole was 647m.
--  The rotary wells were completed with 8 or 10 inch PVC or iron piping.
They were pumped for over 48 hours to ensure the brine flowed from the
aquifer and that all remaining traces of drill mud was removed. Outflow
was typically sampled at six-hour intervals. All samples were averaged
(typically 6 to 10 samples were collected in each well) and the sample
concentration was attributed to the gravel pack interval of the well.
--  The diamond drill holes were cored with HQ triple tube.
--  Of the 56 holes used for the mineral resource estimate, nine reached the
basement at depths ranging from 50m (in the western boundary of the
salar) to 647m in the eastern border of the salar. All others were
terminated after reaching target depth or due to drill limitations.
--  The total thickness of the basin exceeds 650m on the eastern side, and
brine saturated sediments are present throughout the majority of the
sequence; the exception is relatively fresher-water zones where surface
inflows occur.
--  A total of 230 brine samples plus 74 QA/QC samples were collected from
the drill holes during drilling and from completed wells; and 45 surface
samples were collected from the 3Q and Verde lagunas. Repeat samples
were averaged resulting in 184 unique sample locations, that were used
to calculate the resource estimate.
--  Brine samples were collected from the diamond drill holes during
drilling, using a standard packer technique (both single and double
packer) to obtain samples from discrete levels of the formation.
Fluorescein dye was used to ensure that the samples were representative
of the collection interval. Sampling intervals range from 2m to 50m,
depending on the hole.
--  Brine was sampled (and bathymetry conducted) in Laguna 3Q and Laguna
Verde, located at the north and south ends of the salar, respectively.
Extensive sampling indicates that the brine composition in these lagunas
is essentially continuous with the brine under the salar crust.
--  Brine samples interpreted to reflect the influence of freshwater inflows
(Rio Salado, Rio Nacimiento, and Rio 3Q) were removed from the data set
prior to interpolation. Similarly, volumes of the subsurface associated
with fresher water were also removed from the salar volume for resource
estimation.
<>>
The previous (2018) mineral resource estimate used a search radius
criteria technique to classify measured, indicated and inferred resources. In
the current estimate the approach was revised to a borehole density method.
Both methods are widely used in both brine and hard rock resource estimation.
The borehole density method was considered more appropriate based on an
increasing body of site data, which continue to support spatially predictable
geology and brine trends.
Geology and Brine Model
Geology and brine models were assembled in the numerical modeling
software FEFLOW. Geology was interpreted from surface mapping, diamond
drilling core and rotary borehole logging. Eight primary geological units were
identified:
<<

--  Brine lakes: standing bodies of surface brine at the north and south
ends of the salar complex (Laguna 3Q and Laguna Verde, respectively);
--  Hyper-Porous Halite: karstic, near surface halite (typically less than
50m depth);
--  Upper Sediments: formed by sand, silt and conglomerates located at
surface or near surface;
--  Porous Halite: formed by halite with moderate porosity that is readily
identified by visual methods;
--  Massive Halite: this unit generally occurs as labelled, but often
contains interbedded layers of clay, volcaniclastics, and halite with
greater visible porosity. Consistent with this observation, a range of
tests have indicated potentially important porosity in this unit.
--  Lower Sediments: well rounded sand, silt and minor conglomerates hosted
below the Massive Halite (typically 300m to 500 m deep);
--  Fanglomerates: sedimentary polymictic angular breccia with sand matrix
located below the Lower Sediments and above the Basement, typically
below 500 m depth; and
--  Hydrostratigraphic Basement: Permian andesites and dacites; generally
considered to have negligible or low drainable porosity.
<>>Core samples were packed in Lexan tubing and shipped to Daniel B.
Stephens & Associates Inc. ("DBS"), Inc., a laboratory in the U.S., to measure
Relative Brine Release Capacity (RBRC). This method of porosity determination
is designed to estimate Specific Yield, which is the portion of the total
porosity that can reasonably be expected to drain through pumping. General
porosity trends were consistent with geology, with considerable variability
also noted within geological units.
RBRC was measured in 307 core samples (across all drilling campaigns), to
estimate the Specific Yield of each geological unit. Pumping tests were also
completed in the Hyper-Porous Halite, Upper Sediments and Porous Halite.
A summary of the RBRC measurements and the percentage of the resource in
each unit is provided in Table 4.
Table 4 - RBRC Results and the Distribution of the Resource between the
Primary Geological Units
Hydrostratigraphic         (number sign) of          Average           % of the
Units                   Samples      Specific          Resource
Yield

---





Brine Lakes                                                               1

---

Hyper-Porous Halite(x)                 66             14.74                  11

---



Upper Sediments(x)                     14              9.12                  22

---



Porous Halite(x)                       97              6.33                  16

---



Massive Halite                       84              3.85                  15

---



Lower Sediments                      12              5.18                  11

---



Fanglomerate                         33             11.23                  24

---

Hydrological Basement                 1              1.73                   0

---
(x)Units evaluated with
Pumping Tests
The Hyper-Porous Halite hosts 11% of the resource. A pumping test was
completed in this unit that included the use of fluorescein dye, which enabled
estimation of Effective Porosity, a parameter that is closely related to
Specific Yield. The test provided an Effective Porosity value of 15%, which is
consistent with the average RBRC value for the unit.
The Lower Sediments and Fanglomerates host a combined 35% of the total
resource (almost entirely classified as inferred resource, due to depth and
lower borehole density). Only 13 boreholes penetrate to these units, and only
two completely penetrate the units. Further exploration is required at depth
along the entire salar complex with the objective of converting these inferred
resources into the measured and indicated categories.
The brine data were interpolated directly within FEFLOW, to minimize the
potential for errors in transferring distributions between software packages.
Mass calculations were conducted within FEFLOW, with consideration of the
assigned drainable porosity and the interpolated grade in each model cell.
Further Drilling and Blue Sky
The expansion of the resource estimate in the high-grade zone is based on
the discovery of high-grade brine at depth and to the east (and outside) of
the previous mineral resource estimate. As a result, the company decided to
continue the drilling campaign in the high-grade mineral resource in the next
season (starting September 2021). This follow-up drilling campaign will focus
on the high-grade mineral resource at depth. The deepest hole in the
high-grade zone is currently 365 m, and it did not reach basement. This is
taken as an indication of further discovery potential at depth and to the east
of Laguna 3Q under a large flanking alluvial fan. The upcoming drilling
campaign will not delay the company's work to initiate pond construction in
the coming austral summer, since it is located some distance from the
construction sites.
Qualified Person
Neo Lithium requested Groundwater Insight, Inc. based in Nova Scotia,
Canada to supervise the preparation of an independent lithium brine resource
estimate for the Company's 3Q Project brine deposit in Argentina. Dr. Mark
King, Ph.D., P. Geo., Hydrogeologist with Groundwater Insight Inc., served as
the Qualified Person (QP) for this work, as such terms are defined by NI
43-101. The mineral resource estimate was prepared by Engineer and Numerical
Modeler Paul Martin (P. Eng., Aqua Insight Inc.) using the FEFLOW software.
The current increase of total resources (taking into account measured,
indicated and inferred mineral resource categories) is approximately 9%.
Therefore, the company is of the view that issuance of a new NI 43-101
Technical Report, to document the resource, is not required at this time.
The final Technical Report (including a resource and reserve estimate to
be supervised by Groundwater Insight, Inc.) will be prepared in accordance
with NI 43-101 and will be consistent with the standards and guidelines set
out by the Canadian Institute of Mining, Metallurgy and Petroleum. The report
is now in preparation by Worley, and it will be issued as a Definitive
Feasibility Study at the end of Q3 or beginning of Q4 2021.
Dr. King has read and approved the contents of this news release,
concerning the preparation of the mineral resource estimate. Waldo Perez,
Ph.D. and P.Geo., is the internal Qualified Person for the 3Q Project in
accordance with NI 43-101.
Brine Sample Collection (QA/QC)
The brine samples collected in the field were delivered by the Company to
Andesmar Transport Company ("Andesmar") in Catamarca city, in the province of
Catamarca. Andesmar delivered the samples by truck to Alex Stewart
Laboratories ("ASL"), an ISO 9001-2008-certified laboratory in Mendoza,
Argentina.
ASL used the following analytical methodologies: ICP-OES
(inductively-coupled plasma-optical (atomic) emission spectrometry) to
quantify boron, barium, calcium, lithium, magnesium, manganese, and potassium;
an argentometric method to assay for chloride; a gravimetric method to analyze
for sulfate; a volumetric analysis (acid/base titration) for the evaluation of
alkalinity (as CaCO3); a gravimetric method to determine density and total
dissolved solids; and, a laboratory pH meter to determine pH.
All analytical work is subject to systematic and rigorous Quality
Assurance-Quality Control procedures. A reference ("standard") sample was
inserted into the sample stream at a frequency of approximately 1 in 15
samples; a field blank was inserted at a frequency of approximately 1 in 15
samples; and a field duplicate sample was inserted at a frequency of
approximately 1 in 15 samples.
About Neo Lithium Corp.
Neo Lithium Corp. has quickly become a prominent new name in lithium
brine development by virtue of its high quality 3Q Project and experienced
team. Neo Lithium is rapidly advancing its 100% owned 3Q Project - a unique
high-grade lithium brine lake and salar complex in Latin America's "Lithium
Triangle".
The 3Q Project is located in the Catamarca Province, the largest lithium
producing area in Argentina covering approximately 35,000 ha including a salar
complex of approximately 16,000 ha.
Additional information regarding Neo Lithium Corp. is available on SEDAR
at www.sedar.com under the Company's profile and at its website at
www.neolithium.ca, including various pictures of ongoing work at the project.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this press release.
Cautionary Statements Regarding Forward-Looking Statements - Certain
information set forth in this news release may contain forward-looking
statements. Such statements include but are not limited to, statements
concerning the Sidecar Placement and the Brokered Offering, the intended use
of proceeds therefrom, the Closing Date and receipt of regulatory approvals,
including the approval of the TSXV. Generally, forward-looking statements can
be identified by the use of words such as "plans", "expects" or "is expected",
"scheduled", "estimates" "intends", "anticipates", "believes", or variations
of such words and phrases, or statements that certain actions, events or
results "can", "may", "could", "would", "should", "might" or "will", occur or
be achieved, or the negative connotations thereof. These forward-looking
statements are subject to numerous risks and uncertainties, certain of which
are beyond the control of the Company, which could cause the actual results,
performance or achievements of the Company to be materially different from the
future results, performance or achievements expressed or implied by such
statements. These risks include, without limitation, failure to obtain
adequate financing on a timely basis and on acceptable terms, political and
regulatory risks associated with mining and exploration activities, including
environmental regulation, risks and uncertainties relating to the
interpretation of drill and sample results and to mineral resource and reserve
calculations, risks related to the uncertainty of cost and time estimation and
the potential for unexpected delays, costs and expenses, risks related to
metal price fluctuations, the market for lithium products, and other risks and
uncertainties related to the Company's prospects, properties and business
detailed elsewhere in the Company's disclosure record. Although the Company
believes its expectations are based upon reasonable assumptions and has
attempted to identify important factors that could cause actual actions,
events or results to differ materially from those described in forward-looking
statements, there may be other factors that cause actions, events or results
not to be as anticipated, estimated or intended and undue reliance should not
be placed on forward-looking statements.
SOURCE Neo Lithium Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/June2021/09/c8932.html

-0-                           06/09/2021
/For further information: Neo Lithium Corp., Carlos Vicens,
cvicens(at)neolithium.ca/
/Web Site: http://neolithium.ca/ /
(NTTHF NE2 NLC.)

CO:  Neo Lithium Corp.
ST:  Ontario
IN:  MNG
SU:

-30-