Source	CANADA NEWSWIRE
Date	06/10/2021
Time	04:34:01 AM

Company	 GR Silver Mining Ltd.
Title	GR Silver Mining Intersects 10,777 g/t AgEq Over 0.65 m at the La
Colorada Vein, in the San Juan Area





    CDNX Symbol: GRSL











Press Release




" BC-GRSilverSanJuan   06-10 2620
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.338617:
^GR Silver Mining Intersects 10,777 g/t AgEq Over 0.65 m at the La
Colorada Vein, in the San Juan Area@

VANCOUVER, BC, June 10, 2021 /CNW/ - GR Silver Mining Ltd. (TSXV: GRSL)
(OTCQB: GRSLF) (FRANKFURT: GPE) ("GR Silver Mining" or the "Company") - is
pleased to report drill results representing intersections of high-grade Ag-Au
epithermal veining at the La Colorada and San Juan Veins at the Plomosas
Silver Project ("Plomosas Project") in Sinaloa, Mexico.
Drilling Highlights:
LCS21 -04
<<

--  9.0 m (at) 946 g/t AgEq1, from 170.0 m including 0.65 m (at) 10,777 g/t AgEq
(8,519 g/t Ag, 18.77 g/t Au, 8.9 % Pb, 0.7 % Zn, 0.2 % Cu) from 176.9 m
<>>
SJD-06
<<

--  6.9 m (at) 467 g/t AgEq from 29.6 m, including 2.1 m (at) 1,306 g/t AgEq 
(938
g/t Ag, 3.3 g/t Au, 0.3 % Pb, 0.7 % Zn) from 32.3 m
<>>
SJD-20
<<

--  2.1 m (at) 492 g/t AgEq from 66.8 m
<>>
A listing of significant drill results from the San Juan Area is
presented in Table 1 of Appendix A.
GR Silver Mining President and CEO, Marcio Fonseca, commented "The
results from the 2021 surface drilling program at the La Colorada Vein are
very encouraging. La Colorada, together with the San Juan and Yecora veins,
continue to deliver near surface, high-grade silver and gold results over
significant widths. These results are being incorporated into the maiden San
Juan Area resource estimation, expanding the mineralized zones along strike
and down dip."
San Juan Area Drilling Details
The following figure (Figure 1) illustrates the location of all surface
drill holes released to date on the San Juan Area. The La Colorada and Yecora
Veins represent a combined 1,000 m long vein system parallel to the San Juan
Vein system. Hole LCS21-04 expanded the known mineralization by 50 m to the
south, at a similar elevation to the previously reported high-grade LCS18-03
hole (1,723 g/t AgEq over 2.7 m [15.1 g/t Au, 45 g/t Ag, 3.1 % Pb and 0.9 %
Zn], including 5,055 g/t AgEq over 0.9 m [46.9 g/t Au, 76 g/t Ag, 3.3 % Pb and
2.2 % Zn]). Results from drill hole LCS21-04 also confirm that the La Colorada
Vein is connected along strike with the Yecora Vein, due to the proximity of
previously reported high-grade intersections on both veins (Figure 2).

________________


(1) AgEq is based on long term gold, silver,
zinc, lead and copper prices of US$1,600 per
ounce gold, US$16.50 per ounce silver, US$0.85
per pound zinc, US$0.95 per pound lead and
US$2.00 per pound copper. The metallurgical
recoveries are assumed as 90% Ag, 95% Au, 78%
Pb, 70% Zn and 70% Cu.
Hole LCS21-05, also being reported in this News Release, is located
approximately 100 m south of LCS21-04, The mineralized zone in this hole
returned wide, but lower-grade assays results, including 33.0 m (at) 59 g/t 
AgEq.
Assay results for LCS21-06 to LCS21-11 are pending release from the
laboratory.
The La Colorada vein is a hydrothermal breccia that contains Au-Ag-Pb-Zn
values in a mineralized quartz and hematite matrix. It is hosted in andesite
and ignimbrite country rock. Sphalerite, galena and acanthite (Ag-bearing
mineral) are found in the quartz veins.
The longitudinal section (Figure 2) represents the N-S trend of the San
Juan Area, displaying the location of all surface and underground drill holes
released to date and the upside potential for additional Ag-Au mineralization
to be discovered along strike and down dip.
The Company has released results from a total of 368 surface and
underground drill holes from the Plomosas Project, which also includes the San
Juan Area. All results released for this area are being incorporated into a 3D
model for resource estimation.
Qualified Person
The scientific and technical data contained in this News Release related
to the Plomosas Project was reviewed and/or prepared under the supervision of
Marcio Fonseca, P. Geo. He has approved the disclosure herein.
Quality Assurance Program and Quality Control Procedures ("QA/QC")
The Company has implemented QA/QC procedures which include insertion of
blank, duplicate and standard samples in all sample lots sent to SGS de
México, S.A. de C.V laboratory facilities in Durango, Mexico, for sample
preparation and assaying. For every sample with results above Ag >100 ppm
(over limits), these samples are submitted directly by SGS de Mexico to SGS
Canada Inc at Burnaby, BC. The analytical methods are 4-acid Digest and
Inductively Coupled Plasma Optical Emission Spectrometry with Lead Fusion Fire
Assay with gravimetric finish for silver above over limits. For gold assays
the analytical methods are Lead Fusion and Atomic Absorption Spectrometry Lead
Fusion Fire Assay and gravimetric finish for gold above over limits.
The recent drill holes, completed by First Majestic from 2016 to 2018,
followed QA/QC protocols reviewed and validated by GR Silver Mining, including
insertion of blank and standard samples in all sample lots sent to First
Majestic's Laboratorio Central facilities in La Parilla, Durango, for sample
preparation and assaying. Additional validation and check assays were
performed by an independent laboratory at SGS de México, S.A. de C.V.
facilities in Durango, Mexico. The analytical methods applied for these recent
holes for Ag and Au assays comprised of Fire Assay with Atomic Absorption
finish for samples above Au >10ppm and Ag >300ppm and Gravimetric Finish. Lead
and Zn were analyzed using Inductively Coupled Plasma Optical Emission
Spectrometry. GR Silver Mining has not received information related to the
Grupo Mexico QA/QC and assay protocols and at this stage is considering the
information historic for news release purposes.
About GR Silver Mining Ltd.
GR Silver Mining Ltd. is a Mexico-focused Company engaged in
cost-effective silver-gold resource expansion on its 100%-owned assets which
lie on the eastern edge of the Rosario Mining District, in the southeast of
Sinaloa State, Mexico.
Plomosas Silver Project
GR Silver Mining's 8,515 ha Plomosas Silver Project is located near the
historic mining village of La Rastra and within 5 km of the Company's San
Marcial Silver Project, in the Rosario Mining District. The Project is a
past-producing asset where only one mine, the Plomosas lead-zinc(-silver-gold)
underground mine, operated a 600 tpd crush-mill-flotation circuit from 1986 to
2001, producing approximately 8 M ounces of silver, 73 M pounds of lead and 28
M pounds of zinc.
The March 2020 acquisition of the Plomosas Silver Project included 563
historical and recent drill holes from both surface and underground locations.
These drill holes represent an extensive database allowing the Company to
advance towards resource estimation and potential project development in the
near future.
The Company is completing a drilling program with surface holes focused
on expanding known mineralization along strike in two areas, the Plomosas Mine
Area and the San Juan Area. Underground drilling included in the program is
targeting the extension of recent Au-rich discoveries at the lowest level (775
m RL, or ~250 m below surface) of the Plomosas Mine Area and six low
sulphidation epithermal veins at the San Juan Area. Both areas are currently
the subject of NI 43-101 resource estimations.
The assets include all facilities and infrastructure including access
roads, surface rights agreement, water use permit, 8,000 m of underground
workings, water access, 60 km - 33 KV power line, offices, shops, 120-person
camp, infirmary, warehouses and assay lab representing approximately US$30 M
of previous capital investments. The previous owners invested approximately
US$18 M in exploration, including extensive geophysics and geochemistry
programs.
The silver-gold mineralization on this Project displays the alteration,
textures, mineralogy and deposit geometry characteristics of a low
sulphidation epithermal silver-gold-base metal mineralized vein/breccia
system. Previous exploration was focused on polymetallic (Pb-Zn+/-Ag-Au)
shallow mineralization, hosted in NW-SE structures in the vicinity of the
Plomosas Mine. The E-W portion of the mineralization and extensions of the
main N-S Plomosas Fault remain under-explored.
In addition to the resource potential at Plomosas, a review of the
existing drill hole database, geophysical surveys and geochemical data
covering most of the concession, has defined 16 new exploration targets of
which 11 have high priority for future exploration programs.
San Marcial Project
San Marcial is a near-surface, high-grade silver-lead-zinc open
pit-amenable project. The Company filed a National Instrument 43-101 ("NI
43-101") report entitled "San Marcial Project Resource Estimation and
Technical Report, Sinaloa, Mexico" having an effective date of March 18, 2019
and an amended date of June 10, 2020 (the "Report"), which contains a 36 Moz
AgEq (Indicated) and 11 Moz AgEq (Inferred) resource estimate. The Report was
prepared by Todd McCracken and Marcelo Filipov of WSP Canada Inc. and is
available on SEDAR. The company recently completed over 320 m of underground
development in the San Marcial Resource Area, from which underground drilling
is planned to expand the high-grade portions of the resource down-dip. The
Company recently discovered additional mineralization in the footwall, outside
of the existing resource, and will also be drilling this area. GR Silver
Mining is the first company to conduct exploration at San Marcial in over 10
years.
Recent exploration has identified silver and gold mineralization in areas
previously defined as non-mineralized, discovering evidence of pervasively
altered rocks with intense silicification, veining and associated wide, silver
and gold mineralized zones on the footwall of the NI 43-101 resource area.
La Trinidad Project
The La Trinidad Project was acquired in March 2021. While La Trinidad has
been the focus of artisanal mining activity over many decades, commercial
operations began late in the 20th century. Anaconda Minerals Corp. was first
to drill the project in the mid-late 1980s. After initially taking up an
option on the Project in 1993, Eldorado Gold Corp. then commenced an open pit
gold mine at La Trinidad in 1995, known as the Taunus Pit, with ore being
processed via a heap leach operation. The mine operated until 1998, producing
approximately 52,000 oz of gold2.
Exploration undertaken by Oro Gold from 2006 identified additional
resources below the Taunus Pit and operations recommenced late in 2014. Gold
output from the heap leach pads continued until late 2019 for a total
cumulative production by Oro Gold of 112,000 oz gold3,4. In addition to La
Trinidad, the portfolio acquired by GR Silver Mining includes an extensive
regional database of geological, geochemical and geophysical information
resulting from historical exploration expenditure by Oro Gold of more than
CDN$18.6 M since 2006.
Cimarron Project
Cimarron is another advanced stage project that was acquired along with
the La Trinidad Project in March 2021 and is located 40 km to the NW of La
Trinidad. A number of targets have been identified at Cimarron including
Calerita, El Prado, Huanacaxtle, Betty and Veteranos, however Calerita is the
only target to have been drilled to date. The near surface historical Inferred
Resource at the Calerita prospect contains 3.7 Mt at 0.65 g/t Au for
approximately 77,000 oz of gold5, which is considered to be open along strike
and down dip.
While the 2011 resource is considered by GR Silver Mining to be a
historical resource, the Company considers the resource estimate as being
relevant and reliable, considering a lack of significant additional
exploration work since its release. A key parameter in the historical resource
is the usage of a US$1,200/oz gold price compared to a much higher current
spot gold price. A Qualified Person (QP) would be required to review the
historical resource report and make recommendations in order to verify and
upgrade it to a current resource. A QP has not done sufficient work to
classify the historical estimate as current mineral resources. The Company is
treating the 2011 resource estimate as a historical estimate. The company
plans to re-assess the work completed by previous owners and define the
feasibility of additional drilling, aiming at identifying additional
near-surface mineralization.
The Plomosas, San Marcial and La Trinidad Projects collectively represent
a geological setting resembling the multi-million-ounce San Dimas Mining
District which has historically produced more than 600 Moz Ag and 11 Moz Au
over a period of more than 100 years.
Other Projects
GR Silver Mining's other projects are situated in areas attractive for
future discoveries and development in the same vicinity of Plomosas, La
Trinidad and San Marcial in the Rosario Mining District. Following the
acquisition of Marlin Gold Mining Ltd. ("Marlin") in March 2021, GR Silver
Mining controls a concession portfolio of over 1,000 km2, two previously
producing mines fully permitted for future developments and a total combined
75 km of structures with field evidence of 24 Ag-Au veins in historic old
workings.

___________


(2) Refer to Marlin Gold Mining
Ltd. 2nd Amended NI 43-101
Technical Report dated February
1, 2013


(3) Refer to Marlin Gold Mining
Ltd. MD&A dated April 30, 2015,
April 29, 2016, May 1, 2017,
April 30, 2018, August 29, 2018


4 Refer to Mako Mining Corp. MD&A
dated August 28, 2019, April 29,
2020


5 Refer to Oro Mining Ltd. NI
43-101 Technical Report dated
March 18, 2011
GR Silver Mining Ltd.Mr. Marcio Fonseca, P. Geo.President & CEO
Facebook LinkedIn Twitter
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accept
responsibility for the adequacy or accuracy of this press release.
Disclaimer for Forward-Looking Information
This press release contains forward-looking statements and information
that are based on the beliefs of management and reflect the Company's current
expectations. When used in this press release, the words "estimate","project", 
"belief", "anticipate", "intend", "expect", "plan", "predict",
"may" or "should" and the negative of these words or such variations thereon
or comparable terminology are intended to identify forward-looking statements
and information. Such statements and information reflect the current view of
the Company. Risks and uncertainties may cause actual results to differ
materially from those contemplated in those forward-looking statements and
information. By their nature, forward-looking statements involve known and
unknown risks, uncertainties and other factors which may cause our actual
results, performance or achievements, or other future events, to be materially
different from any future results, performance or achievements expressed or
implied by such forward-looking statements.
Appendix A
Table 1: Drill Hole Assay Results for this June 10, 2021 News Release
From       To        Drilled         True     Ag        Au     Pb %     Zn 
%        Cu %            AgEq
(m)       (m)       width           width      g/t       
g/t                                         g/t
Hole No.                              (m)             (m)

---

LCS21-04                    170.0     179.0             9.0                  
710       1.82      1.1      0.3            0.1             946

---

includes     176.9     177.5             0.7                8,519      
18.77      8.9      0.7            0.2          10,777

---

LCS21-05                               165.3     198.3            
33.0                   20       0.11      0.5      0.3 
n/a        

" BC-GRSilverSanJuan   06-10 2620
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.338617:
^GR Silver Mining Intersects 10,777 g/t AgEq Over 0.65 m at the La
Colorada Vein, in the San Juan Area@

VANCOUVER, BC, June 10, 2021 /CNW/ - GR Silver Mining Ltd. (TSXV: GRSL)
(OTCQB: GRSLF) (FRANKFURT: GPE) ("GR Silver Mining" or the "Company") - is
pleased to report drill results representing intersections of high-grade Ag-Au
epithermal veining at the La Colorada and San Juan Veins at the Plomosas
Silver Project ("Plomosas Project") in Sinaloa, Mexico.
Drilling Highlights:
LCS21 -04
<<

--  9.0 m (at) 946 g/t AgEq1, from 170.0 m including 0.65 m (at) 10,777 g/t AgEq
(8,519 g/t Ag, 18.77 g/t Au, 8.9 % Pb, 0.7 % Zn, 0.2 % Cu) from 176.9 m
<>>
SJD-06
<<

--  6.9 m (at) 467 g/t AgEq from 29.6 m, including 2.1 m (at) 1,306 g/t AgEq 
(938
g/t Ag, 3.3 g/t Au, 0.3 % Pb, 0.7 % Zn) from 32.3 m
<>>
SJD-20
<<

--  2.1 m (at) 492 g/t AgEq from 66.8 m
<>>
A listing of significant drill results from the San Juan Area is
presented in Table 1 of Appendix A.
GR Silver Mining President and CEO, Marcio Fonseca, commented "The
results from the 2021 surface drilling program at the La Colorada Vein are
very encouraging. La Colorada, together with the San Juan and Yecora veins,
continue to deliver near surface, high-grade silver and gold results over
significant widths. These results are being incorporated into the maiden San
Juan Area resource estimation, expanding the mineralized zones along strike
and down dip."
San Juan Area Drilling Details
The following figure (Figure 1) illustrates the location of all surface
drill holes released to date on the San Juan Area. The La Colorada and Yecora
Veins represent a combined 1,000 m long vein system parallel to the San Juan
Vein system. Hole LCS21-04 expanded the known mineralization by 50 m to the
south, at a similar elevation to the previously reported high-grade LCS18-03
hole (1,723 g/t AgEq over 2.7 m [15.1 g/t Au, 45 g/t Ag, 3.1 % Pb and 0.9 %
Zn], including 5,055 g/t AgEq over 0.9 m [46.9 g/t Au, 76 g/t Ag, 3.3 % Pb and
2.2 % Zn]). Results from drill hole LCS21-04 also confirm that the La Colorada
Vein is connected along strike with the Yecora Vein, due to the proximity of
previously reported high-grade intersections on both veins (Figure 2).

________________


(1) AgEq is based on long term gold, silver,
zinc, lead and copper prices of US$1,600 per
ounce gold, US$16.50 per ounce silver, US$0.85
per pound zinc, US$0.95 per pound lead and
US$2.00 per pound copper. The metallurgical
recoveries are assumed as 90% Ag, 95% Au, 78%
Pb, 70% Zn and 70% Cu.
Hole LCS21-05, also being reported in this News Release, is located
approximately 100 m south of LCS21-04, The mineralized zone in this hole
returned wide, but lower-grade assays results, including 33.0 m (at) 59 g/t 
AgEq.
Assay results for LCS21-06 to LCS21-11 are pending release from the
laboratory.
The La Colorada vein is a hydrothermal breccia that contains Au-Ag-Pb-Zn
values in a mineralized quartz and hematite matrix. It is hosted in andesite
and ignimbrite country rock. Sphalerite, galena and acanthite (Ag-bearing
mineral) are found in the quartz veins.
The longitudinal section (Figure 2) represents the N-S trend of the San
Juan Area, displaying the location of all surface and underground drill holes
released to date and the upside potential for additional Ag-Au mineralization
to be discovered along strike and down dip.
The Company has released results from a total of 368 surface and
underground drill holes from the Plomosas Project, which also includes the San
Juan Area. All results released for this area are being incorporated into a 3D
model for resource estimation.
Qualified Person
The scientific and technical data contained in this News Release related
to the Plomosas Project was reviewed and/or prepared under the supervision of
Marcio Fonseca, P. Geo. He has approved the disclosure herein.
Quality Assurance Program and Quality Control Procedures ("QA/QC")
The Company has implemented QA/QC procedures which include insertion of
blank, duplicate and standard samples in all sample lots sent to SGS de
México, S.A. de C.V laboratory facilities in Durango, Mexico, for sample
preparation and assaying. For every sample with results above Ag >100 ppm
(over limits), these samples are submitted directly by SGS de Mexico to SGS
Canada Inc at Burnaby, BC. The analytical methods are 4-acid Digest and
Inductively Coupled Plasma Optical Emission Spectrometry with Lead Fusion Fire
Assay with gravimetric finish for silver above over limits. For gold assays
the analytical methods are Lead Fusion and Atomic Absorption Spectrometry Lead
Fusion Fire Assay and gravimetric finish for gold above over limits.
The recent drill holes, completed by First Majestic from 2016 to 2018,
followed QA/QC protocols reviewed and validated by GR Silver Mining, including
insertion of blank and standard samples in all sample lots sent to First
Majestic's Laboratorio Central facilities in La Parilla, Durango, for sample
preparation and assaying. Additional validation and check assays were
performed by an independent laboratory at SGS de México, S.A. de C.V.
facilities in Durango, Mexico. The analytical methods applied for these recent
holes for Ag and Au assays comprised of Fire Assay with Atomic Absorption
finish for samples above Au >10ppm and Ag >300ppm and Gravimetric Finish. Lead
and Zn were analyzed using Inductively Coupled Plasma Optical Emission
Spectrometry. GR Silver Mining has not received information related to the
Grupo Mexico QA/QC and assay protocols and at this stage is considering the
information historic for news release purposes.
About GR Silver Mining Ltd.
GR Silver Mining Ltd. is a Mexico-focused Company engaged in
cost-effective silver-gold resource expansion on its 100%-owned assets which
lie on the eastern edge of the Rosario Mining District, in the southeast of
Sinaloa State, Mexico.
Plomosas Silver Project
GR Silver Mining's 8,515 ha Plomosas Silver Project is located near the
historic mining village of La Rastra and within 5 km of the Company's San
Marcial Silver Project, in the Rosario Mining District. The Project is a
past-producing asset where only one mine, the Plomosas lead-zinc(-silver-gold)
underground mine, operated a 600 tpd crush-mill-flotation circuit from 1986 to
2001, producing approximately 8 M ounces of silver, 73 M pounds of lead and 28
M pounds of zinc.
The March 2020 acquisition of the Plomosas Silver Project included 563
historical and recent drill holes from both surface and underground locations.
These drill holes represent an extensive database allowing the Company to
advance towards resource estimation and potential project development in the
near future.
The Company is completing a drilling program with surface holes focused
on expanding known mineralization along strike in two areas, the Plomosas Mine
Area and the San Juan Area. Underground drilling included in the program is
targeting the extension of recent Au-rich discoveries at the lowest level (775
m RL, or ~250 m below surface) of the Plomosas Mine Area and six low
sulphidation epithermal veins at the San Juan Area. Both areas are currently
the subject of NI 43-101 resource estimations.
The assets include all facilities and infrastructure including access
roads, surface rights agreement, water use permit, 8,000 m of underground
workings, water access, 60 km - 33 KV power line, offices, shops, 120-person
camp, infirmary, warehouses and assay lab representing approximately US$30 M
of previous capital investments. The previous owners invested approximately
US$18 M in exploration, including extensive geophysics and geochemistry
programs.
The silver-gold mineralization on this Project displays the alteration,
textures, mineralogy and deposit geometry characteristics of a low
sulphidation epithermal silver-gold-base metal mineralized vein/breccia
system. Previous exploration was focused on polymetallic (Pb-Zn+/-Ag-Au)
shallow mineralization, hosted in NW-SE structures in the vicinity of the
Plomosas Mine. The E-W portion of the mineralization and extensions of the
main N-S Plomosas Fault remain under-explored.
In addition to the resource potential at Plomosas, a review of the
existing drill hole database, geophysical surveys and geochemical data
covering most of the concession, has defined 16 new exploration targets of
which 11 have high priority for future exploration programs.
San Marcial Project
San Marcial is a near-surface, high-grade silver-lead-zinc open
pit-amenable project. The Company filed a National Instrument 43-101 ("NI
43-101") report entitled "San Marcial Project Resource Estimation and
Technical Report, Sinaloa, Mexico" having an effective date of March 18, 2019
and an amended date of June 10, 2020 (the "Report"), which contains a 36 Moz
AgEq (Indicated) and 11 Moz AgEq (Inferred) resource estimate. The Report was
prepared by Todd McCracken and Marcelo Filipov of WSP Canada Inc. and is
available on SEDAR. The company recently completed over 320 m of underground
development in the San Marcial Resource Area, from which underground drilling
is planned to expand the high-grade portions of the resource down-dip. The
Company recently discovered additional mineralization in the footwall, outside
of the existing resource, and will also be drilling this area. GR Silver
Mining is the first company to conduct exploration at San Marcial in over 10
years.
Recent exploration has identified silver and gold mineralization in areas
previously defined as non-mineralized, discovering evidence of pervasively
altered rocks with intense silicification, veining and associated wide, silver
and gold mineralized zones on the footwall of the NI 43-101 resource area.
La Trinidad Project
The La Trinidad Project was acquired in March 2021. While La Trinidad has
been the focus of artisanal mining activity over many decades, commercial
operations began late in the 20th century. Anaconda Minerals Corp. was first
to drill the project in the mid-late 1980s. After initially taking up an
option on the Project in 1993, Eldorado Gold Corp. then commenced an open pit
gold mine at La Trinidad in 1995, known as the Taunus Pit, with ore being
processed via a heap leach operation. The mine operated until 1998, producing
approximately 52,000 oz of gold2.
Exploration undertaken by Oro Gold from 2006 identified additional
resources below the Taunus Pit and operations recommenced late in 2014. Gold
output from the heap leach pads continued until late 2019 for a total
cumulative production by Oro Gold of 112,000 oz gold3,4. In addition to La
Trinidad, the portfolio acquired by GR Silver Mining includes an extensive
regional database of geological, geochemical and geophysical information
resulting from historical exploration expenditure by Oro Gold of more than
CDN$18.6 M since 2006.
Cimarron Project
Cimarron is another advanced stage project that was acquired along with
the La Trinidad Project in March 2021 and is located 40 km to the NW of La
Trinidad. A number of targets have been identified at Cimarron including
Calerita, El Prado, Huanacaxtle, Betty and Veteranos, however Calerita is the
only target to have been drilled to date. The near surface historical Inferred
Resource at the Calerita prospect contains 3.7 Mt at 0.65 g/t Au for
approximately 77,000 oz of gold5, which is considered to be open along strike
and down dip.
While the 2011 resource is considered by GR Silver Mining to be a
historical resource, the Company considers the resource estimate as being
relevant and reliable, considering a lack of significant additional
exploration work since its release. A key parameter in the historical resource
is the usage of a US$1,200/oz gold price compared to a much higher current
spot gold price. A Qualified Person (QP) would be required to review the
historical resource report and make recommendations in order to verify and
upgrade it to a current resource. A QP has not done sufficient work to
classify the historical estimate as current mineral resources. The Company is
treating the 2011 resource estimate as a historical estimate. The company
plans to re-assess the work completed by previous owners and define the
feasibility of additional drilling, aiming at identifying additional
near-surface mineralization.
The Plomosas, San Marcial and La Trinidad Projects collectively represent
a geological setting resembling the multi-million-ounce San Dimas Mining
District which has historically produced more than 600 Moz Ag and 11 Moz Au
over a period of more than 100 years.
Other Projects
GR Silver Mining's other projects are situated in areas attractive for
future discoveries and development in the same vicinity of Plomosas, La
Trinidad and San Marcial in the Rosario Mining District. Following the
acquisition of Marlin Gold Mining Ltd. ("Marlin") in March 2021, GR Silver
Mining controls a concession portfolio of over 1,000 km2, two previously
producing mines fully permitted for future developments and a total combined
75 km of structures with field evidence of 24 Ag-Au veins in historic old
workings.

___________


(2) Refer to Marlin Gold Mining
Ltd. 2nd Amended NI 43-101
Technical Report dated February
1, 2013


(3) Refer to Marlin Gold Mining
Ltd. MD&A dated April 30, 2015,
April 29, 2016, May 1, 2017,
April 30, 2018, August 29, 2018


4 Refer to Mako Mining Corp. MD&A
dated August 28, 2019, April 29,
2020


5 Refer to Oro Mining Ltd. NI
43-101 Technical Report dated
March 18, 2011
GR Silver Mining Ltd.Mr. Marcio Fonseca, P. Geo.President & CEO
Facebook LinkedIn Twitter
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accept
responsibility for the adequacy or accuracy of this press release.
Disclaimer for Forward-Looking Information
This press release contains forward-looking statements and information
that are based on the beliefs of management and reflect the Company's current
expectations. When used in this press release, the words "estimate","project", 
"belief", "anticipate", "intend", "expect", "plan", "predict",
"may" or "should" and the negative of these words or such variations thereon
or comparable terminology are intended to identify forward-looking statements
and information. Such statements and information reflect the current view of
the Company. Risks and uncertainties may cause actual results to differ
materially from those contemplated in those forward-looking statements and
information. By their nature, forward-looking statements involve known and
unknown risks, uncertainties and other factors which may cause our actual
results, performance or achievements, or other future events, to be materially
different from any future results, performance or achievements expressed or
implied by such forward-looking statements.
Appendix A
Table 1: Drill Hole Assay Results for this June 10, 2021 News Release
From       To        Drilled         True     Ag        Au     Pb %     Zn 
%        Cu %            AgEq
(m)       (m)       width           width      g/t       
g/t                                         g/t
Hole No.                              (m)             (m)

---

LCS21-04                    170.0     179.0             9.0                  
710       1.82      1.1      0.3            0.1             946

---

includes     176.9     177.5             0.7                8,519      
18.77      8.9      0.7            0.2          10,777

---

LCS21-05                               165.3     198.3            
33.0                   20       0.11      0.5      0.3 
n/a                        59

---


LRD-23                                  29.3      40.4            
11.1                  139       0.69      0.1      0.2        
n/a                218

---


LRD-25                                  77.0      89.2            
12.3                  100       0.05      0.3      0.6 
n/a                       134

---

SJD-05      17.6      17.8             0.2                1,160       0.05      
0.3      0.4            0.1           1,185

---

SJD-06                       29.6      36.5             7.0                  
341       1.00      0.2      0.6            n/a            467

---

includes      32.3      34.4             2.1                  938       
3.30      0.3      0.7            n/a          1,306

---

SJD-20                       66.8      68.9             2.1                  
480       0.05      0.2      0.2            n/a            492

---


SJS-01                                 212.4     218.4             
6.0                   73       0.04      0.1      0.4 
n/a                        92

---
AgEq is based on long term gold,
silver, zinc, lead and copper
prices of US$1,600 per ounce
gold, US$16.50 per ounce
silver, US$0.85 per pound zinc,
US$0.95 per pound lead and
US$2.00 per pound copper. The
metallurgical recoveries are
assumed as 90% Ag, 95% Au, 78%
Pb, 70% Zn and 70% Cu. All
numbers are rounded. Results
are uncut and undiluted. "n/a"
(equal sign) no relevant assays.
Table 2: Drill Hole Locations
Hole
No.   East (m) North (m)  RL (m)   Dip ()    Azimuth ()     Depth (m)

Type


---

LCS21-04(x)   447889    2551115      888       -60            250            179
SURFACE

---

LCS21-05(x)   447895    2551043      867       -50            250            213
SURFACE

---

LRD-
23         448189    2550609      885       -90              0          53.55
SURFACE

---

LRD-
25         448208    2550625      901       -90              0          92.65
SURFACE

---

SJD-
05         448154    2550675      872       -50            235           40.0
UG

---

SJD-
06         448155    2550669      872       -45            195           54.6
UG

---

SJD-
20         448203    2550674      873       -70            336           77.2
UG

---

SJS-
01         448422    2550616      976       -90              0          283.6
SURFACE

---
(x) drill holes are drilled by
GRSL and remaining holes
represent historic drill
holes drilled by Grupo
Mexico.; East (m) and North
(m) are UTM coordinates in
WGS84, zone 13. All numbers
are rounded.

SOURCE GR Silver Mining Ltd.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/June2021/10/c0974.html

-0-                           06/10/2021
/For further information: Please contact: Brenda Dayton, VP Corporate
Communications, Telephone: +1.604.558.6248, Email: 
bdayton(at)grsilvermining.com/
/Web Site: http://www.grsilvermining.com/ /
(GRSLF GRSL. GPE)

CO:  GR Silver Mining Ltd.
ST:  British Columbia
IN:  MIN MNG PRM OTC
SU:

-30-