Source	CANADA NEWSWIRE
Date	06/14/2021
Time	04:02:53 AM

Company	 K2 Gold Corporation
Title	K2 Reports Significant Gold Mineralization on Western Side of Mojave
Property





    CDNX Symbol: KTO











Press Release




" BC-K2Gold-MojaveProperty   06-14 2452
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.304452:
^K2 Reports Significant Gold Mineralization on Western Side of Mojave
Property@

TSX-V: KTO
VANCOUVER, BC, June 14, 2021 /CNW/ - K2 Gold Corporation ("K2" or the
"Company") (TSXV: KTO) (OTCQB: KTGDF; FRANKFURT: 23K) is pleased to report
that it has successfully expanded the gold mineralization footprint at the
Stega Target on the western side of the Company's Mojave project in Southern
California. A total of 42 prospecting rock/grab samples and 385 continuous
chip-channel samples over five lines were collected on the Stega gold zone
("Stega Gold Zone").
Highlights:
<<

--  Recent sampling expands the gold zone at the Stega target to an area of
800m x 1,800m.
--  Remains open to the NW and may extend to the Boland target, 1.2 km to
the SE.
--  1,051 samples have been collected on the Stega Gold Zone and includes 87
samples >1 g/t Au and 126 samples >0.5 g/t Au (up to 12.68 g/t Au).
<>>
"The expansion of the Stega Gold Zone, parallel to the recently announced
Stega Copper Zone, is further evidence of the overall mineral endowment of the
Mojave Project," stated Jodie Gibson, Vice President of Exploration for K2.
"The work completed to date, together with work in progress, are providing us
with a greater understanding of the geological controls of the gold, copper,
and base metal mineralization at Mojave and will help guide our future
exploration and drilling efforts."
Steve Swatton, President and CEO of K2 added: "As we move west from the
Newmont gold zone, the property continues to deliver exciting exploration
results from various disparate locations, some anticipated but most are new.
The vectorisation of the mineral zones is particularly intriguing, and we
expect to find further mineralized zones as we continue exploring to the west.
I am also pleased to report that the permitting process for the next phase of
drilling at Dragonfly / Newmont is nearing the 30-day public consultation
stage with the Bureau of Land Management expected to soon post our Plan of
Operations for public input."
Please CLICK HERE to view all figures related to this news release.
Stega Target
The Stega target is located on the western side of the Mojave property,
approximately 3.4km NW of the Newmont target, covering a 1.5km x 2km NW
trending zone of alteration and mineralization in strongly folded and faulted
Triassic siltstone, limestone, and shales with at least two generations of
porphyritic sills and dikes. Mineralization on the target is polymetallic and
shows a sharp zonation consisting of a silver-lead (+/- zinc) zone, a central
copper zone, and an eastern gold zone. Individual mineralized zones are hosted
along NW oriented normal faults and NE trending thrust faults and fold hinges,
and are typically associated with silicification, quartz-carbonate veining,
strong iron-oxide development, sericite - argillic alteration (gold-copper
zones), and/or propylitic alteration (silver-lead zones). The mineralization
is interpreted as intrusion-related and shows strong similarities to
polymetallic skarn, replacement, and/or structurally controlled mineralization
in the Cerro Gordo district, 5.5km to the north.
Stega Gold Zone
A total of 42 prospecting rock/grab samples and 385 continuous
chip-channel samples over five lines were collected on the Stega Gold Zone.
The sampling was conducted to follow up on the southern extension of the gold
zone. Sampling performed in the central portion of the zone by the Company in
2020 included continuous rock chip samples of 5.14 g/t Au over 11.6m and
individual samples up to 10.8 g/t Au (see the Company's news release dated
July 2, 2020). The southern portion of the gold zone was the focus of historic
exploration efforts by Mobil Mineral Resources and Asamera in the mid 1980's
and the historic work included the placement of one trench and 19 shallow
drill holes for 703.87m. Highlights of the historic work include 5.28 g/t Au
over 5.33m from the trench and hole DG87-02: 1.82 g/t Au over 7.62m from
12.19m depth (Clarke 1986 & Niemeyer 1987).
Table 1: Highlights of Historic Trenching and Drilling on the Stega
Target


Hole ID From (m) To (m)  Int (m)   Au (g/t)

---


Surface Trench            0    5.33      5.33        5.28

---


DG-01                  9.45   23.17     13.72        0.86

---


DG87-02               12.19   19.81      7.62        1.82

---


DG87-09                9.14   22.86     13.72        0.75

---



Incl.      18.29   22.86      4.57        1.13

---
These drill results are historical in nature and the Company has not
undertaken any independent investigation of the sampling nor has it
independently analyzed the results of the historical exploration work to
verify the results.
Individual results from the program ranged from trace to 7.84 g/t gold
and the gold mineralization is associated with anomalous
arsenic-antimony-mercury and locally anomalous lead (up to 0.28% Pb), zinc (up
to 0.23% Zn), and molybdenum (up to 99ppm Mo). The mineralization is hosted
within a sequence of strongly folded and faulted Triassic limestone and
siltstone with mineralization occurring along structural zones and lithologic
contacts and is associated with quartz-sericite alteration and strong
iron-oxide development.
Highlights of the sampling include:
21-MOC-001
Consisted of a 9m continuous chip line along a NW trending outcrop of
silicified limestone with a historic adit. The line returned 0.51 g/t gold
over 9m; starting and ending in mineralization.
21-MOC-002
Consisted of a 47.5m continuous chip line across outcrop of strongly
silicified limestone adjacent to a NW trending normal fault. The line returned
0.28 g/t gold over 33m.
21-MOT-003
Consisted of a NW trending 25m channel along the trace of the historic
Asamera trench. The channel returned 1.7 g/t gold over 15m; starting in
mineralization. This includes a higher-grade zone of 3.4 g/t gold over 7m. The
mineralization occurs within strongly sericite altered siltstone with local
silicification and strong iron-oxide development at the intersection of a NW
trending normal fault and NE trending thrust fault.
21-MOT-004
Consisted of a NE trending 20m channel that crosses 21-MOT-003. The
channel returned 2.25 g/t gold over 20m; starting and ending in
mineralization. The mineralization occurs within strongly sericite altered
siltstone and silicified limestone with strong iron-oxide development at the
intersection of a NW trending normal fault and NE trending thrust fault.
21-MOT-005
Consisted of a 155m channel along a NE plunging fold hinge approximately
250m SW of 21-MOT-003/004. The channel returned 0.95 g/t gold over 48m;
including 1.68 g/t gold over 25.3m. The mineralization occurs within a folded
sequence of silicified limestone and sericite altered siltstone that is
interpreted to occur in the hanging wall of the thrust fault associated with
mineralization in 21-MOT-003. Silicification and strong iron oxide development
occurs along the hinge of the fold, in all units, with the strongest
mineralization at lithologic contacts. Prospecting samples of 2.88 g/t Au,
2.52 g/t Au, and 2.13 g/t Au from separate 1 -2m chips were also collected
along the trend.
Combined with historic sampling, the Stega Gold Zone is up to 600m in
width, 1.8km in length, and is open to the NW and may extend to the Boland
target, 1.2 km to the SE. Including work by the Company, 1,051 samples have
been collected on the Stega Gold Belt and includes 87 samples >1 g/t Au and
126 samples >0.5 g/t Au (up to 12.68 g/t Au). Numerous historic workings occur
along the trend and additional work is in progress to fully evaluate the zone
and identify potential drill targets including geologic mapping, soil
sampling, chip-channel sampling, and heliborne EM-resistivity (VTEM),
magnetic, and radiometric surveys. Additional results from the ongoing work on
the Stega, and other targets on the Mojave property, will be released in due
course.
Exploration Overview at Mojave
This work is part of an on-going evaluation of the entire Mojave
property. The 2021 exploration results now confirm previous work from the
1980's and 1990's that interpreted the entire Mojave project area as part a
large multi-commodity mineral zone that hosts gold, silver, copper and other
base metals. The broader district has seen exploration and mining activity
from the mid 1800's to present. This includes the Cerro Gordo district which
produced an estimated 4.4 million ounces of silver, 37 tons of lead, and
12,000 tons of zinc with lesser amounts of gold and copper (Merriam 1963); the
Santa Rosa Mine which produced 76,584 tons of ore averaging 0.45 g/t gold,
397.7 g/t silver, 16.3% lead, and 0.7% copper (MacKevatt 1953 & Dixon 1991);
and numerous other high-grade gold, silver, and base-metal mines and
prospects. The gold, as reported by K2 from the Eastern Target Areas was
discovered only more recently (1980's and 1990's).
A VTEM (+ magnetics and radiometrics) geophysical survey has also
recently been completed over the Mojave property, and is currently being
processed. The survey consisted of 1036 line-km on 50m spaced lines and
covered all known target areas on the property. This includes the Owens, a
target identified by previous operators as having potential for porphyry
copper mineralization beneath colluvial cover 3km to the west of Stega. Ionic
leach sampling is also planned on the Owens target and other areas of
colluvial cover including Upland Valley. Results of the VTEM, in combination
with rock, soil, and ionic leach geochemistry and previously completed
WorldView-3 and LiDAR surveys, will assist in the interpretation and
definition of drill targets outside of the Eastern Target area.
All mineralization at Mojave is interpreted to be part of an intrusion
related polymetallic system(s). The gold mineralization in the Eastern Area
(Dragonfly, Newmont, Flores) is structurally controlled with similarities to
both low sulfidation epithermal and Carlin type systems and may represent the
distal expression of a much larger intrusion-related hydrothermal system.
Whereas targets on the Western target area including Stega, Boland, Belshaw,
Soda Canyon/Soda Ridge, and, potentially, Owens are likely proximal to
causative intrusions and demonstrate the potential for sediment-hosted,
polymetallic, skarn, epithermal, and, potentially, porphyry styles of
mineralization.
Next Steps for 2021 Drilling Plan Taken
The USDI Bureau of Land Management ("BLM") is taking the next actions for
the environmental review process of the Mojave Project Exploration Drilling
and will be announcing a 30-day period for public input on the issues to be
evaluated. The BLM intends to post the Plan of Operations, an overview of the
project and the items for preliminary consideration in an Environmental
Assessment.
Assay Methodology & QA/QC
The analytical work on the Mojave project is being performed by MSALABS
an internationally recognized analytical services provider, at its laboratory
in Langley, British Columbia. All rock and drilling samples will be prepared
using procedure PRP-910 (dry, crush to 70% passing 2mm, riffle split off 250g,
pulverize split to better than 85% passing 75 microns) and analyzed by method
FAS-111 (30g fire assay with AAS finish) and IMS-130 (0.5g, aqua regia
digestion and ICP-AES/MS analysis). Any samples containing >10g/t Au will be
reanalyzed using method FAS-415 (30g Fire Assay with gravimetric finish).
Samples containing >100 ppm Ag and/or >1% Cu, Pb, & Zn will be reanalyzed
using method ICF-6 (0.2g, 4-acid digest and ore grade ICP-AES analysis).
The reported work was completed using industry standard procedures,
including a quality assurance/quality control ("QA/QC") program consisting of
the insertion of certified standard, blanks and duplicates into the sample
stream.
About K2
K2 is a well-financed gold exploration company with approximately C$5M
and projects in SW USA and the Yukon. In the USA, the Company is represented
by its 100% subsidiary, Mojave Precious Metals Inc. ("MPM"). The Company is
focused on the Mojave property in California, a 5,830-hectare oxide gold
project with base metal targets. The location of Mojave enables the Company to
have year-round news flow on multiple previously recognized surface gold
targets that have been successfully drilled in the past by majors BHP and
Newmont. Besides affording immediate drill targets based on the Company's soil
data integrated with LiDAR and Worldview-3 data, the property also has
undrilled locations with gold enriched historical trench results including one
at the Flores zone which recorded 8.4 g/t gold over 25.6m (see October 30,
2013 news release from Great Bear Resources Ltd.).
K2 and MPM are committed to transparency, accountability, environmental
stewardship, safety, diversity and inclusion, and community engagement.
On behalf of the Board of Directors,
"Stephen Swatton"
President and CEO
K2 Gold Corporation.
K2 Gold Corporation is a member of Discovery Group based in Vancouver,
Canada. For more information please visit: discoverygroup.ca.
Cautionary Statement on Forward-Looking Statements
This news release contains forward-looking statements that are not
historical facts. Forward-looking statements involve risks, uncertainties and
other factors that could cause actual results, performance, prospects and
opportunities to differ materially from those expressed or implied by such
forward-looking statements, including statements regarding the exploration
program at Mojave, including results of drilling, and future exploration plans
at Mojave. Factors that could cause actual results to differ materially from
these forward-looking statements include, but are not limited to, variations
in the nature, quality and quantity of any mineral deposits that may be
located, the Company's inability to obtain any necessary permits, consents or
authorizations required for its planned activities, and the Company's
inability to raise the necessary capital or to be fully able to implement its
business strategies. The reader is referred to the Company's public disclosure
record which is available on SEDAR (www.sedar.com). Although the Company
believes that the assumptions and factors used in preparing the
forward-looking statements are reasonable, undue reliance should not be placed
on these statements, which only apply as of the date of this news release, and
no assurance can be given that such events will occur in the disclosed time
frames or at all. Except as required by securities laws and the policies ofthe 
TSX Venture Exchange, the Company disclaims any intention or obligation to
update or revise any forward-looking statement, whether as a result of new
information, future events or otherwise.
This news release does not constitute an offer to sell or a solicitation
of an offer to buy, nor shall there be any sale of any of the securities in
any jurisdiction in which such offer, solicitation or sale would be unlawful,
including any of the securities in the United States of America. No securities
of the Company have been or will, in the foreseeable future, be registered
under the United States Securities Act of 1933 (the "1933 Act") or any state
securities laws and may not be offered or sold within the United States or to,
or for account or benefit of, U.S. Persons (as defined in Regulation S under
the 1933 Act) unless registered under the 1933 Act and applicable state
securities laws, or an exemption from such registration requirements is
available.
NEITHER TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS
THAT TERM IS DEFINED IN POLICIES OF THE TSX VENTURE 

" BC-K2Gold-MojaveProperty   06-14 2452
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention co.304452:
^K2 Reports Significant Gold Mineralization on Western Side of Mojave
Property@

TSX-V: KTO
VANCOUVER, BC, June 14, 2021 /CNW/ - K2 Gold Corporation ("K2" or the
"Company") (TSXV: KTO) (OTCQB: KTGDF; FRANKFURT: 23K) is pleased to report
that it has successfully expanded the gold mineralization footprint at the
Stega Target on the western side of the Company's Mojave project in Southern
California. A total of 42 prospecting rock/grab samples and 385 continuous
chip-channel samples over five lines were collected on the Stega gold zone
("Stega Gold Zone").
Highlights:
<<

--  Recent sampling expands the gold zone at the Stega target to an area of
800m x 1,800m.
--  Remains open to the NW and may extend to the Boland target, 1.2 km to
the SE.
--  1,051 samples have been collected on the Stega Gold Zone and includes 87
samples >1 g/t Au and 126 samples >0.5 g/t Au (up to 12.68 g/t Au).
<>>
"The expansion of the Stega Gold Zone, parallel to the recently announced
Stega Copper Zone, is further evidence of the overall mineral endowment of the
Mojave Project," stated Jodie Gibson, Vice President of Exploration for K2.
"The work completed to date, together with work in progress, are providing us
with a greater understanding of the geological controls of the gold, copper,
and base metal mineralization at Mojave and will help guide our future
exploration and drilling efforts."
Steve Swatton, President and CEO of K2 added: "As we move west from the
Newmont gold zone, the property continues to deliver exciting exploration
results from various disparate locations, some anticipated but most are new.
The vectorisation of the mineral zones is particularly intriguing, and we
expect to find further mineralized zones as we continue exploring to the west.
I am also pleased to report that the permitting process for the next phase of
drilling at Dragonfly / Newmont is nearing the 30-day public consultation
stage with the Bureau of Land Management expected to soon post our Plan of
Operations for public input."
Please CLICK HERE to view all figures related to this news release.
Stega Target
The Stega target is located on the western side of the Mojave property,
approximately 3.4km NW of the Newmont target, covering a 1.5km x 2km NW
trending zone of alteration and mineralization in strongly folded and faulted
Triassic siltstone, limestone, and shales with at least two generations of
porphyritic sills and dikes. Mineralization on the target is polymetallic and
shows a sharp zonation consisting of a silver-lead (+/- zinc) zone, a central
copper zone, and an eastern gold zone. Individual mineralized zones are hosted
along NW oriented normal faults and NE trending thrust faults and fold hinges,
and are typically associated with silicification, quartz-carbonate veining,
strong iron-oxide development, sericite - argillic alteration (gold-copper
zones), and/or propylitic alteration (silver-lead zones). The mineralization
is interpreted as intrusion-related and shows strong similarities to
polymetallic skarn, replacement, and/or structurally controlled mineralization
in the Cerro Gordo district, 5.5km to the north.
Stega Gold Zone
A total of 42 prospecting rock/grab samples and 385 continuous
chip-channel samples over five lines were collected on the Stega Gold Zone.
The sampling was conducted to follow up on the southern extension of the gold
zone. Sampling performed in the central portion of the zone by the Company in
2020 included continuous rock chip samples of 5.14 g/t Au over 11.6m and
individual samples up to 10.8 g/t Au (see the Company's news release dated
July 2, 2020). The southern portion of the gold zone was the focus of historic
exploration efforts by Mobil Mineral Resources and Asamera in the mid 1980's
and the historic work included the placement of one trench and 19 shallow
drill holes for 703.87m. Highlights of the historic work include 5.28 g/t Au
over 5.33m from the trench and hole DG87-02: 1.82 g/t Au over 7.62m from
12.19m depth (Clarke 1986 & Niemeyer 1987).
Table 1: Highlights of Historic Trenching and Drilling on the Stega
Target


Hole ID From (m) To (m)  Int (m)   Au (g/t)

---


Surface Trench            0    5.33      5.33        5.28

---


DG-01                  9.45   23.17     13.72        0.86

---


DG87-02               12.19   19.81      7.62        1.82

---


DG87-09                9.14   22.86     13.72        0.75

---



Incl.      18.29   22.86      4.57        1.13

---
These drill results are historical in nature and the Company has not
undertaken any independent investigation of the sampling nor has it
independently analyzed the results of the historical exploration work to
verify the results.
Individual results from the program ranged from trace to 7.84 g/t gold
and the gold mineralization is associated with anomalous
arsenic-antimony-mercury and locally anomalous lead (up to 0.28% Pb), zinc (up
to 0.23% Zn), and molybdenum (up to 99ppm Mo). The mineralization is hosted
within a sequence of strongly folded and faulted Triassic limestone and
siltstone with mineralization occurring along structural zones and lithologic
contacts and is associated with quartz-sericite alteration and strong
iron-oxide development.
Highlights of the sampling include:
21-MOC-001
Consisted of a 9m continuous chip line along a NW trending outcrop of
silicified limestone with a historic adit. The line returned 0.51 g/t gold
over 9m; starting and ending in mineralization.
21-MOC-002
Consisted of a 47.5m continuous chip line across outcrop of strongly
silicified limestone adjacent to a NW trending normal fault. The line returned
0.28 g/t gold over 33m.
21-MOT-003
Consisted of a NW trending 25m channel along the trace of the historic
Asamera trench. The channel returned 1.7 g/t gold over 15m; starting in
mineralization. This includes a higher-grade zone of 3.4 g/t gold over 7m. The
mineralization occurs within strongly sericite altered siltstone with local
silicification and strong iron-oxide development at the intersection of a NW
trending normal fault and NE trending thrust fault.
21-MOT-004
Consisted of a NE trending 20m channel that crosses 21-MOT-003. The
channel returned 2.25 g/t gold over 20m; starting and ending in
mineralization. The mineralization occurs within strongly sericite altered
siltstone and silicified limestone with strong iron-oxide development at the
intersection of a NW trending normal fault and NE trending thrust fault.
21-MOT-005
Consisted of a 155m channel along a NE plunging fold hinge approximately
250m SW of 21-MOT-003/004. The channel returned 0.95 g/t gold over 48m;
including 1.68 g/t gold over 25.3m. The mineralization occurs within a folded
sequence of silicified limestone and sericite altered siltstone that is
interpreted to occur in the hanging wall of the thrust fault associated with
mineralization in 21-MOT-003. Silicification and strong iron oxide development
occurs along the hinge of the fold, in all units, with the strongest
mineralization at lithologic contacts. Prospecting samples of 2.88 g/t Au,
2.52 g/t Au, and 2.13 g/t Au from separate 1 -2m chips were also collected
along the trend.
Combined with historic sampling, the Stega Gold Zone is up to 600m in
width, 1.8km in length, and is open to the NW and may extend to the Boland
target, 1.2 km to the SE. Including work by the Company, 1,051 samples have
been collected on the Stega Gold Belt and includes 87 samples >1 g/t Au and
126 samples >0.5 g/t Au (up to 12.68 g/t Au). Numerous historic workings occur
along the trend and additional work is in progress to fully evaluate the zone
and identify potential drill targets including geologic mapping, soil
sampling, chip-channel sampling, and heliborne EM-resistivity (VTEM),
magnetic, and radiometric surveys. Additional results from the ongoing work on
the Stega, and other targets on the Mojave property, will be released in due
course.
Exploration Overview at Mojave
This work is part of an on-going evaluation of the entire Mojave
property. The 2021 exploration results now confirm previous work from the
1980's and 1990's that interpreted the entire Mojave project area as part a
large multi-commodity mineral zone that hosts gold, silver, copper and other
base metals. The broader district has seen exploration and mining activity
from the mid 1800's to present. This includes the Cerro Gordo district which
produced an estimated 4.4 million ounces of silver, 37 tons of lead, and
12,000 tons of zinc with lesser amounts of gold and copper (Merriam 1963); the
Santa Rosa Mine which produced 76,584 tons of ore averaging 0.45 g/t gold,
397.7 g/t silver, 16.3% lead, and 0.7% copper (MacKevatt 1953 & Dixon 1991);
and numerous other high-grade gold, silver, and base-metal mines and
prospects. The gold, as reported by K2 from the Eastern Target Areas was
discovered only more recently (1980's and 1990's).
A VTEM (+ magnetics and radiometrics) geophysical survey has also
recently been completed over the Mojave property, and is currently being
processed. The survey consisted of 1036 line-km on 50m spaced lines and
covered all known target areas on the property. This includes the Owens, a
target identified by previous operators as having potential for porphyry
copper mineralization beneath colluvial cover 3km to the west of Stega. Ionic
leach sampling is also planned on the Owens target and other areas of
colluvial cover including Upland Valley. Results of the VTEM, in combination
with rock, soil, and ionic leach geochemistry and previously completed
WorldView-3 and LiDAR surveys, will assist in the interpretation and
definition of drill targets outside of the Eastern Target area.
All mineralization at Mojave is interpreted to be part of an intrusion
related polymetallic system(s). The gold mineralization in the Eastern Area
(Dragonfly, Newmont, Flores) is structurally controlled with similarities to
both low sulfidation epithermal and Carlin type systems and may represent the
distal expression of a much larger intrusion-related hydrothermal system.
Whereas targets on the Western target area including Stega, Boland, Belshaw,
Soda Canyon/Soda Ridge, and, potentially, Owens are likely proximal to
causative intrusions and demonstrate the potential for sediment-hosted,
polymetallic, skarn, epithermal, and, potentially, porphyry styles of
mineralization.
Next Steps for 2021 Drilling Plan Taken
The USDI Bureau of Land Management ("BLM") is taking the next actions for
the environmental review process of the Mojave Project Exploration Drilling
and will be announcing a 30-day period for public input on the issues to be
evaluated. The BLM intends to post the Plan of Operations, an overview of the
project and the items for preliminary consideration in an Environmental
Assessment.
Assay Methodology & QA/QC
The analytical work on the Mojave project is being performed by MSALABS
an internationally recognized analytical services provider, at its laboratory
in Langley, British Columbia. All rock and drilling samples will be prepared
using procedure PRP-910 (dry, crush to 70% passing 2mm, riffle split off 250g,
pulverize split to better than 85% passing 75 microns) and analyzed by method
FAS-111 (30g fire assay with AAS finish) and IMS-130 (0.5g, aqua regia
digestion and ICP-AES/MS analysis). Any samples containing >10g/t Au will be
reanalyzed using method FAS-415 (30g Fire Assay with gravimetric finish).
Samples containing >100 ppm Ag and/or >1% Cu, Pb, & Zn will be reanalyzed
using method ICF-6 (0.2g, 4-acid digest and ore grade ICP-AES analysis).
The reported work was completed using industry standard procedures,
including a quality assurance/quality control ("QA/QC") program consisting of
the insertion of certified standard, blanks and duplicates into the sample
stream.
About K2
K2 is a well-financed gold exploration company with approximately C$5M
and projects in SW USA and the Yukon. In the USA, the Company is represented
by its 100% subsidiary, Mojave Precious Metals Inc. ("MPM"). The Company is
focused on the Mojave property in California, a 5,830-hectare oxide gold
project with base metal targets. The location of Mojave enables the Company to
have year-round news flow on multiple previously recognized surface gold
targets that have been successfully drilled in the past by majors BHP and
Newmont. Besides affording immediate drill targets based on the Company's soil
data integrated with LiDAR and Worldview-3 data, the property also has
undrilled locations with gold enriched historical trench results including one
at the Flores zone which recorded 8.4 g/t gold over 25.6m (see October 30,
2013 news release from Great Bear Resources Ltd.).
K2 and MPM are committed to transparency, accountability, environmental
stewardship, safety, diversity and inclusion, and community engagement.
On behalf of the Board of Directors,
"Stephen Swatton"
President and CEO
K2 Gold Corporation.
K2 Gold Corporation is a member of Discovery Group based in Vancouver,
Canada. For more information please visit: discoverygroup.ca.
Cautionary Statement on Forward-Looking Statements
This news release contains forward-looking statements that are not
historical facts. Forward-looking statements involve risks, uncertainties and
other factors that could cause actual results, performance, prospects and
opportunities to differ materially from those expressed or implied by such
forward-looking statements, including statements regarding the exploration
program at Mojave, including results of drilling, and future exploration plans
at Mojave. Factors that could cause actual results to differ materially from
these forward-looking statements include, but are not limited to, variations
in the nature, quality and quantity of any mineral deposits that may be
located, the Company's inability to obtain any necessary permits, consents or
authorizations required for its planned activities, and the Company's
inability to raise the necessary capital or to be fully able to implement its
business strategies. The reader is referred to the Company's public disclosure
record which is available on SEDAR (www.sedar.com). Although the Company
believes that the assumptions and factors used in preparing the
forward-looking statements are reasonable, undue reliance should not be placed
on these statements, which only apply as of the date of this news release, and
no assurance can be given that such events will occur in the disclosed time
frames or at all. Except as required by securities laws and the policies ofthe 
TSX Venture Exchange, the Company disclaims any intention or obligation to
update or revise any forward-looking statement, whether as a result of new
information, future events or otherwise.
This news release does not constitute an offer to sell or a solicitation
of an offer to buy, nor shall there be any sale of any of the securities in
any jurisdiction in which such offer, solicitation or sale would be unlawful,
including any of the securities in the United States of America. No securities
of the Company have been or will, in the foreseeable future, be registered
under the United States Securities Act of 1933 (the "1933 Act") or any state
securities laws and may not be offered or sold within the United States or to,
or for account or benefit of, U.S. Persons (as defined in Regulation S under
the 1933 Act) unless registered under the 1933 Act and applicable state
securities laws, or an exemption from such registration requirements is
available.
NEITHER TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS
THAT TERM IS DEFINED IN POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE
SOURCE K2 Gold Corporation



View original content:
http://www.newswire.ca/en/releases/archive/June2021/14/c0248.html

-0-                           06/14/2021
/For further information: about K2 Gold Corporation or this news release,
please visit our website at k2gold.com or contact Investor Relations Offices
in Canada 604-653-9464, or in the USA at Lone Pine, California +1 (760)
614-5605 or by email at info(at)k2gold.com./
/Web Site: http://www.k2gold.com/ /
(KTGDF 23K KTO.)

CO:  K2 Gold Corporation
ST:  British Columbia
IN:  PRM MNG OTC
SU:

-30-