Source	Business Wire
Date	06/16/2021
Time	04:04:42 AM

Company	 RUPERT RESOURCES LTD.
Title	[EXTERNAL] Rupert Resources Reports Further Drilling From Ikkari Extending 
Min...





    CDNX Symbol: RUP











Press Release




June 16, 2021 11:03 UTC

Rupert Resources Reports Further Drilling From Ikkari Extending Mineralisation 
in the West and Below 450m 

NEWS RELEASE SUBMITTED BY BUSINESS WIRE 

FOR: Rupert Resources Ltd 

TSX VENTURE SYMBOL: RUP 

TORONTO--(BUSINESS WIRE)-- Rupert Resources Ltd (“Rupert” or “the Company”, 
TSX-V: RUP) reports new drill results from its Ikkari prospect, the focus of 
its ongoing exploration programme at the 100% owned Pahtavaara Project in the 
Central Lapland Greenstone Belt, Finland (figure 1). The mineralised strike 
length at Ikkari is at least 650m in total (figure 2) with mineralisation on 
all sections intersected to a depth of at least 300 to 500m. 

Highlights

Hole 121063 demonstrated multiple zones of higher grade gold mineralisation 
re-emerging at depthin the western section of Ikkari contained within a broad 
intercept of 1.9g/t gold over 142m 
Hole 121028 intersected 3.1g/t gold (“Au”) over 76m from 248m as part of the 
infill program in the central portion of the discovery and a step back hole 
121030 beneath this intersected two strongly mineralised zones of 3.7g/t gold 
over 77m from 245m and 2.8g/t Au over 65m from 346m 
Hole 121029 is a shallow step out hole to the northwest and intersected 2.1g/t 
Au over 25m from 124m 
Hole 121032 intersected mineralisation both at surface and in multiple zones 
including 1.6g/t Au over 74m from 396m, with mineralisation extending to >450m 
vertical meters. 
Mineralised system at Ikkari remains open in all directions 

James Withall, CEO of Rupert Resources commented “The infill holes reported 
today confirm the exceptional widths and continuity of grade at Ikkari with 
hole 121032 and 121063 indicating that the system remains open at depth with 
higher grade material re-emerging in the west below hitherto weaker 
mineralisation reported in January 2021. As previously announced, we expect to 
report a maiden mineral resource estimate for Ikkari this summer although 
drilling continues with the aim of further expanding the resource inventory 
over time as we refine our geology model and commence work to understand the 
full economic potential of the Ikkari Discovery.”  

Summary of new drill results 

Partial results from hole 121063 (assays pending from the upper and lower parts 
of the hole) demonstrate increasing grade with depth in this western part of 
the deposit (figure 2). Shallower holes previously drilled on this section 
(figure 3a), suggested narrowing of the mineralised zone (hole 120100 - 2.4g/t 
Au over 22m from 265m (200m vertical) and 2.4g/t over 32m from 333m (255m 
vertical), see release January 28, 2021), but these results from 121063 
indicate that the mineralised zone widens again at depth and includes 
high-grade intercepts: 2.1g/t Au over 19m, from 328m; 6.4g/t Au over 10m from 
367m (including 57g/t Au over 1m), 7.9g/t Au over 14m from 412m (including 
18g/t Au over 4m), and 1.0g/t Au over 43m from 514m. The vertical depth of the 
mineralised zone now extends to 445m on this section and remains open. 

Further results from infill sections in the central part of Ikkari confirm 
continuity of grade to depths of ~350m vertical. Infill holes 121028 and 121030 
reinforce mineralisation to these depths (figure 3b), beneath previously 
reported holes 121024, 121025 and 121026 (see release 20/04/2021). Similarly, 
hole 121032 (figure 3c) extends mineralisation to nearly 400m vertical on the 
adjacent section, with 1.6g/t Au over 74m from 396m including high-grade parts 
such as 8.4g/t Au over 6m and including 21.4g/t Au over 1m at 445m. 

Hole 121029 further confirms mineralised intercepts in the west of the Ikkari 
deposit (figure 2) to a depth of 100m vertical, with further drilling planned 
in this area to extend mineralisation further west and to depth. 

Hole 121033 was drilled to validate shallow grade in the centre part of Ikkari 
and successfully demonstrated a well-mineralised zone at only 40m below glacial 
till cover. Hole 121035 also tracked shallow mineralisation in the eastern part 
of the deposit, with 1.0g/t Au over 18m at 50m below till cover sediments. 

Table 1. Headline assay results from Ikkari (16 June 2021) 


Hole ID  
	
	From (m) 
		
		To (m) 
			
			Interval (m) 
				
				Grade Au g/t 
				

121063 
	
	328.0 
		
		470.0 
			
			142.0 
				
				1.9 
				

121063 
	
	514.0 
		
		557.0 
			
			43.0 
				
				1.0 
				

121033 
	
	63.0 
		
		90.0 
			
			27.0 
				
				2.2 
				

121032 
	
	396.0 
		
		470.0 
			
			74.0 
				
				1.6 
				

121030 
	
	245.0 
		
		322.0 
			
			77.0 
				
				3.7 
				

121030 
	
	346.0 
		
		411.0 
			
			65.0 
				
				2.8 
				

121028 
	
	248.0 
		
		324.0 
			
			76.0 
				
				3.1 
				

Notes to table: No upper cut-off grade and a 0.4g/t Au lower cut-off applied. 
Unless specified, true widths cannot be accurately determined from the 
information available. Full breakdown of new holes with “includings” in Table 
3. Refer to this link for spreadsheet of previously released drilling 
intercepts. 

Drilling continues with further infill sections being completed across the 
deposit, as well as selected deeper holes, that will contribute to a resource 
estimation later in the year. To date, 39,000 metres have been drilled at 
Ikkari in 107 holes, with results reported for 75 holes. Drilling is also 
ongoing at other Area 1 prospects as part of the continuing new target 
generation programme. 

Table 2. Collar locations of new drill holes 


Hole ID
	
	Prospect 
		
		Easting
			
			Northing 
				
				Elevation 
					
					Azimuth
						
						Dip 
							
							EOH (m)
							

121063 
	
	Ikkari 
		
		454092.1 
			
			7496585.0 
				
				226.8 
					
					336.3 
						
						-54.9 
							
							740.4 
							

121035 
	
	Ikkari 
		
		454273.8 
			
			7496946.9 
				
				224.2 
					
					152.5 
						
						-60.2 
							
							251.4 
							

121033 
	
	Ikkari 
		
		454123.4 
			
			7496890.6 
				
				224.3 
					
					151.5 
						
						-49.9 
							
							106.7 
							

121032 
	
	Ikkari 
		
		454182.3 
			
			7496574.9 
				
				229.2 
					
					339.0 
						
						-55.0 
							
							680.4 
							

121030 
	
	Ikkari 
		
		454098.4 
			
			7496659.7 
				
				225.7 
					
					337.8 
						
						-52.8 
							
							473.6 
							

121029 
	
	Ikkari 
		
		453767.9 
			
			7496926.5 
				
				226.3 
					
					152.7 
						
						-51.9 
							
							210.3 
							

121028 
	
	Ikkari 
		
		454073.6 
			
			7496713.1 
				
				224.9 
					
					333.2 
						
						-52.4 
							
							359.3 
							

Notes to table: The coordinates are in ETRS89 Z35 and all holes are surveyed at 
3m intervals down hole and all core is orientated. 

Geological description of the Ikkari Discovery 

Mineralisation at Ikkari is characterised by intense alteration and 
deformation. Gold is associated with fine-grained disseminated pyrite within 
planar quartz-carbonate veins and / or disseminated in the host rocks, commonly 
as fine-grained visible gold. Mineralisation is hosted by sedimentary rocks 
overprinted by albite-sericite alteration, and strongly foliated 
chlorite-altered mafic-ultramafic rocks. A broader, variably mineralised 
alteration zone comprising magnetite ± hematite ± tourmaline ± K-feldspar ± 
fuchsite is also present. Holes demonstrate strong foliation, shearing, and 
veining that is predominantly parallel to the dominant structural fabric and 
gold appears to be concentrated in sedimentary intercalations associated with 
zones of structural disruption at lithological boundaries, represented by 
irregular, cross-cutting vein associations and brittle fracture in 
albite-altered rocks. The regional structural data collected so far suggest a 
subvertical, broad and linear structure, within which cross-cutting fractures 
and variably dipping lithologies, as well as possibly folded bedding, appear to 
have controlled the introduction of gold-bearing fluids and associated 
alteration zones. In general, alteration and structure appear to be 
sub-vertical, with lithologies generally dipping ~70 degrees north. 

Review by Qualified Person, Quality Control and Reports  

Dr Charlotte Seabrook, MAIG, RPGeo. Exploration Manager is the Qualified Person 
as defined by National Instrument 43-101 responsible for the accuracy of 
scientific and technical information in this news release. 

Samples are prepared by ALS Finland in Sodankylä and assayed in ALS 
laboratories in Ireland, Romania or Sweden. All samples are under watch from 
the drill site to the storage facility. Samples are assayed using fire assay 
method with aqua regia digest and analysis by AAS for gold. Over limit analysis 
for >10 ppm Au is conducted using fire assay and gravimetric finish for assays 
over >100ppm Au. For hole 120071 all mineralised samples were submitted for 
screen fire assays with gravimetric finish. For multi-element assays Ultra 
Trace Level Method by HF-HNO3-HClO4 acid digestion, HCl leach and a combination 
of ICP-MS and ICP-AES is used. The Company’s QA/QC program includes the regular 
insertion of blanks and standards into the sample shipments, as well as 
instructions for duplication. Standards, blanks and duplicates are inserted at 
appropriate intervals. Approximately five percent (5%) of the pulps and rejects 
are sent for check assaying at a second lab. 

Base of till samples are prepared in ALS Sodankylä by dry-sieving method 
prep-41, and assayed by fire assay with ICP-AES finish for gold. Multi-elements 
are assayed in ALS laboratories in either of Ireland, Romania or Sweden by aqua 
regia with ICP-MS finish. Rupert maintains a strict chain of custody procedure 
to manage the handling of all samples. The Company’s QA/QC program includes the 
regular insertion of blanks and standards into the sample shipments, as well as 
instructions for duplication. 

About Rupert 

Rupert is a Canadian based gold exploration and development company that is 
listed on the TSX Venture Exchange under the symbol “RUP”. The Company owns the 
Pahtavaara gold mine, mill, and exploration permits and concessions located in 
the Central Lapland Greenstone Belt in Northern Finland (“Pahtavaara”). 
Pahtavaara previously produced over 420koz of gold and 474koz remains in an 
Inferred mineral resource (4.6 Mt at a grade of 3.2 g/t Au at a 1.5 g/t Au 
cut-off grade, see the technical report entitled “NI 43-101 Technical Report: 
Pahtavaara Project, Finland” with an effective date of April 16, 2018, prepared 
by Brian Wolfe, Principal Consultant, International Resource Solutions Pty 
Ltd., an independent qualified person under National Instrument 43-101 – 
Standards of Disclosure for Mineral Projects). The Company also holds a 100% 
interest in the Surf Inlet Property in British Columbia, a 100% interest in 
properties in Central Finland and a 20% carried participating interest in the 
Gold Centre property located adjacent to the Red Lake mine in Ontario. 

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release. 

Cautionary Note Regarding Forward Looking Statements  

This press release contains statements which, other than statements of 
historical fact constitute “forward-looking statements” within the meaning of 
applicable securities laws, including statements with respect to: results of 
exploration activities, mineral resources. The words “may”, “would”, “could”, 
“will”, “intend”, “plan”, “anticipate”, “believe”, “estimate”, “expect” and 
similar expressions, as they relate to the Company, are intended to identify 
such forward-looking statements. Investors are cautioned that forward-looking 
statements are based on the opinions, assumptions and estimates of management 
considered reasonable at the date the statements are made, and are inherently 
subject to a variety of risks and uncertainties and other known and unknown 
factors that could cause actual events or results to differ materially from 
those projected in the forward-looking statements. These factors include the 
general risks of the mining industry, as well as those risk factors discussed 
or referred to in the Company's annual Management's Discussion and Analysis for 
the year ended February 29, 2020 available at www.sedar.com. Should one or more 
of these risks or uncertainties materialize, or should assumptions underlying 
the forward-looking statements prove incorrect, actual results may vary 
materially from those described herein as intended, planned, anticipated, 
believed, estimated or expected. Although the Company has attempted to identify 
important factors that could cause actual actions, events or results to differ 
materially from those described in forward-looking information, there may be 
other factors that cause actions, events or results not to be as anticipated, 
estimated or intended. There can be no assurance that such information will 
prove to be accurate as actual results and future events could differ 
materially from those anticipated in such statements. The Company does not 
intend, and does not assume any obligation, to update these forward-looking 
statements except as otherwise required by applicable law.  

APPENDIX  

Table 3. New Intercepts at Ikkari 


Hole ID  
	
	  
		
		From (m) 
			
			To (m) 
				
				Interval (m) 
					
					Grade Au g/t 
					

121063 
	
	  
		
		0.0 
			
			285.0 
					
					Results pending 
					

  
	
	  
		
		328.0 
			
			470.0 
				
				142.0 
					
					1.9 
					

  
	
	Including 
		
		338.0 
			
			339.0 
				
				1.0 
					
					4.5 
					

  
	
	Including 
		
		343.0 
			
			347.0 
				
				4.0 
					
					6.1 
					

  
	
	And including 
		
		344.0 
			
			345.0 
				
				1.0 
					
					11.4 
					

  
	
	Including 
		
		367.0 
			
			377.0 


June 16, 2021 11:03 UTC

Rupert Resources Reports Further Drilling From Ikkari Extending Mineralisation 
in the West and Below 450m 

NEWS RELEASE SUBMITTED BY BUSINESS WIRE 

FOR: Rupert Resources Ltd 

TSX VENTURE SYMBOL: RUP 

TORONTO--(BUSINESS WIRE)-- Rupert Resources Ltd (“Rupert” or “the Company”, 
TSX-V: RUP) reports new drill results from its Ikkari prospect, the focus of 
its ongoing exploration programme at the 100% owned Pahtavaara Project in the 
Central Lapland Greenstone Belt, Finland (figure 1). The mineralised strike 
length at Ikkari is at least 650m in total (figure 2) with mineralisation on 
all sections intersected to a depth of at least 300 to 500m. 

Highlights

Hole 121063 demonstrated multiple zones of higher grade gold mineralisation 
re-emerging at depthin the western section of Ikkari contained within a broad 
intercept of 1.9g/t gold over 142m 
Hole 121028 intersected 3.1g/t gold (“Au”) over 76m from 248m as part of the 
infill program in the central portion of the discovery and a step back hole 
121030 beneath this intersected two strongly mineralised zones of 3.7g/t gold 
over 77m from 245m and 2.8g/t Au over 65m from 346m 
Hole 121029 is a shallow step out hole to the northwest and intersected 2.1g/t 
Au over 25m from 124m 
Hole 121032 intersected mineralisation both at surface and in multiple zones 
including 1.6g/t Au over 74m from 396m, with mineralisation extending to >450m 
vertical meters. 
Mineralised system at Ikkari remains open in all directions 

James Withall, CEO of Rupert Resources commented “The infill holes reported 
today confirm the exceptional widths and continuity of grade at Ikkari with 
hole 121032 and 121063 indicating that the system remains open at depth with 
higher grade material re-emerging in the west below hitherto weaker 
mineralisation reported in January 2021. As previously announced, we expect to 
report a maiden mineral resource estimate for Ikkari this summer although 
drilling continues with the aim of further expanding the resource inventory 
over time as we refine our geology model and commence work to understand the 
full economic potential of the Ikkari Discovery.”  

Summary of new drill results 

Partial results from hole 121063 (assays pending from the upper and lower parts 
of the hole) demonstrate increasing grade with depth in this western part of 
the deposit (figure 2). Shallower holes previously drilled on this section 
(figure 3a), suggested narrowing of the mineralised zone (hole 120100 - 2.4g/t 
Au over 22m from 265m (200m vertical) and 2.4g/t over 32m from 333m (255m 
vertical), see release January 28, 2021), but these results from 121063 
indicate that the mineralised zone widens again at depth and includes 
high-grade intercepts: 2.1g/t Au over 19m, from 328m; 6.4g/t Au over 10m from 
367m (including 57g/t Au over 1m), 7.9g/t Au over 14m from 412m (including 
18g/t Au over 4m), and 1.0g/t Au over 43m from 514m. The vertical depth of the 
mineralised zone now extends to 445m on this section and remains open. 

Further results from infill sections in the central part of Ikkari confirm 
continuity of grade to depths of ~350m vertical. Infill holes 121028 and 121030 
reinforce mineralisation to these depths (figure 3b), beneath previously 
reported holes 121024, 121025 and 121026 (see release 20/04/2021). Similarly, 
hole 121032 (figure 3c) extends mineralisation to nearly 400m vertical on the 
adjacent section, with 1.6g/t Au over 74m from 396m including high-grade parts 
such as 8.4g/t Au over 6m and including 21.4g/t Au over 1m at 445m. 

Hole 121029 further confirms mineralised intercepts in the west of the Ikkari 
deposit (figure 2) to a depth of 100m vertical, with further drilling planned 
in this area to extend mineralisation further west and to depth. 

Hole 121033 was drilled to validate shallow grade in the centre part of Ikkari 
and successfully demonstrated a well-mineralised zone at only 40m below glacial 
till cover. Hole 121035 also tracked shallow mineralisation in the eastern part 
of the deposit, with 1.0g/t Au over 18m at 50m below till cover sediments. 

Table 1. Headline assay results from Ikkari (16 June 2021) 


Hole ID  

	From (m) 
	
		To (m) 
		
			Interval (m) 
			
				Grade Au g/t 
				

121063 

	328.0 
	
		470.0 
		
			142.0 
			
				1.9 
				

121063 

	514.0 
	
		557.0 
		
			43.0 
			
				1.0 
				

121033 

	63.0 
	
		90.0 
		
			27.0 
			
				2.2 
				

121032 

	396.0 
	
		470.0 
		
			74.0 
			
				1.6 
				

121030 

	245.0 
	
		322.0 
		
			77.0 
			
				3.7 
				

121030 

	346.0 
	
		411.0 
		
			65.0 
			
				2.8 
				

121028 

	248.0 
	
		324.0 
		
			76.0 
			
				3.1 
				

Notes to table: No upper cut-off grade and a 0.4g/t Au lower cut-off applied. 
Unless specified, true widths cannot be accurately determined from the 
information available. Full breakdown of new holes with “includings” in Table 
3. Refer to this link for spreadsheet of previously released drilling 
intercepts. 

Drilling continues with further infill sections being completed across the 
deposit, as well as selected deeper holes, that will contribute to a resource 
estimation later in the year. To date, 39,000 metres have been drilled at 
Ikkari in 107 holes, with results reported for 75 holes. Drilling is also 
ongoing at other Area 1 prospects as part of the continuing new target 
generation programme. 

Table 2. Collar locations of new drill holes 


Hole ID

	Prospect 
	
		Easting
		
			Northing 
			
				Elevation 
				
					Azimuth
					
						Dip 
						
							EOH (m)
							

121063 

	Ikkari 
	
		454092.1 
		
			7496585.0 
			
				226.8 
				
					336.3 
					
						-54.9 
						
							740.4 
							

121035 

	Ikkari 
	
		454273.8 
		
			7496946.9 
			
				224.2 
				
					152.5 
					
						-60.2 
						
							251.4 
							

121033 

	Ikkari 
	
		454123.4 
		
			7496890.6 
			
				224.3 
				
					151.5 
					
						-49.9 
						
							106.7 
							

121032 

	Ikkari 
	
		454182.3 
		
			7496574.9 
			
				229.2 
				
					339.0 
					
						-55.0 
						
							680.4 
							

121030 

	Ikkari 
	
		454098.4 
		
			7496659.7 
			
				225.7 
				
					337.8 
					
						-52.8 
						
							473.6 
							

121029 

	Ikkari 
	
		453767.9 
		
			7496926.5 
			
				226.3 
				
					152.7 
					
						-51.9 
						
							210.3 
							

121028 

	Ikkari 
	
		454073.6 
		
			7496713.1 
			
				224.9 
				
					333.2 
					
						-52.4 
						
							359.3 
							

Notes to table: The coordinates are in ETRS89 Z35 and all holes are surveyed at 
3m intervals down hole and all core is orientated. 

Geological description of the Ikkari Discovery 

Mineralisation at Ikkari is characterised by intense alteration and 
deformation. Gold is associated with fine-grained disseminated pyrite within 
planar quartz-carbonate veins and / or disseminated in the host rocks, commonly 
as fine-grained visible gold. Mineralisation is hosted by sedimentary rocks 
overprinted by albite-sericite alteration, and strongly foliated 
chlorite-altered mafic-ultramafic rocks. A broader, variably mineralised 
alteration zone comprising magnetite ± hematite ± tourmaline ± K-feldspar ± 
fuchsite is also present. Holes demonstrate strong foliation, shearing, and 
veining that is predominantly parallel to the dominant structural fabric and 
gold appears to be concentrated in sedimentary intercalations associated with 
zones of structural disruption at lithological boundaries, represented by 
irregular, cross-cutting vein associations and brittle fracture in 
albite-altered rocks. The regional structural data collected so far suggest a 
subvertical, broad and linear structure, within which cross-cutting fractures 
and variably dipping lithologies, as well as possibly folded bedding, appear to 
have controlled the introduction of gold-bearing fluids and associated 
alteration zones. In general, alteration and structure appear to be 
sub-vertical, with lithologies generally dipping ~70 degrees north. 

Review by Qualified Person, Quality Control and Reports  

Dr Charlotte Seabrook, MAIG, RPGeo. Exploration Manager is the Qualified Person 
as defined by National Instrument 43-101 responsible for the accuracy of 
scientific and technical information in this news release. 

Samples are prepared by ALS Finland in Sodankylä and assayed in ALS 
laboratories in Ireland, Romania or Sweden. All samples are under watch from 
the drill site to the storage facility. Samples are assayed using fire assay 
method with aqua regia digest and analysis by AAS for gold. Over limit analysis 
for >10 ppm Au is conducted using fire assay and gravimetric finish for assays 
over >100ppm Au. For hole 120071 all mineralised samples were submitted for 
screen fire assays with gravimetric finish. For multi-element assays Ultra 
Trace Level Method by HF-HNO3-HClO4 acid digestion, HCl leach and a combination 
of ICP-MS and ICP-AES is used. The Company’s QA/QC program includes the regular 
insertion of blanks and standards into the sample shipments, as well as 
instructions for duplication. Standards, blanks and duplicates are inserted at 
appropriate intervals. Approximately five percent (5%) of the pulps and rejects 
are sent for check assaying at a second lab. 

Base of till samples are prepared in ALS Sodankylä by dry-sieving method 
prep-41, and assayed by fire assay with ICP-AES finish for gold. Multi-elements 
are assayed in ALS laboratories in either of Ireland, Romania or Sweden by aqua 
regia with ICP-MS finish. Rupert maintains a strict chain of custody procedure 
to manage the handling of all samples. The Company’s QA/QC program includes the 
regular insertion of blanks and standards into the sample shipments, as well as 
instructions for duplication. 

About Rupert 

Rupert is a Canadian based gold exploration and development company that is 
listed on the TSX Venture Exchange under the symbol “RUP”. The Company owns the 
Pahtavaara gold mine, mill, and exploration permits and concessions located in 
the Central Lapland Greenstone Belt in Northern Finland (“Pahtavaara”). 
Pahtavaara previously produced over 420koz of gold and 474koz remains in an 
Inferred mineral resource (4.6 Mt at a grade of 3.2 g/t Au at a 1.5 g/t Au 
cut-off grade, see the technical report entitled “NI 43-101 Technical Report: 
Pahtavaara Project, Finland” with an effective date of April 16, 2018, prepared 
by Brian Wolfe, Principal Consultant, International Resource Solutions Pty 
Ltd., an independent qualified person under National Instrument 43-101 – 
Standards of Disclosure for Mineral Projects). The Company also holds a 100% 
interest in the Surf Inlet Property in British Columbia, a 100% interest in 
properties in Central Finland and a 20% carried participating interest in the 
Gold Centre property located adjacent to the Red Lake mine in Ontario. 

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release. 

Cautionary Note Regarding Forward Looking Statements  

This press release contains statements which, other than statements of 
historical fact constitute “forward-looking statements” within the meaning of 
applicable securities laws, including statements with respect to: results of 
exploration activities, mineral resources. The words “may”, “would”, “could”, 
“will”, “intend”, “plan”, “anticipate”, “believe”, “estimate”, “expect” and 
similar expressions, as they relate to the Company, are intended to identify 
such forward-looking statements. Investors are cautioned that forward-looking 
statements are based on the opinions, assumptions and estimates of management 
considered reasonable at the date the statements are made, and are inherently 
subject to a variety of risks and uncertainties and other known and unknown 
factors that could cause actual events or results to differ materially from 
those projected in the forward-looking statements. These factors include the 
general risks of the mining industry, as well as those risk factors discussed 
or referred to in the Company's annual Management's Discussion and Analysis for 
the year ended February 29, 2020 available at www.sedar.com. Should one or more 
of these risks or uncertainties materialize, or should assumptions underlying 
the forward-looking statements prove incorrect, actual results may vary 
materially from those described herein as intended, planned, anticipated, 
believed, estimated or expected. Although the Company has attempted to identify 
important factors that could cause actual actions, events or results to differ 
materially from those described in forward-looking information, there may be 
other factors that cause actions, events or results not to be as anticipated, 
estimated or intended. There can be no assurance that such information will 
prove to be accurate as actual results and future events could differ 
materially from those anticipated in such statements. The Company does not 
intend, and does not assume any obligation, to update these forward-looking 
statements except as otherwise required by applicable law.  

APPENDIX  

Table 3. New Intercepts at Ikkari 


Hole ID  

	  
	
		From (m) 
		
			To (m) 
			
				Interval (m) 
				
					Grade Au g/t 
					

121063 

	  
	
		0.0 
		
			285.0 
				
				Results pending 
				

  

	  
	
		328.0 
		
			470.0 
			
				142.0 
				
					1.9 
					

  

	Including 
	
		338.0 
		
			339.0 
			
				1.0 
				
					4.5 
					

  

	Including 
	
		343.0 
		
			347.0 
			
				4.0 
				
					6.1 
					

  

	And including 
	
		344.0 
		
			345.0 
			
				1.0 
				
					11.4 
					

  

	Including 
	
		367.0 
		
			377.0 
			
				10.0 
				
					6.4 
					

  

	And including 
	
		369.0 
		
			370.0 
			
				1.0 
				
					57.7 
					

  

	Including 
	
		381.0 
		
			384.0 
			
				2.0 
				
					4.3 
					

  

	Including 
	
		383.0 
		
			384.0 
			
				1.0 
				
					11.8 
					

  

	Including 
	
		392.0 
		
			396.0 
			
				4.0 
				
					4.5 
					

  

	And including 
	
		394.0 
		
			395.0 
			
				1.0 
				
					11.6 
					

  

	Including 
	
		412.0 
		
			426.0 
			
				14.0 
				
					7.9 
					

  

	And including 
	
		419.0 
		
			423.0 
			
				4.0 
				
					18.1 
					

  

	And including 
	
		422.0 
		
			423.0 
			
				1.0 
				
					32.4 
					

  

	Including 
	
		429.0 
		
			431.0 
			
				2.0 
				
					6.6 
					

  

	  
	
		514.0 
		
			557.0 
			
				43.0 
				
					1.0 
					

  

	Including 
	
		524.0 
		
			526.0 
			
				2.0 
				
					5.3 
					

  

	Including 
	
		53.0 
		
			555.0 
			
				3.0 
				
					3.9 
					

  

	  
	
		567.0 
		
			740.4 
				
				Results pending 
				

121035 

	  
	
		84.0 
		
			102.0 
			
				18.0 
				
					1.0 
					

  

	Including 
	
		93.0 
		
			94.0 
			
				1.0 
				
					7.0 
					

  

	  
	
		117.0 
		
			118.0 
			
				1.0 
				
					2.9 
					

  

	  
	
		201.0 
		
			202.0 
			
				1.0 
				
					1.0 
					

121033 

	  
	
		24.0 
		
			34.0 
			
				10.0 
				
					0.5 
					

  

	Including 
	
		27.0 
		
			28.0 
			
				1.0 
				
					1.8 
					

  

	Including 
	
		29.9 
		
			30.9 
			
				1.0 
				
					1.1 
					

  

	  
	
		45.0 
		
			46.0 
			
				1.0 
				
					5.6 
					

  

	  
	
		51.0 
		
			52.0 
			
				1.0 
				
					1.1 
					

  

	  
	
		63.0 
		
			90.0 
			
				27.0 
				
					2.2 
					

  

	Including 
	
		71.0 
		
			72.6 
			
				1.6 
				
					13.4 
					

  

	  
	
		77.0 
		
			78.0 
			
				1.0 
				
					9.7 
					

121032 

	  
	
		34.0 
		
			34.6 
			
				0.6 
				
					15.6 
					

  

	  
	
		231.0 
		
			239.0 
			
				8.0 
				
					0.4 
					

  

	  
	
		302.0 
		
			303.0 
			
				1.0 
				
					1.8 
					

  

	  
	
		310.0 
		
			311.0 
			
				1.0 
				
					1.3 
					

  

	  
	
		324.0 
		
			352.0 
			
				29.0 
				
					0.9 
					

  

	Including 
	
		340.0 
		
			347.0 
			
				7.0 
				
					1.8 
					

  

	And including 
	
		340.0 
		
			341.0 
			
				1.0 
				
					4.6 
					

  

	  
	
		396.0 
		
			470.0 
			
				74.0 
				
					1.6 
					

  

	Including 
	
		407.0 
		
			408.0 
			
				1.0 
				
					10.3 
					

  

	Including 
	
		412.0 
		
			416.0 
			
				4.0 
				
					5.0 
					

  

	And including 
	
		414.0 
		
			415.0 
			
				1.0 
				
					10.6 
					

  

	Including 
	
		434.0 
		
			435.0 
			
				1.0 
				
					4.0 
					

  

	Including 
	
		440.0 
		
			446.0 
			
				6.0 
				
					8.4 
					

  

	And including 
	
		445.0 
		
			446.0 
			
				1.0 
				
					21.4 
					

  

	  
	
		449.0 
		
			501.0 
			
				2.0 
				
					5.3 
					

  

	  
	
		506.0 
		
			507.0 
			
				1.0 
				
					4.1 
					

  

	  
	
		518.0 
		
			526.0 
			
				8.0 
				
					2.2 
					

  

	Including 
	
		519.0 
		
			520.0 
			
				1.0 
				
					6.2 
					

  

	Including 
	
		522.0 
		
			523.0 
			
				1.0 
				
					6.2 
					

  

	  
	
		553.0 
		
			554.0 
			
				1.0 
				
					7.9 
					

  

	  
	
		563.0 
		
			571.0 
			
				1.0 
				
					0.8 
					

  

	  
	
		594.0 
		
			604.0 
			
				10.0 
				
					1.2 
					

  

	Including 
	
		597.0 
		
			598.0 
			
				1.0 
				
					8.2 
					

121030 

	  
	
		245.0 
		
			322.0 
			
				77.0 
				
					3.7 
					

  

	Including 
	
		256.0 
		
			257.0 
			
				1.0 
				
					12.0 
					

  

	Including 
	
		265.0 
		
			266.0 
			
				1.0 
				
					17.8 
					

  

	Including 
	
		278.0 
		
			279.0 
			
				1.0 
				
					13.9 
					

  

	Including 
	
		283.0 
		
			287.0 
			
				4.0 
				
					9.7 
					

  

	Including 
	
		305.0 
		
			307.0 
			
				2.0 
				
					10.8 
					

  

	Including 
	
		311.0 
		
			312.0 
			
				1.0 
				
					32.1 
					

  

	Including 
	
		319.0 
		
			320.0 
			
				1.0 
				
					14.9 
					

  

	  
	
		346.0 
		
			411.0 
			
				65.0 
				
					2.8 
					

  

	Including 
	
		375.0 
		
			376.0 
			
				1.0 
				
					10.6 
					

  

	Including 
	
		405.0 
		
			411.0 
			
				6.0 
				
					12.1 
					

121029 

	  
	
		87.0 
		
			96.0 
			
				9.0 
				
					0.6 
					

  

	  
	
		107.0 
		
			110.0 
			
				3.0 
				
					1.1 
					

  

	  
	
		124.0 
		
			149.0 
			
				25.0 
				
					2.1 
					

  

	Including 
	
		142.7 
		
			144.0 
			
				1.3 
				
					9.2 
					

  

	  
	
		156.0 
		
			157.0 
			
				1.0 
				
					1.9 
					

  

	  
	
		163.0 
		
			169.0 
			
				6.0 
				
					1.0 
					

  

	Including 
	
		163.0 
		
			164.0 
			
				1.0 
				
					3.0 
					

121028 

	  
	
		224.0 
		
			225.0 
			
				1.0 
				
					2.0 
					

  

	  
	
		248.0 
		
			324.0 
			
				76.0 
				
					3.1 
					

  

	Including 
	
		255.0 
		
			256.0 
			
				1.0 
				
					11.8 
					

  

	Including 
	
		261.0 
		
			263.0 
			
				2.0 
				
					12.6 
					

  

	Including 
	
		290.0 
		
			291.0 
			
				1.0 
				
					6.3 
					

  

	Including 
	
		300.0 
		
			300.5 
			
				0.5 
				
					13.0 
					

  

	Including 
	
		311.0 
		
			316.0 
			
				5.0 
				
					7.9 
					

  

	And including 
	
		311.0 
		
			312.0 
			
				1.0 
				
					11.3 
					

No upper cut-off grade and a 0.4g/t Au lower cut-off applied. Unless specified, 
true widths cannot be accurately determined from the information available. 
Bold intervals referred to in text of release. Refer to this spreadsheet for 
details of previously released drilling intercepts. Eoh – End of Hole. 

[IMAGE]

View source version on businesswire.com: 
https://www.businesswire.com/news/home/20210616005468/en/

Contacts

James Withall  Chief Executive Officer  jwithall@rupertresources.com 

Thomas Credland  Head of Corporate Development  tcredland@rupertresources.com 

Rupert Resources Ltd  82 Richmond Street East, Suite 203, Toronto, Ontario M5C 
1P1  Tel: +1 416-304-9004 

Web: http://rupertresources.com/ 

Source: Rupert Resources Ltd
Powered by Business Wire