Source	CANADA NEWSWIRE
Date	06/23/2021
Time	08:10:41 AM

Company	 Artemis Gold Inc.
Title	Artemis Provides Final Results of Grade Control Drilling of High-Grade
Near Surface Mineralization





    CDNX Symbol: ARTG











Press Release




" BC-Artemis-GradeControl   06-23 1984
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.409100:
^Artemis Provides Final Results of Grade Control Drilling of High-Grade
Near Surface Mineralization@

<<

--  12 m grading 17.5 g/t gold (starting at 15 m)
--  12 m grading 15.3 g/t gold (starting at 3 m)
--  45 m grading 5.6 g/t gold (starting at 18 m)
--  33 m grading 10.4 g/t gold (starting at 33 m)
--  21 m grading 12.4 g/t gold (starting at 18 m)
--  39 m grading 6.5 g/t gold (starting at 21 m)
--  27 m grading 12.5 g/t gold (starting at 24 m)
>>
VANCOUVER, BC, June 23, 2021 /CNW/ - Artemis Gold Inc. (TSXV: ARTG)
("Artemis" or the "Company") is pleased to provide a final report on the
results of its Grade Control drilling program (the "Program") targeting the
planned high- grade starter pit at the Company's Blackwater Gold project in
Central British Columbia, Canada ("Blackwater" or the "Project").
With all of the final assay results now completed and interpreted, the
Program has significantly increased confidence in the elevated gold grades
within the wide, near surface mineralization in the target area earmarked for
the first year of operations at Blackwater. Based on the results, the Program
supports the elevated gold grades at the beginning of the mine life as
outlined in the 2020 Pre-Feasibility Study for Blackwater ("Blackwater Gold
Project British Columbia NI 43- 101 Technical Report on Pre-Feasibility Study"
with an effective date of August 26, 2020, available on the Company's website
and on SEDAR at www.sedar.com ("2020 PFS")).
Grade Control Drilling Program The Program consisted of 561 holes and
33,216 m of reverse circulation ("RC") drilling, which commenced in mid-
November 2020 and concluded at the end of March 2021, one month ahead of
schedule.
The Program was designed to bring the drill density from up to 50 x 50m
diamond drill hole ("DDH") spacing down to 12.5 x 12.5m spacing, generating up
to 16 times the data when compared to the reserve definition drill program
conducted by the Project's previous owner, New Gold Inc. The Program targeted
a zone within the first 60 m (six mining benches) from surface containing in
excess of five million tonnes of high-grade ore to improve short-term mine
planning at the start of production.
The other primary objectives of the Program were to:
<<

--  Optimize the grade selectivity and mine schedule for managing the ore
tonnes and grade to be processed in the first year of operations;
--  More accurately delineate ore and waste boundaries to mitigate dilution;
--  Optimize drill and blast designs;
--  Provide a larger sample size to reduce grade variability.
<>>
In production, Artemis plans a continuous grade control drilling program
targeting mine blocks 9-12 months ahead of ore production to the mill to
maintain this discipline throughout the life of mine operations.
Summary of Selected Grade Control Drilling Results
Assay results from the full Program of 10,258 samples have now been
returned, confirming the planned high-grade early mining phase for Blackwater
(see attached Figure 1). Selected results from the last batch of assay results
from the Program are highlighted below:
Table 1: Near-Surface Intercepts from Grade Control Drilling Program1


Hole ID(x)

East

North   From

To (m)     Interval     Au             Ag
(m)                                 (g/t)(x)(x)        (g/t)(x)(x)




(x)(x)(x)
BWRC00088     375612.5     5892750.0         21             39           
18            9.3            23.8




(x)(x)(x)
BWRC00101     375450.0     5892750.0         24             39           
15            6.7            12.8




(x)(x)(x)
BWRC00110     375600.0     5892762.5         18             63           
45            5.6            11.1



(x)(x)(x)
incl.                                  18             21            3           
30.5            18.7




(x)(x)(x)
BWRC00119     375487.5     5892762.5          3             42           
39            4.0            10.5




(x)(x)(x)
BWRC00122     375450.0     5892762.5          3             45           
42            3.7            12.7




(x)(x)(x)
BWRC00147     375400.0     5892775.0          3             33           
30            3.5             5.6




(x)(x)(x)
BWRC00157     375537.5     5892787.5         33             66           
33           10.4            12.7



(x)(x)(x)

incl.                                  45             51            6           
39.4            36.3




(x)(x)(x)
BWRC00179     375575.0     5892800.0         21             45           
24            5.9             9.3




(x)(x)(x)
BWRC00180     375562.5     5892800.0         27             54           
27            5.8             9.5




(x)(x)(x)
BWRC00190     375437.5     5892800.0         18             39           
21           12.4            12.2



(x)(x)(x)

incl.                                  21             24            3           
43.2            29.2




(x)(x)(x)
BWRC00193     375400.0     5892800.0          9             18            
9           11.4            11.5



(x)(x)(x)

incl.                                   9             12            3           
22.5            11.9




(x)(x)(x)
BWRC00250     375250.0     5892812.5          6             60           
54            3.2             7.1




(x)(x)(x)
BWRC00251     375237.5     5892812.5         21             60           
39            6.5            10.8



(x)(x)(x)

incl.                                  51             54            3           
26.4            12.3




(x)(x)(x)
BWRC00259     375700.0     5892825.0          6             36           
30            4.0             4.2




(x)(x)(x)
BWRC00265     375625.0     5892825.0         45             54            
9           12.1            31.5



(x)(x)(x)

incl.                                  48             51            3           
21.5            57.2




(x)(x)(x)
BWRC00267     375600.0     5892825.0         21             48           
27            6.8            14.8




(x)(x)(x)
BWRC00280     375437.5     5892825.0         48             60           
12           12.6            15.5



(x)(x)(x)

incl.                                  51             54            3           
24.9            25.8




(x)(x)(x)
BWRC00297     375225.0     5892825.0         45             60           
15           11.9            36.4



(x)(x)(x)

incl.                                  54             57            3           
30.8            72.3




(x)(x)(x)
BWRC00298     375212.5     5892825.0         42             60           
18           48.7            12.0



(x)(x)(x)

incl.                                  57             60            3           
21.9            21.4




(x)(x)(x)
BWRC00319     375512.5     5892837.5         24             51           
27           12.5            16.7



(x)(x)(x)

incl.                                  39             42            3           
58.5            54.3




(x)(x)(x)
BWRC00344     375200.0     5892837.5         33             57           
24            7.9             6.3



(x)(x)(x)

incl.                                  45             48            3           
21.2            15.1




(x)(x)(x)
BWRC00357     375600.0     5892850.0         30             42           
12            9.9            68.7




(x)(x)(x)
BWRC00389     375200.0     5892850.0         45             57           
12           13.8            12.2



(x)(x)(x)

incl.                                  51             54            3           
27.5            13.9




BWRC00435     375450.0     5892875.0          3             15           
12           15.3            24.6




incl.                                   6              9            3           
50.7            81.3




BWRC00463     375512.5     5892887.5         33             57           
24            5.7            10.2




BWRC00520     375212.5     5892900.0         24             54           
30            3.5            13.0




BWRC00532     375225.0     5892912.5         21             54           
33            3.7             8.5




BWRC00538     375262.5     5892925.0         15             27           
12           17.5            25.8




incl.                                  18             24            6           
29.4            43.0
(x) All holes were drilled with a dip of -90º (vertical). Drill hole intercepts 
reflect minimum 70% of the true widths of the orebody. Only intercepts greater 
than 9 m of length and width x grade greater than 100 g-m of gold are reflected 
in
this news release.



(x)(x) Assay results are based on the leached Au and Ag after 5-hour 
LeachWELLTM accelerated leach, and exclude Au and Ag remaining in residue 
solids.



(x)(x)(x)Previously released grade control intercepts

______________________


(1) Refer to notes 1, 2, and 3 within the section entitled "Technical 
Disclosure" at the end of this press release
The LeachWELLTM assay method was selected to increase the sample size
from a more standard 50g to 1,000g sample, which reduces variability and
increases repeatability of assay results. Additionally, the LeachWELLTM method
increases the understanding of leachability of the orebody with the
information feeding directly into the process design. Extensive duplicate
analyses highlight excellent LeachWELLTM repeatability of assay results and
recoverable gold and silver.
Of the total samples assayed, 1,207 samples were also assayed for residue
gold and silver concentration in the LeachWELLTM residues, resulting in a
calculated overall recovery of 96.5% for gold and 69.3% for silver.
Including the previously released results, the Program has also confirmed
excellent continuity of mineralization, as illustrated in the sections
provided in Figures 3-7. The location of these sections is provided in Figure
2.
Steven Dean, Chairman and CEO, commented "The final results of the grade
control drilling program continue to indicate the potential for more tonnage
and more contained ounces within the high-grade starter zone, with the
potential to reduce the strip ratio at the beginning of the mine life. This
program confirms the strong continuity of high-grade mineralization at the
start of the mine life and provides a higher confidence level in the Phase 1
mining schedule outlined in the Company's 2020 Pre-Feasibility Study, further
derisking the start up of operations."
Technical Disclosure
Drill sampling consisted of reverse circulation drill cuttings being
collected at a drill mounted Metzke rotating cone splitter by Artemis
personnel on 3 m intervals. Samples were placed into bags and further split at
the Blackwater sampling facility to ~3 kg sample size using a jones riffle
splitter. Samples were tagged with barcodes, placed in a sample crate and a
laboratory dispatch form was completed. Samples were stored in a secure
location prior to shipping. Chain-of-custody procedures consisted of filling
out sample submittal forms that were sent to the laboratory with sample
shipments to make certain that all samples were received by the laboratory.
Sample preparation and analysis were performed by SGS Canada Inc. ("SGS"),
located in Burnaby, British Columbia, Canada. SGS holds ISO/IEC accreditation
for selected sample preparation and analytical techniques and is independent
of the Company. Sample preparation consisted of drying, crushing and
pulverizing to 75% passing 75 µm. Gold and silver analyses were performed
using a 5-hour 1,000 g LeachWELLTM method with an inductively coupled plasma
mass spectrometry finish (ICP-MS).
The representativeness of the LeachWELLTM analytical technique to a
mineral deposit is dependent on the leaching characteristics of the material
submitted. As no certified standard reference material had been prepared from
the same material that was to be leached, no standard reference materials were
inserted in the grade control sample stream to directly monitor analytical
precision. Precision checks consisted of comparisons to results from split
samples using 50 g fire assay methods, comparison of data to existing diamond
drill holes and review of SGS laboratory standards. Additionally, LeachWELLTM
tails solids were consistently checked for non leachable gold and silver using
50 g fire assay for gold and 2 g 4-acid digestion for silver. The Company
randomly inserted blank and duplicate samples into the sample stream as part
of the quality assurance and quality control (QA/QC) monitoring for the
Program at an insertion rate of ~14%. These samples had closely monitored
contamination, splitter functionality and analytical repeatability,
respectively. Mr. Klaus Popelka (Qualified Person) reviewed the available
Program data, and considers that the sample preparation, security, and
analytical procedures are acceptable. There are no drilling, sampling or
recovery factors known to the QP that could materially impact the accuracy and
reliability of the results presented in this news release.
Qualified Persons
Klaus Popelka, P. Geo., Manager Resource Geology for Artemis, and a QP as
defined by National Instrument 43-101, has reviewed, and approved the
scientific and technical information in this news release.
ARTEMIS GOLD INC.On behalf of the Board of Directors"Steven Dean"Chairman and 
Chief Executive Officer+1 604 558 1107
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary Note Regarding Forward-Looking Information
This news release contains certain "forward looking statements" and
certain "forward-looking information" as defined under applicable Canadian and
U.S. securities laws. Forward-looking statements and information can generally
be identified by the use of forward-looking terminology such as "may", "will",
"expect", "intend", "estimate", "anticipate", "believe", "continue", "plans",
"potential" or similar terminology. Forward-looking statements and information
are not historical facts, are made as of the date of this news release, and
include, but are not limited to, statements regarding the Program; the planned
next steps of the Company with respect to the Project, including permitting,
drilling programs, awarding EPC Contracts, arranging debt and equity
financing, consultation with indigenous groups and work on the Definitive
Feasibility Study; and other plans and expectations of the Company with
respect to the Project. These forward- looking statements involve numerous
risks and uncertainties and actual results may vary. Important factors that
may cause actual results to vary include without limitation, risks related to
the ability of the Company to accomplish its plans and objectives with respect
to the development of the Project within the expected timing or at all, the
timing and receipt of certain required approvals, changes in commodity prices,
changes in interest and currency exchange rates, risks inherent in exploration
and development activities, changes in development or mining plans due to
changes in logistical, technical or other factors, unanticipated operational
difficulties (including failure of plant, equipment or processes to operate in
accordance with specifications, cost escalation, unavailability of materials,
equipment or third party contractors, delays in the receipt of government
approvals, industrial dist
price of $0.10 per share to settle
outstanding debt for $3,184,355.

Number of Creditors:         4 Creditors




Insider /Pro Group
Participation:




Insider(equal sign)Y /

Amount Deemed Price


Creditor

Progroup(equal sign)P

Owing  per Share     (number sign) of Shares


Hamad M. Al-Wazzan
Y                   $1,184,355         $0.10    11,843,550


GEM Global Yield Fund LLC
SCS and GEM Investments
America, LLC (Christopher
Brown)
Y                   $1,500,000         $0.10    15,000,000
For further details, please refer to the Company's news release dated May
11, 2021. The Company shall issue a news release when the shares are issued
and the debt extinguished.
________________________________________
SOURCE TSX Venture Exchange



View original content:
http://www.newswire.ca/en/releases/archive/June2021/22/c1553.html

-0-                           06/22/2021
/For further information: Market Information Services at 1-888-873-8392,
or email: information(at)venture.com/
/Web Site: tsxventure.com /

CO:  TSX Venture Exchange
ST:  British Columbia
IN:  FIN


" BC-Artemis-GradeControl   06-23 1984
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.409100:
^Artemis Provides Final Results of Grade Control Drilling of High-Grade
Near Surface Mineralization@

<<

--  12 m grading 17.5 g/t gold (starting at 15 m)
--  12 m grading 15.3 g/t gold (starting at 3 m)
--  45 m grading 5.6 g/t gold (starting at 18 m)
--  33 m grading 10.4 g/t gold (starting at 33 m)
--  21 m grading 12.4 g/t gold (starting at 18 m)
--  39 m grading 6.5 g/t gold (starting at 21 m)
--  27 m grading 12.5 g/t gold (starting at 24 m)
>>
VANCOUVER, BC, June 23, 2021 /CNW/ - Artemis Gold Inc. (TSXV: ARTG)
("Artemis" or the "Company") is pleased to provide a final report on the
results of its Grade Control drilling program (the "Program") targeting the
planned high- grade starter pit at the Company's Blackwater Gold project in
Central British Columbia, Canada ("Blackwater" or the "Project").
With all of the final assay results now completed and interpreted, the
Program has significantly increased confidence in the elevated gold grades
within the wide, near surface mineralization in the target area earmarked for
the first year of operations at Blackwater. Based on the results, the Program
supports the elevated gold grades at the beginning of the mine life as
outlined in the 2020 Pre-Feasibility Study for Blackwater ("Blackwater Gold
Project British Columbia NI 43- 101 Technical Report on Pre-Feasibility Study"
with an effective date of August 26, 2020, available on the Company's website
and on SEDAR at www.sedar.com ("2020 PFS")).
Grade Control Drilling Program The Program consisted of 561 holes and
33,216 m of reverse circulation ("RC") drilling, which commenced in mid-
November 2020 and concluded at the end of March 2021, one month ahead of
schedule.
The Program was designed to bring the drill density from up to 50 x 50m
diamond drill hole ("DDH") spacing down to 12.5 x 12.5m spacing, generating up
to 16 times the data when compared to the reserve definition drill program
conducted by the Project's previous owner, New Gold Inc. The Program targeted
a zone within the first 60 m (six mining benches) from surface containing in
excess of five million tonnes of high-grade ore to improve short-term mine
planning at the start of production.
The other primary objectives of the Program were to:
<<

--  Optimize the grade selectivity and mine schedule for managing the ore
tonnes and grade to be processed in the first year of operations;
--  More accurately delineate ore and waste boundaries to mitigate dilution;
--  Optimize drill and blast designs;
--  Provide a larger sample size to reduce grade variability.
<>>
In production, Artemis plans a continuous grade control drilling program
targeting mine blocks 9-12 months ahead of ore production to the mill to
maintain this discipline throughout the life of mine operations.
Summary of Selected Grade Control Drilling Results
Assay results from the full Program of 10,258 samples have now been
returned, confirming the planned high-grade early mining phase for Blackwater
(see attached Figure 1). Selected results from the last batch of assay results
from the Program are highlighted below:
Table 1: Near-Surface Intercepts from Grade Control Drilling Program1


Hole ID(x)

East

North   From

To (m)     Interval     Au             Ag
(m)                                 (g/t)(x)(x)        (g/t)(x)(x)




(x)(x)(x)
BWRC00088     375612.5     5892750.0         21             39           
18            9.3            23.8




(x)(x)(x)
BWRC00101     375450.0     5892750.0         24             39           
15            6.7            12.8




(x)(x)(x)
BWRC00110     375600.0     5892762.5         18             63           
45            5.6            11.1



(x)(x)(x)
incl.                                  18             21            3           
30.5            18.7




(x)(x)(x)
BWRC00119     375487.5     5892762.5          3             42           
39            4.0            10.5




(x)(x)(x)
BWRC00122     375450.0     5892762.5          3             45           
42            3.7            12.7




(x)(x)(x)
BWRC00147     375400.0     5892775.0          3             33           
30            3.5             5.6




(x)(x)(x)
BWRC00157     375537.5     5892787.5         33             66           
33           10.4            12.7



(x)(x)(x)

incl.                                  45             51            6           
39.4            36.3




(x)(x)(x)
BWRC00179     375575.0     5892800.0         21             45           
24            5.9             9.3




(x)(x)(x)
BWRC00180     375562.5     5892800.0         27             54           
27            5.8             9.5




(x)(x)(x)
BWRC00190     375437.5     5892800.0         18             39           
21           12.4            12.2



(x)(x)(x)

incl.                                  21             24            3           
43.2            29.2




(x)(x)(x)
BWRC00193     375400.0     5892800.0          9             18            
9           11.4            11.5



(x)(x)(x)

incl.                                   9             12            3           
22.5            11.9




(x)(x)(x)
BWRC00250     375250.0     5892812.5          6             60           
54            3.2             7.1




(x)(x)(x)
BWRC00251     375237.5     5892812.5         21             60           
39            6.5            10.8



(x)(x)(x)

incl.                                  51             54            3           
26.4            12.3




(x)(x)(x)
BWRC00259     375700.0     5892825.0          6             36           
30            4.0             4.2




(x)(x)(x)
BWRC00265     375625.0     5892825.0         45             54            
9           12.1            31.5



(x)(x)(x)

incl.                                  48             51            3           
21.5            57.2




(x)(x)(x)
BWRC00267     375600.0     5892825.0         21             48           
27            6.8            14.8




(x)(x)(x)
BWRC00280     375437.5     5892825.0         48             60           
12           12.6            15.5



(x)(x)(x)

incl.                                  51             54            3           
24.9            25.8




(x)(x)(x)
BWRC00297     375225.0     5892825.0         45             60           
15           11.9            36.4



(x)(x)(x)

incl.                                  54             57            3           
30.8            72.3




(x)(x)(x)
BWRC00298     375212.5     5892825.0         42             60           
18           48.7            12.0



(x)(x)(x)

incl.                                  57             60            3           
21.9            21.4




(x)(x)(x)
BWRC00319     375512.5     5892837.5         24             51           
27           12.5            16.7



(x)(x)(x)

incl.                                  39             42            3           
58.5            54.3




(x)(x)(x)
BWRC00344     375200.0     5892837.5         33             57           
24            7.9             6.3



(x)(x)(x)

incl.                                  45             48            3           
21.2            15.1




(x)(x)(x)
BWRC00357     375600.0     5892850.0         30             42           
12            9.9            68.7




(x)(x)(x)
BWRC00389     375200.0     5892850.0         45             57           
12           13.8            12.2



(x)(x)(x)

incl.                                  51             54            3           
27.5            13.9




BWRC00435     375450.0     5892875.0          3             15           
12           15.3            24.6




incl.                                   6              9            3           
50.7            81.3




BWRC00463     375512.5     5892887.5         33             57           
24            5.7            10.2




BWRC00520     375212.5     5892900.0         24             54           
30            3.5            13.0




BWRC00532     375225.0     5892912.5         21             54           
33            3.7             8.5




BWRC00538     375262.5     5892925.0         15             27           
12           17.5            25.8




incl.                                  18             24            6           
29.4            43.0
(x) All holes were drilled with a dip of -90º (vertical). Drill hole intercepts 
reflect minimum 70% of the true widths of the orebody. Only intercepts greater 
than 9 m of length and width x grade greater than 100 g-m of gold are reflected 
in
this news release.



(x)(x) Assay results are based on the leached Au and Ag after 5-hour 
LeachWELLTM accelerated leach, and exclude Au and Ag remaining in residue 
solids.



(x)(x)(x)Previously released grade control intercepts

______________________


(1) Refer to notes 1, 2, and 3 within the section entitled "Technical 
Disclosure" at the end of this press release
The LeachWELLTM assay method was selected to increase the sample size
from a more standard 50g to 1,000g sample, which reduces variability and
increases repeatability of assay results. Additionally, the LeachWELLTM method
increases the understanding of leachability of the orebody with the
information feeding directly into the process design. Extensive duplicate
analyses highlight excellent LeachWELLTM repeatability of assay results and
recoverable gold and silver.
Of the total samples assayed, 1,207 samples were also assayed for residue
gold and silver concentration in the LeachWELLTM residues, resulting in a
calculated overall recovery of 96.5% for gold and 69.3% for silver.
Including the previously released results, the Program has also confirmed
excellent continuity of mineralization, as illustrated in the sections
provided in Figures 3-7. The location of these sections is provided in Figure
2.
Steven Dean, Chairman and CEO, commented "The final results of the grade
control drilling program continue to indicate the potential for more tonnage
and more contained ounces within the high-grade starter zone, with the
potential to reduce the strip ratio at the beginning of the mine life. This
program confirms the strong continuity of high-grade mineralization at the
start of the mine life and provides a higher confidence level in the Phase 1
mining schedule outlined in the Company's 2020 Pre-Feasibility Study, further
derisking the start up of operations."
Technical Disclosure
Drill sampling consisted of reverse circulation drill cuttings being
collected at a drill mounted Metzke rotating cone splitter by Artemis
personnel on 3 m intervals. Samples were placed into bags and further split at
the Blackwater sampling facility to ~3 kg sample size using a jones riffle
splitter. Samples were tagged with barcodes, placed in a sample crate and a
laboratory dispatch form was completed. Samples were stored in a secure
location prior to shipping. Chain-of-custody procedures consisted of filling
out sample submittal forms that were sent to the laboratory with sample
shipments to make certain that all samples were received by the laboratory.
Sample preparation and analysis were performed by SGS Canada Inc. ("SGS"),
located in Burnaby, British Columbia, Canada. SGS holds ISO/IEC accreditation
for selected sample preparation and analytical techniques and is independent
of the Company. Sample preparation consisted of drying, crushing and
pulverizing to 75% passing 75 µm. Gold and silver analyses were performed
using a 5-hour 1,000 g LeachWELLTM method with an inductively coupled plasma
mass spectrometry finish (ICP-MS).
The representativeness of the LeachWELLTM analytical technique to a
mineral deposit is dependent on the leaching characteristics of the material
submitted. As no certified standard reference material had been prepared from
the same material that was to be leached, no standard reference materials were
inserted in the grade control sample stream to directly monitor analytical
precision. Precision checks consisted of comparisons to results from split
samples using 50 g fire assay methods, comparison of data to existing diamond
drill holes and review of SGS laboratory standards. Additionally, LeachWELLTM
tails solids were consistently checked for non leachable gold and silver using
50 g fire assay for gold and 2 g 4-acid digestion for silver. The Company
randomly inserted blank and duplicate samples into the sample stream as part
of the quality assurance and quality control (QA/QC) monitoring for the
Program at an insertion rate of ~14%. These samples had closely monitored
contamination, splitter functionality and analytical repeatability,
respectively. Mr. Klaus Popelka (Qualified Person) reviewed the available
Program data, and considers that the sample preparation, security, and
analytical procedures are acceptable. There are no drilling, sampling or
recovery factors known to the QP that could materially impact the accuracy and
reliability of the results presented in this news release.
Qualified Persons
Klaus Popelka, P. Geo., Manager Resource Geology for Artemis, and a QP as
defined by National Instrument 43-101, has reviewed, and approved the
scientific and technical information in this news release.
ARTEMIS GOLD INC.On behalf of the Board of Directors"Steven Dean"Chairman and 
Chief Executive Officer+1 604 558 1107
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Cautionary Note Regarding Forward-Looking Information
This news release contains certain "forward looking statements" and
certain "forward-looking information" as defined under applicable Canadian and
U.S. securities laws. Forward-looking statements and information can generally
be identified by the use of forward-looking terminology such as "may", "will",
"expect", "intend", "estimate", "anticipate", "believe", "continue", "plans",
"potential" or similar terminology. Forward-looking statements and information
are not historical facts, are made as of the date of this news release, and
include, but are not limited to, statements regarding the Program; the planned
next steps of the Company with respect to the Project, including permitting,
drilling programs, awarding EPC Contracts, arranging debt and equity
financing, consultation with indigenous groups and work on the Definitive
Feasibility Study; and other plans and expectations of the Company with
respect to the Project. These forward- looking statements involve numerous
risks and uncertainties and actual results may vary. Important factors that
may cause actual results to vary include without limitation, risks related to
the ability of the Company to accomplish its plans and objectives with respect
to the development of the Project within the expected timing or at all, the
timing and receipt of certain required approvals, changes in commodity prices,
changes in interest and currency exchange rates, risks inherent in exploration
and development activities, changes in development or mining plans due to
changes in logistical, technical or other factors, unanticipated operational
difficulties (including failure of plant, equipment or processes to operate in
accordance with specifications, cost escalation, unavailability of materials,
equipment or third party contractors, delays in the receipt of government
approvals, industrial disturbances, job action, and unanticipated events
related to heath, safety and environmental matters), the COVID-19 pandemic,
political risk, social unrest, changes in general economic conditions or
conditions in the financial markets, and other risks related to the ability of
the Company to proceed with its plans for the Project and other risks set out
in the Company's most recent MD&A. In making the forward-looking statements in
this news release, the Company has applied several material assumptions,
including without limitation, the assumptions that: (1) market fundamentals
will result in sustained mineral demand and prices; (2) the receipt of any
necessary approvals and consents in connection with the development of the
Project; (3) the availability of financing on suitable terms for the
development, construction and continued operation of the Project; (4)
sustained commodity prices such that the Project remains economically viable;
and (5) that the COVID-19 pandemic and restrictions related thereto will not
materially impact the Company or prevent the Company from operating its
business as planned. The actual results or performance by the Company could
differ materially from those expressed in, or implied by, any forward-looking
statements. Accordingly, no assurances can be given that any of the events
anticipated by the forward-looking statements will transpire or occur, or if
any of them do so, what impact they will have on the results of operations or
financial condition of the Company. Except as required by law, the Company is
under no obligation, and expressly disclaim any obligation, to update, alter
or otherwise revise any forward-looking statement, whether written or oral,
that may be made from time to time, whether as a result of new information,
future events or otherwise, except as may be required under applicable
securities laws.
SOURCE Artemis Gold Inc.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/June2021/23/c2822.html

-0-                           06/23/2021
/For further information: Nick Campbell, VP Capital Markets, +1 (604)
558-1107/
(ARTG.)

CO:  Artemis Gold Inc.
ST:  British Columbia
IN:  MNG
SU:

-30-



price of $0.10 per share to settle
outstanding debt for $3,184,355.

Number of Creditors:         4 Creditors




Insider /Pro Group
Participation:




Insider(equal sign)Y /

Amount Deemed Price


Creditor

Progroup(equal sign)P

Owing  per Share     (number sign) of Shares


Hamad M. Al-Wazzan
Y                   $1,184,355         $0.10    11,843,550


GEM Global Yield Fund LLC
SCS and GEM Investments
America, LLC (Christopher
Brown)
Y                   $1,500,000         $0.10    15,000,000
For further details, please refer to the Company's news release dated May
11, 2021. The Company shall issue a news release when the shares are issued
and the debt extinguished.
________________________________________
SOURCE TSX Venture Exchange



View original content:
http://www.newswire.ca/en/releases/archive/June2021/22/c1553.html

-0-                           06/22/2021
/For further information: Market Information Services at 1-888-873-8392,
or email: information(at)venture.com/
/Web Site: tsxventure.com /

CO:  TSX Venture Exchange
ST:  British Columbia
IN:  FIN