Source	MARKET NEWS
Date	03/16/2005
Time	08:49:06 AM
Company	American Bonanza Gold Mining Corp.
Title	Drills 24.1 Grams per Tonne Gold over 7.5 Metres 3





  DMIS Processed No  CDNX Symbol: BZA
Exchange: VSE  Symbol: BZA
Exchange:   Symbol: 
Exchange:   Symbol: 








Press Release	




[200/News Release]BZAVAMERICAN BONANZA GOLD MINING CORPMAR 16 2005  08:46 
AMDrills 24.1 Grams per Tonne Gold over 7.5 Metres 3.0 MetresTrue Thickness 
--->@NEWS RELEASEAMERICAN BONANZA GOLD MINING CORP  ("BZA-V")
- Drills 24.1 Grams per Tonne Gold over 7.5 Metres-3.0 Metres
- True Thickness

AMERICAN BONANZA GOLD MINING CORP. announces an update to the
underground drilling program at its 100% owned high-grade Copperstone
gold project in Arizona.
D-Zone Underground Core Drilling
Underground core drilling continues at the D-Zone. Objectives of this
underground core drilling program are conversion of known historic
indicated and inferred resources into measured resources and reserves, and
mine planning. A total of 61 holes have been drilled with a combined length
of 5,780 metres. Approximately 1,350 metres in 15 planned holes remain to
be drilled in the program, which is about 80% complete and has a budget for
the entire program of approximately US$1 million.
The most significant intercepts in the new assay results include a 7.5
metre zone grading 24.1 g/t gold in drill hole number DU5-57; a 3.5 metre
zone grading 24.7 g/t gold in drill hole number DU5-58; and a 4.3 metre
zone grading 26.9 g/t gold in drill hole number DU5-59.
As previously reported, these D-Zone drill intercepts are oblique to
the mineralized Copperstone fault; true thicknesses of the D-Zone range up
to 7 metres thick. True thickness of the DU5-57 intercept is 3 metres, with
true thickness for the other intercepts announced here being generally
between 2 and 3 metres.
The following table is a summary of assay results for this group of
underground holes from the D-Zone drilling program:

//st

Hole ID      From - To     Intercept    Gold      Gold    Copper
(ft)         (m)       (g/t)    (opt)      (%)

DU5-57        90.7-115.5      7.5       24.1     0.702      TR

including     90.7-95.2       1.4       59.2     1.726      TR

DU5-58        39.4-51.0       3.5       24.7     0.720      0.3

and           57.2-67.0       3.0        3.4     0.098      1.2

DU5-59           0-5.8        1.8       14.5     0.424      0.3

and           16.5-24.0       2.3       14.5     0.424      0.3

and          114.4-118.4      1.2       29.5     0.860      TR

and          140.5-154.5      4.3       26.9     0.786      TR

DU5-60           0-14.0       4.3       12.1     0.352      TR

DU5-61           0-2.3        0.7       21.6     0.631      TR

and           72.9-79.2       1.9       32.1     0.937      TR

and           85.1-107.0      6.7       14.9     0.436      TR

//et

Surface drilling programs continue on the project with a total of 6
drilling rigs currently active.
American Bonanza Gold Mining Corp. and International Taurus Resources
Inc. (TSX VENTURE:ITS) have signed a Definitive Agreement to merge
companies, and have signed an agreement with Fairstar Explorations Inc.
(TSX:FFR) to consolidate ownership of the Fenelon Gold Project in Quebec.
All three Boards of Directors are unanimously in support of the
transaction. Approval for this agreement will be voted on by the
shareholders of the companies at individual meetings to be held on March
24, 2005. We encourage all shareholders to vote "YES" for the merger and
transaction.
DETAILED INFORMATION
The Copperstone gold mineralization occurs within a package of
sedimentary and volcanic rocks, in northwest striking, moderate to
shallow dipping fault zones, principally the Copperstone Fault.
Intensely sheared, altered and replaced rock characterizes the
Copperstone Fault in the vicinity of the D-Zone. Alteration consisting
of intense hematite and magnetite replacement, chloritization and
silicification has been observed in the Copperstone Fault underground
and is consistent with alteration visible in previous drilling and the
current drilling from surface.
Gold mineralization is restricted to these fault zones, with little to
no gold mineralization present in the wallrocks. Future exploration and
development efforts will target these mineralized faults to follow up along
strike and dip from the current results and previously drilled
mineralization.
Drilling services are being provided by international drilling
contractors: Layne Christensen Company of Chandler, Arizona. The
drilling and assaying are conducted under the supervision of Gregory
French, CPG #10708, a Qualified Person as defined in Canadian National
Instrument 43-101.
Underground core is NQ size, equaling 2 inches in diameter. The core
samples are collected by Bonanza personnel at the drill for each drill
hole. All of Bonanza's facilities are secure, inside the fenced compound.
The core is transported to Bonanza's core processing facility on site at
Copperstone by Bonanza personnel.
All core is logged for recovery and other geotechnical features, prior
to being sawed lengthwise in half by Bonanza personnel. Individual core
samples are selected on a geological basis to characterize the gold
mineralization associated with various rock types, alteration types and
structural horizons. Subsequent to sawing and sampling, the remaining half
core is geologically logged and stored on site as reference samples.
Assay sample sizes average 5.9 pounds for the underground drilling.
The core samples are bagged, labeled and tied at the Copperstone project
site by Bonanza personnel. Geologic information is recorded on standardized
sample description forms which included color, rock type, alteration,
mineral species and abundance. Samples are stored in a secure facility at
the Copperstone project site.
DATS Trucking, Inc. collects samples from the secure facility at
Copperstone and transports the samples to representatives of American
Assay Laboratories (AAL) in Sparks, Nevada. There, representatives of
American Assay Laboratories (AAL) in Sparks, Nevada receive the samples
and take custody of the samples. AAL is ISO / IEC 17025 certified and
has successfully completed Canadian proficiency testing (CCRMP).
At the AAL laboratory, the core samples are dried, crushed to -10
mesh, pulverized to -150 mesh, split to 1,000 gram pulps, and fire assayed
for gold two times using 2-assay ton fire assay charges with a gravimetric
finish. Reported gold grades are the average of these two assays for each
sample. A total of 296 core samples from the underground drilling were
assayed in duplicate. There is good correlation between the duplicate
assays. All samples greater than 0.100 opt, standards, and blanks are
routinely submitted to additional labs for verification. An additional 21
standards were inserted for assay for the drill holes announced here.
Check assays are routinely submitted to BSI-Inspectorate, Sparks, NV
5-assay ton gold analysis. BSI-Inspectorate is ISO 9002 certified. Bonanza
personnel deliver the samples to the check labs.
Additional information about Bonanza can be obtained at:
www.americanbonanza.com
AMERICAN BONANZA GOLD MINING CORP.
Brian Kirwin, President and Chief Executive Officer

Capitalization Report for American Bonanza Gold Mining Corp
Shares Issued: 188029350
Shares Escrow: 0

TSX Venture closing price for American Bonanza
Date: 2005/03/15
Closing Price: 0.155

TEL:  (604) 688-7523    American Bonanza Gold Mining Corp.
Catherine Tanaka, Investor Relations
Internet: www.americanbonanza.com
______________________________
___________________________________________________________________
(c) Market News Publishing Inc.  Tel:(604) 689-1101
All rights reserved.         Fax:(604) 689-1106
MarketbyFax(tm) - To get the NEWS as it happens, call (604) 689-3041.

050316KF+5+000319


[200/News Release]BZAVAMERICAN BONANZA GOLD MINING CORPMAR 16 2005  08:46 
AMDrills 24.1 Grams per Tonne Gold over 7.5 Metres 3.0 MetresTrue Thickness 
--->@NEWS RELEASEAMERICAN BONANZA GOLD MINING CORP  ("BZA-V")
- Drills 24.1 Grams per Tonne Gold over 7.5 Metres-3.0 Metres
- True Thickness

AMERICAN BONANZA GOLD MINING CORP. announces an update to the
underground drilling program at its 100% owned high-grade Copperstone
gold project in Arizona.
D-Zone Underground Core Drilling
Underground core drilling continues at the D-Zone. Objectives of this
underground core drilling program are conversion of known historic
indicated and inferred resources into measured resources and reserves, and
mine planning. A total of 61 holes have been drilled with a combined length
of 5,780 metres. Approximately 1,350 metres in 15 planned holes remain to
be drilled in the program, which is about 80% complete and has a budget for
the entire program of approximately US$1 million.
The most significant intercepts in the new assay results include a 7.5
metre zone grading 24.1 g/t gold in drill hole number DU5-57; a 3.5 metre
zone grading 24.7 g/t gold in drill hole number DU5-58; and a 4.3 metre
zone grading 26.9 g/t gold in drill hole number DU5-59.
As previously reported, these D-Zone drill intercepts are oblique to
the mineralized Copperstone fault; true thicknesses of the D-Zone range up
to 7 metres thick. True thickness of the DU5-57 intercept is 3 metres, with
true thickness for the other intercepts announced here being generally
between 2 and 3 metres.
The following table is a summary of assay results for this group of
underground holes from the D-Zone drilling program:

//st

Hole ID      From - To     Intercept    Gold      Gold    Copper
(ft)         (m)       (g/t)    (opt)      (%)

DU5-57        90.7-115.5      7.5       24.1     0.702      TR

including     90.7-95.2       1.4       59.2     1.726      TR

DU5-58        39.4-51.0       3.5       24.7     0.720      0.3

and           57.2-67.0       3.0        3.4     0.098      1.2

DU5-59           0-5.8        1.8       14.5     0.424      0.3

and           16.5-24.0       2.3       14.5     0.424      0.3

and          114.4-118.4      1.2       29.5     0.860      TR

and          140.5-154.5      4.3       26.9     0.786      TR

DU5-60           0-14.0       4.3       12.1     0.352      TR

DU5-61           0-2.3        0.7       21.6     0.631      TR

and           72.9-79.2       1.9       32.1     0.937      TR

and           85.1-107.0      6.7       14.9     0.436      TR

//et

Surface drilling programs continue on the project with a total of 6
drilling rigs currently active.
American Bonanza Gold Mining Corp. and International Taurus Resources
Inc. (TSX VENTURE:ITS) have signed a Definitive Agreement to merge
companies, and have signed an agreement with Fairstar Explorations Inc.
(TSX:FFR) to consolidate ownership of the Fenelon Gold Project in Quebec.
All three Boards of Directors are unanimously in support of the
transaction. Approval for this agreement will be voted on by the
shareholders of the companies at individual meetings to be held on March
24, 2005. We encourage all shareholders to vote "YES" for the merger and
transaction.
DETAILED INFORMATION
The Copperstone gold mineralization occurs within a package of
sedimentary and volcanic rocks, in northwest striking, moderate to
shallow dipping fault zones, principally the Copperstone Fault.
Intensely sheared, altered and replaced rock characterizes the
Copperstone Fault in the vicinity of the D-Zone. Alteration consisting
of intense hematite and magnetite replacement, chloritization and
silicification has been observed in the Copperstone Fault underground
and is consistent with alteration visible in previous drilling and the
current drilling from surface.
Gold mineralization is restricted to these fault zones, with little to
no gold mineralization present in the wallrocks. Future exploration and
development efforts will target these mineralized faults to follow up along
strike and dip from the current results and previously drilled
mineralization.
Drilling services are being provided by international drilling
contractors: Layne Christensen Company of Chandler, Arizona. The
drilling and assaying are conducted under the supervision of Gregory
French, CPG #10708, a Qualified Person as defined in Canadian National
Instrument 43-101.
Underground core is NQ size, equaling 2 inches in diameter. The core
samples are collected by Bonanza personnel at the drill for each drill
hole. All of Bonanza's facilities are secure, inside the fenced compound.
The core is transported to Bonanza's core processing facility on site at
Copperstone by Bonanza personnel.
All core is logged for recovery and other geotechnical features, prior
to being sawed lengthwise in half by Bonanza personnel. Individual core
samples are selected on a geological basis to characterize the gold
mineralization associated with various rock types, alteration types and
structural horizons. Subsequent to sawing and sampling, the remaining half
core is geologically logged and stored on site as reference samples.
Assay sample sizes average 5.9 pounds for the underground drilling.
The core samples are bagged, labeled and tied at the Copperstone project
site by Bonanza personnel. Geologic information is recorded on standardized
sample description forms which included color, rock type, alteration,
mineral species and abundance. Samples are stored in a secure facility at
the Copperstone project site.
DATS Trucking, Inc. collects samples from the secure facility at
Copperstone and transports the samples to representatives of American
Assay Laboratories (AAL) in Sparks, Nevada. There, representatives of
American Assay Laboratories (AAL) in Sparks, Nevada receive the samples
and take custody of the samples. AAL is ISO / IEC 17025 certified and
has successfully completed Canadian proficiency testing (CCRMP).
At the AAL laboratory, the core samples are dried, crushed to -10
mesh, pulverized to -150 mesh, split to 1,000 gram pulps, and fire assayed
for gold two times using 2-assay ton fire assay charges with a gravimetric
finish. Reported gold grades are the average of these two assays for each
sample. A total of 296 core samples from the underground drilling were
assayed in duplicate. There is good correlation between the duplicate
assays. All samples greater than 0.100 opt, standards, and blanks are
routinely submitted to additional labs for verification. An additional 21
standards were inserted for assay for the drill holes announced here.
Check assays are routinely submitted to BSI-Inspectorate, Sparks, NV
5-assay ton gold analysis. BSI-Inspectorate is ISO 9002 certified. Bonanza
personnel deliver the samples to the check labs.
Additional information about Bonanza can be obtained at:
www.americanbonanza.com
AMERICAN BONANZA GOLD MINING CORP.
Brian Kirwin, President and Chief Executive Officer

Capitalization Report for American Bonanza Gold Mining Corp
Shares Issued: 188029350
Shares Escrow: 0

TSX Venture closing price for American Bonanza
Date: 2005/03/15
Closing Price: 0.155

TEL:  (604) 688-7523    American Bonanza Gold Mining Corp.
Catherine Tanaka, Investor Relations
Internet: www.americanbonanza.com
______________________________
___________________________________________________________________
(c) Market News Publishing Inc.  Tel:(604) 689-1101
All rights reserved.         Fax:(604) 689-1106
MarketbyFax(tm) - To get the NEWS as it happens, call (604) 689-3041.

050316KF+5+000319