Source	CCNMatthews
Date	03/16/2005
Time	08:38:43 AM
Company	AMERICAN BONANZA GOLD MINING CORP.
Title	American Bonanza Drills 24.1 Grams per Tonne Gold over 7.5 Metres-3.0 
Metres True Thickness





  DMIS Processed No  CDNX Symbol: BZA
Exchange: Mining Corp.TSX VENTURE  Symbol: BZA
Exchange:   Symbol: 
Exchange:   Symbol: 








Press Release	




[IMAGE] [IMAGE]

[IMAGE]


NEWS RELEASE TRANSMITTED BY CCNMatthews[IMAGE]FOR : American Bonanza Gold 
Mining Corp.TSX VENTURE SYMBOL:  BZA


March 16, 2005American Bonanza Drills 24.1 Grams per Tonne Gold over 7.5 
Metres-3.0 Metres
True ThicknessVANCOUVER, BRITISH COLUMBIA--(CCNMatthews - March 16, 2005) - 
AMERICAN BONANZA
GOLD MINING CORP. (TSX VENTURE:BZA) announces an update to the underground
drilling program at its 100% owned high-grade Copperstone gold project in
Arizona.

D-Zone Underground Core Drilling

Underground core drilling continues at the D-Zone. Objectives of this
underground core drilling program are conversion of known historic indicated
and inferred resources into measured resources and reserves, and mine planning.
A total of 61 holes have been drilled with a combined length of 5,780 metres.
Approximately 1,350 metres in 15 planned holes remain to be drilled in the
program, which is about 80% complete and has a budget for the entire program of
approximately US$1 million.

The most significant intercepts in the new assay results include a 7.5 metre
zone grading 24.1 g/t gold in drill hole number DU5-57; a 3.5 metre zone
grading 24.7 g/t gold in drill hole number DU5-58; and a 4.3 metre zone grading
26.9 g/t gold in drill hole number DU5-59.

As previously reported, these D-Zone drill intercepts are oblique to the
mineralized Copperstone fault; true thicknesses of the D-Zone range up to 7
metres thick. True thickness of the DU5-57 intercept is 3 metres, with true
thickness for the other intercepts announced here being generally between 2 and
3 metres.

The following table is a summary of assay results for this group of underground
holes from the D-Zone drilling program:

/T/

Hole ID      From - To    Intercept Gold   Gold   Copper
   (ft)       (m) (g/t)  (opt)     (%)
-----------------------------------------------------------------
DU5-57       90.7-115.5      7.5 24.1  0.702     TR
-----------------------------------------------------------------
including     90.7-95.2       1.4 59.2  1.726     TR
-----------------------------------------------------------------
DU5-58       39.4-51.0       3.5 24.7  0.720     0.3
-----------------------------------------------------------------
and       57.2-67.0       3.0  3.4  0.098     1.2
-----------------------------------------------------------------
DU5-59   0-5.8       1.8 14.5  0.424     0.3
-----------------------------------------------------------------
and       16.5-24.0       2.3 14.5  0.424     0.3
-----------------------------------------------------------------
and      114.4-118.4      1.2 29.5  0.860     TR
-----------------------------------------------------------------
and      140.5-154.5      4.3 26.9  0.786     TR
-----------------------------------------------------------------
DU5-60   0-14.0       4.3 12.1  0.352     TR
-----------------------------------------------------------------
DU5-61   0-2.3       0.7 21.6  0.631     TR
-----------------------------------------------------------------
and       72.9-79.2       1.9 32.1  0.937     TR
-----------------------------------------------------------------
and       85.1-107.0      6.7 14.9  0.436     TR
-----------------------------------------------------------------

/T/

Surface drilling programs continue on the project with a total of 6 drilling
rigs currently active.

American Bonanza Gold Mining Corp. and International Taurus Resources Inc. (TSX
VENTURE:ITS) have signed a Definitive Agreement to merge companies, and have
signed an agreement with Fairstar Explorations Inc. (TSX:FFR) to consolidate
ownership of the Fenelon Gold Project in Quebec. All three Boards of Directors
are unanimously in support of the transaction. Approval for this agreement will
be voted on by the shareholders of the companies at individual meetings to be
held on March 24, 2005. We encourage all shareholders to vote "YES" for the
merger and transaction.

DETAILED INFORMATION

The Copperstone gold mineralization occurs within a package of sedimentary and
volcanic rocks, in northwest striking, moderate to shallow dipping fault zones,
principally the Copperstone Fault. Intensely sheared, altered and replaced rock
characterizes the Copperstone Fault in the vicinity of the D-Zone. Alteration
consisting of intense hematite and magnetite replacement, chloritization and
silicification has been observed in the Copperstone Fault underground and is
consistent with alteration visible in previous drilling and the current
drilling from surface.

Gold mineralization is restricted to these fault zones, with little to no gold
mineralization present in the wallrocks. Future exploration and development
efforts will target these mineralized faults to follow up along strike and dip
from the current results and previously drilled mineralization.

Drilling services are being provided by international drilling contractors:
Layne Christensen Company of Chandler, Arizona. The drilling and assaying are
conducted under the supervision of Gregory French, CPG #10708, a Qualified
Person as defined in Canadian National Instrument 43-101.

Underground core is NQ size, equling 2 inches in diameter. The core samples
are collected by Bonanza personnel at the drill for each drill hole. All of
Bonanza's facilities are secure, inside the fenced compound. The core is
transported to Bonanza's core processing facility on site at Copperstone by
Bonanza personnel.

All core is logged for recovery and other geotechnical features, prior to being
sawed lengthwise in half by Bonanza personnel. Individual core samples are
selected on a geological basis to characterize the gold mineralization
associated with various rock types, alteration types and structural horizons.
Subsequent to sawing and sampling, the remaining half core is geologically
logged and stored on site as reference samples.

Assay sample sizes average 5.9 pounds for the underground drilling. The core
samples are bagged, labeled and tied at the Copperstone project site by Bonanza
personnel. Geologic information is recorded on standardized sample description
forms which included color, rock type, alteration, mineral species and
abundance. Samples are stored in a secure facility at the Copperstone project
site.

DATS Trucking, Inc. collects samples from the secure facility at Copperstone
and transports the samples to representatives of American Assay Laboratories
(AAL) in Sparks, Nevada. There, representatives of American Assay Laboratories
(AAL) in Sparks, Nevada receive the samples and take custody of the samples.
AAL is ISO / IEC 17025 certified and has successfully completed Canadian
proficiency testing (CCRMP).

At the AAL laboratory, the core samples are dried, crushed to -10 mesh,
pulverized to -150 mesh, split to 1,000 gram pulps, and fire assayed for gold
two times using 2-assay ton fire assay charges with a gravimetric finish.
Reported gold grades are the average of these two assays for each sample. A
total of 296 core samples from the underground drilling were assayed in
duplicate. There is good correlation between the duplicate assays. All samples
greater than 0.100 opt, standards, and blanks are routinely submitted to
additional labs for verification. An additional 21 standards were inserted for
assay for the drill holes announced here.

Check assays are routinely submitted to BSI-Inspectorate, Sparks, NV 5-assay
ton gold analysis. BSI-Inspectorate is ISO 9002 certified. Bonanza personnel
deliver the samples to the check labs.

Additional information about Bonanza can be obtained at:www.americanbonanza.com
AMERICAN BONANZA GOLD MINING CORP.

Brian Kirwin, President and Chief Executive Officer



- 30 -FOR FURTHER INFORMATION PLEASE CONTACT :
American Bonanza Gold Mining Corp.
Catherine Tanaka
Investor Relations
Phone: (604) 688-7523
or
American Bonanza Gold Mining Corp.
Suite 1606-675 W. Hastings St.
Vancouver, BC V6B 1N2www.americanbonanza.comThe TSX Venture Exchange has not 
reviewed and does not accept responsibility
for the adequacy or accuracy of this news release.
INDUSTRY : ONF
SUBJECT : DRM

[IMAGE]

[IMAGE][IMAGE][IMAGE]