Source	Marketwire
Date	03/26/2013
Time	06:00:39 AM

Company	 VENERABLE VENTURES LTD.
Title	Venerable Ventures Ltd. Hits 0.33 g/t Gold Over 47.8 Metres at Trout





    CDNX Symbol: VLV











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRE


FOR: Venerable Ventures Ltd.

TSX VENTURE SYMBOL: VLV

March 26, 2013

Venerable Ventures Ltd. Hits 0.33 g/t Gold Over 47.8 Metres at Trout


VANCOUVER, BRITISH COLUMBIA--(Marketwire - March 26, 2013) - Venerable Ventures 
Ltd. (TSX VENTURE:VLV) ("Venerable" or the "Company") is pleased to provide an 
update for its exploration activities on the Trout Property. Four of the seven 
target areas previously identified by the Company known as the Cap, Camp, Camp 
(North) and Discovery zones were tested with eight trenches and ten drill holes 
during 2012.

Highlights of results include drill hole TR12-05 assaying 0.33 g/t gold over 
47.8 metres from the Camp Zone and drill hole TR12-09 assaying 0.44 g/t gold 
over 16.0 metres from the Camp (North) Zone located 425 metres northeast. These 
results combined with other untested geochemical and geophysical anomalies 
outline significant zones of gold enrichment in areas that have seen little or 
no previous work. Further work is anticipated by the Company.

Gold is associated with a graben bounding fault structure. Structures such as 
these are well documented for hosting both bulk and high-grade bonanza style 
gold and silver deposition.

In July Venerable trenched a total of 206 metres across eight profiles in the 
Camp and Camp (North) areas. Rock chip samples with gold were hosted in 
predominantly brecciated and vuggy zones of silicified porphyritic volcanic 
rock. Significant results from the Camp Zone include 21.1 metres grading 0.41 
g/t gold in trench TR-B and 16.0 metres grading 0.13 g/t gold in trench TR-E. 
At the Camp (North) Zone limited bedrock exposure from trenching was only able 
to isolate a single 2 metre outcrop that assayed 2.13 g/t gold.

The diamond drill program took part from September to October, 2012. Ten holes 
were drilled into four target areas within the boundaries of the graben feature 
for a total of 2019 metres.

/T/

----------------------------------------------------------------------------
HOLE-ID           FROM m       TO m  LENGTH m  AU_PPM  AG_PPM           Zone
----------------------------------------------------------------------------
TR12-01                      Lost at 53m                                 Cap
----------------------------------------------------------------------------
TR12-1A                No significant results                            Cap
----------------------------------------------------------------------------
TR12-02                No significant results                            Cap
----------------------------------------------------------------------------
TR12-03                No significant results                            Cap
----------------------------------------------------------------------------
TR12-04       Overburden  Hole lost                                      Cap
----------------------------------------------------------------------------
TR12-05            36.00      54.00     18.00    0.09     0.8           Camp
----------------------------------------------------------------------------
TR12-05            74.00     121.82     47.82    0.33     1.8           Camp
----------------------------------------------------------------------------
TR12-06            15.00      23.00      8.00    0.11     2.0           Camp
----------------------------------------------------------------------------
TR12-06            43.00      49.00      6.00    0.14     0.9           Camp
----------------------------------------------------------------------------
TR12-06            81.00      85.70      4.70    0.22     2.3           Camp
----------------------------------------------------------------------------
TR12-07                    no samples taken                             Camp
----------------------------------------------------------------------------
TR12-08            12.26      40.00     27.74    0.24     1.2   Camp (North)
----------------------------------------------------------------------------
TR12-09            18.29      27.34      9.05    0.20     1.0   Camp (North)
----------------------------------------------------------------------------
TR12-09            42.00      58.00     16.00    0.44     2.4   Camp (North)
----------------------------------------------------------------------------
TR12-09            78.00     100.00     22.00    0.10     1.2   Camp (North)
----------------------------------------------------------------------------
TR12-10            18.29      84.00     65.71    0.17     2.2      Discovery
----------------------------------------------------------------------------

/T/

All samples were delivered by truck to ALS Geochemistry in North Vancouver, BC, 
where each complete sample was crushed to 70% material less than 2mm in 
diameter. A 1kg split was then pulverized to better than 85% passing 75 microns 
(approx. 200 mesh). A 1.0 gram portion of the pulp was then digested in hot 
aqua regia and analyzed for 34 elements by ICP-AES method. All samples were 
also analyzed specifically for gold by fire assay and ICP-AES with a 30g 
nominal weight.

At the Cap Zone, holes TR12-01A thru TR12-03 tested a 300 metre by 300 metre IP 
chargeability and resistivity anomaly occurring at depths between 150 and 225 
metres below surface. The holes intersected up to 125 metres of partially 
silicified pyrite rich quartz feldspar porphyry intrusive, likely representing 
the cause of the IP anomaly. The unit intrudes rhyodacite, trachyte and minor 
andesite and conglomeratic formations. Although gold was not found in the drill 
core this intrusive activity could be key in generating surrounding epithermal 
overprints within the Trout graben.

Holes TR12-05 thru TR12-10 show that gold mineralization at the Camp, Camp 
(North) and Discovery zones occurs predominantly in altered volcanic rocks 
predominately rhyodacitic to trachytic in composition. The best exploration 
potential in this area lies within the Camp (North) Zone where holes TR12-08 
and 09 intercepted wide zones of gold mineralization associated with quartz 
healed porphyritic trachyte breccia unit. The zone outcrops immediately below 
thin overburden, measures 300 metres by 200 metres in diameter and varies in 
thicknesses from 16 to 27 metres. It has a moderate resistivity IP signature 
and remains open in three directions.

Besides additional drill testing on the Camp (North) and the Cap Zones during 
the 2013 field season, including follow-up studies on Targets 5, 6 and 7 the 
Company plans to widen its exploration efforts to cover other prospective areas 
on the property that have received little or no previous work.

Technical information in this news release has been reviewed and approved by 
Jim Cuttle P.Geo a Qualified Person as defined in NI 43-101. For more 
information see the Company's technical report entitled "Technical Report: 
Trout Property" dated March 23, 2011, available on SEDAR at www.sedar.com.

About the Company

Venerable Ventures is a Canadian natural resource company engaged in the 
acquisition, exploration and development of mineral properties, with its 
primary focus on the Trout Property. The Trout Property is 65km southwest of 
Vanderhoof, BC on the Nechako Plateau and covers an area of 7179 Hectares. The 
property is approximately 40km NNE of NewGold'sBlackwater Project.

ON BEHALF OF THE BOARD

VENERABLE VENTURES LTD.

Ryan Sharp, President, Chief Executive Officer and Director

- 30 -

CONTACT INFO:

Venerable Ventures Ltd.
Ryan Sharp
President and CEO
(604) 647-0146
Fax: (604) 647-0143
ryan@venerableventuresltd.com
www.venerableventuresltd.com

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

MWDisclaimer
If you no longer want to receive announcements from us, please do 
not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=414410093