Source	MARKET NEWS
Date	03/20/2014
Time	08:27:31 AM

Company	 Rockhaven Resources Ltd.
Title	Plans 
12,000 M Of Diamond Drilling At Klaza Proj





    CDNX Symbol: RK











Press Release	





ROCKHAVEN RESOURCES LTD ("RK-V")
- Plans 12,000 M Of Diamond Drilling At Klaza Project, Yukon

Rockhaven Resources Ltd. ("Rockhaven") is pleased to announce that
funding is in place for the 2014 exploration program at its 100% owned
Klaza gold-silver property, located in the Dawson Range Gold Belt of
southern Yukon. Drilling and trenching at the road-accessible Klaza
property since 2010 have identified nine main mineralized structural
zones and numerous subsidiary structures within an 2000 by 4000 m
corridor. Individually, the main zones range from 1 to 75 m in width
and are continuously mineralized over strike lengths of 250 to 2400 m.
The zones have been traced over a cumulative strike length of 9400 m
and all remain open for expansion along strike and to depth.

The proposed 2014 program will include 12,000 m of diamond
drilling and will focus on delineating and expanding areas of
high-grade gold and silver mineralization ()8.00 g/t gold EQ). 2014
drill targets will include:

//st

The Western BRX Zone, where 2013 trenching and limited
broadly-spaced drilling have returned strong results over a 750 m strike
length, including 68.27 g/t gold EQ (50.1 g/t gold and 910 g/t silver) over
3.25 m from trench TR-13-58 and 8.00 g/t gold EQ (5.78 g/t gold and 111 g/t
silver) over 15.62 m from hole DH-12-96;

The Western Klaza Zone, where trenching and drilling returned numerous gold
and silver-rich intervals including 11.15 g/t gold EQ (4.51 g/t gold and
332 g/t silver) over 7.12 m from hole DH-12-115;

The Central Klaza Zone beneath hole DH-12-133, the deepest intercept to
date on the zone, which intersected 12.00 g/t gold EQ (11.90 g/t gold and
5.23 g/t silver) over 6.70 m at a depth of 310 m below surface; and,

The Pearl Zone, a 2013 discovery where two excavator trenches situated 450
m apart averaged 29.04 g/t gold EQ (23.98 g/t gold and 254 g/t silver) over
1.22 m.

//et

"We are very excited to build on the success and knowledge gained
from recent programs at the Klaza property which have outlined multiple
mineralized structures over long strike lengths," stated Matt Turner,
CEO of Rockhaven Resources. "We are now in a position to focus on
defining the higher-grade parts of these extensive systems, while
advancing other blue-sky targets within this evolving gold district."

Maps and cross-sections related to the Klaza project can be viewed
at the Company's website at www.rockhavenresources.com. Further details
of the 2014 exploration program and targets follow below:

Western BRX Zone

The Western BRX Zone is the main target of 2014 diamond drilling.
Infill and step-out excavator trenching in 2013 at the Western BRX Zone
confirmed continuity of the mineralized structure and further
delineated areas of high-grade gold and silver that were partially
outlined by widely-spaced drill holes in 2011 and 2012. Highlight
results are shown below:

//st

Drill Hole/     From     To    Interval   Gold   Silver  Gold EQ
Trench          (m)     (m)    (m)(+)    (g/t)   (g/t)   (g/t)*
=============  ======  ======  ========  ======  ======  =======
DH-11-37        81.13   95.93     14.80    5.43      50     6.43
-------------  ------  ------  --------  ------  ------  -------
DH-11-39       151.29  152.94      1.65   23.50     239    28.28
-------------  ------  ------  --------  ------  ------  -------
DH-12-72       178.48  179.81      1.33   10.60      23    11.06
-------------  ------  ------  --------  ------  ------  -------
DH-12-96       329.74  345.36     15.62    5.78     111     8.00
-------------  ------  ------  --------  ------  ------  -------
TR-13-47        30.05   31.20      1.15    87.0     768   102.36
-------------  ------  ------  --------  ------  ------  -------
TR-13-49         1.61    2.92      1.31    8.42     548    19.38
-------------  ------  ------  --------  ------  ------  -------
TR-13-58         3.35    6.60      3.25    50.1     910    68.27
-------------  ------  ------  --------  ------  ------  -------
TR-13-59        11.05   15.20      4.15    7.47     537    18.20
-------------  ------  ------  --------  ------  ------  -------
TR-13-67        35.00   38.55      3.55   31.38     310    37.59
-------------  ------  ------  --------  ------  ------  -------
TR-13-73         3.70    6.20      2.50   26.10     574    37.58
-------------  ------  ------  --------  ------  ------  -------
TR-13-74        12.45   14.70      2.25   31.20    1030    51.80
-------------  ------  ------  --------  ------  ------  -------
TR-13-75         4.75    6.20      1.45   11.50    1680    45.10
-------------  ------  ------  --------  ------  ------  -------
and            17.24   20.24      3.00   34.70     160    37.90
------------  ------  ------  --------  ------  ------  -------
TR-13-77         5.08    7.18      2.10   14.40     729    28.98
-------------  ------  ------  --------  ------  ------  -------



+ Represents the diamond drill hole or trench sample
length. True widths are estimated to be approximately
80-90% of the interval.
* Gold equivalence (EQ) has been calculated using
metal prices of $1300 per ounce gold and $26.00 per
ounce silver, to be consistent with earlier calculations
and assumes 100% recoveries.

Central and Western Klaza Zones

The Central and Western Klaza Zones host discrete veins, breccias and
sheeted veinlets that have been traced over a strike length of 1000 m and
to a depth of 325 m down dip. Focused diamond drilling in 2014 will expand
the area of known mineralization to the west and to depth where some of the
best results have been returned to date. Highlight results from the Central
and Western Klaza Zone include:



Drill Hole/    From     To    Interval   Gold   Silver  Gold EQ
Trench         (m)     (m)    (m)(+)    (g/t)   (g/t)   (g/t)*
============  ======  ======  ========  ======  ======  =======
DH-10-07      134.00  149.30     15.30    7.20     260    12.40
------------  ------  ------  --------  ------  ------  -------
DH-11-16       88.04   94.82      6.78    6.09     101     8.11
------------  ------  ------  --------  ------  ------  -------
DH-11-28      253.66  255.12      1.46   10.25     585    21.95
------------  ------  ------  --------  ------  ------  -------
DH-12-79       91.56   94.77      3.21    3.18     516    13.50
------------  ------  ------  --------  ------  ------  -------
DH-12-115     214.47  221.59      7.12    4.51     332    11.15
------------  ------  ------  --------  ------  ------  -------
DH-12-133     439.00  445.70      6.70   11.90    5.23    12.00
------------  ------  ------  --------  ------  ------  -------
TR-13-51       11.19   29.98     18.79    5.61     300    11.61
------------  ------  ------  --------  ------  ------  -------
TR-13-52        3.75   10.59      6.84   16.20     158    19.36
------------  ------  ------  --------  ------  ------  -------
TR-13-66       18.72   20.99      2.27   25.70     449    34.68
------------  ------  ------  --------  ------  ------  -------
TR-13-69        5.16    9.76      4.60    8.29     295    14.20
------------  ------  ------  --------  ------  ------  -------
TR-13-70        2.50    5.53      3.03   16.76    1052    37.80
------------  ------  ------  --------  ------  ------  -------
//et

//st
+ Represents the diamond drill hole or trench sample length. True widths
are estimated to be approximately 80-90% of the interval.
* Gold equivalence (EQ) has been calculated using metal prices of $1300 per
ounce gold & $26.00 per ounce silver, to be consistent with earlier
calculations & assumes 100% recoveries.

//et

Pearl Zone

The Pearl Zone was discovered in 2013 and represents the most
easterly, and if projected westward, the most northerly mineralized
structure identified at the Klaza property. Two excavator trench
exposures located 450 m apart returned 28.2 g/t gold and 359 g/t silver
(35.38 g/t gold EQ) over 1.20 m and 19.75 g/t gold and 148 g/t silver
(22.71 g/t gold EQ) over 1.25 m (see Rockhaven news release dated
October 3, 2013). The results are particularly important as no
mineralization was previously known in this area. Detailed follow-up
drilling will be done in 2014 to evaluate this new high-grade gold and
silver discovery, which is open to extension along strike in both
directions.

Other Targets

A small proportion of the planned drilling will evaluate
particularly encouraging areas in the other six known mineralized
zones. In addition, some prospecting, geological mapping and
geophysical surveying will be completed in other areas of the property
to define additional targets for drilling or trenching. All of the
mineralized zones discovered to date at Klaza are marked by linear
magnetic lows with coincident soil geochemical anomalies. In areas
surveyed, these magnetic lows coincide with distinct chargeability
highs and resistivity lows. The focus will be on defining and, as
warranted, drill testing similar anomalies elsewhere on the property,
with particular emphasis on overburden covered areas to the west of the
Western BRX and Western Klaza Zones. In conjunction with 2014 work,
ongoing baseline environmental surveys and geotechnical data collection
will continue to advance the Klaza property toward the permitting
process.

The 2014 exploration program is scheduled to start in early June.
The $3,000,000 non-brokered private placement financing announced on
February 25 2014 is fully subscribed and subject to TSX Venture
Exchange acceptance, will be closed in the coming days.

The 2014 program will be managed by Archer, Cathro & Associates
(1981) Limited (Archer Cathro). Technical information in this news
release has been approved by Matthew R. Dumala, P.Eng., a geological
engineer with Archer Cathro and qualified person for the purpose of
National Instrument 43-101.

Rockhaven Resources Ltd. is a well-funded company focused on
growth through exploration of its own wholly-owned projects and
continues to work towards adding new advanced-stage projects to its
portfolio. For additional information concerning Rockhaven Resources
Ltd. or its various exploration projects please visit Rockhaven's
website at www.rockhavenresources.com.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
RELEASE.

TSX Venture closing price for RK-V
Date: 2014/03/19
Closing Price: 0.21

TEL:  604-688-2568 Matthew Turner, CEO and Director
EMAIL:  mturner@nordacres.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1407800027TS11407801772-08253120140320