Source	Marketwire
Date	03/20/2014
Time	08:15:13 AM

Company	 ROCKHAVEN RESOURCES LTD.
Title	Rockhaven Resources Ltd. Plans 12,000 m of Diamond Drilling at Klaza 
Project, Yukon





    CDNX Symbol: RK











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Rockhaven Resources Ltd.

TSX VENTURE SYMBOL: RK

March 20, 2014

Rockhaven Resources Ltd. Plans 12,000 m of Diamond Drilling at Klaza Project, 
Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - March 20, 2014) - Rockhaven 
Resources Ltd. (TSX VENTURE:RK) ("Rockhaven") is pleased to announce that 
funding is in place for the 2014 exploration program at its 100% owned Klaza 
gold-silver property, located in the Dawson Range Gold Belt of southern Yukon. 
Drilling and trenching at the road-accessible Klaza property since 2010 have 
identified nine main mineralized structural zones and numerous subsidiary 
structures within an 2000 by 4000 m corridor. Individually, the main zones 
range from 1 to 75 m in width and are continuously mineralized over strike 
lengths of 250 to 2400 m. The zones have been traced over a cumulative strike 
length of 9400 m and all remain open for expansion along strike and to depth.

The proposed 2014 program will include 12,000 m of diamond drilling and will 
focus on delineating and expanding areas of high-grade gold and silver 
mineralization (greater than 8.00 g/t gold EQ). 2014 drill targets will include:

/T/

--  The Western BRX Zone, where 2013 trenching and limited broadly-spaced
drilling have returned strong results over a 750 m strike length,
including 68.27 g/t gold EQ (50.1 g/t gold and 910 g/t silver) over 3.25
m from trench TR-13-58 and 8.00 g/t gold EQ (5.78 g/t gold and 111 g/t
silver) over 15.62 m from hole DH-12-96;
--  The Western Klaza Zone, where trenching and drilling returned numerous
gold and silver-rich intervals including 11.15 g/t gold EQ (4.51 g/t
gold and 332 g/t silver) over 7.12 m from hole DH-12-115;
--  The Central Klaza Zone beneath hole DH-12-133, the deepest intercept to
date on the zone, which intersected 12.00 g/t gold EQ (11.90 g/t gold
and 5.23 g/t silver) over 6.70 m at a depth of 310 m below surface; and,
--  The Pearl Zone, a 2013 discovery where two excavator trenches situated
450 m apart averaged 29.04 g/t gold EQ (23.98 g/t gold and 254 g/t
silver) over 1.22 m.

/T/

"We are very excited to build on the success and knowledge gained from recent 
programs at the Klaza property which have outlined multiple mineralized 
structures over long strike lengths," stated Matt Turner, CEO of Rockhaven 
Resources. "We are now in a position to focus on defining the higher-grade 
parts of these extensive systems, while advancing other blue-sky targets within 
this evolving gold district."

Maps and cross-sections related to the Klaza project can be viewed at the 
Company's website at www.rockhavenresources.com. Further details of the 2014 
exploration program and targets follow below:

Western BRX Zone

The Western BRX Zone is the main target of 2014 diamond drilling. Infill and 
step-out excavator trenching in 2013 at the Western BRX Zone confirmed 
continuity of the mineralized structure and further delineated areas of 
high-grade gold and silver that were partially outlined by widely-spaced drill 
holes in 2011 and 2012. Highlight results are shown below:

/T/

--------------------------------------------------------------------------
Drill Hole/       From        To   Interval      Gold    Silver    Gold EQ
Trench             (m)       (m)       (m)+     (g/t)     (g/t)   (g/t)(i)
--------------------------------------------------------------------------
--------------------------------------------------------------------------
DH-11-37         81.13     95.93      14.80      5.43        50       6.43
--------------------------------------------------------------------------
DH-11-39        151.29    152.94       1.65     23.50       239      28.28
--------------------------------------------------------------------------
DH-12-72        178.48    179.81       1.33     10.60        23      11.06
--------------------------------------------------------------------------
DH-12-96        329.74    345.36      15.62      5.78       111       8.00
--------------------------------------------------------------------------
TR-13-47         30.05     31.20       1.15      87.0       768     102.36
--------------------------------------------------------------------------
TR-13-49          1.61      2.92       1.31      8.42       548      19.38
--------------------------------------------------------------------------
TR-13-58          3.35      6.60       3.25      50.1       910      68.27
--------------------------------------------------------------------------
TR-13-59         11.05     15.20       4.15      7.47       537      18.20
--------------------------------------------------------------------------
TR-13-67         35.00     38.55       3.55     31.38       310      37.59
--------------------------------------------------------------------------
TR-13-73          3.70      6.20       2.50     26.10       574      37.58
--------------------------------------------------------------------------
TR-13-74         12.45     14.70       2.25     31.20      1030      51.80
--------------------------------------------------------------------------
TR-13-75          4.75      6.20       1.45     11.50      1680      45.10
--------------------------------------------------------------------------
and             17.24     20.24       3.00     34.70       160      37.90
--------------------------------------------------------------------------
TR-13-77          5.08      7.18       2.10     14.40       729      28.98
--------------------------------------------------------------------------
+ Represents the diamond drill hole or trench sample length. True widths are
estimated to be approximately 80-90% of the interval.
(i) Gold equivalence (EQ) has been calculated using metal prices of $1300
per ounce gold and $26.00 per ounce silver, to be consistent with earlier
calculations and assumes 100% recoveries.

/T/

Central and Western Klaza Zones

The Central and Western Klaza Zones host discrete veins, breccias and sheeted 
veinlets that have been traced over a strike length of 1000 m and to a depth of 
325 m down dip. Focused diamond drilling in 2014 will expand the area of known 
mineralization to the west and to depth where some of the best results have 
been returned to date. Highlight results from the Central and Western Klaza 
Zone include:

/T/

--------------------------------------------------------------------------
Drill Hole/       From        To   Interval      Gold    Silver    Gold EQ
Trench             (m)       (m)       (m)+     (g/t)     (g/t)   (g/t)(i)
--------------------------------------------------------------------------
--------------------------------------------------------------------------
DH-10-07        134.00    149.30      15.30      7.20       260      12.40
--------------------------------------------------------------------------
DH-11-16         88.04     94.82       6.78      6.09       101       8.11
--------------------------------------------------------------------------
DH-11-28        253.66    255.12       1.46     10.25       585      21.95
--------------------------------------------------------------------------
DH-12-79         91.56     94.77       3.21      3.18       516      13.50
--------------------------------------------------------------------------
DH-12-115       214.47    221.59       7.12      4.51       332      11.15
--------------------------------------------------------------------------
DH-12-133       439.00    445.70       6.70     11.90      5.23      12.00
--------------------------------------------------------------------------
TR-13-51         11.19     29.98      18.79      5.61       300      11.61
--------------------------------------------------------------------------
TR-13-52          3.75     10.59       6.84     16.20       158      19.36
--------------------------------------------------------------------------
TR-13-66         18.72     20.99       2.27     25.70       449      34.68
--------------------------------------------------------------------------
TR-13-69          5.16      9.76       4.60      8.29       295      14.20
--------------------------------------------------------------------------
TR-13-70          2.50      5.53       3.03     16.76      1052      37.80
--------------------------------------------------------------------------
+ Represents the diamond drill hole or trench sample length. True widths are
estimated to be approximately 80-90% of the interval.
(i) Gold equivalence (EQ) has been calculated using metal prices of $1300
per ounce gold and $26.00 per ounce silver, to be consistent with earlier
calculations and assumes 100% recoveries.

/T/

Pearl Zone

The Pearl Zone was discovered in 2013 and represents the most easterly, and if 
projected westward, the most northerly mineralized structure identified at the 
Klaza property. Two excavator trench exposures located 450 m apart returned 
28.2 g/t gold and 359 g/t silver (35.38 g/t gold EQ) over 1.20 m and 19.75 g/t 
gold and 148 g/t silver (22.71 g/t gold EQ) over 1.25 m (see Rockhaven news 
release dated October 3, 2013). The results are particularly important as no 
mineralization was previously known in this area. Detailed follow-up drilling 
will be done in 2014 to evaluate this new high-grade gold and silver discovery, 
which is open to extension along strike in both directions.

Other Targets

A small proportion of the planned drilling will evaluate particularly 
encouraging areas in the other six known mineralized zones. In addition, some 
prospecting, geological mapping and geophysical surveying will be completed in 
other areas of the property to define additional targets for drilling or 
trenching. All of the mineralized zones discovered to date at Klaza are marked 
by linear magnetic lows with coincident soil geochemical anomalies. In areas 
surveyed, these magnetic lows coincide with distinct chargeability highs and 
resistivity lows. The focus will be on defining and, as warranted, drill 
testing similar anomalies elsewhere on the property, with particular emphasis 
on overburden covered areas to the west of the Western BRX and Western Klaza 
Zones. In conjunction with 2014 work, ongoing baseline environmental surveys 
and geotechnical data collection will continue to advance the Klaza property 
toward the permitting process.

The 2014 exploration program is scheduled to start in early June. The 
$3,000,000 non-brokered private placement financing announced on February 25 
2014 is fully subscribed and subject to TSX Venture Exchange acceptance, will 
be closed in the coming days.

The 2014 program will be managed by Archer, Cathro & Associates (1981) Limited 
(Archer Cathro). Technical information in this news release has been approved 
by Matthew R. Dumala, P.Eng., a geological engineer with Archer Cathro and 
qualified person for the purpose of National Instrument 43-101.

Rockhaven Resources Ltd. is a well-funded company focused on growth through 
exploration of its own wholly-owned projects and continues to work towards 
adding new advanced-stage projects to its portfolio. For additional information 
concerning Rockhaven Resources Ltd. or its various exploration projects please 
visit Rockhaven's website at www.rockhavenresources.com.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

- 30 -

CONTACT INFO:

Rockhaven Resources Ltd.
Matthew Turner
CEO and Director
604-688-2568
mturner@nordacres.com
www.rockhavenresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=472995314