Source	Marketwire
Date	03/27/2014
Time	05:45:13 AM

Company	 FLINDERS RESOURCES LIMITED
Title	Flinders Commissions Rod Mill at Woxna Graphite Mine, Sweden





    CDNX Symbol: FDR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Flinders Resources Limited

TSX VENTURE SYMBOL: FDR

March 27, 2014

Flinders Commissions Rod Mill at Woxna Graphite Mine, Sweden


VANCOUVER, BRITISH COLUMBIA--(Marketwired - March 27, 2014) - Flinders 
Resources Limited ("Flinders" or the "Company") (TSX VENTURE:FDR) is pleased to 
provide an update on the work program underway to restart graphite production 
from the Woxna mine and processing facility in central Sweden. Woxna is a fully 
permitted brownfields graphite mine, having been on care and maintenance since 
2001. The plant refurbishment is on track to recommence production in July 2014.

Key points:

/T/

--  The Company has completed the dry commissioning of the refurbished rod
mill;
--  Process controls systems refurbishment activities are progressing on
schedule and budget;
--  Material handling equipment re-installation works are underway after
grit blasting and painting completed earlier this month;
--  Further plant equipment is being refurbished as required to enable the
plant to commence production by July 2014.

/T/

Flinders' President and CEO, Blair Way said: "The rod mill is a critical piece 
of equipment and its commissioning is a key milestone for the restart of 
operations. Our refurbishment plan is coming together well, and we are tracking 
on budget and schedule for our July restart. Our site team is doing a great job 
pulling all these components together for our restart."

On behalf of the Board,

Blair Way, President and CEO

Forward-Looking Information

Certain information in this presentation may constitute forward-looking 
statements or forward-looking information within the meaning of applicable 
securities laws (collectively, "Forward-Looking Statements"). All statements, 
other than statements of historical fact that address activities, events or 
developments that the Company believes, expects or anticipates will or may 
occur in the future are Forward-Looking Statements. Forward-Looking Statements 
are often, but not always, identified by the use of words such as "seek," 
"anticipate," "believe," "plan," "estimate," "expect," and "intend" and 
statements that an event or result "may," "will," "can," "should," "could," or 
"might" occur or be achieved and other similar expressions. Forward-Looking 
Statements are based upon the opinions and expectations of the Company based on 
information currently available to the Company. Forward-Looking Statements are 
subject to a number of factors, risks and uncertainties that may cause the 
actual results of the Company to differ materially from those discussed in the 
Forward-Looking Statements including, among other things, the Company has yet 
to generate a profit from its activities;
there can be no guarantee that the estimates of quantities or qualities of 
minerals disclosed in the Company's public record will be economically 
recoverable; uncertainties relating to the availability and costs of financing 
needed in the future; competition with other companies within the mining 
industry; the success of the Company is largely dependent upon the performance 
of its directors and officers and the Company's ability to attract and train 
key personnel; changes in world metal markets and equity markets beyond the 
Company's control; mineral reserves are, in the large part, estimates and no 
assurance can be given that the anticipated tonnages and grades will be 
achieved or that the indicated level of recovery will be realized; production 
rates and capital and other costs may vary significantly from estimates; the 
Company's decision to restart production at the Woxna graphite project is based 
on historical production and the Company's preliminary economic assessment of 
the project and the Company has no plans to first complete a pre-feasibility or 
feasibility study on the project, as a result there is an increased risk of 
technical and economic failure for the Woxna graphite project; unexpected 
geological conditions; delays in obtaining or failure to obtain necessary 
permits and approvals from government authorities; all phases of a mining 
business present environmental and safety risks and hazards and are subject to 
environmental and safety regulation, and rehabilitation and restitution costs; 
the Company does not maintain insurance against environmental risks; and 
management of the Company have experience in mineral exploration but may lack 
all or some of the necessary technical training and experience to successfully 
develop and operate a mine. Although the Company believes that the expectations 
reflected in the Forward-Looking Statements, and the assumptions on which such 
Forward-Looking Statements are made, are reasonable, there can be no assurance 
that such expectations will prove to be correct. Readers are cautioned not to 
place undue reliance on Forward-Looking Statements, as there can be no 
assurance that the plans, intentions or expectations upon which the 
Forward-Looking Statements are based will occur. Forward-Looking Statements 
herein are made as at the date hereof, and unless otherwise required by law, 
the Company does not intend, or assume any obligation, to update these 
Forward-Looking Statements.

Preliminary Economic Assessment

The Company advises that it has not based its production decision on a 
feasibility study of mineral reserves, demonstrating economic and technical 
viability, and, as a result, there may be an increased uncertainty of achieving 
any particular level of recovery of minerals or the cost of such recovery, 
including increased risks associated with developing a commercially mineable 
deposit. Historically, such projects have a much higher risk of economic and 
technical failure. There is no guarantee that production will begin as 
anticipated or at all or that anticipated production costs will be achieved. 
Failure to commence production would have a material adverse impact on the 
Company's ability to generate revenue and cash flow to fund operations. Failure 
to achieve the anticipated production costs would have a material adverse 
impact on the Company's cash flow and future profitability.

The Company further cautions that the PEA is preliminary in nature. No mining 
study has been completed. Mineral resources are not mineral reserves and do not 
have demonstrated economic viability. There is no certainty that the PEA will 
be realized.

Cautionary Note to United States Readers Concerning Resource and Reserve 
Estimates:

This release has been prepared in accordance with the requirements of the 
securities laws in effect in Canada which differ in certain material respects 
from the disclosure requirements of United States securities laws.

The terms "mineral resource," "measured mineral resource," "indicated mineral 
resource" and "inferred mineral resource" are Canadian mining terms as defined 
in accordance with National Instrument 43-101 - Standards of Disclosure for 
Mineral Projects ("NI 43-101") and the Canadian Institute of Mining, Metallurgy 
and Petroleum's (the "CIM") - CIM Definition Standards on Mineral Resources and 
Mineral Reserves, adopted by the CIM Council, as may be amended from time to 
time by the CIM. These terms are not defined terms under the United States 
Securities and Exchange Commission (the "SEC") Industry Guide 7 ("SEC Industry 
Guide 7") under the Securities Act of 1933 and normally are not permitted to be 
used in reports and registration statements filed with the SEC.

Readers are cautioned not to assume that any part or all of the mineral 
deposits in these categories will ever be converted into "reserves" (as defined 
in SEC Industry Guide 7). "Inferred mineral resources" have a great amount of 
uncertainty as to their existence, and great uncertainty as to their economic 
and legal feasibility. It cannot be assumed that all or any part of an inferred 
mineral resource will ever be upgraded to a higher category. Under Canadian 
rules, estimates of inferred mineral resources may not form the basis of an 
economic analysis, except a preliminary economic assessment provided certain 
additional disclosure requirements are met. Readers are cautioned not to assume 
that all or any part of an inferred mineral resource exists or is economically 
or legally mineable. Disclosure of "contained ounces" in a resource is 
permitted disclosure under Canadian regulations; however, the SEC normally only 
permits issuers to report mineralization that does not constitute "reserves" by 
SEC Industry Guide 7 standards as in place tonnage and grade without reference 
to unit measures.

Accordingly, information contained in this presentation and any documents 
incorporated by reference herein containing descriptions of our mineral 
deposits may not be comparable to similar information made public by U.S. 
companies subject to the reporting and disclosure requirements under the United 
States federal securities laws and the rules and regulations thereunder.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or the accuracy of this news release.

- 30 -

CONTACT INFO:

Flinders Resources Limited
Jim Powell
+1 647-478-5806
info@flindersresources.com

INDUSTRY: Environment - Natural Resource Management
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=473996202