Source	MARKET NEWS
Date	03/10/2014
Time	06:10:49 AM

Company	 Vulcan Minerals Inc.
Title	Completes 
Labrador Nickel copper pge Property Da





    CDNX Symbol: VUL











Press Release	





VULCAN MINERALS INC ("VUL-V;VULMF-0")
- Completes Labrador Nickel-copper-pge Property Data Evaluation

Vulcan Minerals Inc. ("the Company" - "Vulcan") has completed an
internal report entitled 'Report on a Review of Geophysical Data,
Tasisuak Lake Property, Labrador (Nickel, Copper, Platinum Group
Elements)" authored by Corwin Northcott, P. Geo.,
Geophysicist/Exploration Manager for the Company. The report is not
compliant with National Instrument 43-101 Standards as it is designed
for internal exploration program design purposes. A comprehensive
review, digitization and database creation was completed to allow
several vintages of geophysical data to be integrated and correlated
with drill results and geology. The data were internally correlated
with historic information which required geo-referencing and digital
editing. As a result the Company now has an unprecedented database from
which to advance the understanding, exploration and development of this
property.

The Company owns a 100% working interest in the property covering
219 claims (13,529 acres) in northern Labrador approximately 50
kilometres northwest of the Voisey's Bay nickel-copper mine. In excess
of $3,000,000 of exploration expenses have been incurred on the
property by previous operators, the bulk of those expenditures were by
parties that had optioned the property from the Company. The company
re-acquired a 100% interest in the property in 2012 subject to a capped
royalty with buyout rights.

The Property has undergone four rounds of drilling, 2040 metres
(m) in 1995, 1700 m in 1996 (associated with the Voisey's Bay staking
rush), 2300 m in 2005 and 1960 m in 2008. Much of the drilling focussed
on outcrop mineralization and as a result had relatively shallow depth
penetration of less than 150 metres. In addition to the nickel-copper
discoveries, anomalous platinum group elements and gold were also
encountered in the mineralized zones. Some of the near surface drilling
highlights are as follows; Nickel (Ni), Copper (Cu) Cobalt (Co):

//st

14 metres of 1.02% Ni, 0.51% Cu, 0.03% Co, (Hole 08-AA-60)

9 metres of 1.02% Ni, 0.55% Cu, 0.04% Co, (Hole 08-LP-55)

3 metres of 1.04% Ni, 0.38% Cu, 0.03% Co (Hole 08-LP-56)

3 metres of 1.01% Ni, 0.39% Cu, 0.04% Co (Hole 08-AA-62)

//et

The property includes claims covered by three airborne frequency
domain electromagnetic systems spread over three different grids
(1400km) in 1995 and a VTEM time domain system (610km) in 2008. Ground
surveys include three magnetic and HLEM grids, three UTEM grids, two
gravity grids and one induced polarization (IP) grid dating from
1995-2005.

The property contains disseminated, stringer and semi-massive
pyrrhotite, chalcopyrite (Copper) and pentlandite (Nickel) hosted in
norite intrusives; and massive pyrrhotite (barren) in close affinity
with graphite bearing gneisses. All of the rocks have anomalous
magnetic and electrical properties. The exploration challenge is to
discriminate the nickel-copper sulphides from the unmineralized
pyrrhotite and graphitic gneiss. As a result of the interpretational
work, several matrices were used to identify and prioritize potential
drill targets with geophysical attributes comparable to the known
nickel-copper bearing norite occurrences. Multiple new drill targets
have been identified over trends exceeding seven (7) km in length. This
is in addition to the delineation targets on the known mineralized
zones.

The Company is of the view that the property requires an extensive
drill campaign to systematically evaluate the various targets,
especially given the proven nickel-copper magmatic sulphides already
discovered at surface. The Company plans to solicit joint venture
partners to advance the exploration of the property. However the
Company is currently reviewing the merits of conducting its own 2014
summer field program to ground check the various new drill targets
identified from the geophysical/geological review. Plans for a 2014
work program will be released as formulated.

Patrick J. Laracy, P. Geo, President, and Corwin Northcott, P.
Geo, Exploration Manager, are qualified persons responsible for the
contents of this news release as defined in National Instrument 43-101.


Vulcan is a diversified junior exploration company with mineral
exploration and petroleum interests in Canada.

The TSX Venture Exchange has not reviewed and does not accept
responsibility for the adequacy or accuracy of this release. This
release may contain certain forward-looking statements. Actual events
or results may differ from the Company's expectations. Certain risk
factors beyond the Company's control may affect the actual results
achieved. Accordingly, readers are advised not to place undue reliance
on forward-looking information. Except by law, the Company undertakes
no obligation to publicly update or revise forward-looking information.
We seek safe harbour.

TSX Venture closing price for VUL-V
Date: 2014/03/07
Closing Price: 0.04

TEL:  (709) 754-3186 Patrick Laracy, President
FAX:  (709) 754-3946
EMAIL:  info@vulcanminerals.ca
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1406800015TS11406800934-06100120140310